## Slide 1: Ocean 21 SPR Compliance (FIT/16 WP/5)
Date: 28 October 2008
Presented to: Informal Pacific ATC Co-Ordinating Group (IPACG/29) FANS 1/A Interoperability Team (FIT/16)
By: Tom Kraft, Chief Scientific and Technical Advisor for Aeronautical Communications, Aviation Safety, Federal Aviation Administration Email: tom.kraft@faa.gov Mobile: +1-202-369-2168
DO-306/ED-122 safety requirements for ground systems

## Slide 2: Overview
Introduction
Assessment results
FIT/16 action

## Slide 3: Introduction
DO-306/ED-122, Oceanic SPR Standard
  Twenty seven (27) safety requirements for the application of data link services in oceanic airspace
  Twenty four (24) are applicable to ATSP ground systems
  See Appendix A of WP
FAA has completed its assessment to determine the level of compliance with these requirements
Summary of assessment  Not compliant with 2 requirements, partially compliant with 1

## Slide 4: Assessment results
Timestamp in every uplink CPDLC message (SR-9)
  Target compliance date – February 2009
Indication to controller upon receipt of message that exceeds the ETTRN (SR-15)
  Some questions on implementation strategy related to mixed performance capability, e.g., HF aircraft versus satellite & use of message header timestamp
  Others should clarify safety benefit

## Slide 5: Assessment results
Indication to controller when operational response is not received by ETTRN (SR-14)
  Partially compliance, value set to 300 seconds, but ETTRN is 210 seconds
  Long term solution  differentiate between RCP 240 and RCP 400 operations
  Target compliance date – to be determined

## Slide 6: FIT/16 action
Note the safety requirements allocated to the ATSP ground system by the Oceanic SPR standard
Note the ongoing work by the FAA to comply with these requirements in the Ocean 21 ATSP ground system
Request participating States to report to the FIT the compliance of their ATSP ground system(s) with the allocated safety requirements
Track the status of any non-compliant systems

## Slide 7: Thank you
Remarks