## Slide 1
IPACG 30
Seattle, Washington
Date: May 20-22, 2009
Central
East
Pacific
Flexible
Track
Trial
IP/05

## Slide 2: CEP Flexible Track Trial
A study was completed by MITRE which predicted a possible annual fuel saving of over 6.8 million kg by implementing flexible tracks in the CEP.
The CEP Flexible Track Trial began on January 13, 2009 and was to end on May 31.
The Trial could be extended by consensus or terminated early if necessary.
The flexible tracks were very similar to the PACOTS Tracks between Hawaii and Asia that have been in use for years.

## Slide 3: CEP Flexible Track Trial
Oakland Center System Operations generated 4 one-way tracks between Hawaii and California.
  SHCEP = KSFO to PHNL
  HSCEP = PHNL to KSFO
  LHCEP = KLAX to PHNL
  HLCEP = PHNL to KLAX
Most of the days the current CEP fixed routes were more efficient than the flexible tracks.

## Slide 4: CEP Flexible Track Trial
The routes were published in a TDM (Track Definition Message).
The routes were defined by published waypoints and whole degrees of latitude and longitude.
The CEP flexible tracks were effective at 1500 UTC for a 23 hour period
The effective time of the CEP flexible track was based on the time the aircraft entered oceanic airspace.

## Slide 5: CEP Flexible Track Trial
Determining when to Flex the CEP Routes:
  These CEP flexible tracks were generated using either LHCEP or SHCEP as the primary route.
  The CEP Flex Tracks had to remain laterally separated from each other
  The order of track generation affected the efficiency of the later generated tracks.

## Slide 6
Order of Track Generation affects other Tracks.
Track Placement determination

## Slide 7: CEP Flexible Track Trial
City-pairs were analyzed to determine the overall efficiency of the proposed flex tracks.
The ultimate goal in the CEP flexible track generation was to provide a fuel savings for all aircraft.
The tracks were generated in a manner that does not negatively impact any CEP flexible track by more than 1000 pounds of fuel so long as an overall benefit of 500 pounds of fuel savings can be realized for each City Pair.

## Slide 8: CEP Flexible Track Trial
February 19 status telcon:
  Flex Tracks had been published on 5 different days
  Operators reported mixed results
    Some felt there were benefits to be gained at times
    Others felt there were no benefits
Consensus was that there was not a clear benefit to the flex tracks that supported the extra workload on dispatchers.
It was agreed by all to stop the trial.

## Slide 9: February 19 Telcon cont:
Some ATC issues were identified during the flex track trial.
It was felt that these issues could be resolved procedurally and they were not a reason to stop the trial.

## Slide 10: February 19 Telcon cont:
Some of the greatest benefits of the trial were seen when the CEP Flex Tracks went north of the CEP Route System.
Savings of 1000 kg of fuel were projected.
To take advantage of this opportunity to save fuel:
  Operators were given approval to flight plan User Preferred Routes North of the CEP ATS Routes.
  UPR Flights must join ATS Route A331 or A332 in Honolulu Control Facilities Airspace.

## Slide 11: CEP Flex Routes Operational Trial January 13 –February 19, 2009

## Slide 12: CEP Flexible Track Trial Overview
While the CEP Flexible Track Trial did not yield the projected benefits, it did have some positive outcomes:
  The Trial was a great collaboration of efforts by the Operators and the FAA to reach a common goal.
  The Trial demonstrated that many things are possible through creative thinking.
  The UPRs north of the CEP ATS routes will reduce fuel burn and CO2 emissions.

## Slide 13
The meeting is invited to note the information presented in this paper.