## Slide 1: Problem Reports
IPACG-30/FIT-17
Seattle, WA
May 19, 2009
Gordon Sandell

## Slide 2: Problem Reports
New Problem Report Summary
New Problem Reports
  Problems Reported Since FIT-16
Specific Reports for Discussion

## Slide 3: New Problem Report Summary
47 North/South Pacific Problem Reports generated
Additional 24 categorized as duplicates or non-problems

## Slide 4: New Problem Reports
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
632 | Difficulty Establishing CPDLC connection with A332 | Air | So Pac | In Progress | N | 
634 | A345 - Incorrect Estimate Following Weather Deviation Clearance | Air | So Pac | OPEN | N | Issue expected for correction with Honeywell FMS release 1A to be certified by 1Q2011
635 | A345 - Unable to establish ADS-C | Air | So Pac | RFF | Y | FANS A+ corrects this issue
636 | Frequent Occurrence of ADS-C Periodic Reports with Erroneous Next Waypoint Estimate | Air | So Pac | In Progress | Y | 
637 | B764 - Bad Performers | Air | So Pac | Waiting for info | N | 
638 | KC35 - Bad Performers | Air | So Pac | In Progress | N | 
639 | A332/333 Bad Performers | Air | So Pac | In Progress | N | 
641 | CSPs Asked to Reconsider Logic for Transition from VHF to Satcom to Satisfy DO306 Requirements | link | So Pac | OPEN | N | 
642 | ATSU Considered Duplicate DR1 Downlink as Valid | ground | So Pac | OPEN | N | 

## Slide 5: New Problem Reports (cont’d)
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
643 | B744s not Supplying Intent Data | Air | So Pac | OPEN | Y | 
644 | Unable to Communicate with Airplane after Transition to Satcom | Air | So Pac | In Progress | N | Airplane apparently was not sending Satcom Established Media Advisory when SATCOM is established
645 | B744 - First 2 ADS-C Intermediate Intent Points are Identical | Air | No Pac | In Progress | N | 
646 | B777 - Erroneous ETA for First Intermediate Intent Point | Air | No Pac | In Progress | N | 
647 | B744 - Erroneous ETA for First Intermediate Intent Point | Air | No Pac | In Progress | N | 
648 | B772 - Numerous FN_CON Messages Received During 1 Hour Period | Air | So Pac | In Progress | N | 
650 | B744 - Unable to Establish CPDLC Connection | Air/link | So Pac | RFF | N | Possible FMC reset
651 | "Lost" CPDLC Uplink During GES Transition | link | So Pac | RFF | N | 
652 | A380 - Rejects Multi-Element Uplink Containing [routeclearance] Element | Air | So Pac | OPEN | Y | Airbus will certify a new A380 ATC software (CLA3.x) that will correct this issue, allowing freetext message combination to route clearance.

## Slide 6: New Problem Reports (cont’d)
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
653 | B744 - Amended Route Clearance Loads Differently to Route 1 and Route 2 | Air | So Pac | Waiting for info | Y | 
654 | ATSU Incorrectly Paring NDA and EOS in Same Message | ground | So Pac | In Progress | Y | 
658 | B777 - Poor Performance at VHF to Satcom Transition | Air | So Pac | In Progress | N | 
659 | B772 - No LOAD FMC Prompt for Uplinked Route Clearance | Air | So Pac | In Progress | N | 
660 | A380 - Rejects Multi-Element Uplink Containing Position Report Request | Air/Ground | So Pac | OPEN | Y | 
661 | Logon Rejected by ATSU due to ACARS vs FMC Registration Number Mis-match | Air | So Pac | RFF | N | Crew procedure issue
662 | A320 - Rejects 'Due To Airspace Restriction' When sent in Single Element Uplink | Air | So Pac | OPEN | Y | 
663 | Unable to Connect to Aircraft due to DSP not Forwarding Media Advisory | ground | No Pac | Waiting for info | N | 
664 | Odd Intercept and MAS-F Received for one MD-11 Operator | link | So Pac | Waiting for info | N | 

## Slide 7: New Problem Reports (cont’d)
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
665 | B744 - Uplinked Climb Instruction not Received | Air | So Pac | OPEN | N | 
666 | Datalink Lost with A332 | Air | So Pac | In Progress | N | 
667 | B744 - Unexpected ADS-C Lateral Deviation Event Report Received | Air | So Pac | In Progress | N | 
669 | New ATSU - GS Sometimes Ignores Connect Confirm Message | ground | So Pac | In Progress | N | 
672 | B738 - Incorrect IPI Bearing and Distance | Air | So Pac | In Progress | N | 
673 | B738 - Incorrect Intent Data at Change of UTC Day | Air | So Pac | In Progress | N | 
677 | A380 - No CPDLC Following Second CR1 from NDA | Air | So Pac | In Progress | Y | 
679 | A332 - Position Report Received which Appeared to be from Previous Route Segment | Air | So Pac | In Progress | N | 
680 | Large Number of Duplicate ADS Reports from Multiple Airplane Models | Air | So Pac | In Progress | Y | 

## Slide 8: New Problem Reports (cont’d)
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
681 | A380 - Intermittent CR1 Rejects | Air | So Pac | OPEN | Y | Airbus will certify a new A380 ATC software (CLA3.x) that will correct this issue
683 | B744 - Incorrect ADS Estimate in Both WPR and On-Demand Report | Air | So Pac | In Progress | N | 
684 | B772 - Bad Performers | Air | So Pac | In Progress | N | 
685 | Data Missing from Media Advisories | link | No Pac | OPEN | Y | 
686 | B744 - No CPDLC or ADS-C - Suspected Issue with MU Media Management | Air | So Pac | In Progress | N | 
687 | B772 - Loss of CPDLC and ADS-C | Air | So Pac | RFF | N | 
689 | B744 - CPDLC and ADS-C Lost When Airplane Left VHF Coverage | Air | So Pac | RFF | N | 

## Slide 9: New Problem Reports (cont’d)
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
690 | A332 - Unexpected CPDLC Error Message | Air | So Pac | In Progress | N | 
691 | B772 - Incorrect Ref Lat/Lon for PBD | Air | So Pac | In Progress | Y | Problem with same description closed in Block Point 98
693 | A380 - Disproportionate Number of Uplinks Routed Via HF | link | So Pac | RFF | Y | Behavior was result of DSP's routing configuration in their ATC Gateway that handles ATS internetworking. Configuration change made to correct this problem
694 | A380 - Pilot Defined Waypoints Limited to 20 | Air | So Pac | OPEN | N | 

## Slide 10: New Problem Reports (cont’d)
PR# | Title | Air/ ground/ link | Region | Status | Discuss at FIT? | Comments
696 | Erroneous Flight Number Entry | Air | NAT | Lesson Learned | Y | 
697 | Duelling ATC Centers | Gnd | No Pac | In Progress | Y | 
698 | B777 - New Message Shown as ACCEPTED | Air | No Pac | In Progress | Y | 
699 | B767 - ATC Messages Not Delivered | Air | CE Pac | In progress | Y | 

## Slide 11: Specific Reports for Discussion
Chronic ADS-C Issues
A380 PRs
Other Noteworthy PRs

## Slide 12: Chronic ADS-C Issues
No Intent Data included in Report
  PR 643 - B744s not Supplying Intent Data
    Reported numerous times from Tailored Arrivals trials
    Still under investigation

## Slide 13: Chronic ADS-C Issues (cont’d)
Reports with Incorrect ETAs
  PR 636 - Frequent Occurrence of ADS-C Periodic Reports with Erroneous Next Waypoint Estimate
    Observed with multiple airplane models and manufacturers
Duplicate ADS Reports
  PR 680 - Large Number of Duplicate ADS Reports from Multiple Airplane Models
    772/3’s are prime offenders
    Also received from A330, A340, and B744

## Slide 14: A380 PRs
PR 652 - A380 - Rejects Multi-Element Uplink Containing [routeclearance] Element
  Airbus will certify a new A380 ATC software (CLA3.x) that will correct this issue, allowing freetext message combination to route clearance
PR 660 - A380 - Rejects Multi-Element Uplink Containing Position Report Request
  Position Report request must be uplinked as single element message

## Slide 15: A380 PRs (cont’d)
PR 677 - A380 - No CPDLC Following Second CR1 from NDA
  Anomaly occurred when two CR1 messages were received from NDA
  CPDLC is not able to answer to CPDLC messages
  Can recover CPDLC by resetting ATC system on airplane
PR 681 - A380 - Intermittent CR1 Rejects
  CPDLC connections occasionally denied with an ACARS label HX (SMI REJ) rather than with normal DR1
  Can recover CPDLC by resetting ATC system on airplane
  Airbus will certify a new A380 ATC software (CLA3.x) that will correct this issue

## Slide 16: Other Noteworthy PRs (cont’d)
PR 653 - B744 - Amended Route Clearance Loads Differently to Route 1 and Route 2
  ATSU reported that uplinked element 83 resulted in complete route replacement, not modification
  Discovered via testing at Boeing that element loads differently to active RTE 1 (loads correctly) and identical active RTE 2 (loads incorrectly)
  First known issue with active RTE 1 vs active RTE 2 in nearly 20 years of operation…

## Slide 17: Other Noteworthy PRs (cont’d)
PR 654 - ATSU Incorrectly Paring NDA and EOS in Same Message
  Failed transfers to new ATSU attributed to illegal paring of Next Data Authority and End Service message elements
  Per requirements, such a paring results in disconnect of active and inactive connections
PR 662 - A320 - Rejects 'Due To Airspace Restriction' When sent in Single Element Uplink
  Converse of soon-to-be corrected PR 652

## Slide 18: Other Noteworthy PRs (cont’d)
PR 685 - Data Missing from Media Advisories
  Problem with a particular CMU
  Manufacturer intends to correct problem in software being developed for 747-8
  Plan for other airplane models TBD
PR 691 - B772 - Incorrect Ref Lat/Lon for PBD
  Optional lat/lon appeared to correlate to PBD rather than position of parent waypoint
  Of interest because the problem shows as corrected in AIMS Block Point 98

## Slide 19: Other Noteworthy PRs (cont’d)
PR 693 - A380 - Disproportionate Number of Uplinks Routed Via HF
  Behavior was result of DSP's routing configuration in their ATC Gateway that handles ATS internetworking
  Configuration change recently made to correct this problem
  Did configuration change correct the problem?
PR 696 - Erroneous Flight Number Entry
  Flight crew entered flight number for logon with leading zero (XXX0nn instead of XXXnn)
  Lesson learned/reminder to use the filed flight identifier for the logon

## Slide 20: Other Noteworthy PRs (cont’d)
PR 697 - Duelling ATC Centers
  Airplane scheduled to transfer from one ATC center to another and back
  Transfer began normally, and established inactive (NEXT CENTER) connection
  Second center (although not yet the active center) initiated a transfer back to the original center
  First center then reestablished CPDLC and reinitiated a transfer back to the second center
  This happened 8 times in a period of 37 minutes until the transfer occurred
  Second center sent a free text request indicating CPDLC wasn’t working well and asking the crew to log off
  Airplane then logged back on to the first center 12 minutes after the transfer

## Slide 21: Other Noteworthy PRs (cont’d)
PR 698 - B777 - New Message Shown as ACCEPTED
  After the transfers in PR697, airplane received an uplink shown as ACCEPTED
  Crew couldn’t cancel the uplink
  No ACCEPT (WILCO) response actually sent
  Problem is a display anomaly
  Under investigation

## Slide 22: Other Noteworthy PRs (cont’d)
PR 699 - B767 – ATC Messages Not Delivered
  Normal logon in VHF coverage
  Repeated logon (incomplete) at edge of VHF coverage
  No other CPDLC, AFN, ADS downlink
  Other SATCOM messages OK
  Received UNABLE TO SEND scratchpad messages
  Repeat of problem seen with several CMUs

## Slide 23: Questions?