## Slide 1
CPWG/9
Montreal
April 28-30, 2010
A Report From Cross Polar Working Group 9
IP/07

## Slide 2: RVSM in the Russian Far East
State ATM Corporation provided an update on the planned implementation of reduced vertical separation minimum (RVSM) in Russia, the Central Asian States and Mongolia. The target date for implementation of RVSM is 17 November 2011.

## Slide 3: RVSM in the Russian Far East
Anchorage Air Route Traffic Control Center (ZAN) has many issues with the transition of aircraft from feet to meters.
With the implementation of RVSM, controllers will be assigning flight levels in feet. This will greatly enhance capacity and make our controllers very happy.

## Slide 4: RNP10 in the Arctic FIR
The FAA provided an update on the planned implementation of required navigation performance 10 (RNP 10) in the Anchorage Arctic FIR.
50 nautical miles (NM) lateral separation will be utilized between aircraft authorized for RNP 10. The current lateral separation standard is 90 NM.

## Slide 5: RNP10 in the Arctic FIR
The planned implementation date is 18 November 2010 for the FAA. NAV CANADA’s implementation is tied to the installation and use of the Canadian Automated Air Traffic System (CAATS) which is scheduled for 20 November 2010. Discussions are underway for agreement on the procedure for implementation.

## Slide 6: Tactical Reroutes into Russian Airspace
Tactical reroutes are conducted in many regions of the world with minimal complexity between the operator and the various air traffic service providers.
Generally a reroute is either requested by the pilot when the filed routing and/or filed flight level are not available due to traffic.
The ANSP may also initiate a request to the operator, through the Airline Operations Center (AOC) or directly to the pilot, when a conflict will occur and a tactical reroute could eliminate that conflict.

## Slide 7: Tactical Reroutes into Russian Airspace
There are several factors that make the same process more complex when a flight is approaching Russian airspace and the need for a tactical reroute exists.
Russia requires a Change Message FPL to be sent, which is not consistent with global practices for operators.

## Slide 8: Tactical Reroutes into Russian Airspace
Evaluation of the reroute is more essential for the operator due to onward routings within and/or out of Russia to the west which must be considered.
This process is somewhat labor intensive and time consuming.

## Slide 9: Tactical Reroutes into Russian Airspace
A successful paper trial was conducted on 7 April 2010 between United Airlines, the ZAN Traffic Management Unit, and the Russian Main Air Traffic Flow Management Center in Moscow
Additional paper trials will be conducted over the next few months in an effort to simplify the procedure.

## Slide 10: New routes thru the Russian Far East
Users have requested increased route flexibility in the area of the ZAN/RJJJ FIR.
State ATM has proposed additional fixes and transitions from the two Northern NOPAC tracks up to B932 with possible transitions back to the NOPAC tracks in Fukuoka airspace.

## Slide 11
New routes thru the Russian Far East
OGDEN
NETRI
R220
R580
A590
NUZAN
NYMPH
RIMLI
B932
NIPPI
NEW FIX
OLCOT
R451
G215
G583
RED – State ATM Proposal BLUE – Airline Proposals

## Slide 12: New routes thru the Russian Far East
B932
R220
NETRI
NODAN
NIPPI
OMOTO
PASRO
BLUE – Airline Proposals

## Slide 13: New routes thru the Russian Far East
This proposal by State ATM was met with great interest by ZAN and the JCAB representatives, Mr. Morishima & Mr. Masuda.
The ANSPs, in coordination with the airlines, continue to explore new airways and fixes to improve efficiency.

## Slide 14: New routes thru the Russian Far East
State ATM Corporation developed an ATS Route Catalogue that would contain all proposals as well as responses.
This will be a useful tool for the ANSPs and airlines as they continue to increase the efficiencies of the Cross Polar Region.

## Slide 15: CPWG 10
The ICAO European and North Atlantic Office will host the next meeting of the CPWG in Paris. The meeting dates are planned for 3-5 November 2010.

## Slide 16
Questions ?