## Slide 1: Problem Reports
IPACG-32/FIT-19
Honolulu, Hawaii
May 11, 2010
Gordon Sandell

## Slide 2: Problem Reports
New IPACG Problem Report
  Summary
  Problems Reported/Processed Since FIT-18
FANS-Over-Iridium Reports
ISPACG Problem Reports
NAT Problem Reports

## Slide 3: New IPACG Problem Report Summary
10 Problem Reports generated for issues in NOPAC/CEPAC/CENPAC regions

## Slide 4: New IPACG Problem Reports
PR# | Title | Air/Gnd/Link | Region | Status | Comments
797 | Route Clearance Going Backwards | Gnd | NOPAC | RFF | 
798 | Rejected Logons | Gnd | NOPAC | RFF | 
799 | Flight Number Didn't Propagate to LOGON Page | Air | NOPAC | RFF | 
800 | Logons to Fukuoka Rejected | Gnd | NOPAC | RFF | 
801 | No Response to Logons to Oakland | Gnd | NOPAC | RFF | 
802 | Failed Transfer from Oakland to Fukuoka | Gnd | NOPAC | RFF | 

## Slide 5: New IPACG Problem Reports (Cont.)
PR# | Title | Air/Gnd/Link | Region | Status | Comments
803 | Multiple Flight Plans for One Flight | Gnd | NOPAC | RFF | 
804 | Downlinks Stopped Being Sent | Air | NOPAC | In Progress | Similar to PRs 706, 699,…
805 | ADS Reporting Interval | Gnd | NOPAC | RFF | 

## Slide 6: PR 797 Route Clearance Going Backwards
Airplane received unsolicited route clearance (um80)
      CLEARED ROUTE CLEARANCE
      ARRIVAL: GOLDN5
      VIA TO
      DIRECT N4716.0W13151.0
      DIRECT FULMR
      DIRECT HEMLO
      DIRECT ENI
After passing FULMR, airplane started sharp turn back towards HEMLO (now behind the airplane)
Discussed informally at IPACG-31
Resolved as controller error

## Slide 7: PR 798 Rejected Logons
Attempts to logon to Fukuoka and Anchorage were rejected
Reason code 4
  “Could not match ID/position to flight plan”
Implies flight plan filing/processing issue

## Slide 8: PR 799 Flight Number Didn't Propagate to LOGON Page
On B777, airline sent route uplink to FMS with flight number
Flight number displayed on RTE page, but did not propagate to LOGON/STATUS page
This is a known problem with B777 that it does not propagate if there was no previous entry
Problem is resolved in Blockpoint v14 software
  Available on AIMS-2
  Awaiting certification on AIMS-1
Close as airplane problem now fixed

## Slide 9: PR 800 Logons to Fukuoka Rejected
Transfer from Anchorage to Fukuoka failed
Subsequent logon attempts rejected by Fukuoka
  Reason code 4
Same flight plan filing/processing issue as PR 798

## Slide 10: PR 801 No Response to Logons to Oakland
Airplane made eight attempts to logon to Oakland
No response from Oakland to the first seven
  The last one was successful
The time/date corresponds to a TELCO line outage at Oakland
Conclusion is that this was a result of the line issue.
Close as problem fixed.

## Slide 11: PR 802 Failed Transfer from Oakland to Fukuoka
Airplane didn’t transfer from Oakland to Fukuoka at the FIR boundary (KEITH)
  Airplane sent position report
  Transfer eventually occurred 23 minutes after passing KEITH
Apparently there was a pending uplink that prevented the automation from working
  The only uplink pending a few minutes before passing KEITH would be the CONTACT uplink (response was within one minute of the uplink)

## Slide 12: PR 803 Multiple Flight Plans for One Flight
Flight from China to Oceania
  Filed flight plan as XXXnn
  Had to logon to Fukuoka, Oakland as XXX0nn (leading zero)
  Had to logon to Brisbane as XXXnn (no leading zero)
  Happens regularly
Apparently China forwards FPL after inserting leading zero
  Airline has issued second FPL on some occasions to allow departure
ATSUs need to be aware of this…

## Slide 13: PR 804 Downlinks Stopped Being Sent
After establishing CPDLC and ADS connections, B764 airplane stopped sending CPDLC/ADS downlinks
  When in SATCOM-only area
Similar behaviour seen in FIT PRs 706, 699,…
Avionics/airframe manufacturers unable to reproduce in lab

## Slide 14: PR 805 ADS Reporting Interval
Review of airplane message log revealed 11 ADS uplinks and 28 ADS downlinks in a 2-hour segment in Fukuoka airspace
ODP uses 10-minute rate (9 min 36 sec) normally, but 5 min 20 sec
  if 300 ft from planned altitude (e.g. not yet reached planned alt),
  or if 5NM between planned route and current route (inc WXR deviations)
Also use demand reports
No action required. Information only.

## Slide 15: FANS-Over-Iridium Reports
B737s with FANS-1 and Iridium SATCOM operating in Fukuoka/Oakland airspace
45 PRs investigated since 1 Jan
  2% airplane equipment fault
  11% ATS ground system issue (not Iridium-related)
  18% flight plan filing/processing issues
  51% Iridium drop-out
  2% short Iridium connection loss
  11% known existing FMC issue (not Iridium-related)
  4% still under investigation

## Slide 16: ISPACG Problem Reports
Reported on 72 PRs (in addition to those reported here and in NAT)
  PRs 695, 697-700 and 711-777
Key Subjects
  Use of HFDL (uplink and downlink)
  B777 performance issues (fixed in BP v14)
  Network outage notification
  CPDLC and ADS connections on A33x airplanes
  Route clearance loading on A3xx
  ADS delays in NZZO
  Failed transfers from WAAF
  Short sector transits
  Comm issues with new operators
  B767 sending dm64 with blank CDA
  Dm63 without MRN (per Boeing design)
  No altitude range change report from B777
  Inappropriate DESCENDING TO appended to POS REPORT
  B744 spurious uplink printing

## Slide 17: NAT Problem Reports
15 North Atlantic Problem Reports generated between Sept 2009 and March 2010 (PRs 778 – 792)
  2 related to ADS waypoint change event reports (B777 sending duplicates in one downlink)
  2 involving ground termination immediately after connection establishment (ground system issue)
  7 flight plan filing/processing issues
  1 route uplink issue
  2 airborne SATCOM system issues
  1 duplicate message delivery issue (ARINC 623 messages)

## Slide 18: Questions?