## Slide 1: ADS-B In-Trail Procedure (ITP) and ADS-C Climb/Descend Procedure (CDP)
Status Update
IP/03
Presented to: IPACG/32
Date: 10-14 May 2010

## Slide 2: ADS-B In-Trail Procedures (ITP)
US SBS Program Office developing airborne ADS-B applications expected to provide benefits to operators who equip their aircraft with appropriate avionics
One such airborne ADS-B application being developed is ADS-B ITP
  enable flight level changes for aircraft equipped with ADS-B receivers and on-board automation

## Slide 3
ADS-B ITP
Maneuvering aircraft obtains flight ID, altitude, position and ground speed transmitted by proximate ADS-B equipped non-maneuvering aircraft
Based on ADS-B data from the non-maneuvering aircraft, a pilot can make an ITP altitude change request to ATC
Controller verifies the ITP and reference aircraft are same track and maximum closing Mach differential not exceeded
Clearance for the climb or descent issued
Maneuvering aircraft may then vertically transition through the altitude of non-maneuvering aircraft

## Slide 4: ADS-B ITP Operational Trial
FAA has entered into agreement with United Airlines for an operational trial of ADS-B ITP in the South Pacific on revenue flights
Equipped United Airlines 747-400’s operating between the US West Coast and Australia and on return flights
Planned that between one third and one half of the 747’s operating on the route will be equipped and authorized to request an ITP maneuver
Initial expectations are between one and two ITP procedures performed per week of operations

## Slide 5: ADS-B ITP Operational Trial
Adopted as an initiative within the ASPIRE program
Establishes a cooperative agreement between the FAA and Airservices Australia which will allow the two organizations to share data and provide a mechanism for providing mutual support of the operational trial

## Slide 6: ADS-B ITP Operational Trial
FAA desires to lead operational trial of ADS-B ITP along SOPAC routes within next 18 months
Other required work includes
  Performing all required safety management system (SMS) processes and analyses
  Obtaining FAA aircraft certification and flight standards approvals
  Working with international community on development and approval of applicable separation standards and obtaining regional authorization for application

## Slide 7: ADS-C Climb/Descend Procedures (CDP)
FAA is evaluating oceanic ADS-C CDP
  Climb/descend to a Requested Flight Level through one intermediate FL occupied by a blocking aircraft
  Based on existing ADS-C equipment and technology coupled with new ATC procedures
ADS-C CDP will have smaller longitudinal separation minima (e.g. 16 nm) than standard rules (e.g., 30 nm, 50 nm) with aircraft at intermediate flight levels
ADS-C CDP is a controller initiated procedure after a pilot request

## Slide 8: ADS-C CDP Operational Trial
FL350
FL360
FL370
16 nm minima
FL350
FL360
FL370
16 nm minima
Trailing Climb
Leading Climb
FL350
FL360
FL370
16 nm minima
FL350
FL360
FL370
16 nm minima
Trailing Descent
Leading Descent
Blocking aircraft
Maneuvering aircraft
Applied between RNP4 maneuvering and blocking aircraft pairs
Blocking aircraft is 1000 feet above or below the maneuvering aircraft
Controller initiated procedure after pilot request
Manually utilize Ocean21 current functionality – no software changes
Maneuvering aircraft will climb or descend to CDP target altitude if clearance is granted
Notes: The ADS-C ITP concept [1] is to develop a new procedure that would allow an aircraft to climb or descend through the altitude of another aircraft with a smaller longitudinal separation distance than the minimum standard separation distance (e.g., smaller than 30 nm) until vertical separation is established. The objective of improved altitude changes has similarities with other concepts: the TCAS in-trail climb (ITC) trial [2], ADS-B ITP concept [3], and current procedures that allow 30 nm and 50 nm separation distances during altitude changes (Appendix A).
ADS-C ITP does not require new equipage. A safety case that meets FAA and ICAO requirements for a new separation standard and a detailed procedure are needed.
The ADS-C ITP concept addresses factors that would affect a business case. The first factor is that the procedure would be limited to situations where both aircraft are properly equipped. The requesting and blocking aircraft would need to be using controller pilot data link communications (CPDLC), and ADS-C position reporting. Aircraft are likely to need RNP-4 navigation capability. In today’s system, FANS 1/A equipped aircraft are likely to satisfy these requirements.
The procedure would be limited to situations where both aircraft are level (and will remain level for approximately 30 minutes) and flying on the same track in same direction. A key factor that affects the frequency the procedure can be used is the minimum separation distance between the requesting and block aircraft. Based on the TCAS ITC safety analysis [2], 15 nm is used herein. ADS-C ITP safety case analysis may support a smaller minimum separation distance.

## Slide 9: ADS-C ITP
OC1 and OC2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: ADS-C CDP Check- list
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: ADS-C CDP Operational Trial
Target start date in Oakland Oceanic FIR, July 2010
Approximately 25 percent of ZOA ADS flights currently file RNP4
Based on Oakland ARTCC traffic, with a 35% FANS equipage rate, benefits analysis projected total combined fuel savings up to 44,000 kg or 139,040 kg of CO2 per day
ADS-C CDP will be evaluated during the operational trial to determine if requirements can be modified to improve operational usage
  Allow larger altitude changes for a CDP target altitude (allow at least a 4000 foot altitude change to CDP target altitude or possibly allow unbounded altitude change)
  Allow a larger initial vertical separation distance between maneuvering and blocking aircraft (e.g., allow 2000 feet vertical separation)

## Slide 12: Thank you
Comments?
Questions?
Karen Chiodini Specialist, Oceanic & Offshore Operations karen.l.chiodini@faa.gov (202) 385-8931