## Slide 1: Problem Reports
NAT CNSG/4
Paris
March 7-11, 2011
Gordon Sandell
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 2: Problem Reports
New Problem Report Summary
New Problem Reports
  Problems Reported Since NAT CNSG/3
Individual Reports
B777 Messages Discarded
Proposed Enhancement
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 3: New Problem Report Summary
24 North Atlantic Problem Reports generated
Transitioning to using ISPACG website and database
  http://www.ispacg-cra.com/
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 4: New Problem Reports
PR # | Title | Air, Gnd, or Link | Comments
863 | CPA831 failure to establish active CPDLC connection with BIRD | Air | Data unavailable
879 | Thales FMC includes latitude and longitude in DM24 | Air | Assigned to Airbus
880 | UM80's which contain an International STAR are rejected | Gnd | Assigned to Airbus
882 | Using a NAT track as an airway in CPDLC | Gnd | 
889 | Performance degradation EIK GES | Link | Assigned to ARINC
892 | Missing ADS Reports (Default Data) | Air/Gnd | Question for Nav Canada
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 5: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
893 | Position Report Exchange Issue | Gnd | Question for Nav Canada
895 | Route Clearance Responded to but Ignored | Air | Crew issue
896 | Delayed Weather deviation Clearance | Air/Gnd | Question for Nav Canada
897 | Multi-Element Clearance Concerns | Gnd | 
898 | Logon Fail Due to Messages Not Delivered by DSP | Link | Existing ARINC action item
899 | Logon Fail Due to Erroneous Center Identifier | Air | Entry error
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 6: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
902 | Missing Position Reports for Gander | Gnd | Question for Nav Canada
906 | Delayed AFN Logon | Air | Assigned to Honeywell and Gulfstream
909 | CPDLC FAULT ATC CLEARANCE – UPLINK DELAY EXCEEDED | ? | Human issues
910 | Missing FMC WPRs | Gnd | Assigned to Santa Maria
911 | More DOWNLINK ERROR Messages | Gnd | Future fix
914 | Unable to Logon to Gander | Gnd | Awaiting Nav Canada analysis
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 7: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
916 | Logged on to Shanwick without proper indication | Gnd | Fix identified
917 | Unable to Logon to Gander or Reykjavik | Gnd | Awaiting Nav Canada analysis
918 | Disconnect Due to Imagined Congestion | Air | 
919 | Additional Disconnect Due to Imagined Congestion | Air | Same as 918
924 | Message Assurance Failure When Message Was Delivered | Link | Discussion item
930 | Conditional Clearance Executed After New Clearance Received | Air/Gnd | For discussion
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 8: Individual Reports
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 9: PR 863, CPA831 failure to establish active CPDLC connection with BIRD
7 logons sent in a period of ~1 hour
  Connections set up OK
  Operational uplinks rejected “not current data authority”
Consistent with not getting an end-service from previous center and crew logging on without turning ATC COMM off first
DLMA didn’t request data in time, so can’t confirm
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 10: PR 879, Thales FMC includes latitude and longitude in DM24
Airbus aircraft equipped with a GE/Thales FMC
  (a) put the optional lat/long for every waypoint in a route
  (b) use the single character identifier for the approach type (e.g. I25L instead of ILS25L), and
  (c) don't put the intersection waypoints between airways in the route
(a) is part of the DO-219/DO-258 message set and should be allowed (ground system deficiency)
Airbus has indicated that (b) and (c) will be fixed in an upcoming software release
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 11: PR 880, UM80's which contain an International STAR are rejected
Report was that airplanes were rejecting uplinks with STARs of more than 5 characters
In reality, the STAR was encoded as an airway in the route portion, so was nonsense, and was properly rejected
  Airways are limited to 5 characters, so encoding one with a length of 7 also violated the ASN.1 rules for that
STAR names are limited to 6 characters (plus five for a transition, if included)
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 12: PR 882, Using a NAT track as an airway in CPDLC
Route uplink from KZWY
  (a) tried to use one of the NAT tracks as an airway (that would never be in the nav database in an FMC), and
  (b) tried to use a lat/long as an airway entry point (which would only work on 787)
Crew then loaded without noticing PARTIAL CLEARANCE LOADED or the resulting DISCONTINUITY
Question for NAT/CNSG is how to avoid this happening again?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 13: PR 889, Performance degradation EIK GES
Under investigation by ARINC
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 14: PR 892, Missing ADS Reports (Default Data)
CPDLC message sent from Gander
  REQUEST POSITION REPORT
  FOR 50W
Gander contacted on HF and advised they were not receiving the position reports
ADS report for 50W included default predicted altitude
  Indicates data not available
Is that why it was “missing”?
Continued on PR893…
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 15: PR 893, Position Report Exchange Issue
…Continuing from PR892
Airplane responded by sending CPDLC position report and got MESSAGE NOT SUPPORTED BY THIS FACILITY
Why send REQUEST POSITION REPORT if you can’t accept the response?
Are there plans to support position report downlinks?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 16: PR 895, Route Clearance Responded to but Ignored
ATC uplinked a clearance to the airplane
Airplane sends WILCO
ADS reports show the airplane not following the new track
Crew says they didn’t see the uplink
Logs show the uplink was received and WILCO’ed while the crew was sending a long free text downlink (one of 3)
Crew too absorbed in typing and didn’t realize that one of the pages they viewed was a route clearance?
Perhaps a lesson learned about over-use of free text?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 17: PR 896, Delayed Weather deviation Clearance
According to flight crew report:
  Couldn’t send “offset at” request so just requested L25
  Then sent cruise climb request
  Got “MESSAGE NOT SUPPORTED” for offset request
  Voice exchanges to get clearances
  Then got climb clearance with REPORT LEVEL FL390
  No response to level report
Two issues. First is crew training
  Lack of “offset at” was because they were requesting a weather deviation
  Cruise climbs aren’t supported by Gander (the message not supported was for that, not the cruise climb
  There is no response to a level report
The other issue is why Gander took over10 minutes to respond to the weather deviation request
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 18: PR 897, Multi-Element Clearance Concerns
KZWY sent this message (arrived at 1522z)
  CLIMB TO REACH FL370 BY 1537z
  REPORT LEVEL FL370
  WHEN CAN YOU ACCEPT FL380
  WHEN CAN YOU ACCEPT FL390
Response was
  WILCO
  WE CAN ACCEPT FL380 AT 1522z
  WE CAN ACCEPT FL390 AT 1522z
Not entirely clear how the crew did that (free text entry?)
In any case, this kind of combination is discouraged by GOLD
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 19: PR 898, Logon Fail Due to Messages Not Delivered by DSP
Flight crew sent logon to CZQX, but no CPDLC connection resulted
Airline is a SITA customer, and the logons were delivered to (and discarded by) ARINC
This is very similar to PR842, reported at NAT/CNSG
ARINC has an action item arising from PR842
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 20: PR 899, Logon Fail Due to Erroneous Center Identifier
Same airline as PR898
Attempted to logon to Gander
  Used CYQX instead of CZQX
Same effect as PR898 (no connection)
Cause was pilot entry error
  But I note that oceanic clearance requests for Gander are sent to CYQX
  Is this well covered on charts?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 21: PR 902, Missing Position Reports for Gander
Coordination error between NY and Gander
  First position report at 40W via HF
  ADS report for 30W
AFN address forwarding went OK, but Gander didn’t initiate ADS or CPDLC till after the airplane passed 40W
  Gander to address
Also noted:
  No time stamps in CPDLC messages from Gander
  Time stamp in AFN messages up to 70 seconds AHEAD of delivery time
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 22: PR 906, Delayed AFN Logon
Airplane sent several logons to BIRD via STG (Stavanger)
Seven hours later, sent another via TEB (Teterboro) time-stamped one second after the last one
Presumably stuck in VHF transmit queue?
Gulfstream/Honeywell to address
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 23: PR 909, CPDLC FAULT ATC CLEARANCE – UPLINK DELAY EXCEEDED
Flight crew rejected climb clearance with free text saying it couldn’t climb 1000ft for >4 hours
Then rejected two descent clearances
  One from 350 to 210
Accepted MAINTAIN 350, but rejected two weather deviation clearances
Crew report said some had “UPLINK DELAY EXCEEDED” which would be very odd
???
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 24: PR 910, Missing FMC WPRs
Airline reported Santa Maria indicated not receiving FMC waypoint reports from some flights
Forwarded to Santa Maria, but may be too old to allow investigation
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 25: PR 911, More DOWNLINK ERROR Messages
Flight crew received DOWNLINK ERROR indication on connection to Shanwick
Shanwick sent a second CPDLC connect request
  Does this when response delayed
  Airplane responded to both
  Ground didn’t like getting both responses
Under consideration for a fix in a future release
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 26: PR 914, Unable to Logon to Gander
Airplane sent two logon requests to CYQX
  No response (incorrect identifier)
Then sent oceanic clearance request to CYQX
  No clearance received by datalink
Then 3 logons to CZQX
  34, 17 and 11 minutes before entering oceanic airspace
  AFN acks, but no CPDLC requests
Still awaiting Nav Canada analysis
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 27: PR 916, Logged on to Shanwick without proper indication
Airplane logged on to Shanwick
  ADS-C contract initiated, but no CPDLC
Oceanic clearance request rejected
Then a confusing crew report that “Shanwick says we’re logged on, but we don’t have a message that we are logged on”
Apparently SAATS “thought” the CPDLC connect request had been sent
SAATS has a bug
UK NATS issue
  Does Nav Canada have a similar issue?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 28: PR 917, Unable to Logon to Gander or Reykjavik
Logon to Gander
  Accepted (AFN ack) but no CPDLC connect request
Again, no sign of an oceanic clearance (but via airline host, not A623)
Under investigation by Nav Canada
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 29: PR 918, Disconnect Due to Imagined Congestion
B772 responded to an ADS contract request from Reykjavik with a disconnect and a reason code of “congestion”
  Only legitimate cause is if already 5 connections.
  There weren’t (only 2 including this one)
Under investigation by airframe manufacturer and avionics supplier
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 30: PR 919, Additional Disconnect Due to Imagined Congestion
Same as PR918
  Different airline
  More ADS contracts, but still not 5
Same investigation status
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 31: PR 924, Message Assurance Failure When Message Was Delivered
Reykjavik has received Message Assurance Fail (MAS-F) indications for messages attempted via HFDL
  Subsequently received application responses for those messages
Concern is with releasing airspace for another flight if there is “no response” from an airplane
NAT CNSG discussion?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 32: PR 930, Conditional Clearance Executed After New Clearance Received
At 1627z, ZNY sent this clearance (which crew WILCOed)
    MAINTAIN FL370
    AT 1836z DESCEND TO AND MAINTAIN FL280
    DESCEND TO REACH FL280 BY 1845z
    REPORT LEVEL FL280
Then at 1708z, ZNY sent a new clearance (also WILCOed)
    CLEARED ROUTE CLEARANCE
    ROUTE HAS BEEN CHANGED
    MAINTAIN FL370
Then crew sent
    CONFIRM WE DO NOT DES AT 1836z TO FL280
ZNY responded:
    DO NOT DESCEND
    MAINTAIN FL370
AT 1845z ZNY received the report for LEVEL FL280
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 33: PR 930 (Cont.)
Crew received a reminder from the airplane system to execute the conditional clearance
  Not cancelled by superseding clearance
  No manual cancellation possible
Captain determines that airplane must follow the old clearance despite First Officer misgivings and the earlier exchange indicating the new clearance superseded the first
  Flight deck procedures?
And is the conditional clearance for 2 hours away acceptable?
GOLD guidance required?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 34: B777 Messages Discarded
Several recent FIT PRs in which a B777 has behaved as though uplinks have had a CRC failure
  Ignored AFN ack, so CPDLC connect request receives a disconnect response
  CPDLC operational messages ignored
  ADS-C contract requests result in no response to ATC, but an AOC uplink reject to the airline
  In all cases, there’s a network ack (so you’ll get message assurance success (MAS-S)
  All BPv14 software (or later)
PRs 877, 886, 888, 901, 904, 908, 923
Under investigation by airframe manufacturer and avionics supplier
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 35: Proposed Enhancement
Typing errors in logons will result in the airplane waiting 10 minutes to time out
  No indication of the error
DSP has to perform 4-character ICAO ID → 7-character address translation
  Similar to D-ATIS
  DSPs provide “NO PARTICIPATING AIRPORT” message for D-ATIS
Could DSPs provide something similar for erroneous ATC logons?
( IPACG-34 FIT-21 IP-01 Attachment 1 )

## Slide 36: Questions?
( IPACG-34 FIT-21 IP-01 Attachment 1 )