## Slide 1: Problem Reports
IPACG-34/FIT-21
Honolulu, Hawaii
May 24, 2010
Gordon Sandell

## Slide 2: Problem Reports
New IPACG Problem Report
  Summary
  Problems Reported/Processed Since FIT-20
Reports From Other Regions

## Slide 3: New IPACG Problem Report Summary
7 Problem Reports generated for issues in NOPAC/CEPAC/CENPAC regions
Ongoing discussions with CRASA-J to assist in PR resolution

## Slide 4: New IPACG Problem Reports
PR# | Title | Air/Gnd/Link | Region | Status | Comments
900 | PARTIAL CLEARANCE LOADED for Route Uplink | Air/Gnd | NOPAC | RFR | 
912 | Unable to Logon to PAZN | Gnd | NOPAC | RFR | Lack of flight plan check
913 | Unable to Communicate with Magadan |  | NOPAC / RFE | RFR | 
926 | Unable to Logon to Edmonton (CZEG) | Gnd | NOPAC/ North America | RFR | 
927 | Intermittent display of "link lost". | Gnd | NOPAC / RFE | RFR | 
932 | Unable to Logon to Oakland | Gnd | NOPAC | RFR | 
933 | No CPDLC or ADS Downlink Messages Sent | Air | CEPAC | RFR | CMU issue

## Slide 5: PR 900, PARTIAL CLEARANCE LOADED for Route Uplink
Crew report:
  We loaded 45N140W and FATMO into RTE 2 in the FMC.
  Selected RTE 2 on the ROUTE Request page.
  Uplink read “CLEARED ROUTE CLEARANCE”
  When we used "LOAD“, we got "PARTIAL CLEARANCE LOADED“
Crew used the inactive route that had a different origin
  RJCC (CTS), but flight was from RJAA (NRT)
  Oakland sent clearance uplink by repeating downlink
  Cannot change origin (history) in FMC
  Hence partial load

## Slide 6: PR 912, Unable to Logon to PAZN
Crew report:
  We are logged onto PAZA but ATC cannot get it to transfer to PAZN
PAZN operation was correct
  PAZA shouldn’t have allowed the logon
Flight plan was filed as XXXn, but airplane was logging on as XXX0n (extra leading zero)
PAZA is not performing the check against the filed flight plan
  This is a basic assumption of the FANS safety analysis
  Magadan also doesn’t make the check
  What do regulators think?

## Slide 7: PR 913, Unable to Communicate with Magadan
Crew report:
  Cannot communicate CPDLC or ADS in Magadan.
  We receive messages from Magadan, but they don’t receive us.
  Then a little later:
  CPDLC working again. Logged off and relogged on. Messages going both ways.
The first connection was conducted over HFDL with airplane at ~85N
Second connection largely on SATCOM (some HFDL uplinks)
HFDL connection seemed to be very poor

## Slide 8: PR926, Unable to Logon to Edmonton (CZEG)
PAZA instructed that CZEG was the next center
  The crew was unable to logon to CFEG
  DCDU showed "ATC CENTER - NOTIFIED FAILED“
Logons to Edmonton (CZEG) were ignored
  Address forwarding, as well as crew-initiated
  Edmonton is ADS-only (no CPDLC)
Airplane responded per design
  Timed out, hence the indication
ATC asked for explanation of why logons were ignored

## Slide 9: PR927, Intermittent Display of “Link Lost".
Intermittently displayed “link Lost”
Appears to be result of address forwarding from Anchorage to Magadan
  Anchorage forwarded to GDXGWXA
  Magadan responded from GDXE1XA
  Airbus airplanes will reject (ignore) such responses
  Magadan established CPDLC connection OK
    Doesn’t require AFN for a transfer
  So CPDLC was continuous, although crew would have seen “NOTIFICATION FAILED”
Need better coordination between Anchorage and Magadan on addresses
Perhaps additional crew training on system behaviour

## Slide 10: PR932, Unable to Logon to Oakland
Crew reported unable to logon to Oakland
Oakland responded to AFN logons with reason code 4
  Flight plan mismatch
  Unfortunately too late to ask Oakland why
  Could be flight plan filing issue or coordination issue
  Asked airline if they still have flight plan

## Slide 11: PR 933, No CPDLC or ADS Downlink Messages Sent
Flight crew logged on and it appeared that CPDLC and ADS were established
  No messages sent to ATC
    Should have been CPDLC connect confirm, CPDLC downlinks, ADS acks and reports
  After an hour and a half, disconnected and logged on again
    Disconnect sent, plus one ADS report 67 minutes old, and a downlink containing ADS reports 23, 27 and 37 minutes old
Seems to have begun as soon as ADS and CPDLC uplinks were acked
  Next downlink was 7 minutes later (Q0 to different VDL2 site)
  Crew saw UNABLE TO SEND MSG, which indicates FMC/CMU protocol problems
Appears to be an issue when CMU goes into VDL2 search phase
Could be related to previous problems of “unable to send FMC messages on SATCOM”

## Slide 12: Reports From Other Regions
PR 883, 907, ADS-C processing with GLF5
B777 Messages Discarded (multiple PRs)

## Slide 13: PR 883, 907, ADS-C processing with GLF5
Wind direction reported erroneously in MET group of ADS report
  In error by 180°
Airplane also responded improperly to standard contract request
Under investigation by Gulfstream/Honeywell
  …on the list to fix in an upcoming certification
  … still in the planning stage so cannot provide a timeline

## Slide 14: B777 Messages Discarded
Several recent FIT PRs in which a B777 has behaved as though uplinks have had a CRC failure
  Ignored AFN ack, so CPDLC connect request receives a disconnect response
  CPDLC operational messages ignored
  ADS-C contract requests result in no response to ATC, but an AOC uplink reject to the airline
  In all cases, there’s a network ack (so you’ll get message assurance success (MAS-S)
  All BPv14 software (or later)
PRs 877, 886, 888, 901, 904, 908, 923
Investigated by airframe manufacturer and avionics supplier
  Fix for this problem planned in BPv15A software release

## Slide 15: Questions?