## Slide 1: Problem Reports
ISPACG-25/FIT-18
Honolulu, HI
March 22, 2011
Suzie Ness, Gordon Sandell
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 2: Problem Reports
New Problem Report Summary
New Problem Reports
  Problems Reported Since ISPACG-24
Individual Reports
Discussion of PR from NAT
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 3: New Problem Report Summary
25 South Pacific Problem Reports generated
Transitioning to using ISPACG website and database
  http://www.ispacg-cra.com/
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 4: New Problem Reports
PR # | Title | Air, Gnd, Link | Comments
862 | Incorrect Route Uplink Loaded | Air | 777 Rte Problem
873 | Delayed message sequence A343 | ? | 
874 | Temporary Loss of ADS-C for QFA141 | ? | 
875 | DAL16 - Difficulty in establishing a CPDLC connection | Air | 777 CRC Problem
876 | ASY364 - Multiple Address Forwarding failures | Gnd | 
877 | SIA217 - Uplinks not delivered | Air | 777 CRC Problem
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 5: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, Link | Comments
878 | A388 operating with no SATCOM, HFDL and VHF only | Air | 
881 | No operational response received on clearance uplink | Air | 777 CRC Problem
883 | ADS-C processing with GLF5 | Air | Assigned to Gulfstream/Honeywell
884 | (MAS131 - Loss of data link (CPDLC and ADS-C) | ? | 
885 | Crew receive uplink climb clearance + indication of invalid ATC uplink | Air | 
886 | Unable to establish CPDLC Connection with DAL16 | Air | 777 CRC Problem
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 6: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, Link | Comments
887 | Unable to establish ADS-C with JST4 |  | Assigned to Airbus
888 | Unable to establish CPDLC Connection with DAL16 | Air | 777 CRC Problem
890 | Poor latency performance observed for ADS-C downlink messages | Link | Assigned to ARINC/SITA
901 | No Response to TA | Air | 777 CRC Problem
904 | Loss of ADS | Air | 777 CRC Problem
905 | Unable to load TA route uplink | Air | 777 Rte Problem
907 | ADS Issues with Gulfstream 5 | Air | Assigned to Gulfstream/Honeywell
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 7: New Problem Reports (Concl.)
PR # | Title | Air, Gnd, Link | Comments
908 | Unable to Logon to Melbourne | Air | 777 CRC Problem
920 | N401HB - max value of distanceoffset = 30NM | Air | Assigned to Gulfstream/Honeywell
921 | REU772 - Multiple CPDLC connections + disconnections... | Air | 
922 | QFA141 - Temporary loss of ADS-C | Link | 
923 | ANZ90 - Several undelivered CPDLC uplinks | Air | 777 CRC Problem
925 | Unable to establish CPDLC & ADS-C with LAN801 | Link | 
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 8: Individual Reports
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 9: PR 862, Incorrect Route Uplink Loaded
On Pacific One TA into San Francisco, TA clearance displayed but different route loaded on B777
  Route was an uplink received on a previous flight
  FMC master switch after first route uplink and again before second (same FMC now master)
Problem replicated in Honeywell lab
Fix planned for FMC in next release
PR 905 believed to be a manifestation of same basic issue
  Occurred after FMC master switch
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 10: PR 873, Delayed message sequence A343
Three ADS-C reports time stamped by FMS between 0151-0153 not received by NTTT until 0232.
Data was not available,
Received empty audit report.
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 11: PR 874, Temporary Loss of ADS-C for QFA141
Aircraft was in transition from VHF to SATCOM
ADS contract uplink via VHF was received but the aircraft’s ACK was not seen on the ground
The ground re-transmitted the ADS contract 8 times in VHF at 10 sec apart before switched to SATCOM
The ground received Media Advisory from aircraft to inform of “loss of VHF” after the 3rd re-transmission
Aircraft NAK’ed duplicate ADS contract
  After 3 NAKs, ADS connection was terminated
After 2 ADS contract uplinks each with 8 re-transmissions in VHF, the ground switched to SATCOM and the system was back to normal
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 12: PR 875, DAL16 - Difficulty in establishing a CPDLC connection
See later chart on “777 Messages Discarded’
Logon failed, with AFN ack from the ground being ignored
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 13: PR 876, ASY364 - Multiple Address Forwarding failures
Brisbane reported multiple attempts to address forward to Nadi failed
Logs show airplane sent AFN contact to Nadi, but each time Nadi responded with a reject
  Reason code 4 (flight plan mismatch)
Nadi flight plan issue or coordination issue
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 14: PR 877, SIA217 - Uplinks not delivered
See later chart on “777 Messages Discarded’
CPDLC uplinks not displayed and ADS messages rejected
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 15: PR 878, A388 operating with no SATCOM, HFDL and VHF only
Airplane operated without SATCOM for most/all of the flight
  Filed as RNP 4
  ~50% of ADS reports meeting Type/180
Issue was that ATC needs to know when not to apply reduced separation
Airline amending procedures to require ATC notification of in-flight SATCOM failures
Does GOLD need updating to reflect this, and will ATC interpret it correctly?
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 16: PR 881, No operational response received on clearance uplink
See later chart on “777 Messages Discarded’
CPDLC uplinks not displayed
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 17: PR 883, ADS-C processing with GLF5
Wind direction reported erroneously in MET group of ADS report
Airplane responded improperly to standard contract request
Under investigation by Gulfstream/Honeywell
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 18: PR 884, (MAS131 - Loss of data link (CPDLC and ADS-C)
The aircraft flew out of VHF range
SATCOM was not available, system failure
Aircraft lost datalink for more than 1 hour
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 19: PR 885, Crew receive uplink climb clearance + indication of invalid ATC uplink
B744
Crew requested climb to FL380
NZZO responded CLIMB TO AND MAINTAIN FL380/REPORT LEVEL FL380
Crew report “saw clearance but it was accompanied with warning INVALID ATC UPLINK”
On B744 for invalid uplink
  Don’t see clearance
  Can’t respond to clearance
  Downlink error message (dm62) is sent
Can’t square this with what was reported
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 20: PR 886, Unable to establish CPDLC Connection with DAL16
See later chart on “777 Messages Discarded’
Logon failed, with AFN ack from the ground being ignored
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 21: PR 887, Unable to establish ADS-C with JST4
Under investigation by Airbus
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 22: PR 888, Unable to establish CPDLC Connection with DAL16
See later chart on “777 Messages Discarded’
Logon failed, with AFN ack from the ground being ignored
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 23: PR 890, Poor latency performance observed for ADS-C downlink messages
Relates to use of Atlantic satellites in Pacific
Assigned to ARINC and SITA
  `ARINC indicated EIK performance OK
Use of AOR-W and AOR-E satellites in the Pacific is at the edge of coverage
  Loss of signal, reestablishment of link
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 24: PR 901, No Response to TA
See later chart on “777 Messages Discarded’
CPDLC clearance not displayed
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 25: PR 904, Loss of ADS
See later chart on “777 Messages Discarded’
No ADS response, as uplink rejected (CRC failure sent to company)
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 26: PR 905, Unable to load TA route uplink
B777
TA uplink displayed, but no LOAD FMC button
Followed FMC master change
Believed to be another variant of PR862
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 27: PR 907, ADS Issues with Gulfstream 5
Wind direction in ADS-C Met group 180° off
Rejected ADS-C contract request containing two event requests
Assigned to Gulfstream/Honeywell
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 28: PR 908, Unable to Logon to Melbourne
See later chart on “777 Messages Discarded’
Logon failed, with AFN ack from the ground being ignored
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 29: PR 920, N401HB - max value of distanceoffset = 30NM
Gulfstream only allows offset request up to 30 miles
  Same as allowed for offset entry in FMC
Assigned to Gulfstream/Honeywell
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 30: PR 921, REU772 - Multiple CPDLC connections + disconnections...
Logged onto Brisbane and established CPDLC
Then logged onto Nadi
  Nadi requested CPDLC, but got DR1
  Nadi forwarded to Brisbane before attempting CPDLC
Then disconnected from Brisbane
  Looks like crew turned it off
Logged onto Nadi again
  Brisbane attempted (and established) CPDLC before getting address forward
And disconnected again.
Looks as if crew logged onto Brisbane and changed their minds
  Not helped by Nadi address forwarding before establishing CPDLC
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 31: PR 922, QFA141 - Temporary loss of ADS-C
A332
Report of ADS-C contract requests “delayed or not delivered”
Two contract requests actually delivered on VHF
  No network ack, but ADS-C ACK sent (on SATCOM) before uplink attempted on SATCOM
Then received NAK (contract # in use) when they were delivered on SATCOM
Then the flight crew terminated it.
Ground may need to tolerate NAK-after-ACK
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 32: PR 923, ANZ90 - Several undelivered CPDLC uplinks
See later chart on “777 Messages Discarded’
CPDLC uplinks not displayed
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 33: PR 925, Unable to establish CPDLC & ADS-C with LAN801
Logon received, but unable to establish CPDLC
SITA had not received media advisory for establishment of SATCOM
  Couldn’t contact on SATCOM
Media advisory received by ARINC, but not forwarded
  Operator had not requested it
  Operator contacted
Only one airplane like this
  Probable ORT issue, with GES selection
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 34: B777 Messages Discarded
Several recent FIT PRs in which a B777 has behaved as though uplinks have had a CRC failure
  Ignored AFN ack, so CPDLC connect request receives a disconnect response
  CPDLC operational messages ignored
  ADS-C contract requests result in no response to ATC, but an AOC uplink reject to the airline
  In all cases, there’s a network ack (so you’ll get message assurance success (MAS-S)
  All BPv14 software (or later)
PRs 877, 886, 888, 901, 904, 908, 923
Under investigation by airframe manufacturer and avionics supplier
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 35: PR 930, Conditional Clearance Executed After New Clearance Received
PR related to NAT
At 1627z, ATC sent this clearance (which crew WILCOed)
    MAINTAIN FL370
    AT 1836z DESCEND TO AND MAINTAIN FL280
    DESCEND TO REACH FL280 BY 1845z
    REPORT LEVEL FL280
Then at 1708z, ATC sent a new clearance (also WILCOed)
    CLEARED ROUTE CLEARANCE
    ROUTE HAS BEEN CHANGED
    MAINTAIN FL370
Then crew sent
    CONFIRM WE DO NOT DES AT 1836z TO FL280
ATC responded:
    DO NOT DESCEND
    MAINTAIN FL370
AT 1845z ATC received the report for LEVEL FL280
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 36: PR 930 (Cont.)
Crew received a reminder from the airplane system to execute the conditional clearance
  Not cancelled by superseding clearance
  No manual cancellation possible
Captain determined that airplane must follow the old clearance despite First Officer misgivings and the earlier exchange indicating the new clearance superseded the first
  Flight deck procedures?
And is the conditional clearance for 2 hours away acceptable?
GOLD guidance required?
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 37: Proposed Enhancement
Typing errors in logons will result in the airplane waiting 10 minutes to time out
  No indication of the error
DSP has to perform 4-character ICAO ID → 7-character address translation
  Similar to D-ATIS
  DSPs provide “NO PARTICIPATING AIRPORT” message for D-ATIS
Could DSPs provide something similar for erroneous ATC logons?
( IPACG-34 FIT-21 IP-01 Attachment 2 )

## Slide 38: Questions?
( IPACG-34 FIT-21 IP-01 Attachment 2 )