## Slide 1: CPDLC and ADS-C Performance Monitoring For FANS 1/A Over Iridium (FOI)
IPACG-35 FIT-22 IP/2 Attachment A
8 November 2011

## Slide 2: Contents
Summary of Reported Iridium Service Outages/Degradations – 2011
Observed Performance for Fans Over Iridium (FOI)
  RCP240 Performance Specifications for CPDLC
  RSP180 Performance Specifications for ADS-C
ADS-C Latency Analysis by Month – April to September 2011
  Oakland, Anchorage and New York FIR
Comparison of IGW1 (FOI via Sita) and IG1 (FOI via ARINC)
Comparison of Iridium by FIR – Aggregate July to September 2011
Comparison of ADS-C Latency Analysis by Operator and FIR – Aggregate July to September 2011
ADS-C Chart By Airframe – November to April 2011
  ZAN CLX B744
  ZNY CLX B744
Summary of Observed Performance

## Slide 3: Summary of Reported Iridium Service Outages/Degradations - 2011
Date | Start Time (UTC) | Duration (hh:mm:ss) | Explanation
01-Feb-2011 | 21:32 | 00:38:02 | Iridium's SBD service was unavailable.
24-Mar-2011 | 19:47 | 06:16:00 | The Short Burst Data Systems experienced an unexpected anomaly, SBD messaging may have been delayed and users may have received duplicate messages during this time.
5-May-2011 | 7:01 | 1:29:00 | Some customers utilizing SBD Direct IP for Mobile Terminated messages may have seen messages queued due difficulties connecting with the Iridium server. No messages were lost or service outage experienced; only the possibility of Direct IP Mobile Terminated messages being queued and some difficulty connecting to the Iridium SBD DIP MT server
11-Jul-2011 | 10:06 | 3:00:00 | Due to severe thunderstorms which occurred in the vicinity of the Tempe Gateway, customers may have experienced dropped calls and the inability to place or receive calls. Telephony, Paging, SMS messaging, and all Data services may have been affected until the weather anomaly passed. Iridium OpenPort service not affected.

## Slide 4: Summary of Reported Iridium Service Outages/Degradations - 2011
Date | Start Time (UTC) | Duration (hh:mm:ss) | Explanation
19-Aug-2011 | 00:57:00 | 02:03:00 | Due to thunderstorms in the vicinity of Tempe Gateway, customers may experience dropped calls and the inability to place or receive calls.Telephony and data serviced may be affected until weather anomaly has passed.
9-Sep-2011 | 07:00:00 | 0:30:00 | SBD Email MT users may have seen intermittent communications issue with Iridium email servers during this timeframe. All messages that were queued were sent.
9-Sep-2011 | 05:15:00 | 10:45:00 | Iridium Datalink ACARS service is now back to normal. The root cause for the anomaly is still under investigation.
11-Sep-2011 | 10:45:00 | 01:06:00 | During the time frame some customers may have experienced service degradation. All services at this time are back to normal operation.
14-Sep-2011 | 04:56:00 | 10:00:00 | Due to severe thunderstorms in the vicinity of the Tempe Gateway, customers may experience dropped calls and the inability to place or receive calls. Telephony, Paging, SMS messaging, and all Data services may be affected until the weather anomaly has passed. Iridium OpenPort service is not affected.

## Slide 14: Iridium in Oakland FIR – IGW1 vs. IG1
Iridium datalink service – provider GES designators
  IGW1: Sita
  IG1: ARINC
First observed usage of IG1 in July 2011
  BOE - B738
  111 ADS-C messages observed over 4 days in July 2011
Only 2 ADS-C messages observed in August 2011
HAL observed switching from Sita to ARINC in September shifting majority of Oakland Iridium message traffic to IG1

## Slide 25: Summary of Observed FOI Performance
95% criteria for RSP180 ADS-C was met in all of the past 6 months in Oakland FIR
95% criteria for RSP180 ADS-C was met in 2 of the past 6 months in Anchorage FIR
95% criteria for RSP180 ADS-C has been met in New York FIR in one of the past 6 months – May 2011
HAL B763 in ZAK meets 95% criteria for RCP240 ACP and ACTP and RSP180 ADS-C
2 out of 7 FIR/Oper/ACT combinations using FOI meet 95% criteria for RSP180 ADS-C
CLX B744 fleets show variability in ADS-C performance between Anchorage and New York FIR for same airframes
  Note: small message counts increase variability
IG1 first observed in July 2011 – shift in ADS-C latency distribution to the right of that of IGW1 in July 2011 but not in September 2011
HAL switched to ARINC for FOI (IG1) in September 2011 with noticeable impact on ZAK IGW1 performance