## Slide 1: CRA Report on Problem Reports
IPACG-35/FIT-22
Sapporo, Japan
November 7-11, 2011
Gordon Sandell

## Slide 2: Problem Reports
New IPACG Problem Report
  Summary
  Problems Reported/Processed Since FIT-21
Reports From Other Regions

## Slide 3: New IPACG Problem Report Summary
7 Problem Reports generated for issues in NOPAC/CEPAC/CENPAC regions
Ongoing discussions with CRASA-J to assist in PR resolution

## Slide 4: New IPACG Problem Reports
PR# | Title | Air, Gnd or Link | Region | Status | Comments
954 | CPDLC and ADS-C reports not received | AIR | NOPAC | CLOSED | 
955 | No SEND prompt | AIR | NOPAC | CLOSED | 
964 | Illegal Airway Name in DARP Trial Uplink | AIR | NOPAC | CLOSED | 
996 | Datalink outage with One Flight | N/A | NOPAC | CLOSED | Airline would not release data
1021 | UNABLE TO SEND MSG Displayed to the Crew | AIR | NOPAC | OPEN | 
1028 | CPDLC Downlink Message Not Received | AIR | NOPAC | CLOSED | 
1029 | CPDLC Uplink Message Not Received | AIR | NOPAC | CLOSED | 

## Slide 5: PR 954, CPDLC and ADS-C reports not received
B777 airplane successfully logged on, but position report stayed in SENDING state
Log shows 6 ADS contract request uplinks and two CPDLC position report uplinks
  MAS received (network ack) but no application responses
Crew reported performing master reset
Second successful logon about 25 minutes later, and normal operation
Appears to be a result of the router lock-up issue in software releases BPv14 and BPv15
  Fixed in BPv15A

## Slide 6: PR 955, No SEND prompt
B767 crew reported not getting SEND prompt on ATC page(s)
Log shows MSNs resetting to zero just before the crew report, followed by media advisories for establishment of SATCOM and HFDL
Appears that CMU went through a reset
  No link, so no SEND prompts
ADS/CPDLC connections unaffected by this

## Slide 7: PR 964, Illegal Airway Name in DARP Trial Uplink (1)
Airline performing “DARP Trial”
Crew sent ATC route request to Oakland using free text
Received INVALID ATC UPLINK
Received INVALID ATC UPLINK

## Slide 8: PR 964, Illegal Airway Name in DARP Trial Uplink (2)
Route uplink contained airways with illegal characters where “DCT” appeared in downlink
Oakland looking into the uplink encoding
Main issue is DARP procedure
  No company uplink (maybe just for trial)
  Use of free text for request
GOLD procedure for DARP is for airline to send route, and flight crew to use ROUTE REQUEST page
ATC DL Uplink Message AT1 - OAKODYA - .JA701J - CRC is valid
9,,06:34:11
0(83) : At [pos] Cleared [routeclr]
pos(l/l): N25 0.0 W170 0.0
dest airport(): RJTT
route info(): 18
(l/l): N25 0.0 W170 0.0
(l/l): N28 0.0 W180 0.0
(l/l): N30 0.0 E170 0.0
(l/l): N32 0.0 E160 0.0
(l/l): N33 0.0 E150 0.0
(pub): MORAY
(airway): OTR15
(pub): SMOLT
(airway): OTR16
(pub): SUNNS
(airway): [40]
(pub): SHOES
(airway): G223
(pub): CHEVY
(airway): Y824
(pub): ADDUM
(airway): [40]
(pub): HND

## Slide 9: PR 996, Datalink outage with One Flight
Anchorage reported loss of CPDLC and ADS contact with a flight for 30+ minutes
Airline refused permission for CRA access to the logs

## Slide 10: PR 1021, UNABLE TO SEND MSG Displayed to the Crew
B767 crew reported UNABLE TO SEND MSG displayed, and no downlinks sent
Review of message log shows this occurred just as VHF link lost
Appears to be a repeat of FMC/CMU problem that has been reported at several FIT meetings
FMC/CMU manufacturers aware of the issue, but unable to replicate it in labs

## Slide 11: PR 1028, CPDLC Downlink Message Not Received
B777 airplane requested climb from Anchorage
ATC reported clearance issued, and saw (via ADS) airplane climb to FL340, but never received WILCO
Logs show climb issued twice (7 minutes apart, different MIN), but only the second was responded to (and delivered)
Conclusion:
  Some confusion due to duplicate uplinks
  First uplink probably lost due to BPv14/v15 issue (same as PR 1029)

## Slide 12: PR 1029, CPDLC Uplink Message Not Received
Anchorage sent uplink to B777 that received MAS, but flight crew indicated it was not received
Logs show a free text CONTACT message that received no response at the time in question
Seems to be one of the BPv14/v15 issues that caused uplinks to fail the CRC check
  Fixed in BPv15A

## Slide 13: Reports From Other Regions (1)
PR 1030, No optional latitude longitude and airway to airway join in route requests
  Issue with B777 airplane
  Route downlinks should add a lat/long to any fix that has duplicates in the database (avoids ambiguity)
  Route downlinks should identify the fix at which route transitions from one airway to another
  B777 doesn’t do either
Candidate for future fix, but at present this is for info only, so that ATC is aware of these limitations

## Slide 14: Reports From Other Regions (2)
NAT CNSG/5 (Sept 2011 in Bodø, Norway) occurred since IPACG/34
DLMA (Data Link Monitoring Agency) report provided for info only
  Not presented!

## Slide 15: Questions?