## Slide 1: Problem Reports
NAT CNSG/5
Bodo
September 26-30, 2011
Gordon Sandell

## Slide 2: Problem Reports
New Problem Report Summary
New Problem Reports
  Problems Reported Since NAT CNSG/4
Individual Reports

## Slide 3: New Problem Report Summary
38 North Atlantic Problem Reports generated
  Including some duplicates
Encouraging use of ISPACG website and database for all problem reporting:
  http://www.ispacg-cra.com/

## Slide 4: New Problem Reports
PR # | Title | Air, Gnd, or Link | Comments
931 | Missed uplink message | GND | 
938 | Routine use of H.F. in CPDLC airspace | GND | For discussion Action: Shanwick
939 | ADS disconnection |  | Action: Airbus
940 | Reported ADS-C times grossly inaccurate |  | Action: Airbus
941 | Reported ADS-C times grossly inaccurate | - | Duplicate of PR940
942 | Reported ADS-C times grossly inaccurate | - | Duplicate of PR940

## Slide 5: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
945 | Uplink Clearance Msg received with no option Stdby or reject | AIR | 
947 | Logon delay CZQX | GND | No log
948 | Problems logging on to CZQX | GND | 
950 | No CPDLC connection with Gander | GND | 
951 | FMC WPR/ATS Crew Report of Missing ETA | AIR | 
952 | Unable to log on | GND | Action: Gander

## Slide 6: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
959 | ADS-C reports contain INVALID data |  | Action: Airbus
965 | Unable to Logon to Shanwick - No Flight Plan | GND | 
966 | DOWNLINK ERROR Due To Multiple CR1 Delivery | AIR/ LINK | 
967 | FMC Messages Not Sent via SATCOM | AIR | 
968 | Unable to Logon to Bodo | AIR | 
969 | Inoperative ADS Function | AIR | Action: Airbus

## Slide 7: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
970 | Wrong Format Oceanic Clearance From Gander | GND | 
971 | Gander Failed to send Oceanic clearance | GND | 
972 | Oceanic Clearance Not Displayed to Crew | AIR | 
973 | Unable to Establish CPDLC with Santa Maria Due to Misformatted Uplink | GND | Action: Santa Maria
974 | Oceanic Clearance Issues with Gander | GND | 
975 | Unable to Logon to Santa Maria - Erroneous Message Format | GND | Action: Santa Maria

## Slide 8: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
976 | Missing ADS Waypoint Report | AIR | 
978 | 777 Sent Duplicate Waypoint Change Event Reports in Downlink | AIR | 
979 | ATC Logon Ignored Then Rejected | GND | Action: Gander
980 | No ACCEPT For Oceanic Clearance | GND | 
981 | Oceanic Clearance in Wrong Format | GND | 
982 | Santa Maria Not Receiving FMC WPR | GND | Action: Santa Maria

## Slide 9: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
983 | 777 Sent ADS Report With 2 Waypoint Change Event Reports | AIR | 
984 | Unable to Logon to Gander | GND | Action: Gander
985 | 757 Sent Climb Request with Invalid Free Text Appended | AIR | 
986 | No Transfer to Santa Maria | GND | Action: Santa Maria
988 | Unable to Logon to Gander | AIR | 
989 | No Position Report at 20W | GND | Action: Shanwick

## Slide 10: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
990 | Erroneous CLIMB clearance | GND/ AIR | Action: Airbus
998 | A388 D-AIMF not able to log on to Gander Oceanic CZQX |  | Action: Airbus
1002 | No CDA message to aircraft E/Bound at 30W | - | Non-issue
1003 | No pos reports via datalink while aircraft showed logged on normally | AIR | 
1005 | RCL message lacking ACARS "envelope" formatting | AIR | 
1006 | Oceanic Clearance and ATC Logon Problems with Gander | GND | 

## Slide 11: New Problem Reports (Cont.)
PR # | Title | Air, Gnd, or Link | Comments
1007 | Failed Logon Due to SATCOM Uplink Non-Delivery | LINK | 
987 | Unable to Logon to EGGX (SATCOM IN PROG Displayed) | AIR/ LINK | 

## Slide 12: Individual Reports

## Slide 13: PR931, Missed uplink message
Crew did not receive CONTACT message from Shanwick to contact Scottish Center at 0516z
Connect request (CR1) received at 0514z
End service not received from Reykjavik until 0519z
Airplane sent "NOT CURRENT DATA AUTHORITY" to Shanwick
Conclusion: Shanwick was not the active center when it sent the uplink

## Slide 14: PR938, Routine use of H.F. in CPDLC airspace
Shanwick repeatedly using HF for routine exchanges with CPDLC-equipped airplanes
Frequent occurrence
Open to Shanwick…

## Slide 15: PR939, ADS disconnection
Whenever New York sent ADS-C contract request, received “ADS disconnect – no reason specified”
Recently assigned to Airbus

## Slide 16: PR940 Reported ADS-C times grossly inaccurate
New York received ADS-C reports indicating next waypoint would be passed at current time
  Event, demand and periodic reports
  CPDLC query got the correct answer
Recently assigned to Airbus
PR941 and PR942 are duplicate entries (website/database issue)

## Slide 17: PR945, Uplink Clearance Msg received with no option Stdby or reject
Pilot reported OCL message did not have STANDBY or REJECT options
These are not available options for an ARINC 623 OCL
Pilot training issue

## Slide 18: PR947, Logon delay CZQX
No log obtained, but appears to be the same as PR950

## Slide 19: PR948, Problems logging on to CZQX
Airplane unable to logon to Gander
Gander investigated and found issues with use of multiple addresses for OCL and FANS
Software fix installed to resolve these issues

## Slide 20: PR950, No CPDLC connection with Gander
Flights crossed into Gander airspace over PEPKI
Airplane attempted ATC logon before entry but no CPDLC connection
Issue was with Gander adaptation that didn't detect conditions to initiate CPDLC connection
Gander has now adjusted airspace boundaries in the system, so it will properly trigger CPDLC connection

## Slide 21: PR951, FMC WPR/ATS Crew Report of Missing ETA
Airplane (757) was using FMC WPR ATC reported that position report didn't include ETA
Logs show position report omitted ETA
POSN51003W050001,N51000W050000,025845,370,N55000W040000,,N57000W030000,M48,31039,458,791/TS025845,010411D740
FMC will do this if no computed ETA is available.

## Slide 22: R952, Unable to log on
Airplane could not logon to Gander
Reason code 4 ("Could not match ID/position to flight plan")
Flight plan filing process or ATC ground system issue
Nav Canada investigating

## Slide 23: PR959, ADS-C reports contain INVALID data
ADS-C reports received containing invalid default?) data for NEXT and NEXT+1 waypoints
Report indicated most/all were Airbus airplanes
Recently assigned to Airbus

## Slide 24: PR965, Unable to Logon to Shanwick - No Flight Plan
Airplane could not logon to Shanwick
Reason code 4 ("Could not match ID/position to flight plan")
Shanwick did not receive flight plan (ACT from Santa Maria)
CFMU did not send FPL to Shanwick as Tel Aviv AIS did not address it to them
Flight plans filed locally for security reasons

## Slide 25: PR966, DOWNLINK ERROR Due To Multiple CR1 Delivery
Crew received DOWNLINK ERROR indication
Airplane received connect request (CR1) uplink twice
  Once on VHF
  Once on SATCOM (retry)
Airplane then sent two CC1 downlinks referencing the same uplink MIN
Gander sent an ERROR response for the second, as the MIN was closed by the time that happened
Known issue that happens occasionally
  We have a means to avoid this for operational uplinks, but it would potentially preclude legitimate reconnects if applied to CR1s

## Slide 26: PR967, FMC Messages Not Sent via SATCOM
Airplane was unable to transmit ATC (or FMC) messages over SATCOM
UNABLE TO SEND MSG displayed
Other ACARS messages OK
This is a known FMC/CMU issue
Boeing and FMC/CMU manufacturers unable to replicate in lab
Remains an open issue

## Slide 27: PR968, Unable to Logon to Bodo
Airplane unable to logon to Bodo
Not surprising, as Bodo doesn't have CPDLC
Crew training issue

## Slide 28: PR969, Inoperative ADS Function
A330 airplanes logon to BIRD
  Receive CPDLC request and ADS-C contract request (including intent groups)
Airplane disconnects CPDLC and ADS-C
All subsequent ADS-C requests are ignored
Also reported in PR851
Airbus investigating

## Slide 29: PR970, Wrong Format Oceanic Clearance From Gander
Crew complained that oceanic clearance had no ACCEPT button
Airplane sent oceanic clearance request (ARINC 623 format)
Gander sent oceanic clearance in ARINC 620 format
No CRC, treated by airplane as airline free text uplink (hence no ACCEPT)
Gander reported this was an issue with airplanes sending RCL before they received the flight estimate (CPL)
Problem has been corrected

## Slide 30: PR971, Gander Failed to send Oceanic clearance
Crew received "RCL RECEIVED GANDER CLEARANCE NOT ACKNOWLEDGED. SEND DATA LINK ACCEPTANCE NOW" but no OCL
Gander reported this was an issue because the flight plan went through 0 deg longitude
Software fix has been implemented

## Slide 31: PR972, Oceanic Clearance Not Displayed to Crew
Crew did not receive oceanic clearance
Oceanic clearance sent to and acked by airplane
Airline working with CMU supplier

## Slide 32: PR973, Unable to Establish CPDLC with Santa Maria Due to Misformatted Uplink
Airplane unable to establish CPDLC with Santa Maria (LPPO)
CPDLC fine with Gander (CZQX) and Shanwick (EGGX)
Santa Maria sent connect request with the correct SMI (FMD), but without the IMI and supplementary address (/AA SMACAYA.)
Santa Maria investigating

## Slide 33: PR974, Oceanic Clearance Issues with Gander
Airplane requested OCL and got rejection
Then got clearance
Accepted, then got "CLRNCE NOT ACKNOWLEDGED - SEND DATALINK ACCEPTANCE NOW“
Gander indicated a gateway failure at this time, which caused loss of some data
Software fix implemented to resolve cause of gateway failure

## Slide 34: PR975, Unable to Logon to Santa Maria - Erroneous Message Format
Airplane was unable to logon to Santa Maria (LPPO)
Cause similar to PR973
AFN ACK sent with correct SMI, but missing IMI and supplementary address (/A0 SMACAYA.)
Santa Maria investigating

## Slide 35: PR976, Missing ADS Waypoint Report
Missing ADS-C position (waypoint change event) report
B777 sent downlink containing 2 copies of the report
Same as PR978

## Slide 36: PR978, 777 Sent Duplicate Waypoint Change Event Reports in Downlink
Gander reported missing ADS reports at 30W and 40W
Airplane actually sent waypoint change event reports at 30W and 40W
Reports to Gander contained two identical copies of the report
Airplane was a B777
Reports to Shanwick for the same waypoints were OK
Gander discards reports with multiple reports in them

## Slide 37: PR979, ATC Logon Ignored Then Rejected
Airplane tried to log on to Gander but was rejected (flight plan mismatch)
Under investigation by Gander
Same event as PR980

## Slide 38: PR980, No ACCEPT For Oceanic Clearance
Airplane received oceanic clearance without ACCEPT button
Repeat of PR981

## Slide 39: PR981, Oceanic Clearance in Wrong Format
Received OCL without ACCEPT button
Gander offers ARINC 620 and ARINC 623 OCL service
Airline has to define default, which is used when OCL sent before RCL is received
This particular issue solved by having airline defined as ARINC 623
Leaves an issue for airlines with mixed fleets

## Slide 40: PR982, Santa Maria Not Receiving FMC WPR
Santa Maria reported not receiving FMC waypoint reports (WPR)
Log shows reports sent at W050, W040, W030 and W020 and forwarded to Santa Maria
Santa Maria investigating

## Slide 41: PR983, 777 Sent ADS Report With 2 Waypoint Change Event Reports
Gander reported not receiving 30W ADS report
ADS report sent containing the same waypoint change event report twice
Airplane was a B777
Same as PR 978

## Slide 42: PR984, Unable to Logon to Gander
Airplane reported unable to logon to Gander
Gander established CPDLC as NEXT Center
Shanwick sent end-service
DR1 sent to Shanwick and Gander (crew turned ATC off?)
Crew logon to Gander, but no response
Gander investigating

## Slide 43: PR985, 757 Sent Climb Request with Invalid Free Text Appended
757 Airplane sent altitude change request
Then had DOWNLINK ERROR displayed (Gander had responded with error uplink)
This was a repeat of an old problem (believed fixed), where the airplane appended a free text element with non-displayable characters
Under investigation by Boeing and Honeywell

## Slide 44: PR986, No Transfer to Santa Maria
No transfer from New York to Santa Maria
Another case of Santa Maria sending the uplinks in an improper format (correct SMI, but missing IMI and supplementary address)
Issue for Santa Maria

## Slide 45: PR987, Unable to Logon to EGGX (SATCOM IN PROG Displayed)
Crew reported that after disconnect from Santa Maria, they could not send logon to Gander
  SATCOM IN PROG displayed on the ACARS page
Iridium airplane (757) was sending ADS reports (event and periodic to 2 centers)
  Send ADS report (first try)
  3-minute wait and retry same ADS report
  Send next ADS report and repeat…
Seems to be an issue with Iridium transceiver not seeing network acks

## Slide 46: PR988, Unable to Logon to Gander
Airplane reported unable to logon to Gander
7 AFN logons with a flight identifier having a zero in one of the first 3 characters (airline identifier)
  Each received AFN ACK with reason code 4 (flight plan mismatch)
8th AFN logon had a letter “O” instead of the zero
  Success
Put this down to pilot finger trouble

## Slide 47: PR989, No Position Report at 20W
Aircrew reported no position report sent at 20W
Message log shows ADS-C waypoint change event report sent and delivered to Shanwick
Assigned to Shanwick for investigation

## Slide 48: PR990, Erroneous CLIMB clearance
Crew reported requesting climb, receiving STANDBY, then a non-standard uplink, then the climb clearance, then CANCEL CLIMB
ATC actually sent:
  STANDBY
  UNABLE + free text “REQUESTED FLIGHT LEVEL STAND BY”
  Free text "MESSAGE SENT IN ERROR STAND BY FOR CLIMB CLEARANCE“
  Climb clearance
Crew responded to climb clearance, but not free text
Appears as if crew saw the climb clearance first (arrived 3 seconds after free text)
Airbus looking into this

## Slide 49: PR998, A388 D-AIMF not able to log on to Gander Oceanic CZQX
Airplane unable to logon to Gander, but logged on to Reykjavik and Shanwick fine.
Recently assigned to Airbus

## Slide 50: PR1002, No CDA message to aircraft E/Bound at 30W
Report was that the airplane didn’t receive the CDA message on entering Shanwick, so logged off and logged back on again
Crew actually responded ROGER to the welcome message, and there was no ATC comm termination or re-logon
Have to presume the report was for the wrong flight/date.

## Slide 51: PR1003, No pos reports via datalink while aircraft showed logged on normally
Gander reported not receiving ADS reports at W030 and W040 on westbound flight
  Flight crew logged off and on again between those two
Problem was repeat of PR976, 978 and 983
  Airplane sent one downlink containing two copies of the same waypoint change event report
Problem under investigation by Boeing and Honeywell

## Slide 52: PR1005, RCL message lacking ACARS "envelope" formatting
Reykjavik received oceanic clearance request in near-ARINC 623 format from a B777
  No CRC at the end
  No IMI at the start (OC1)
That operator doesn’t have the ARINC 623 option
  Request sent was from a company application
Could become an issue with mixed fleet operation
Interesting conundrum for operators with mixed fleet keeping track of how to get OCLs in different FIRs with different equipage…

## Slide 53: PR1006, Oceanic Clearance and ATC Logon Problems with Gander
Airplane unable to receive OCL from Gander, or to logon to Gander
  FLIGHT PLAN NOT HELD response to OCL request
  ATC logon rejected with reason code 4 (flight plan mismatch)
Gander actually received the flight plan, but was unable to process it because of format error (additional data after closing bracket)
Airline working with service provider to avoid this

## Slide 54: PR1007, Failed Logon Due to SATCOM Uplink Non-Delivery
Airplane unable to logon to Shanwick
Problem was with (non-)delivery of messages over SATCOM
Airline has different providers for Inmarsat and Iridium-equipped airplanes
SITA used single default SATCOM provider for both fleets, so uplinks to Iridium airplanes were forwarded to ARINC and then rejected
Change implemented to resolve this issue.

## Slide 55: Questions?