## Slide 1: CPDLC and ADS-C Data Link Performance Monitoring for Fans Over HFDL (FOH)
IPACG-35 FIT-22 IP/3 Attachment A
8 November 2011

## Slide 2: Contents
Summary of Observed Performance for Fans Over HFDL (FOH)
  Hawaiian Airlines (HAL) - B763
  Oakland FIR
  RCP400 Performance Specifications for CPDLC
  Type400 Performance Specifications for ADS-C
Analysis by Month – April to September 2011
ADS-C Analysis by Airframe – Aggregate July to September 2011
  No CPDLC charts due to low sample size of CPDLC message counts
Plot of HAL HFDL ADS-C Position Reports
Summary of Observed Performance

## Slide 8
HAL HFDL ADS-C Position Reports
Latency > 300 sec
Latency > 400 sec
HAL HFDL ADS-C Downlink Latency Plot - February to April 2011

## Slide 9: Summary of Observed HFDL Performance
The 95% criteria for RCP400 ACTP criteria was met in 4 of the past 6 months including August and September 2011
The 95% criteria for RCP400 ACP was met in 2 of the past 6 months
  Not met in August and September but these months show improvement over July
The 95% criteria for RSP400 ADS-C was met in 1 of the past 6 months – April 2011
For the aggregate time period from July to September 2011, 7 of the 17 HAL B763 airframes meet the 95% criteria for RSP400 ADS-C