## Slide 1: CPDLC and ADS-C Data Link Performance Monitoring
IPACG-35 FIT-22 IP/1 Attachment A
8 November 2011

## Slide 2: Contents
Summary of Inmarsat Reported Service Outages/Degradations
GOLD Analysis Overview
CPDLC and ADS-C Monthly Performance
  Oakland, Anchorage, New York
  RCP240 and RSP180 for SAT, VHF
  RCP400 and RSP400 for HF
  Comparison of SAT Performance by FIR
Performance by GES Designator
  Oakland, Anchorage, New York
  Monthly performance for Eik (XXE)
Performance by Operator
  New York, Oakland, Anchorage
  FIR/Aircraft Type Performance Comparison for Operator A

## Slide 3: Summary of Inmarsat Reported Service Outages/Degradations 2010 to Present
Date | DSP | Region Affected | Start Time (UTC) | Duration (min) | Explanation
01-Feb-2010 | Sita | POR AOW/AOE | 18:00:00 | 45 | Failure of an X25 to IP gateway cluster in Montreal which impacted all connections to the AIRCOM VHF stations, satellite GES and X25 hosts Customer Hosts
03-Feb-2010 | Sita | POR AOW/AOE | 23:10:00 | 16 | Unknown
01-Mar-2010 | ARINC | POR | 12:22:00 | 473 | The ARINC GLOBALINK GES XXC located in Santa Paula, CA was impaired due to problems with AERO Voice calls supporting the Pacific Ocean Region (POR).
10-Mar-2010 | ARINC | POR | 11:01:50 | 55 | The ARINC AGN AT&T MPLS core node in Livermore, California was out of service due to a major network failure in the AT&T Sonet Network
19-Mar-11 | Sita | IOR | 7:08:00 | 72 | Satellite Voice, Fax and PC Data and Data Services were not avaliable over IOR2 region due to an equipment failure. POR2 was not affected by the interruption.
07-Oct-2010 | Sita | AOW | 18:21:00 | 11 | Faulty part caused equipment failure at GES.
19-Mar-2011 | Sita | IOR | 07:08:00 | 72 | Equipment failure.
02-Apr-2011 | Sita | AOW/AOE | 19:41:00 | 71 | Power outage at Aussaguel GES.
27-Jul-11 | Sita | IOR | 14:35:00 | 163 | Antenna fault at Perth GES.

## Slide 4: GOLD Analysis Overview: CPDLC Message Set
According to the guidance in the Global Operational Data Link Document (GOLD) only a specific message set in considered
  All uplink communications transfer messages and typical intervention messages such as climb clearances with an observed CPDLC “WILCO” and/or “Unable” response attribute are assessed
  These messages are considered to be intervention messages critical to the communications used when applying reduced separation standards
Notes: FAA is developing and deploying decision support tools to aid the air traffic controller. DSTs have many functions such as probing for aircraft-aircraft and/or aircraft-airspace conflicts, safely and efficiently metering aircraft into airports, and providing advisors to air traffic management specialists that specific regions of airspace will reach capacity levels.
Fundamental to all these DSTS is the trajectory modeler function which generates aircraft trajectory predictions. An aircraft trajectory is the actual or prediction of the four-dimensional path of the aircraft. Each DST has required levels of accuracy for its trajectory predictions based on its unique functions and capabilities.

## Slide 5: GOLD Analysis Overview: CPDLC Performance Measures
Actual Communication Performance (ACP)
  Total time required by the communication transaction
  Begins when the CPDLC uplink message is sent to aircraft
  Ends when the WILCO is received
Actual Communication Technical Performance (ACTP)
  Time required for the message delivery part of the communication transaction, includes:
    CPDLC clearance uplink transit time
    WILCO downlink transit time
Pilot Operational Response Time (PORT)
  Time required for crew response
  Estimated by ACP - ACTP

## Slide 6: GOLD Analysis Overview: CPDLC Performance Measures

## Slide 7: GOLD Analysis Overview: ADS-C Messages and Performance Measure
Surveillance Latency
  All downlink ADS-C messages are included
  Measures transit time for downlink message delivery
  Begin time estimated by timestamp of aircraft when sent
  End time estimated by timestamp of ATC receipt

## Slide 8: GOLD Analysis Overview: Interpreting GOLD Charts
** In this example the observed performance meets the 95% criteria but does not meet the 99.9% criteria
Observed Performance
95% Criteria (180 sec)
Actual 95 % level
99.9% Criteria (210 sec)

## Slide 9: Note: Y-axis Scale on Performance Charts
Please note the y-axis scale in various performance charts
  Most charts show the 90 to 100% portion of the cumulative distribution of the respective performance measure
  Due to some cases where performance is below that shown on the 90 to 100% portion, the y-axis will be shifted down below 90%
Please note that some charts are presented twice on two different scales
  One showing the full 0 to 100% of the cumulative distribution of the respective performance measure
  One showing the 90 to 100% portion of the cumulative distribution of the respective performance measure
Please note the difference in the y-axis scale for charts showing the relative distribution vs. the cumulative distribution

## Slide 10: GOLD Performance Criteria
Performance Measure | Percent of Messages Required to Meet Criteria | RSP180 Criteria (sec) | RSP400 Criteria (sec) | RCP240 Criteria (sec) | RCP400 Criteria (sec)
ADS-C Latency | 95% | 90 | 300 | -- | --
 | 99.9% | 180 | 400 | -- | --
ACTP | 95% | -- | -- | 120 | 260
 | 99.9% | -- | -- | 150 | 310
ACP | 95% | -- | -- | 180 | 320
 | 99.9% | -- | -- | 210 | 370
PORT | 95% | -- | -- | 60 | 60

## Slide 11: Oakland Monthly Performance April to September 2011

## Slide 21: Summary of Performance in ZAK
SAT and VHF meet 95% criteria for RCP240 ACP, ACTP and RSP180 ADS-C for the last 6 months
HF meets 95% criteria for RCP400 for ACTP in 3 of the last 6 months
HF meets 95% criteria for RCP400 for ACP in 2 of the last 6 months
HF does not meet 95% criteria for RSP400 for ADS-C in any of the last 6 months

## Slide 22: Anchorage Monthly Performance April to September 2011

## Slide 30: Summary of Performance in ZAN
SAT and VHF meet 95% criteria for RCP240 ACP, ACTP and RSP180 ADS-C for the last 6 months
HF met 95% criteria for RSP400 for ADS-C in July 2011
Not enough data for RCP400 ACP, ACTP

## Slide 31: New York Monthly Performance April to September 2011

## Slide 39: Summary of Performance in ZNY
SAT and VHF meet 95% criteria for RCP240 ACP, ACTP and RSP180 ADS-C for the last 6 months
HF meets 95% criteria for RSP400 for ADS-C in two of the past 6 months (May and September 2011)
Not enough data for monthly RCP400 ACP, ACTP

## Slide 40: Comparison of SAT Performance by FIR Aggregate July to September 2011

## Slide 45: Summary of Comparison of SAT Performance by FIR
All 3 FIR meet 95% criteria for RCP240 ACP, ACTP and RSP180 ADS-C
All 3 FIR are close to meeting 99.9% criteria for RCP240 ACTP
Oakland and Anchorage are close to meeting the 99.9% criteria for RSP180 ADS-C
Anchorage and Oakland meet 95% within 60 sec for PORT
  New York is close to meeting 95% for PORT

## Slide 46
ADS-C Performance by GES Designator Aggregate July to September 2011

## Slide 47: GES Locations and Designators
SITA
  Aussaguel, France: AOW2, AOE2
  Eik, Norway: AOW3, AOE3, IOR5
  Perth, Australia: POR1, IOR2
  Santa Paula, CA, US: POR4
ARINC:
  Santa Paula, CA, US: XXC
  Eik, Norway: XXE
Inmarsat - I4
  Fucino, Italy
    SITA: EUA1
    ARINC: XXF
  Paumalu, HI, US
    SITA: APK1, AME1
    ARINC: XXH
Iridium
  Phoenix, AZ, US
    SITA: IGW1
    ARINC: IG1

## Slide 54: Summary of Observed ADS-C Performance by GES
All GES meet RSP180 95% criteria in Oakland except for XXE
All GES meet RSP180 95% criteria in Anchorage except for IGW1, XXE and AME1 (XXE and AME1 have very small message counts in Anchorage FIR)
All GES meet RSP180 95% criteria in New York except for AOW3 and IGW1
  XXE is still well below the other main Atlantic GES, AOE and AOW
Performance for the two main Pacific GES, XXC and POR1, is noticeably better in Oakland than in Anchorage

## Slide 55: Observed GES Performance - XXE April to September 2011

## Slide 59: Observations
ARINC email notifications indicated significant maintenance activity on XXE in January and February 2011
No significant, sustained improvement

## Slide 60: Performance By Operator

## Slide 61: Performance By Operator
Analysis separate by FIR: Oakland, Anchorage and New York
Analysis period: aggregate July to September 2011
SAT operations only
RSP180 and RCP240 performance criteria
Operators contributing top 90% of SAT ADS-C downlink messages
Operators ordered in summary tables by descending count of ADS-C downlink messages
Operators not meeting 95% criteria highlighted in red
Operators meeting 99.9% criteria highlighted in blue
Additional charts by aircraft type and by airframe for operators not meeting 95% criteria

## Slide 62: Observed SAT Performance by Operator Oakland FIR – July to September 2011
Oper Code | Count of SAT ADS-C | % of Total SAT ADS-C | ADS-C 95% | ADS-C 99.9% | Count of SAT CPDLC | % of Total SAT CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
A | 90,501 | 14.67% | 98.36% | 99.55% | 7,346 | 13.12% | 99.44% | 99.56% | 99.14% | 99.50% | 95.26%
D | 60,215 | 9.76% | 98.32% | 99.56% | 4,132 | 7.38% | 99.47% | 99.66% | 99.59% | 99.69% | 97.73%
B | 47,880 | 7.76% | 99.29% | 99.67% | 4,081 | 7.29% | 99.51% | 99.56% | 99.14% | 99.41% | 98.09%
G | 40,823 | 6.62% | 99.73% | 99.82% | 6,037 | 10.78% | 99.85% | 99.90% | 99.77% | 99.78% | 99.30%
L | 38,625 | 6.26% | 98.81% | 99.76% | 3,895 | 6.95% | 99.49% | 99.59% | 98.64% | 98.97% | 95.61%
Q | 34,565 | 5.60% | 98.38% | 99.64% | 3,146 | 5.62% | 99.59% | 99.68% | 99.65% | 99.68% | 98.19%
E | 25,390 | 4.12% | 99.24% | 99.64% | 1,960 | 3.50% | 99.59% | 99.69% | 99.49% | 99.69% | 98.78%
J | 23,906 | 3.88% | 99.62% | 99.91% | 2,800 | 5.00% | 99.86% | 99.86% | 99.71% | 99.86% | 99.43%
O | 22,443 | 3.64% | 99.26% | 99.91% | 1,730 | 3.09% | 99.94% | 99.94% | 99.83% | 100.0% | 98.67%
F | 21,370 | 3.46% | 99.34% | 99.84% | 3,170 | 5.66% | 99.91% | 99.94% | 99.75% | 99.84% | 99.09%
M | 20,345 | 3.30% | 98.35% | 99.40% | 1,440 | 2.57% | 99.38% | 99.51% | 99.24% | 99.44% | 97.99%

## Slide 63: Observed SAT Performance by Operator Oakland FIR – July to September 2011 (Continued)
Oper Code | Count of SAT ADS-C | % of Total SAT ADS-C | ADS-C 95% | ADS-C 99.9% | Count of SAT CPDLC | % of Total SAT CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
H | 18,058 | 2.93% | 99.52% | 99.80% | 2,624 | 4.68% | 99.70% | 99.85% | 99.81% | 99.96% | 98.86%
T | 16,112 | 2.61% | 99.40% | 99.85% | 1,926 | 3.44% | 99.58% | 99.74% | 99.58% | 99.74% | 98.75%
N | 14,975 | 2.43% | 99.49% | 99.59% | 1,050 | 1.87% | 99.43% | 99.43% | 99.05% | 99.43% | 98.57%
K | 14,727 | 2.39% | 98.87% | 99.38% | 1,360 | 2.43% | 99.34% | 99.41% | 99.49% | 99.93% | 98.38%
R | 13,524 | 2.19% | 98.11% | 99.61% | 1,118 | 2.00% | 99.55% | 99.64% | 99.64% | 100.0% | 97.94%
S | 12,409 | 2.01% | 98.57% | 99.53% | 921 | 1.64% | 99.89% | 99.89% | 99.67% | 99.67% | 98.70%
V | 10,728 | 1.74% | 99.93% | 99.97% | 842 | 1.50% | 100.0% | 100.0% | 99.88% | 100.0% | 99.52%
Y | 10,297 | 1.67% | 98.76% | 99.31% | 394 | 0.70% | 98.73% | 98.98% | 97.97% | 98.48% | 96.70%
RCH | 8,905 | 1.44% | 98.60% | 99.15% | 463 | 0.83% | 98.70% | 98.70% | 96.11% | 96.33% | 87.04%
NNN | 7,742 | 1.26% | 96.22% | 98.88% | 430 | 0.77% | 98.14% | 98.84% | 96.51% | 97.91% | 92.79%
W | 7,634 | 1.24% | 97.59% | 99.92% | 623 | 1.11% | 99.68% | 100.0% | 100.0% | 100.0% | 98.56%

## Slide 64: Summary of Observed SAT Performance By Operator Oakland FIR – July to September 2011
There are 22 commercial operators contributing to the top 90% of ADS-C downlink messages
All 22 operators meet the 95% criteria for RSP180 ADS-C and RCP240 ACTP and ACP
20 of the 22 operators meet the 95% criteria for PORT within 60 seconds
4 of the operators meet the 99.9% criteria for RSP180 ADS-C
7 of the operators meet the 99.9% criteria for RCP240 ACTP
7 of the operators meets the 99.9% criteria for RCP240 ACP

## Slide 65: Observed SAT Performance by Operator Anchorage FIR – July to September 2011
Oper Code | Count of SAT ADS-C | % of Total SAT ADS-C | ADS-C 95% | ADS-C 99.9% | Count of SAT CPDLC | % of Total SAT CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
Q | 23,796 | 14.42% | 97.94% | 99.58% | 962 | 13.88% | 99.48% | 99.69% | 99.48% | 99.90% | 96.15%
D | 15,301 | 9.28% | 97.09% | 99.49% | 390 | 5.63% | 99.74% | 99.74% | 99.74% | 100.0% | 96.41%
Y | 15,019 | 9.10% | 96.10% | 97.74% | 258 | 3.72% | 97.67% | 97.67% | 96.51% | 97.29% | 94.96%
L | 14,997 | 9.09% | 99.08% | 99.79% | 569 | 8.21% | 99.65% | 99.65% | 98.95% | 99.30% | 93.85%
A | 10,577 | 6.41% | 95.51% | 99.22% | 430 | 6.20% | 99.77% | 99.77% | 98.84% | 99.77% | 92.79%
H | 10,561 | 6.40% | 99.35% | 99.81% | 630 | 9.09% | 99.68% | 99.84% | 99.37% | 100.0% | 98.25%
S | 10,272 | 6.23% | 97.54% | 99.78% | 542 | 7.82% | 99.45% | 100.0% | 98.89% | 99.08% | 94.65%
J | 8,716 | 5.28% | 99.86% | 99.92% | 484 | 6.98% | 100.0% | 100.0% | 100.0% | 100.0% | 98.97%

## Slide 66: Observed SAT Performance by Operator Anchorage FIR – July to September 2011 (Continued)
Oper Code | Count of SAT ADS-C | % of Total SAT ADS-C | ADS-C 95% | ADS-C 99.9% | Count of SAT CPDLC | % of Total SAT CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
F | 8,489 | 5.15% | 97.89% | 99.81% | 544 | 7.85% | 99.26% | 99.63% | 99.63% | 99.63% | 98.35%
G | 7,584 | 4.60% | 99.66% | 99.93% | 453 | 6.53% | 99.78% | 99.78% | 99.34% | 99.34% | 99.12%
R | 6,156 | 3.73% | 95.74% | 99.27% | 277 | 4.00% | 98.92% | 99.28% | 98.92% | 99.28% | 96.03%
P | 4,878 | 2.96% | 97.81% | 99.59% | 258 | 3.72% | 98.84% | 99.22% | 97.29% | 98.06% | 90.31%
T | 4,738 | 2.87% | 98.65% | 99.66% | 237 | 3.42% | 98.73% | 99.16% | 99.16% | 99.16% | 98.31%
QQQ | 4,546 | 2.76% | 99.43% | 99.65% | 215 | 3.10% | 100.0% | 100.0% | 100.0% | 100.0% | 99.53%
M | 3,796 | 2.30% | 96.94% | 99.24% | 149 | 2.15% | 100.0% | 100.0% | 96.64% | 96.64% | 93.29%

## Slide 67: Summary of Observed SAT Performance By Operator Anchorage FIR – July to September 2011
There are 15 commercial operators contributing to the top 90% of ADS-C downlink messages
All of the 15 operators meet the 95% criteria for RSP180 ADS-C
All 15 operators meet the 95% criteria for RCP240 ACTP and ACP
11 of the 15 operators meet the 95% criteria for PORT within 60 seconds
2 of the operators meet the 99.9% criteria for RSP180 ADS-C
4 of the operators meet the 99.9% criteria for RCP240 ACTP
5 of the operators meets the 99.9% criteria for RCP240 ACP

## Slide 68: Observed SAT Performance by Operator New York FIR – July to September 2011
Oper Code | Count of SAT ADS-C | % of Total SAT ADS-C | ADS-C 95% | ADS-C 99.9% | Count of SAT CPDLC | % of Total SAT CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
BB | 30,074 | 14.46% | 99.21% | 99.45% | 2,110 | 12.09% | 98.86% | 98.91% | 98.77% | 99.19% | 95.73%
AA | 23,722 | 11.41% | 99.02% | 99.66% | 3,013 | 17.27% | 99.70% | 99.80% | 99.40% | 99.67% | 96.85%
FF | 16,386 | 7.88% | 97.17% | 99.17% | 1,494 | 8.56% | 99.13% | 99.33% | 98.86% | 99.20% | 96.32%
L | 15,853 | 7.62% | 96.10% | 99.22% | 1,640 | 9.40% | 98.54% | 99.15% | 97.74% | 98.48% | 92.13%
DD | 12,812 | 6.16% | 95.85% | 99.25% | 1,266 | 7.25% | 98.58% | 99.45% | 97.79% | 98.18% | 91.55%
EE | 11,544 | 5.55% | 99.21% | 99.59% | 933 | 5.35% | 99.46% | 99.57% | 98.82% | 99.36% | 92.82%
GG | 9,932 | 4.78% | 99.73% | 99.94% | 677 | 3.88% | 99.85% | 100.0% | 99.26% | 99.26% | 96.75%
JJ | 8,957 | 4.31% | 99.53% | 99.90% | 439 | 2.52% | 100.0% | 100.0% | 98.63% | 99.09% | 93.17%
CC | 7,024 | 3.38% | 98.56% | 99.17% | 643 | 3.68% | 98.76% | 98.91% | 98.91% | 99.22% | 93.93%
HH | 6,599 | 3.17% | 99.85% | 99.95% | 393 | 2.25% | 99.75% | 100.0% | 98.73% | 99.24% | 95.67%

## Slide 69: Observed SAT Performance by Operator New York FIR – July to September 2011 (Continued)
Oper Code | Count of SAT ADS-C | % of Total SAT ADS-C | ADS-C 95% | ADS-C 99.9% | Count of SAT CPDLC | % of Total SAT CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
RCH | 5,820 | 2.80% | 94.76% | 96.22% | 254 | 1.46% | 99.21% | 99.21% | 96.85% | 97.24% | 90.55%
M | 5,264 | 2.53% | 91.58% | 95.74% | 373 | 2.14% | 96.51% | 97.05% | 95.17% | 96.25% | 90.88%
LL | 5,245 | 2.52% | 98.84% | 99.56% | 671 | 3.85% | 99.40% | 99.40% | 98.81% | 99.25% | 97.17%
R | 5,178 | 2.49% | 95.15% | 99.03% | 406 | 2.33% | 98.28% | 99.01% | 99.26% | 99.75% | 95.32%
PP | 5,167 | 2.48% | 98.49% | 99.79% | 421 | 2.41% | 99.76% | 100.0% | 99.52% | 99.76% | 95.96%
DDDD | 4,341 | 2.09% | 99.95% | 99.98% | 380 | 2.18% | 100.0% | 100.0% | 98.68% | 99.74% | 95.26%
MM | 4,339 | 2.09% | 99.82% | 99.86% | 280 | 1.60% | 99.64% | 100.0% | 99.64% | 100.0% | 95.71%
SS | 4,285 | 2.06% | 98.41% | 99.72% | 276 | 1.58% | 99.64% | 99.64% | 98.19% | 99.28% | 92.03%
KKKK | 3,341 | 1.61% | 99.61% | 99.73% | 380 | 2.18% | 100.0% | 100.00% | 99.74% | 100.0% | 96.58%
A | 2,910 | 1.40% | 92.58% | 98.28% | 151 | 0.87% | 97.35% | 97.35% | 99.34% | 99.34% | 94.04%

## Slide 70: Summary of Observed SAT Performance By Operator New York FIR – July to September 2011
There are 20 commercial operators contributing to the top 90% of ADS-C downlink messages
2 of the 20 operators do not meet the 95% criteria for RSP180 ADS-C
  Operator M: operates fleet of 4 aircraft types in New York FIR
    B772 fleet meets 95% criteria for RSP180 ADS-C
    B762 fleet does not meet 95% criteria for RSP180 ADS-C
    B764 fleet does not meet 95% criteria for RSP180 ADS-C
    B752 fleet does not meet 95% criteria for RSP180 ADS-C
  Operator A: operates B772 fleet only in New York FIR
All 20 operators meet the 95% criteria for RCP240 ACTP and ACP
11 of the 20 operators meet the 95% criteria for PORT within 60 seconds
5 of the 20 operators meet the 99.9% criteria for RSP180 ADS-C
7 of the 22 operators meet the 99.9% criteria for RCP240 ACTP
2 of the 22 operators meet the 99.9% criteria for RCP240 ACP

## Slide 80: Operator A Comparison of Performance Between Aircraft Type and FIR Aggregate July to September 2011

## Slide 86: Summary of Comparison of Performance By FIR For Operator A
For RCP240 ACTP:
  All FIR/Aircraft Type combinations meet 95% criteria in the July to September 2011 sample
  ZAN/B744 also meets 99.9% criteria
For RCP240 ACP:
  All FIR/Aircraft Type combinations meet 95% criteria in July to September 2011 sample
  ZAK/B772, ZAN/B772, and ZANB744 meet 99.9% criteria in July to September 2011 sample
For RSP180 ADS-C:
  All FIR/Aircraft Type combinations except ZNY/B772 meet 95% criteria in July to September 2011 sample