## Slide 1: GOLD Performance Monitoring
IPACG-36 FIT-23 IP/05 Attachment A
15 May 2012

## Slide 2: Overview
Summary of Reported Service Outages/Degradations
  October 2011 to Present
GOLD Analysis Overview
Aggregate Data Link Performance for Oakland and Anchorage
  Performance for All Media Types Combined
  Performance by Media Type
ADS-C Performance by Station Identifier for Oakland and Anchorage
Data Link Performance by Operator for Oakland and Anchorage

## Slide 3: Summary of Reported Outages/Degradations October 2011 to Present

## Slide 4
Start Date | Start Time (UTC) | Duration (hh:mm:ss) | Service Impacted | Satellite Region Impacted | Notification Source | Notes
18-Oct-11 | 18:10 | 02:35:00 | ARINC Iridium | Global | ARINC | ARINC Iridium Service operating in an impaired state
22-Oct-11 | 8:58 | 13:52:00 | All POR | POR | ARINC, Sita | Inmarsat POR outage
1-Nov-11 | 2:00 | 00:39:00 | Iridium | Global | ARINC, Sita | 
1-Nov-11 | 1:18 | 00:17:00 | Iridium | Global | ARINC, Sita | 
2-Nov-11 | 2:01:00 | 02:35:00 | Iridium | Global | ARINC, Sita | Voicemail, SMS and all Paging services are now available. No reason given for outage.
17-Jan-12 | 21:45 | 00:30:00 | Iridium | Global | ARINC, Sita | Unexpected Service Interruption - SATELLITE AIRCOM-Iridium Datalink ACARS Service (Post-Incident Report) Short Burst Data Service may have been affected during the above timeframe. Voice service was not affected. Location: GLOBAL
18-Mar-12 | 12:15 | 00:40:00 | Iridium | Global | ARINC, Sita | Iridium was experiencing delays with SBD DMT message delivery
2-Apr-12 | 5:45 | 00:58:00 | Sita (Satellite Data Services) | AOE, AOW | Sita | Unexpected service interruption at Aussaguel GES
30-Apr-12 | 6:00 | 10:00:00 | Iridium | Global | ARINC, Sita | Due to an internal network anomaly at the Tempe Gateway, SBD customers will have intermittent use of all SBD services during this period. SBD messages are queing for delivery. Message delivery is delayed 30+ minutes.
1-May-12 | 10:15 | 04:52:00 | Iridium | Global | ARINC, Sita | SBD DMO customers may experience delays in message delivery of up to 30 minutes. The back log of messages are being processed at this time. Engineering is working the issue.

## Slide 5: GOLD Analysis Overview: CPDLC Message Set
According to the guidance in the Global Operational Data Link Document (GOLD) only a specific message set in considered
  All uplink communications transfer messages and typical intervention messages such as climb clearances with an observed CPDLC “WILCO” response attribute are assessed
  These messages are considered to be intervention messages critical to the communications used when applying reduced separation standards
  Uplink message elements related to route clearances are not included (UM79, UM80, UM83)
Notes: <number>
FAA is developing and deploying decision support tools to aid the air traffic controller. DSTs have many functions such as probing for aircraft-aircraft and/or aircraft-airspace conflicts, safely and efficiently metering aircraft into airports, and providing advisors to air traffic management specialists that specific regions of airspace will reach capacity levels.
Fundamental to all these DSTS is the trajectory modeler function which generates aircraft trajectory predictions. An aircraft trajectory is the actual or prediction of the four-dimensional path of the aircraft. Each DST has required levels of accuracy for its trajectory predictions based on its unique functions and capabilities.

## Slide 6: GOLD Analysis Overview: CPDLC Performance Measures
Actual Communication Performance (ACP)
  Total time required by the communication transaction
  Begins when the CPDLC uplink message is sent to aircraft
  Ends when the WILCO is received
Actual Communication Technical Performance (ACTP)
  Time required for the message delivery part of the communication transaction, includes:
    CPDLC clearance uplink transit time
    WILCO downlink transit time
Pilot Operational Response Time (PORT)
  Time required for crew response
  Estimated by ACP - ACTP

## Slide 7: GOLD Analysis Overview: CPDLC Performance Measures

## Slide 8: GOLD Analysis Overview: ADS-C Messages and Performance Measure
Surveillance Latency
  All downlink ADS-C messages are included
    Duplicate messages are filtered out
  Measures transit time for downlink message delivery
  Begin time estimated by timestamp of aircraft when sent (position time)
  End time estimated by timestamp of ATC receipt

## Slide 9: Note: Y-axis Scale on Performance Charts
Please note the y-axis scale in various performance charts
  Most charts show the 90 to 100% portion of the cumulative distribution of the respective performance measure
  Due to some cases where performance is below that shown on the 90 to 100% portion, the y-axis will be shifted down below 90%
Please note that some charts are presented twice on two different scales
  One showing the full 0 to 100% of the cumulative distribution of the respective performance measure
  One showing the 90 to 100% portion of the cumulative distribution of the respective performance measure
Please note the difference in the y-axis scale for charts showing the relative distribution vs. the cumulative distribution

## Slide 10: GOLD Analysis Overview: Interpreting GOLD Charts
In this example:
  the observed performance meets the 95% criteria but does not meet the 99.9% criteria,
  the latency of 95% of downlink ADS-C messages in data set is within 37 seconds
  the latency of 99.9% of downlink ADS-C messages in data set is not shown because it is greater than the 240 seconds included on the chart

## Slide 11: GOLD Performance Criteria
Performance Measure | Percent of Messages Required to Meet Criteria | RSP180 Criteria (sec) | RSP400 Criteria (sec) | RCP240 Criteria (sec) | RCP400 Criteria (sec)
ADS-C Latency | 95% | 90 | 300 | -- | --
 | 99.9% | 180 | 400 | -- | --
ACTP | 95% | -- | -- | 120 | 260
 | 99.9% | -- | -- | 150 | 310
ACP | 95% | -- | -- | 180 | 320
 | 99.9% | -- | -- | 210 | 370
PORT | 95% | -- | -- | 60 | 60

## Slide 12: Aggregate Data Link Performance
Analysis period: October 2011 to March 2012
Aggregate performance - all media types combined
  RCP240 and RSP180 criteria
Performance by media type
  RCP240 and RSP180 criteria for SAT, VHF
  RCP400 and RSP400 criteria for HF

## Slide 20: Performance by Media Type - Oakland
Media Type | ADS-C |  |  | CPDLC |  |  |  |  | 
 | Count of ADS-C Downlink Messages | ADS-C 95% | ADS-C 99.9% | Count of CPDLC Transactions | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
SAT | 1,217,786 (87.3%) | 98.8% | 99.5% | 96,460 (97.2%) | 99.6% | 99.7% | 99.3% | 99.5% | 97.4%
VHF | 165,254 (11.8%) | 99.4% | 99.7% | 1,454 (1.5%) | 99.9% | 100% | 99.7% | 99.8% | 95.9%
HF* | 11,892 (0.9%) | 89.9% | 92.7% | 547 (0.6%) | 92.7% | 94.9% | 91.8% | 93.4% | 75.5%
Total | 1,394,932 | 98.6% | 99.4% | 99,223 | 99.4% | 99.5% | 99.1% | 99.4% | 97.2%
* HF performance is assessed against RSP400/RCP400 criteria. |  |  |  |  |  |  |  |  | 

## Slide 21: Performance by Media Type - Anchorage
Media Type | ADS-C |  |  | CPDLC |  |  |  |  | 
 | Count of ADS-C Downlink Messages | ADS-C 95% | ADS-C 99.9% | Count of CPDLC Transactions | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
SAT | 309,805 (68.8%) | 97.7% | 99.4% | 13,084 (77.9%) | 99.5% | 99.7% | 99.3% | 99.5% | 96.4%
VHF | 138,473 (30.8%) | 99.7% | 99.8% | 3,457 (20.6%) | 99.9% | 99.9% | 99.5% | 99.7% | 97.6%
HF* | 1,836 (0.4%) | 87.8% | 91.6% | 6 (0.04%) | -- | -- | -- | -- | --
Total | 450,114 | 98.2% | 99.4% | 16,799 | 99.5% | 99.7% | 99.2% | 99.4% | 96.5%
* HF performance is assessed against RSP400/RCP400 criteria. |  |  |  |  |  |  |  |  | 

## Slide 22: Summary of Data Link Performance in Oakland and Anchorage October 2011 to March 2012
The 95% criteria for RCP240 ACP, ACTP and RSP180 ADS-C is met in Oakland and Anchorage during the analysis period
The 99.9% criteria for RCP240 ACTP is met for VHF transactions in Oakland and Anchorage during the analysis period

## Slide 23: ADS-C Performance by Station Identifier
Analysis period: October 2011 to March 2012
RSP180 criteria
Station identifiers designate “path” taken by data link messages between aircraft and ATC
“Paths” vary between the four constellations of satellites as well as between the two data link service providers

## Slide 24: Station/Gateway Identifiers
Satellite | GES Location(s) | SITA | ARINC
Inmarsat I‑3 | Aussaguel, France: | AOW2 AOE2 | --
 | Eik, Norway: | AOW3 AOE3 IOR5 | XXE
 | Perth, Australia: | POR1 IOR2 | --
 | Santa Paula, California, US: | POR4 | XXC
Inmarsat I‑4 | Fucino, Italy | EUA1 | XXF
 | Paumalu, HI, US | APK1 AME1 | XXH
MTSAT | Kobe and Hitachiota, Japan | MTS1 | --
Iridium | Phoenix, Arizona, US | IGW1 | IG1

## Slide 29: Summary of Observed ADS-C Performance by Station Identifier
RSP180 95% criteria is met in Oakland for all “paths” except:
  Iridium satellites with data link service provided by SITA (IGW1)
  POR Inmarsat-3 series of satellites via the ground station located in Eik, Norway with data link service provided by SITA (XXE)
  IOR Inmarsat-3 series of satellites via the ground station located in Perth, Australia with data link service provided by SITA (IOR2)
RSP180 95% criteria is met in Anchorage for all “paths” except:
  Iridium satellites with data link service provided by SITA (IGW1)
  POR Inmarsat-3 series of satellites via the ground station located in Eik, Norway with data link service provided by SITA (XXE)
  Inmarsat-4 series of satellites via the ground station located in Paumalu, Hawaii with data link service provided by SITA (APK1)
Performance for the two main Pacific “paths” - designated by XXC and POR1 - is better in Oakland than in Anchorage

## Slide 30: Performance By Operator
Analysis period: October 2011 to March 2012
Analysis separate by FIR: Oakland, Anchorage
All media types combined
RCP240 and RSP180 criteria
Operators contributing top 90% of ADS-C downlink messages
Operators ordered in summary tables by descending count of ADS-C downlink messages
Operators not meeting 95% criteria highlighted in red
Operators meeting 99.9% criteria highlighted in green

## Slide 31: Observed Performance by Operator Oakland FIR – October 2011 to March 2012
Oper Code | ADS-C |  |  |  | CPDLC |  |  |  |  |  | 
 | Count of ADS-C | % of Total ADS-C | ADS-C 95% | ADS-C 99.9% | Count of CPDLC | % of Total CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
A | 221,847 | 15.9% | 98.2% | 99.4% | 12,955 | 13.1% | 99.1% | 99.3% | 98.7% | 99.1% | 95.3%
D | 119,666 | 8.6% | 98.7% | 99.6% | 5,671 | 5.7% | 99.6% | 99.7% | 99.5% | 99.7% | 97.8%
B | 105,894 | 7.6% | 99.1% | 99.5% | 7,022 | 7.1% | 99.6% | 99.7% | 99.4% | 99.6% | 98.2%
L | 99,222 | 7.1% | 98.7% | 99.6% | 7,909 | 8.0% | 99.4% | 99.5% | 98.6% | 99.1% | 95.4%
Q | 84,163 | 6.0% | 98.7% | 99.6% | 5,884 | 5.9% | 99.3% | 99.6% | 99.5% | 99.7% | 98.1%
G | 80,210 | 5.8% | 99.7% | 99.8% | 10,675 | 10.8% | 99.9% | 99.9% | 99.7% | 99.8% | 99.2%
NNN* | 41,969 | 4.5% | 96.8% | 98.8% | 2,953 | 4.4% | 98.7% | 99.0% | 97.1% | 97.6% | 91.3%
E | 60,653 | 4.3% | 99.2% | 99.6% | 4,018 | 4.0% | 99.8% | 99.9% | 99.6% | 99.7% | 98.5%
J | 46,305 | 3.3% | 99.7% | 99.9% | 5,007 | 5.0% | 99.9% | 99.9% | 99.7% | 99.8% | 98.9%
O | 45,239 | 3.2% | 99.2% | 99.8% | 2,777 | 2.8% | 99.8% | 99.8% | 99.8% | 99.9% | 98.5%
F | 41,977 | 3.0% | 99.5% | 99.8% | 4,824 | 4.9% | 99.9% | 99.9% | 99.7% | 99.8% | 99.1%
* Message counts and performance statistics for Operator NNN are for the period from December 2011 to March 2012. |  |  |  |  |  |  |  |  |  |  | 

## Slide 32: Observed Performance by Operator (Continued) Oakland FIR – October 2011 to March 2012
Oper Code | ADS-C |  |  |  | CPDLC |  |  |  |  |  | 
 | Count of ADS-C | % of Total ADS-C | ADS-C 95% | ADS-C 99.9% | Count of CPDLC | % of Total CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
N | 38,986 | 2.8% | 99.4% | 99.6% | 1,980 | 2.0% | 99.3% | 99.4% | 99.3% | 99.8% | 98.6%
H | 36,732 | 2.6% | 99.6% | 99.8% | 4,126 | 4.2% | 99.8% | 99.9% | 99.9% | 100.0% | 99.2%
S | 35,470 | 2.5% | 98.6% | 99.4% | 1,985 | 2.0% | 99.7% | 99.9% | 99.6% | 99.8% | 98.1%
T | 32,516 | 2.3% | 99.3% | 99.7% | 2,564 | 2.6% | 99.6% | 99.7% | 99.3% | 99.4% | 98.5%
K | 30,918 | 2.2% | 98.4% | 99.1% | 2,649 | 2.7% | 98.9% | 99.1% | 99.2% | 99.6% | 98.0%
Y | 30,727 | 2.2% | 97.3% | 98.5% | 845 | 0.9% | 98.9% | 99.4% | 98.6% | 98.8% | 96.5%
R | 30,208 | 2.2% | 98.6% | 99.5% | 2,325 | 2.3% | 99.6% | 99.7% | 99.6% | 99.8% | 97.9%
ZZZZ | 20,770 | 1.5% | 99.0% | 99.4% | 957 | 1.0% | 99.7% | 99.7% | 97.4% | 98.1% | 88.2%
P | 19,044 | 1.4% | 98.8% | 99.5% | 1,669 | 1.7% | 99.3% | 99.3% | 99.2% | 99.6% | 97.6%
M | 17,197 | 1.2% | 97.8% | 99.0% | 867 | 0.9% | 99.3% | 99.7% | 99.1% | 99.7% | 97.9%

## Slide 33: Summary of Observed Performance by Operator Oakland FIR – October 2011 to March 2012
There are 21 commercial operators contributing 90% of the ADS-C downlink messages
All 21 operators meet the 95% criteria for RSP180 ADS-C and RCP240 ACTP and ACP
19 of the 21 operators meet the 95% criteria for PORT within 60 seconds
1 of the operators meets the 99.9% criteria for RSP180 ADS-C
6 of the operators meet the 99.9% criteria for RCP240 ACTP
2 of the operators meet the 99.9% criteria for RCP240 ACP

## Slide 34: Observed Performance by Operator Anchorage FIR – October 2011 to March 2012
Oper Code | ADS-C |  |  |  | CPDLC |  |  |  |  |  | 
 | Count of ADS-C | % of Total ADS-C | ADS-C 95% | ADS-C 99.9% | Count of CPDLC | % of Total CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
D | 50,497 | 11.2% | 98.1% | 99.6% | 1,168 | 7.0% | 99.5% | 99.7% | 99.2% | 99.7% | 96.8%
A | 49,181 | 10.9% | 97.4% | 99.4% | 1,614 | 9.6% | 99.5% | 99.6% | 99.2% | 99.4% | 94.6%
Q | 45,260 | 10.1% | 98.1% | 99.5% | 1,597 | 9.5% | 99.1% | 99.5% | 99.3% | 99.5% | 95.4%
L | 35,781 | 7.9% | 98.7% | 99.6% | 1,358 | 8.1% | 99.6% | 99.6% | 98.8% | 99.0% | 94.1%
S | 35,360 | 7.9% | 97.9% | 99.6% | 1,112 | 6.6% | 99.5% | 99.6% | 98.6% | 99.1% | 96.9%
F | 29,751 | 6.6% | 99.2% | 99.9% | 1,562 | 9.3% | 99.1% | 99.5% | 99.3% | 99.7% | 98.2%
Y | 29,271 | 6.5% | 95.0% | 97.1% | 422 | 2.5% | 99.1% | 99.1% | 98.3% | 98.8% | 94.1%
H | 29,059 | 6.5% | 98.9% | 99.5% | 1,431 | 8.5% | 99.7% | 99.8% | 99.4% | 99.5% | 97.3%
G | 18,209 | 4.0% | 99.7% | 99.9% | 1,232 | 7.3% | 99.9% | 99.9% | 99.8% | 99.9% | 98.8%

## Slide 35: Observed Performance by Operator (Continued) Anchorage FIR – October 2011 to March 2012
Oper Code | ADS-C |  |  |  | CPDLC |  |  |  |  |  | 
 | Count of ADS-C | % of Total ADS-C | ADS-C 95% | ADS-C 99.9% | Count of CPDLC | % of Total CPDLC | ACTP 95% | ACTP 99.9% | ACP 95% | ACP 99.9% | PORT 95%
J | 17,207 | 3.8% | 99.8% | 99.9% | 1,043 | 6.2% | 99.9% | 99.9% | 99.8% | 99.8% | 99.3%
R | 15,975 | 3.5% | 96.3% | 99.7% | 531 | 3.2% | 99.6% | 99.8% | 99.3% | 99.6% | 96.6%
QQQ | 10,737 | 2.4% | 99.2% | 99.5% | 485 | 2.9% | 99.4% | 99.8% | 99.0% | 99.2% | 98.4%
P | 8,771 | 1.9% | 98.5% | 99.5% | 370 | 2.2% | 99.5% | 99.7% | 99.2% | 99.2% | 96.5%
T | 8,734 | 1.9% | 99.2% | 99.7% | 364 | 2.2% | 99.5% | 99.5% | 99.7% | 99.7% | 97.8%
O | 7,999 | 1.8% | 99.4% | 99.9% | 304 | 1.8% | 100.0% | 100.0% | 100.0% | 100.0% | 98.7%
KKK | 6,151 | 1.4% | 99.0% | 99.7% | 152 | 0.9% | 100.0% | 100.0% | 100.0% | 100.0% | 98.7%
B | 6,079 | 1.4% | 99.3% | 99.7% | 284 | 1.7% | 100.0% | 100.0% | 100.0% | 100.0% | 97.2%

## Slide 36: Summary of Observed Performance by Operator Anchorage FIR – October 2011 to March 2012
There are 17 commercial operators contributing 90% of the ADS-C downlink messages
All of the 17 operators meet the 95% criteria for RSP180 ADS-C and for RCP240 ACTP and ACP
14 of the 17 operators meet the 95% criteria for PORT within 60 seconds
4 of the operators meet the 99.9% criteria for RSP180 ADS-C
5 of the operators meet the 99.9% criteria for RCP240 ACTP
4 of the operators meet the 99.9% criteria for RCP240 ACP