## Slide 1: FAA Implementation of Amendment 1
September 2012
Status
IPACG/37<Audience>
Federal Aviation Administration
29 October – 02 November 2012

## Slide 2: Outline
Background
  Amendment
  Summary of Changes
Implementation
  Automation Systems Development
  Testing
  Training
  Procedures and Documentation
Transition

## Slide 3: Background
2003 – ICAO formed Flight Plan Study Group to develop changes to PANS-ATM, Doc 4444, which would address:
  Future needs of aircraft with advanced capabilities
  Requirements of automated ATM systems
2008 – ICAO issued State Letter 50/2008
  Amend. 1 to Doc 4444 effective November 15, 2012
  Changes to Filed Flight Plans & related messages
2009 – ICAO issued Transition Guidelines
  Intended to harmonize global implementation

## Slide 4: Summary of Signicant Changes
Field 10 (Equipment and Capabilities)
  Adds new codes for new capabilities
  New codes are in letter-digit format
  Deletes a small number of obsolete codes
Field 18 (Other Information)
  Adds several new items
  Creates strict format rules for a few existing items
Date of Flight
  Allows up to 5-day advance filing. FAA will not.
  Adds DOF/ to CHG, DLA, CNL messages

## Slide 5: Summary of Significant Changes
To comply with the ICAO standards for the flight plan, the FAA is changing LIFEGUARD to MEDEVAC
  MEDEVAC filed in STS/ (or remarks of NAS flight plan)
  MEDEVAC used in phraseology
ICAO Flight Plan also introduces HOSP as a special handling category
  FAA will not provide automatic priority to such flights

## Slide 6: Item 10a Changes
  A : GBAS Landing Sys M1- M3 : ATC RTF (SATCOM, MTSAT, Iridium)
  B : LPV (APV w/SBAS) O : VOR
  C : LORAN C P1 - P9 : Reserved for RCP
  D : DME R : PBN Approved
  E1 – E3 : ACARS S : Standard equipment
  F : ADF T : TACAN
  G : GNSS U : UHF radio
  H : HF Radio V : VHF radio
  I : INS W : RVSM
  J1 – J7 : CPDLC X : MNPS
  K : MLS Y : VHF w/ 8.33 kHz spacing capability
  L : ILS Z : Other Equipment carried or other
  capabilities
Redefined qualifier
New qualifier

## Slide 7: 10a Items for Oceanic Operations
CPDLC (ATN)
  J1 VDL Mode 2
CPDLC (FANS 1/A)
  J2 HFDL
  J3 VDL Mode A
  J4 VDL Mode 2
  J5 Satcom Inmarsat
  J6 Satcom MTSAT
  J7 Satcom Iridium
R is PBN Approved
Satcom RTF
  M1 Inmarsat
  M2 MTSAT
  M3 Iridium
Req. Comm. Perf.
  P1-P9
  Future
Y is no longer Canadian MNPS
  Now 8.33 kHz VHF capability

## Slide 8: Item 10b Changes
  N : No capability
  A : Mode A B1 : ADS-B 1090 Out
  C : Mode A and C B2 : ADS-B 1090 In/Out
  X : Mode S, no a/c id, no alt U1 : UAT Out
  I : Mode S, a/c id, no alt U2 : UAT In/Out
  S : Mode S, no a/c id, alt V1 : VDL In
  P : Mode S, a/c id, alt V2 : VDL In/Out
  E : Mode S, a/c id, alt, squitter
  H : Mode S, a/c id, alt, enh surv D1 : ADS-C FANS/1
  L : Mode S, a/c id, alt, sqtr, enh G1 : ADS- C ATN
Redefined qualifier
New qualifier

## Slide 9: 10b Items for Oceanic Operations
ADS-C
  D1 FANS 1/A
  G1 ATN

## Slide 10: Item 18 Changes
Added PBN/ for Performance Based Navigation
Modified STS/ to allow only one of 13 identifiers
Added SUR/ for Surveillance capabilities
  we will use it to indicate ADS-B is RTCA 260B compliant
Added
  DOF/ (date of flight),
  DLE/ (delay at a fix),
  ORGN/ (flight plan originator),
  TALT/ (take off alternate, e.g. Hudson River)
Made some minor modifications to content, e.g. PER/, DEP/, DEST/.

## Slide 11: Item 18 for Oceanic Operations
PBN/
  A1 is RNP10
  L1 is RNP4
  If “R” is filed in 10a, must have PBN/
STS/
  Must be one of items in the list
PER/
  Must be a single-letter category
See the brochure for full details on all these items

## Slide 12: FAA Implementation
Ocean21
Oakland Oceanic ARTCC
OFDPS
Honolulu Control Facility
ERAM Host / URET
20 domestic ARTCCS
Ocean21
New York Oceanic ARTCC
Ocean21 / FDP-2000
Anchorage ARTCC

## Slide 13: FAA Automation Impacts
Automation systems have been updated
  ERAM (en route ATC, flight data processing)
  Host (en route ATC, flight data processing)
  ATOP (oceanic ATC, flight data processing)
  FDP-2000 (en route ATC, flight data processing in Alaska)
  OFDPS (en route ATC, flight data processing in Hawaii)
  URET (controller flight data decision support tool)
  HADDS (flight data distribution and data base)
  FS-21 (Flight Services, contracted)
  OASIS (Flight Services in Alaska)
  AISR (Aeronautical Information System, AFTN terminal)
  DUATS (Flight Services, contracted, 2 vendors)

## Slide 14: Testing
All systems have been through
  System testing
  Interface tests between FAA systems
  Interface tests between FAA systems and most other ANSPs
    All interfaces except Australia tested at least once
Interface tests with flight plan filers are underway
  Tests occurring 2 days per month
  Started in May
  Will continue until November
Testing continues as needed

## Slide 15: Training
Many personnel are affected
  Air Traffic Controllers- terminal, en route, oceanic
  Flight Data Communications/Flight Data Repair
  Flight Services (serves General Aviation)
Training package includes
  General overview for all controllers and specialists
  Domain- and System-specific modules
Training was distributed and assigned, (eLMS) should be completed by all facilities

## Slide 16: Documentation- Procedures
Affected ATC Procedures have been identified and relevant document changes generated
  Primarily due to change from Lifeguard to MEDEVAC
Aeronautical Information Manual and Aeronautical Information Publication are being updated to reflect new flight plan instructions
  Change is available on FAA FPL 2012 web site
  Change will be published in NOTAM September 20th
  Change will be in AIM and AIP published next year

## Slide 17: Documentation- NOTAMs
Class II NOTAM announces FAA Requirements for new format on November 15th and expected transition in September
  Published August 23rd
FDC NOTAM published announced start of transition mode on Sept 15

## Slide 18: Transition
We entered Transition Mode on Sept 15
We are receiving a small number of NEW format flight plans at this point
  Typically 10-15 per day across en route facilities
  We have seen a very small number per day at Oceanic sites (1-5)
We are seeing a number of filing errors
  Working with filers to improve their success
  Need to stay on top of this- must do better as more filers switch over