## Slide 1
U.S. ADS-B Update
Presented to: Informal Pacific ATC Coordinating Group/38
By: Federal Aviation Administration
Date: April 24-25, 2013
IP Reference: IP/10

## Slide 2
Notes: We are introducing environmentally friendly technologies to enhance safety and improve efficiencies. These changes directly benefit pilots, controllers, airports, airlines and the public.
En Route IOCs have been completed at:
FY10 sites complete: Anchorage, Houston
FY12 sites complete: Denver, Minneapolis, Seattle, Albuquerque
FY13 site complete: New York, Chicago
Terminal IOCs have been completed at:
CARTS: Louisville, New York TRACON, Southern Cal TRACON, Northern Cal TRACON, Minneapolis,
STARS: Philadelphia, Houston (I90), New Orleans, El Paso, San Antonio, Anchorage, Albuquerque, Kansas City, Shreveport, Seattle, Buffalo, Daytona Beach, Corpus Christi, Miami
FY13 sites complete:
CARTS: none yet
STARS: Orlando, Cleveland, Jacksonville, Charlotte, Pensacola, Tucson, Norfolk, Raleigh-Durham, Pittsburgh, Phoenix, Santa Barbara, Detroit, Columbus
Surface IOCs have been completed at:
FY10: Philadelphia, Louisville
FY12: Orlando, Seattle, Boston, San Diego, Ft. Lauderdale, Newark, LaGuardia, Phoenix, Dallas Ft. Worth, Miami, John Wayne Airport, Washington Reagan, Houston Hobby, Charlotte
FY13: Denver
Rule-Driven ADS-B Out Avionics Equipage (B MOPS): Previous count: 584 (Feb 28th, 2013) New count: 767 (Mar 31st, 2013) 358 UAT (46.7%) 409 1090ES (53.3%) Active UPS, JetBlue, US Airways B MOPS 43 – UPS 35 - JetBlue 11 – US Airways ADS-B In Avionics Equipage (A & B MOPS): Previous count: 1140 (Feb 28th, 2013) New count: 1281 (Apr 1st, 2013) Vehicles 37 UAT B MOPS vehicles detected in BOS (three more than last month)
Equipage counts do not include:
1. Military Aircraft
2. Reserved ICAOs
3. Anonymous operations
4. ICAOs reserved for test (FAAFF1 – FAAFFF block and FAAFC1)
5. Vehicles
Definitions:
TIS-B service provides traffic information to equipped aircraft and surface vehicles based on the conventional radar returns received for non-equipped aircraft. ADS-R provides traffic information to equipped aircraft based on ADS-B transmission from aircraft on independent datalinks. FIS-B provides weather and NAS Status information to equipped aircraft.

## Slide 3: Implementation Status, 04-Apr-2013
http://www.faa.gov/nextgen/flashmap/
Notes: Radio Stations Constructed:
550 (total); 517 (conus); 33 (alaska)
Radio Stations Reporting on the SBS Network:
549 (total); 516 (conus); 33 (alaska)
Radio Stations Under Construction or in Final Design:
76 (total); 72 (conus); 4 (alaska)

## Slide 4
Notes: Op Eval (Operational Evaluation) – An evaluation involving a certified-for-intended-function system built per MOPS, for which use of the system has been granted Operational Approval by FAA, and where the approved system is used in daily NAS operations for a period of 6-12 months
Flight Trial – Operational use of a certified system or systems to gather data that is used to inform the development of MOPS material; where the operator is an airline, this means use in revenue service that may require Operational Approval
Flight Test – Flight testing or Demonstration of an uncertified prototype/experimental system to gather data that is used to inform the development of MOPS material; where the operator is an airline, the aircraft cannot be used in revenue service while configured for the test
MOPS - Minimum Operational Performance Standards; this is an RTCA document on which FAA Technical Standard Orders (TSOs) are typically based
SPR - Safety, Performance and interoperability Requirements document; this is an RTCA document that serves as "homework" for definition of the MOPS
FIM-S/DI is an avionics capability that assists the flight crew in achieving or maintaining an interval or spacing from a target aircraft. ATC will use a new set of (voice or data link) instructions directing, for example, that the flight crew establish and maintain a given time interval behind a reference aircraft. These new instructions will reduce the use of ATC vectoring and speed control, which is expected to reduce the overall number of transmissions. The objective of this application is to create operational benefits through reduced variations in the arrival intervals between aircraft, thus maximizing airspace throughput while reducing ATC workload and enabling more efficient aircraft fuel burn (also reducing environmental impacts). FIM-S is aimed at intervals that are larger than current radar separation standards, while FIM-DI aims to use a "defined interval" risk-based approach to reduce intervals to values that are equivalent to current radar separations.
ITP is an avionics capability that enables flight level change maneuvers that are otherwise not possible within Oceanic procedural separation standards. ITP allows ATC to approve these flight level change requests between properly-equipped aircraft using reduced procedural separation minima during the maneuver. Flight crews request flight level changes for various reasons to improve flight efficiency and safety including; optimum fuel burn, accessing favoring wind conditions, avoidance of turbulence. The objective of this application is to enable more frequent approval of flight level requests between properly equipped aircraft using a reduced separation standard in Oceanic Airspace, improving flight efficiency and safety.
TSAA is an avionics capability that provides traffic advisories by using a traffic display and alerts to assist the pilot with visual acquisition and avoidance of traffic. The application is applicable under both Visual Flight Rules (VFR) and Instrument Flight Rules (IFR). The alert acts as an attention-getting mechanism so the pilot is not required to continually scan the traffic display to determine if and which aircraft are conflicting. After receiving the alert, the pilot will take action in accordance with the operational rules in effect at the time. This application does not provide resolution advisories.
Requirements Definition: Requirements are described in a Safety, Performance and interoperability Requirements (SPR) document as well as specifications for affected NAS subsystems. If this is the final maturity level for the application in the 2012 JRC, then key requirements will be evaluated through flight test of prototype avionics and/or prototype ground equipment (otherwise, the Operational Evaluation in the Requirements Validation level serves as the mechanism to "test" the requirements under real-world conditions).
Requirements Validation: Builds on Requirements Definition by adding:
  for applications requiring new or changed avionics:
    approval of an avionics standard (Minimum Operational Performance Standards, or MOPS);
    certification of a MOPS-compliant system, and
    an FAA policy memorandum basis for installation and operational guidance leading to operational approval for one operator
  for applications requiring a change in ATC automation, all necessary engineering development and ATO operational approval activities to provide the necessary ATC automation functionality in at least an operational prototype configuration
  for all applications, an Operational Evaluation performed by one or more operators to validate performance of the system implementation (avionics, ATM automation, or both) for the application and to quantify application benefits under realistic operating conditions
NAS Enabled: Builds on Requirements Validation by implementing required support for the application in all FAA Systems needed to allow daily use at one or more key sites in the NAS. Such "daily use" involves certified, TSO-authorized avionics and granted Operational Approval by AVS per pertinent 20-series and 90-series ACs, and that the required ATC automation has been declared operationally suitable. For some applications, the Requirements Validation and NAS Enabled maturity levels may need to be simultaneously met.
NAS Implementation: Builds on NAS Enabled by implementing required support for the application in all appropriate FAA Systems to allow daily use at all applicable NAS locations. In most cases, this is the "rollout across the NAS" after satisfactory completion of the NAS Enabled level. An evaluation involving a certified-for-intended-function system built per MOPS, for which use of the system has been granted Operational Approval by FAA, and where the approved system is used in daily NAS operations for a period of 6-12 months
Flight Trial: SBS is partnering with US Airways and ACSS to conduct a flight trial of the ACSS “Merging & Spacing” avionics on US Airways A330s during upper airspace arrival operations at PHL. The “Merging & Spacing” avionics are a precursor to the planned FIM avionics, whose standards are now being developed by RTCA/EUROCAE with FAA SBS support. The Merging & Spacing Flight Trial will be conducted with the US Airways A330s that fly daily from various European airports to PHL. These aircraft generally arrive within a relatively short multi-hour window of time, allowing opportunities for them to pair up and conduct Interval Management operations in en route airspace as they approach PHL.
Although a final decision has not been made by RTCA SC-186 and EUROCAE WG-51, currently it appears that the TSAA MOPS material will be incorporated into DO-317B (along with AIRB, SURF, VSA and ITP), while a separate MOPS document will be created for FIM-S/DI (likely this will be simply called the “FIM MOPS”); per standard RTCA practice, this FIM MOPS document will not be numbered until approved by the RTCA Program Management Committee.
Note that the ITP Op Eval was originally planned to last one year but has been extended into 2013 due to several factors. First, data collection has been hampered by the lack of trained pilots (see SBS Issue Tier-1 #31) and therefore needs to continue beyond 15-Aug-2012; currently we are uncertain by how many months we need to extend data collection. Second, from an AJE-32 and AOV perspective, we will remain in “operational trial” mode at ZOA until ATOP is modified to support ITP so controllers don’t have to execute the manual “checklist” to approve an ITP climb/descent.

## Slide 5
Vehicle ADS-B Summary
June 2011 – Development of MOA partnership with Massport
November 2011 – First article Vehicle ADS-B unit delivered to FAA for performance testing at WJHTC
May 2012 – Production unit FAA testing completed
September 2012 – AC updated with approved unit
September 2012 –$1.2M in AIP grants for Chicago, Denver, and San Francisco for Vehicle ADS-B units
December 2012 – Completed 37 total installations at Boston
April 2013 – Testing of mod to continue transmission with loss of GPS at Boston
Sites Pending – St. Louis and Milwaukee
Notes: 5
April 2013 – Testing of mod to continue transmission with loss of GPS
The requirement to shut off Vehicle ADS-B transmissions automatically upon loss of GPS was changed in October 2011. If the unit was in a transmission area upon loss of GPS, it will continue transmitting in support of multilateration until it reacquires GPS. Exelis has incorporated this change and is proposing a field test at the end of January in STL using a spare unit (STL has agreed to purchase but does not have units delivered yet). This would be witnessed by FAA and then deployed to fielded units.

## Slide 6: FAA Funded Avionics Upgrades (as of 18-Apr-2013)
ADS-B Out
Aircraft: 35 A320
STC approved July 2012
    All 35 modifications complete
ADS-B Out and In
Aircraft: 12 747
STC approved June 2011
12 ADS-B In equipped; Upgrades to DO-260B ADS-B Out TBD
ADS-B Out and In
Aircraft: 20 A330-300/200
STC for ADS-B Out approved August 2012; STC for Merging & Spacing approved January 2013
12 ADS-B Out installs complete
Upgrades complete by October 2013
ADS-B Out
Aircraft: 165
  13 747
  59 767
  53 A300
  38 MD11
  2 757
STC for 767, 747/767 AML, and A300/MD11 AML approved (Dec 2011, Jan 2012, and Jan 2013 respectively)
48 installs complete; Upgrades complete by June 2014 (757 upgrade date TBD)
ADS-B Out
Aircraft: 54 helicopters (9 Chevron and 45 PHI)
STC for Chevron approved June 2012; Approval expected summer 2013 for PHI
  Upgrades to complete by 2015
ADS-B Out
Aircraft: Up to 400 legacy Capstone aircraft
Request for Offer released September 2012 and contract award in spring 2013
Upgrades expected completion by December 2014
ADS-B Out
Aircraft: 110 737NG
Boeing Service Bulletin expected Apr 2014
Upgrades to DO-260B complete by December 2017

## Slide 7
FAA-Approved Version 2 ADS-B Out Avionics
as of 11-Apr-2013
Note: “N/A” indicates equipment has received TSOA, but has not received any other certification
Surveillance Manufacturer | Model # | Approved Position Source(s) | Aircraft | Approval Date | AML Approved
ITT Exelis / FreeFlight | FDL-978-TXG |  | VEHICLE | May 2012 | Massport
ACSS | XS-950 | RCI GLU-925 | B767, B747 | STC Jan 2012 | Yes
Honeywell | XS-852 | CMA-4024-1 SBAS | N/A | Jan 2012 | No
Trig-Avionics | TT-31 | FreeFlight WAAS 1201, Accord Technology NexNav™ Mini GPS unit | Mooney M20B-M20G, M20J & M20K | STC May 2012* | Yes
FreeFlight | FDL-978-TX | FreeFlight WAAS 1201 | Agusta Westland 139 | STC Jun 2012 | No
ACSS | XS-950 | RCI GLU-920 (A320), Thales TLS8755-01-0101A/0102B (A330) | A320, A330 | STC Jul 2012* | No
Honeywell | ISP-80A.1 | Honeywell ADIRU Part#’s HG2030BE02, BE03 or BE04 | A380 | EASA TC Jul 2012 | Yes via Production
Trig-Avionics | TT-22 | FreeFlight WAAS 1201 | King Air C-90A, Aviat/Pitts (aerobatic) S-76C | STC Nov 2012* | No (King Air) Yes (Aviat/Pitts) No (S-76C)
* multiple STC dates; only earliest shown

## Slide 8
FAA-Approved Version 2 ADS-B Out Avionics
as of 11-Apr-2013
Note: “N/A” indicates equipment has received TSOA, but has not received any other certification
Surveillance Manufacturer | Model # | Approved Position Source(s) | Aircraft | Approval Date | AML Approved
Garmin | GDL-88 | Garmin GNS 430W/530W, GTN 650/750, or internal | King Air C-90 | STC Dec 2012 | Yes
FreeFlight | FDL-978-TX | FreeFlight WAAS 1201 | Cessna 172S | STC Dec 2012 | Yes
ACSS | XS-950 | RCI GLU-920 | A300/MD11 | STC Jan 2013 | Yes
Honeywell | MRC XPDR w/ADS-B Out | CMC CMA-3024 SBAS GNSSU MK II and CMA-4024 SBAS GNSSU | AW-139 | EASA TC Feb 2013 | Yes via Production
Rockwell | TDR-94D | Universal UNS-1Fw | N/A | April 2013 | No
* multiple STC dates; only earliest shown

## Slide 9
FAA-Sponsored Projects that will result in Version 2 ADS-B Out Avionics
Surveillance Manufacturer | Model # | Planned Position Source(s) | Aircraft | Planned STC Availability | Operator
Rockwell | TDR-94D | Universal UNS-1Fw | Sikorsky 76/92 | STC Q2 2013 | PHI
FreeFlight | FDL-978-XVR | FreeFlight WAAS 1201 | Bell 206 | STC Q4 2013 | University of North Dakota
Rockwell | TPR 901-205 | RCI GLU 925-001 RCI GLU 925-330 | 737-700/800/900 | Boeing Service Bulletin Q2 2014 | United
Honeywell | ?? | TBD | 747-400 | TBD | United
TBD | TBD | TBD | Various | TBD (goal is by 2014) | Various (approximately 400 aircraft in Alaska)
Notes: Acft broadcast ADS-B out to ground and “In” equipped acft

## Slide 10
FAA-Approved Version 2 ADS-B In Avionics
as of 11-Apr-2013
* Airbus ATSAW (with and without ITP) received EASA approval in May 2011 as TC amendment; all A330/340s produced since Jan 2011 and all A320s produced since mid-2011 are ATSAW/ITP-capable
Manufacturer | Model # | Aircraft | STC Date | AML Approved
Honeywell | TPA-100B | B747-400 | June 2011 | No
Honeywell | TPA-100B | A330/340 | Dec 2011* | Yes via Production
ACSS | TCAS3000SP | A330/340 | Dec 2011* | Yes via Production
Honeywell | TPA-100B | A318/319/320/321 | Feb 2012* | Yes via Production
ACSS | TCAS3000SP | A318/319/320/321 | Feb 2012* | Yes via Production
ACSS | TCAS3000SP | B767-300 | May 2012 | No
Garmin | GDL-88 | King Air C-90 | Dec 2012 | Yes
ACSS | TCAS3000SP | A330 | Jan 2013 | No

## Slide 11
FAA-Sponsored Projects that will result in Version 2 ADS-B In Avionics
Manufacturer | Model # | Aircraft | Planned STC Availability | Operator
FreeFlight | FDL-978-XVR | Bell 206 | Q4 2013 | University of North Dakota
TBD | TBD | Various | TBD (goal is by 2014) | Various (approximately 400 aircraft in Alaska)
Notes: Acft broadcast ADS-B out to ground and “In” equipped acft

## Slide 12: Next Steps
  Complete ground infrastructure deployment
  Reassess FY13 ADS-B deployment schedule based on Sequestration
Continue Requirements Development & Validation for ADS-B-In Applications (i.e. In Trail Procedures, Traffic Situation Awareness with Alerts, and Flight deck Interval Management)
Complete MOA plans for aircraft equipage
Prepare for additional ADS-B-In applications