## Slide 1: ICAO Communication Failure Coordinating Group (CFCG)
Update
IPACG/39
Keith Dutch, FAA
03 – 06 February 2014

## Slide 2: Reason for CFCG
The Cross Polar Working Group (CPWG) proposed a common communication failure procedure for FIRs around North Pole
  Each FIR has its own comm failure procedure
  Aircraft pass through FIRs for relatively short periods
  Proposed that aircraft maintain the last ATC-assigned speed, route, and altitude
Annex 2 procedures and several Regions/ANSPs tell aircraft to follow “flight plan”, which permits step-climbs from Item 15.
ICAO formed CFCG to resolve difference

## Slide 3: CFCG Activity
ICAO CFCG met 23-25 October 2012
The Meeting reviewed communication failure provisions contained
  Annex 2 — Rules of the Air
  Annex 10 — Aeronautical Telecommunications, Volume II — Communication Procedures including those with PANS status
  Current regionally-agreed provisions, amendment proposals submitted by the European Region, North American Region, and many national regulations, which differ from ICAO

## Slide 4: CFCG Activity (continued)
Discussions about “communication failure” and the scope of work for the CFCG
  Failure of ATC comms were considered outside the scope of the CFCG
  Would address single aircraft with partial and total comm (ATC-approved voice, data link, SATCOM, etc. and non-approved [cell phone]) loss
Discussed various scenarios (low-density vs. high-density, surveillance, remote, etc.)

## Slide 5: CFCG Activity (continued)
Phase of flight (departure, en route, descent)
Flight plan (Filed, Current, Repetitive, operational version for aircrew)
Subsequent meetings to be held by WebEx
Unable to progress activity due to differences
  Continue flight according to FPL (altitude changes)
  Continue flight last ATC assigned altitude

## Slide 6: CFCG Current Status
ISAVIA, NAV CANADA, and FAA propose that a flight should not automatically climb in accordance with the flight plan
  ICAO NAT Region clearance formulated to provide conflict-free flight
  Assigned flight level coordinated with downstream ATC
  Level in FPL may no longer be operationally suitable
  Flight crew and ATC may have different understandings of “current flight plan”

## Slide 7: CFCG Current Status (continued)
Others contend flight should automatically climb in accordance with the flight plan
  Last assigned level may not provide terrain and obstacle clearance for the entire route
  Flight plan represents an operationally suitable profile for the flight
  Flight plan is a single point of information about the flight’s intentions

## Slide 8: CFCG Next Meeting
10-14 February 2014
ICAO Montreal, Canada

## Slide 9: CFCG
Questions?