## Slide 1
WP05
10 minutes longitudinal separation minimum
without MNT between Oakland and Fukuoka FIR reporting
Japan Civil Aviation Bureau
Tatsuya IWASE

## Slide 2
1. Background
10 minutes longitudinal separation minimum without MNT , hereinafter referred to as 10 min minimum, within Fukuoka FIR has been implemented since July,2010 for aircraft flying on the ATS routes on conditions that aircraft shall make position reports every 40 minutes.

## Slide 3
1. Background
In July 2011, Doc7030 Regional Supplementary Procedures was amended to incorporate the provisions regarding 10 minutes minimum within Fukuoka FIR, however, those regulations were partly different from what Japan had proposed in October 2010 in the point that the following underlined wordings were inserted.

## Slide 4
1. Background
Doc 7030 6.2.2.3
The minimum longitudinal separation within the Oakland Oceanic and Fukuoka FIRs shall be 10 minutes, whether in level, climbing or descending flight, provided that the aircraft concerned have reported over the same common point and follow the same track or continuously diverging tracks until some other form of separation is provided.

## Slide 5
Current Doc7030
B
Over X at 00:10.
A
Over X at 00:20 .
10 min minimum can be applied only
between A and B.
Point X
C: Not flying over X.

## Slide 6
1. Background
In the IPACG/38 held in April 2012, JCAB and Electronic Navigation Research Institute(ENRI) made the report of the safety assessment about the 10 min minimum. In this report, 10 min minimum can be applied to the aircraft flying on ”the same track " over the whole oceanic control area within Fukuoka FIR, including PACOTS and UPRs on conditions that aircraft shall make position reports every 80 minutes.

## Slide 7
Doc 4444 5.4.2.1.5 a) Same track :
45°
315°
Less than 45°
More than 315°

## Slide 8
C:
Estimate Z at 00:40
Point Z
JCAB’s safety assessment shows‥
Less than 45 degrees
B
Over Z at 00:20.
A
Estimate Z at 00:30 .
10 min minimum can be applied not only between A and B but also B and C , A and C.

## Slide 9
2. JCAB’s proposal of amending Doc 7030
Doc 7030 6.2.2.3
The minimum longitudinal separation within the Oakland Oceanic and Fukuoka FIRs shall be 10 minutes, whether in level, climbing or descending flight, provided that the aircraft concerned
follow the same track or continuously diverging tracks until some other form of separation is provided.
have reported over the same common point and

## Slide 10
2. JCAB’s proposal of amending Doc 7030
TRACK 2
TRACK 3
DARP( to KLAX)
Less than 45 degrees
10 min
A
B

## Slide 11
2. JCAB’s proposal of amending Doc 7030
Action by the meeting
The meeting is invited to note the information provided.
JCAB would like the meeting to support our proposal to amend the Doc7030.

## Slide 12
Questions?