## Slide 1: ADS-C CDP Climb/Descend Procedure
Implementation Project Update
IPACG/39
Keith Dutch, FAA
03 – 06 February 2014

## Slide 2: ADS-C CDP
Climb/Descend an aircraft through the altitude of a blocking aircraft using reduced 15NM separation
CDP developed in response to operator requests to utilize the FANS equipment they invested in for NextGen for which they were receiving no benefit return

## Slide 3: ADS-C CDP Operational Trials
ADS-C CDP was demonstrated in operational trials by manually applying ADS-C CDP without changes to FAA ATOP automation system
  Operational trials began on 15 Feb 2011 in the Oakland Oceanic CTA and ended 15 Feb 2013
  During the two-year timeframe of the trials, the ADS-C CDP was successfully utilized eight times
There are no plans to extend the manual trial
Fast-time simulations are currently being conducted at the FAA William J. Hughes Technical Center (WJHTC)
  These model the use of ADS-C CDP in a more densely populated environment
  Increases opportunity for use and further validates the procedure

## Slide 4: ADS-C Operational Requirements
CPDLC maintained
Distance between aircraft determined from near simultaneous ADS-C demand reports which contain position accuracy of 0.25 NM or better (Figure of Merit 6 or higher)
Distance between aircraft is not less than
  15NM when same speed/faster aircraft in front
  25NM when faster aircraft in back (not more than M0.02)
Altitude difference between aircraft not more than 2000 ft
Clearance assures vertical separation within 15 minutes from first ADS-C report request

## Slide 5
Automated ADS-C CDP
FL360
FL340
FL350
Desired Altitude
Standard Separation
RNP-4, FANS-1/A ADS-C CPDLC
RNP-4, FANS-1/A ADS-C CDPLC
No capabilities required
CDP Separation Standard
Automation requirements
  ATOP conflict probe decision support tool determines when CDP can be applied for climbing/descending aircraft by determining eligibility
  ATOP will account for maneuvering aircraft, blocking aircraft, and all other traffic
  ATOP will be able to handle multiple maneuvers in one or multiple sectors
  Controller either issues the clearance for the climb/descend or UNABLE
Notes: 5

## Slide 6: Manual Controller Actions
From a systems efficiency perspective, ADS-C CDP system will allow for increased efficiency and improved flow for properly equipped aircraft.

## Slide 7: Automated Procedure

## Slide 8: Current Working Schedule
ADS-C CDP automation, when ready as an operational capability, will be installed and employed in Anchorage, Oakland and New York oceanic airspace.