## Slide 1
Presented To: IPACG/39
Presented By: Dennis Addison, FAA
Date: February 5-6, 2014
WP02: Timing Errors in Oakland OCA
Notes: <number>

## Slide 2: Oakland ETA Time Error Analysis
Oceanic Non-Radar Airspace
  Procedural Control
  Reliance on accurate ETAs to maintain longitudinal separation minimas.
  Inaccurate ETAs may lead to aircraft pairs flying too close together.
<number>
Notes: <number>

## Slide 3: ICAO Annex 2 3.6.2.2 change
3.6.2.2 Inadvertent changes. In the event that a controlled flight inadvertently deviates from its current flight plan, the following action shall be taken:
a) Deviation from track: if the aircraft is off track, action shall be taken forthwith to adjust the heading of the aircraft to regain track as soon as practicable.
b) Variation in true airspeed: if the average true airspeed at cruising level between reporting points varies or is expected to vary by plus or minus 5 per cent of the true airspeed, from that given in the flight plan, the appropriate air traffic services unit shall be so informed.
c) Change in time estimate: if the time estimate for the next applicable reporting point, flight information region boundary or destination aerodrome, whichever comes first, is found to be in error in excess of 2 minutes from that notified to air traffic services, or such other period of time as is prescribed by the appropriate ATS authority or on the basis of air navigation regional agreements, a revised estimated time shall be notified as soon as possible to the appropriate air traffic services unit.
3.6.2.2.1 Additionally, when an ADS agreement is in place, the air traffic services unit shall be informed automatically via data link whenever changes occur beyond the threshold values stipulated by the ADS event contract.
<number>
Notes: <number>

## Slide 4: Oceanic Navigation Error Reporting
FAA requires reporting of Oceanic Navigation Errors:
  GNE (Gross Navigation Error) 25nm or more.
  Intervention: Aircraft on different route than ATC.
  Height Error: 300 feet or more.
  Time Errors: Pacific = More than 3 minutes
ONER Reports are forwarded to:
  Flight Standards
  Technical Center, Airspace Safety Calculations.
Oakland has automated Time Error tracking and reporting.
<number>
Notes: <number>

## Slide 5: Oakland ETA Time Error Analysis
At IPACG38 Oakland reported on a new automated tool that captures HF ETA time errors.
In October Oakland began filing ONER Time Error Reports
The data revealed that an unexpectedly large number of ETA time errors are being made.
<number>
Notes: <number>

## Slide 6: ONER Time Errors Tracking
<number>
Notes: <number>

## Slide 7: ONER Time Errors Tracking
<number>
January 2014 ETA ONER Errors
Notes: <number>

## Slide 8: ONER Time Errors December 2013
<number>
Notes: <number>

## Slide 9: Action by the Meeting
The meeting is invited to note the information provided, and:
  Operators are requested to ensure that their flight crews are reminded of their obligation to update ETAs as outlined in ICAO Annex 2 and noted in this paper, and;
Note that failure to update ETAs as required could lead to Pilot Deviations being filed against the crew.
<number>
Notes: <number>

## Slide 10
Notes: <number>