## Slide 1: Analysis of ATC Communication messages Relevant to Altitude Change Requests
Electronic Navigation Research Institute
IPACG/39, 5-6 February 2014,
Fukuoka, Japan

## Slide 2
The most of flights over the Pacific Ocean are long range flight, so pilots request a change to economic altitude with light weight due to fuel consumption other than caused by weather conditions.
For the purpose of measure how much operators’ demand flight being approved, we analyzed ATC communication messages relevant to altitude change requests in oceanic control airspace within Fukuoka FIR.
Introduction

## Slide 3
ATC: CLIMB TO AND MAINTAIN FL350
PILOT: REQUEST CLIMB TO FL350
Pilot Request Altitude Change
We analyzed “Unable” reply ratio;
the ratio of number that the first reply is “Unable” to number of pilot’s request of altitude change, as an indicator of how operators’ demand flight being approved.
PILOT “Request [change altitude].”
ATC “Unable due to [reason].”

## Slide 4
Target period
2009 6/22~6/28, 8/17~8/23, 12/21~12/27
2010 2/15~2/21, 6/21~6/27, 8/16~8/22, 12/20~12/26
2011 2/21~2/27, 7/4~7/10, 9/5~9/11, 11/7~11/13
2012 1/9~1/15, 7/9~7/15
TOTAL 91 days
Analysis of ATC Communication Messages
CPDLC message were analyzed.
17,486 Altitude change request message
4,383 The first answer was “Unable”
Chart: 
| 上昇リクエスト | 降下リクエスト | ブロック高度リクエスト | その他
 | 16075 | 842 | 529 | 43
92% Climb
5% Descent
3% Block
Altitude change request
“Unable” reply ratio is 25%

## Slide 5
“Unable” reply ratio of each city-pair
 | No. Altitude Change Request | No. “unable” reply | “unable” reply ratio
From Japan |  |  | 
Japan → North America | 2248 | 514 | 23%
Japan → Alaska | 152 | 28 | 18%
Japan → Hawaii | 857 | 321 | 37%
Japan → South Pacific | 546 | 135 | 25%
Japan → South-east Asia | 780 | 318 | 41%
For Japan |  |  | 
North America → Japan | 2158 | 437 | 20%
Alaska → Japan | 281 | 43 | 15%
Hawaii → Japan | 955 | 176 | 18%
South Pacific → Japan | 346 | 67 | 19%
South-east Asia → Japan | 188 | 64 | 34%
Over Flight |  |  | 
South-east Asia → North America, Alaska, Hawaii | 3044 | 689 | 23%
East Asia → North America, Alaska, Hawaii, South Pacific | 2065 | 557 | 27%
North America, Alaska, Hawaii → South-east Asia | 2799 | 749 | 27%
North America, Alaska, Hawaii, South Pacific → East Asia | 941 | 255 | 27%

## Slide 6
Manila
A590
-----Radar coverage
ATS Data link airspace
High “unable” reply ratio
Reference: AIP Japan
“Unable” reply ratio
Japan to South-east Asia 41%
South-east Asia to Japan 34%
Airway A590
( extending to the southwest of Japan)
Available Both direction flight

## Slide 7
High “unable” reply ratio
Japan > Hawaii
SE Asia – N America
Other
Around 17Z a day of July 2012
TOKYO
27N165E
Around 15Z a day of May 2012
TOKYO
27N165E
“Unable” reply ratio
Japan to Hawaii 37%
Route configuration
Cross the route of
South east Asia – North America
flight route, especially in summer
Around 15Z a day of Jul 2013
165E

## Slide 8
Analysis of ATC Communication Messages
Chart: 
| 39965 | 40026 | 40148 | 40210 | 40330 | 40391 | 40513 | 40575 | 40725 | 40787 | 40848 | 40909 | 41091
Unable reply ratio | 0.21813 | 0.24747 | 0.22877 | 0.18829 | 0.25768 | 0.25604 | 0.24417 | 0.28472 | 0.2497 | 0.26984 | 0.2735 | 0.25792 | 0.26082
Moving Average | 0.23244 | 0.22485 | 0.22954 | 0.24014 | 0.25336 | 0.26068 | 0.25804 | 0.26607 | 0.26347 | 0.26829 | 0.26434
In 2008, economic crisis was occurred in the world. Traffic volume temporarily dropped. However, traffic volume recovered since around 2010.
Follow the recovery in traffic volume, rate is higher gradually.

## Slide 9
Correlation, Unable reply ratio and Traffic Volume
Traffic No.
Chart: No. Traffic
| 368 | 418 | 335 | 353 | 471 | 517 | 409 | 443 | 437 | 497 | 409 | 404 | 487
0-3 | 0.17 | 0.18462 | 0.11594 | 0.1 | 0.21875 | 0.15854 | 0.14607 | 0.12766 | 0.24 | 0.17647 | 0.23377 | 0.16923 | 0.20769
3-6 | 0.21708 | 0.27358 | 0.25 | 0.20755 | 0.3217 | 0.25153 | 0.25347 | 0.35821 | 0.2642 | 0.24324 | 0.33735 | 0.31429 | 0.34383
6-9 | 0.24 | 0.21788 | 0.11579 | 0.20968 | 0.20468 | 0.25414 | 0.18254 | 0.31746 | 0.21547 | 0.27333 | 0.28485 | 0.19608 | 0.22685
9-12 | 0.22 | 0.24051 | 0.29452 | 0.14504 | 0.30876 | 0.26549 | 0.29891 | 0.27879 | 0.26087 | 0.26636 | 0.26344 | 0.2093 | 0.21318
12-15 | 0.2 | 0.27461 | 0.28641 | 0.22099 | 0.27273 | 0.33193 | 0.29508 | 0.31188 | 0.20085 | 0.31579 | 0.28505 | 0.31288 | 0.21429
15-18 | 0.2619 | 0.31551 | 0.25 | 0.24603 | 0.20886 | 0.27083 | 0.25 | 0.28485 | 0.32414 | 0.35246 | 0.24242 | 0.30435 | 0.27386
18-21 | 0.2 | 0.25658 | 0.125 | 0.12987 | 0.19549 | 0.29885 | 0.25 | 0.18182 | 0.26846 | 0.26471 | 0.25 | 0.22857 | 0.30814
21-0 | 0.20513 | 0.10345 | 0.18367 | 0.097561 | 0.12658 | 0.13084 | 0.13636 | 0.16949 | 0.085366 | 0.16883 | 0.17742 | 0.066667 | 0.1519

## Slide 10
Position | DAY1 | DAY2
Same direction/same track | 27 | 37
Same direction/cross track | 5 | 5
Same direction /converging track | 3 | 4
Opposite direction/same track | 0 | 3
Opposite direction /cross track | 3 | 7
Opposite direction /converging track | 0 | 2
Unidentified* | 22 | 2
TOTAL | 60 | 59
Positions with Related Aircraft
Same track
Cross track
Converging track
*Unidentified
Unfound the related aircraft cause for “unable”. It is thought that securing altitude for the strategic reason or results from a coordination with neighboring ANSPs.
The related aircraft fly the same track in the same direction in most of case.
Flights on the same track with same altitude are affected longitudinal ATC separation.
Notes: There are 60 and 59 unable reply in each two days.
More commonly the case is the related aircraft fly the same track in the same direction.
The same track with same altitude, that is affected longitudinal ATC separation.

## Slide 11
Aircraft 1 RNP10, D/L
Aircraft 2 Neither RNP nor D/L
Required 10 minutes (80NM) separation
Aircraft 1 RNP4, D/L
Aircraft 2 RNP4, D/L
Required 30NM separation
40NM
Aircraft 1
FL330
Aircraft 2
FL340
40NM
Aircraft 1
FL330
Aircraft 2
FL340
Aircraft 1:
Request climb to FL350
ATC:
Unable, due to traffic
ATC:
Climb to and maintain FL350
Aircraft 1:
Request climb to FL350
Effect of PBN
If performance specification were improved, possibilities of taking an optimal altitude will increase.

## Slide 12
 | DAY1 | DAY2
Altitude change will be available if specification improve to RNP10 | 6 | 14
Altitude change will be available if specification improve to RNP4 | 3 | 5
Number of “Unable” reply | 60 | 59
Effect of PBN
If the performance requirements of aircraft that altitude request did not answered have been improved?
One-quarter (1/4) of request which response was “Unable”, had possibilities to be answered their request.
There is a capability to reduce “Unable reply ratio” if more aircraft improve their capabilities.
Chart: 
| Altitude change will be OK | o
 | 28 | 91
Response is “Unable”
Notes: We counted the cases could be answered their altitude change request if the capabilities improved to be applied shorter intervals.
28 cases were counted, their requests could be answered when their capabilities improved to RNP4 or RNAV10 and data link.
This is about a quarter of altitude change request replied “unable”.
There is a capability to reduce “unable reply ratio”, if more aircraft improve their navigation performance or data link function.

## Slide 13
Up to this point, the result came from CPDLC message.
So, How is “unable reply rate” about all message including HF message?
Chart: 
| CPDLC | non CPDLC
 | 6925 | 2686
*Count from Flight Plans
2013/Feb, Mar, Apr

## Slide 14
“Unable” reply ratio CPDLC and HF
Analyzed day
2013 2/4~2/10, 3/4~3/10 , 4/1~4/7
TOTAL 21 days
 | Altitude change request message | “Unable” reply | “Unable” reply ratio
CPDLC | 4,070 | 1,041 | 26%
HF | 1,225 | 401 | 33%
TOTAL | 5,295 | 1,442 | 27%
CPDLC is required to apply reduce separation minima.
This result showed the effectiveness of the reduced separation minima for altitude change requests.

## Slide 15
“Unable” reply ratio CPDLC and HF
Chart: (UTC)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Traffic No. | 475 | 661 | 1236 | 1701 | 1755 | 1576 | 1202 | 1028 | 1149 | 1235 | 1200 | 1339 | 1449 | 1513 | 1404 | 1298 | 1133 | 1019 | 832 | 595 | 556 | 486 | 486 | 428
CPDLC | 0.15556 | 0.18056 | 0.16757 | 0.36599 | 0.33114 | 0.19522 | 0.17722 | 0.21951 | 0.22754 | 0.22346 | 0.22689 | 0.30493 | 0.28378 | 0.2783 | 0.32292 | 0.26111 | 0.26609 | 0.25414 | 0.21978 | 0.24074 | 0.125 | 0.087719 | 0.11628 | 0.11628
HF | 0.11111 | 0.24242 | 0.35065 | 0.31429 | 0.35366 | 0.23077 | 0.30909 | 0.23729 | 0.29167 | 0.41935 | 0.40541 | 0.38298 | 0.47458 | 0.41791 | 0.32759 | 0.35135 | 0.45833 | 0.33333 | 0.36364 | 0.31429 | 0.21053 | 0.18182 | 0.40476 | 0.1875
TOTAL | 0.13889 | 0.2 | 0.22137 | 0.35398 | 0.33457 | 0.20253 | 0.21127 | 0.22527 | 0.24686 | 0.25238 | 0.25091 | 0.31852 | 0.32384 | 0.31183 | 0.324 | 0.2765 | 0.29893 | 0.26906 | 0.26667 | 0.25874 | 0.15686 | 0.12222 | 0.25882 | 0.14667
With the increase in traffic volume, “unable” reply ratio is high.
In most of the time, HF indicating a high “unable” reply ratio than CPDLC.

## Slide 16
Conclusion
The “unable” reply ratio in the Ocean airspace within the Fukuoka FIR was analyzed.
The ratio was related to the route configuration and traffic volume.
Most of the related aircraft fly the same track in the same direction.
About a quarter of the cases in which replies to altitude change requests were “unable”, their requests were approved when their capabilities improved.
There is possibility to reduce the “unable” reply ratio if more aircraft had the data link and improved navigation performance such as RNP4.

## Slide 17
VALID 021800UTC Apr 2013
VALID 051800UTC Apr 2013
VALID 061800UTC Apr 2013
Chart: 高度変更リクエスト件数
| 2月 | 3月 | 4月
南太平洋⇒日本 | 30 | 57 | 110
Reference: JMA FBJP chart
No. of altitude change request
(South Pacific => Japan)
Cumulative number of 7 days
Flights in bad weather area, the altitude change is requested frequently.
For many of the flights between Japan and South Pacific is a non-data link aircraft, it can not be used for reduced separations.
South Pacific⇒Japan 22UTC （Feb. Mar. Apr.） | South Pacific⇒Japan 22UTC （Apr.）
29％ | 43％
Altitude change request in Bad Weather