## Slide 1: ADS-B In-Trail Procedures
Update of the ITP Operational Flight Evaluation for IPACG-40
September 2014
Kenneth M. Jones
FAA SBS ITP Project Lead

## Slide 2
Motivation for ADS-B In-Trail Procedures
The combination of locally dense traffic and large separation minima can limit altitude changes
Use ADS-B ITP to enable altitude changes potentially blocked by current operations
FL360
FL340
FL350
Desired Altitude
Altitude Changes required for better fuel economy, winds, and ride quality
=
NEED
CHALLENGE
OPPORTUNITIES
Standard Separation
ADS-B Transceiver and Onboard Decision Support System
ADS-B Out (required)
No ADS-B capabilities required
ITP Separation Standard
Notes: 2

## Slide 3
Concept Summary
  Maximum of two reference aircraft, ± 2000 feet altitude of ownship
  Aircraft can be any combination of ahead of or behind
  Can climb or descend; no less than 300 fpm in maneuver
  Initiate no closer than 15 NM with no more than 20 knots of closure or 20 NM with no more than 30 knots of closure
    Note: current operational trial limited to no closer than 18 nm
  Must maintain Mach number in climb
  Increased traffic situation awareness (can see traffic ~180 NM away)
ITP Aircraft High Level Requirements
  ADS-B In with on board ITP decision support system CPDLC
Reference or Target Aircraft High Level Requirements
  Valid ADS-B-Out signal (generally met with any GPS-equipped ADS-B out aircraft)
ADS-B ITP
Notes: 3

## Slide 4
Goals
Employ ADS-B ITP in oceanic air carrier operations
Objectives
Validate operational performance of ADS-B ITP
Validate economic benefits of ADS-B ITP
Operational Evaluation
  Partnership
    FAA and United Airlines agreement signed in April 2009
      Additional partners include Honeywell and Goodrich
  Scope
    Retrofit 12 UAL 747-400 aircraft with certified ITP systems
    Gather data on use of ITP in the Pacific starting in 2011
Notes: 4

## Slide 5
ADS-B-In requires hardware, software and crew interface
Electronic Flight Bag (EFB) solution chosen as a retrofit option
ADS-B ITP
Side Mounted Display Flight Crew Interface
EFB installed in a B747
Plan View
Notes: 5

## Slide 6
ADS-B ITP - Flight Crew Interface “ITP Data” View
Notes: 6

## Slide 7: ADS-B ITP Operational Evaluation
Operational Evaluation began on August 15, 2011
  Demonstration flight conducted using two United 747s operating in revenue service (UAL 863 and UAL 869)
  Expanded to encompass entire ZOA FIR December 2011
  Expanded to include New Zealand and Fiji in January 2014
Op Eval has been conducted for three years
  Data has been collected and analyzed during the operational evaluation
  Data has been used to validate safety assumptions and gather data on operational performance and economic benefits
Notes: 7
7

## Slide 8: Operational Evaluation Metrics July 2014
Application Validation Metric | Southern Pacific July 2014 |  | Northern Pacific July 2014 |  | Totals | 
 | Expected | Actual | Expected | Actual | 8/2013 - 7/2014 | 8/2011 - 7/2014
Number of ITP capable flights per month | 0 | 0 | 180 | 220 | 2694 | 4060
Number of ITP requests | 0 | 0 | 12 | 14 | 113 | 216
Number of ITP maneuvers performed | 0 | 0 | 2 | 3 | 20 | 42
Number of "standard" flight level changes | 0 | 0 | 7 | 8 | 44 | 82
Number of denied flight level changes | 0 | 0 | 3 | 1 | 28 | 57
Number of immediate limited standard climbs | 0 | 0 | 0 | 1 | 10 | 14
Number of climbs after moving reference aircraft | 0 | 0 | 0 | 0 | 6 | 11
Number of standard climbs after period of time | 0 | 0 | 0 | 1 | 5 | 10
ITP aircraft received a climb as a result of ITP requests approximately 74% of the time (159/216)
Zero “Southern Pacific” data is a result of United discontinuing 747-service to Australia on 31 March 2014

## Slide 9: Operational Evaluation Metrics
Controllers were temporarily not authorized to approve ITP request from August 15, 2013 to September 30, 2013
Even with the temporary suspension results were similar to projections

## Slide 10: Operational Evaluation Metrics Safety Metrics
Safety results are more conservative than original projections
Safety Related Parameter | Expected Avg. | Measurements (July 2014) |  |  | Measurements (8/2013 - 7/2014) |  |  | Measurements (8/2011 - 7/2014) |  | 
 |  | Min | Mean | Max | Min | Mean | Max | Min | Mean | Max
ITP Initiation Distance | 20 nm | 18.9 | 21.0 | 24.1 | 18.9 | 27.7 | 67.7 | 18.9 | 28.1 | 88.4
ITP Distance at Co-altitude | 18 nm | 19.2 | 21.3 | 24.6 | 19.2 | 28.0 | 67.9 | 19.2 | 28.6 | 88.5
Time From ITP Initiation to Level Off at New Altitude | 7 min | 3.0 | 3.7 | 5.0 | 2.0 | 4.5 | 8.0 | 2.0 | 4.8 | 8.0
Percentage of ITPs where a wake encounter occurred and a wake incident was reported | 2% |  |  |  |  | 0.0 |  |  | 0.0 | 
Wake Turbulence Incident Severity (5-1) (5 is minimal, 1 is catastrophic) | 5 |  | N/A |  |  | N/A |  |  | N/A | 

## Slide 11: Operational Evaluation Metrics Additional operational characteristics
Additional operational characteristics are also more conservative than original projections

## Slide 12: Operational Evaluation Metrics New Zealand and Fiji
Both Fiji and New Zealand authorized ITP operations in January 2014
Due to lack of equipped aircraft in their airspace, ITP operations effectively discontinued after 31 March 2014

## Slide 13: Data Recording Capability
PCMCIA ATA Flash memory cards
  Inserted/ejected from the front panel
  Up to 4GB capacity
Selective Recording
  ITP related parameters
  Signal in space data
No crew or technician action required
  Once the card is installed and the unit is powered up, the unit will continually record the selected parameters to the card; Once the card is full, no further data is recorded

## Slide 14: Sample Electronic Data Results
Total target flights | Minimum unique target airframes | Total ownship flights | Average maximum reception range
86946.0 | 5437.0 | 967.0 | 180.5
Total number of version 0 flights detected | Total number of version 1 flights detected | Total number of version 2 flights detected | Total number of version 1 or 2 flights detected
79582 | 4987 | 1900 | 477
Total number of “targets” and average maximum range
ADS-B signal version detected/received

## Slide 15: Sample Electronic Data Results Target aircraft maximum distance observed

## Slide 16
Notes: Data is for a Boeing 777-200B at Mach .84 with a track entry weight of 580,000 lbs. This is for a standard day with zero winds. UAC total fuel burn is approximately 94,600 pounds for this 6 hour flight on the Pacific Organized Track Structure (PACOTS).
Potential PACOTS Benefit Mechanism
Fuel Burn Comparisons (lb)
290
300
310
320
330
340
350
360
370
380
390
400
FL(feet)
∆ = 4307 lbs
∆ = 2558 lbs
∆ = 1228 lbs
∆ = 325 lbs
∆ = 267 lbs
∆ = 1418 lbs
Unrestricted Altitude Crossing (UAC)
0
1
2
3
4
Time(hrs)
5
6

## Slide 17
Benefits
Predicted direct benefits
  PACOTS benefits
    $113K benefit per equipped aircraft per year
        Average 800 lbs (362 kg) of reduced fuel burn on each equipped flight
  SOPAC (LAX/SFO – SYD) benefits
    $202K benefit per aircraft per year
        based on saving 300 lbs (136 kg) of Captain discretionary fuel (increased cargo carried (MTOGW flights) or ferrying less fuel)
Indirect benefits
  Detailed information on surrounding traffic (~180 nm in all directions)
  Aids strategic decision making and informed request to controllers
Operational trial preliminary results
  United experiences an average of 500 lbs of fuel savings for every ITP climb
  Additionally, the ITP aircraft average approximately 300 lbs of reduced fuel burn on every ITP equipped flight (compared to unequipped)
    potentially from greater situation awareness
Notes: 17

## Slide 18
Amendment 89 to Annex 10 — Aeronautical Telecommunications, Volume II — Communication Procedures
  Approved March 2014, Effective July 2014
  Controller-pilot data link communications (CPDLC) for in-trail procedures (ITP)
Procedures for Air Navigation Services — Aircraft Operations, Volume I — Flight Procedures (PANS-OPS, Doc 8168)
  Approved April 2014, Effective November 2014
  Use of cockpit traffic display by pilots
Procedures for Air Navigation Services, Air Traffic Management (PANS-ATM, Doc 4444)
  Approved June 2014, Effective November 2014
  ADS-B ITP separation standard and procedure
In-Trail Procedure (ITP) Using Automatic Dependent Surveillance — Broadcast (ADS-B)(Cir 325 AN/187)
  Approved 2014
  Summary information on in-trail procedure (ITP), its separation minimum and the work undertaken by ICAO
ADS-B ITP ICAO related documents

## Slide 19
First operational ITP flights conducted during the evening of August 15th in ZOA airspace; operational in the entire ZOA region December 2011
Continuing to collect data to determine operational and economic benefit and to monitor safety
Next steps
  FAA Order for manual use of ITP will go into effect soon
  ITP mods for ATOP
    Designs complete
    Initial operational readiness - August 2016
Summary and Next Steps