## Slide 1
Presented To: IPACG/40
Date: September 8-12, 2015
WP29: Speed Variation
Notes: <number>

## Slide 2: Mach Speed Variation
The FAA has presented papers at IPACG and ISPACG which outline the dangers of unannounced speed changes.
This issue needs attention by ICAO and a Global or Regional Procedure developed.
The ISPACG Working Group has been working on this issue to try and develop a unified regional procedure.
<number>
Notes: <number>

## Slide 3: ICAO Annex 2 3.6.2.2 change
3.6.2.2 Inadvertent changes. In the event that a controlled flight inadvertently deviates from its current flight plan, the following action shall be taken:
a) Deviation from track: if the aircraft is off track, action shall be taken forthwith to adjust the heading of the aircraft to regain track as soon as practicable.
b) Variation in true airspeed: if the average true airspeed at cruising level between reporting points varies or is expected to vary by plus or minus 5 per cent of the true airspeed, from that given in the flight plan, the appropriate air traffic services unit shall be so informed.
c) Change in time estimate: if the time estimate for the next applicable reporting point, flight information region boundary or destination aerodrome, whichever comes first, is found to be in error in excess of 2 minutes from that notified to air traffic services, or such other period of time as is prescribed by the appropriate ATS authority or on the basis of air navigation regional agreements, a revised estimated time shall be notified as soon as possible to the appropriate air traffic services unit.
3.6.2.2.1 Additionally, when an ADS agreement is in place, the air traffic services unit shall be informed automatically via data link whenever changes occur beyond the threshold values stipulated by the ADS event contract.
<number>
Notes: <number>

## Slide 4: Mach Speed Variation
Annex 2 change fails to fully address the issue.
An en route aircraft at 500 knots only has to inform ATC when its true airspeed changes by 25 knots or more from the speed given in the flight plan. This allows for speed changes of 48 knots without informing ATC.
<number>
Notes: <number>

## Slide 5: Mach Speed Variation
<number>

## Slide 6: Flight Planned Speed Changes
(FPL-XXXX-IS
-B744/H-SDE3FGHIJ3J5M1RWXY/LB2D1
-RJAA1025
-M073F290 DCT CUPID Y808 ALLEN/M072F290 Y812 SCORE OTR11 LEPKI DCT 37N160E/M071F290 DCT 35N170E/M084F390 DCT 32N180E DCT 27N170W DCT CANON V15 LILIA/M083F390 DCT KLANI KLANI2
-PHNL0633 PHJR
-PBN/A1L1B1C1D1O1S2 DOF/140508 REG/XXXXX EET/KZAK0227
PHZH0542 SEL/FGJP CODE/XXXX RVR/75 OPR/XXX PER/D RALT/RJCK PMDY RMK/TCAS)
<number>
Notes: <number>

## Slide 7: Mach Speed Variation
In the Pacific, FIRs are applying 30nm longitudinal separation standard using an ADS-C reporting rate of 10 minutes. A 48 knot speed change by one aircraft could result in an 8nm closure between two aircraft between ADS-C reports.
<number>
30nm
Notes: <number>

## Slide 8: Australia AIP Amendment
AIP ENR 1.1 para 21:
A pilot must inform ATS if the average cruising speed, either TAS or Mach whichever is applicable, between reporting points, varies or is expected to vary, by a value equal to or greater than:
a. 5% TAS
b. 0.01 Mach from that given in the flight plan.
<number>
Notes: <number>

## Slide 9: Speed Change NOTAM Proposal
IN ORDER TO PREVENT UNANNOUNCED SPEED CHANGES AIRCREWS ARE REQUIRED TO USE THE FOLLOWING PROCEDURES IN THE KZAK FIR. UPON CROSSING THE KZAK FIR BOUNDARY AIRCRAFT ARE REQUIRED TO REPORT THEIR SPEED IN THE FIR POSITION REPORT VIA CPDLC OR HF VOICE. TURBOJET AIRCRAFT ARE TO REPORT THEIR MACH NUMBER AND NON-TURBOJET AIRCRAFT ARE TO REPORT A TRUE AIRSPEED.
A PILOT MUST INFORM ATS EACH TIME THE CRUISING SPEED, EITHER TAS OR MACH WHICHEVER IS APPLICABLE VARIES OR IS EXPECTED TO VARY BY A VALUE EQUAL TO OR GREATER THAN:
A. 10 KNOTS TAS FROM THE PREVIOUSLY REPORTED SPEED - Non-Turbojet
B. 0.02 MACH FROM THE PREVIOUSLY REPORTED SPEED - Turbojet.
<number>
Notes: <number>

## Slide 10: Speed Change Proposal
Procedurally when an aircraft wanted to change by .02 Mach number, they could downlink DM18 with the requested speed (Mach number).
If ATC required a speed assignment for separation, an appropriate speed assignment would be assigned ie UM106 MAINTAIN Speed.
If ATC did not require a speed assignment, the following could be Uplinked:
UM ROGER?
UM169 Speed change to M0.84 approved
This advises the aircraft that the requested speed change is approved but no speed restriction has been assigned.
<number>
Notes: <number>

## Slide 11: ATMC Speed Change Proposal
IN ORDER TO PREVENT UNANNOUNCED SPEED CHANGES AIRCREWS ARE REQUIRED TO USE THE FOLLOWING PROCEDURES IN THE RJJJ FIR. AIRCRAFT SHOULD REPORT THEIR PRESENT MACH NUMBER WHEN DIFFERS 0.02 MACH NUMBER OR MORE FROM THE FLIGHT PLANNED SPEED.
<number>
Notes: <number>

## Slide 12: Mach Speed Variation
Aircrews predominantly do not monitor their flown speed versus the flight planned speed.
It does not matter whether an ATC system uses the first speed in field 15 of the FPL or accounts for the speed changes imbedded in the route of flight.
<number>
Notes: <number>

## Slide 13: Flight Planned Speed Changes
(FPL-XXXX-IS
-B753/M-SDE2E3FGHIRWXYZ/S
-KSEA0035
-N0396F300 HAROB4 HQM C1418 SEDAR A331 ZINNO/N0463F340 A331 ZIGIE MAGGI3
-PHNL0541
-PBN/A1B1C1D1O1S1T1 NAV/RNVD1E2A1 REG/XXXXX
EET/KZAK0039
SEL/XXXX
RMK/TCAS AGCS EQUIPPED NRP USA)
<number>
Notes: <number>

## Slide 14: Flight Planned Speed Changes
ANA1078 IS B788 SADE2FGHIJ2J4J5J6M1M2RWXYZ LB1D1SH
RJAA KSEA P270 270 N0446 JA806A TR 1
N0446F270 CUPID Y808 ONION OTR5 KALNA/M069F270 DCT 44N160E/M084F390 47N170E
49N180E/M085F410 50N170W 51N160W 52N150W 51N140W DCT ORNAI/N0488F410 DCT
SIMLU DCT KEPKO DCT TOU MARNR3
<number>
Notes: <number>

## Slide 15: Mach Speed Variation
By requiring a speed report upon entering the FIR/CTA, a pilot is made aware of their speed and the need to notify ATC if the speed will change by .02 Mach or more.
The speed report also allows ATC to check the speed the ATC system is using to calculate separation for the aircraft.
<number>
Notes: <number>

## Slide 16: Mach Speed Variation
The ODP system does not highlight the reported TAS nor Mach Number when the position report is processed at the FIR boundary nor at any other waypoints, regardless of HF report, CPDLC, ADS.
The ODP system does not inform ATMC controllers of the differences between the reported speed and the flight planned speed.
When aircraft report present Mach Number and the ODP system and FPL indicates its flight planned TAS, ATMC Controllers have to convert and compare its differences manually.
Even if ATMC could find the reported Mach Number, they could not compare the differences between TAS and MACH. ATMC would have no other choice but to input the aircraft’s reported speed into ODP without exception. And if ATMC needed to keep Mach Number Assignment, we have to add Mach Number with every climb clearance.
<number>
Notes: <number>

## Slide 17
Notes: <number>