## Slide 1
DARP
Notes: <number>

## Slide 2: Dynamic Airborne Reroutes
Allows Airborne Rerouting of Aircraft When Winds Indicate a More Fuel Efficient Route is Available
Reduce Operating Costs by Taking Advantage of Updated Winds
FANS and Air Traffic Services Inter-facility Data Communications (AIDC) Required
Ongoing Trials in the South Pacific

## Slide 3: Dynamic Airborne Reroute Procedure
User Preferred Route
Dynamic Reroute
ZOA
New Weather
Forecast
AOC
Revised Route
Route Clrce
AIDC New Route
Auckland

## Slide 4
Oakland FIR DARP Usage
<number>

## Slide 5: DARP Trial Flights
DARP operational procedures are published in the GOLD

## Slide 6: DARP Trial Flights
Operational CPDLC is required for aircraft requesting airborne DARP reroutes.
A DARP request must be made within Oakland Oceanic Control Area and at least 1 hour prior to crossing the FIR common boundary. This is necessary to permit adequate time for clearance delivery and AIDC messaging to take place.
The downlink CPDLC reroute request should be made by the flight crew at least 20 minutes before the divergence waypoint to allow processing time by controller and flight crew.

## Slide 7: DARP Request Boundary Proximity
REQ DARP
UNABLE
DARP MUST BE REQUESTED AT LEAST 60 MINUTES PRIOR TO FIR

## Slide 8: Dynamic Airborne Reroutes
<number>
The FAA encountered a problem where aircraft DARP requests that contained a duplicate waypoint lat/long would be incorrectly processed and the uplink route clearance would contain the lat/long for the waypoint immediately following the waypoint.
This was corrected in the Ocean21 T20 software build.

## Slide 9: Dynamic Airborne Reroutes
<number>
There is an open FANS PR where Boeing aircraft downlink requests for a reroute do not include the waypoint between two routes.
If this route is uplinked to the aircraft it loads correctly with the correct route, but it frequently causes AIDC rejects because of the missing waypoint.

## Slide 10
Actual & Potential Result (TYO – LAX / SFO)
Notes: <number>

## Slide 11
Notes: <number>