## Slide 1: CFCG
ICAO Communication Failure Coordinating Group
IPACG/40
Keith Dutch, AJV-84
8-12 September 2014

## Slide 2: CFCG
History
Meetings
CFCG/2 Outcome

## Slide 3: CFCG History
ICAO communication failure provisions revised six times since the Rules of the Air and Air Traffic Control (RAC) introduced in 1945
In 2011, two ICAO regional offices offered proposals relating to communication failure provisions
  EUR proposal merges flight crew Standards from Annex 10 Vol. II into Annex 2 and adds new provisions for an aircraft flying IFR that chooses to continue VFR
  CPWG proposed that the aircraft maintain the last ATC assigned speed and level, without regard for changes filed in the flight plan, until exiting the airspace defined in the SUPPS proposal.

## Slide 4: CFCG Meetings
CFCG/1 October 2012 at ICAO HQ in Montréal
No agreements reached between conflicting “camps”
  NAM and NAT affirm that safety and integrity guaranteed only if aircraft flies by last ATC clearance
  EUR expects aircraft will change speed and altitude(s) in accordance with Current Flight Plan (CPL) Item 15. (Route)
CFCG/2 February 2014 at ICAO HQ
  Proposed common procedure, without variation due to oceanic/remote or continental airspace
  Simple, unambiguous for a rare single aircraft event
  Reached consensus

## Slide 5: CFCG/2 Outcome
CFCG/2 Proposed
  Aircrew must attempt to use all communication methods (“… all available means …” includes, inter alia, data link, satellite voice and mobile phones.)
  Maintain last assigned speed, level, and routing for 20 minutes after squawking 7600
  Add RCF procedures to SIDs/STARs
  “Filed Flight Plan” (FPL) revised to include mods prior to departure
  IFR flights continue to destination according to last ATC clearance
  ATC separates RCF aircraft from other aircraft, based on above
  Squawk 7601 if pilot goes VFR to suitable airport
Rationales are being developed for proposed changes
Following rationales and CFCG satisfaction, submitted to
  Air Traffic Management Operations Panel
  Flight Operations Panel