## Slide 1: Significant delay in AIDC transaction
IPACG/40
September, 2014
Systems Development, Evaluation
and Contingency management Center
(SDECC)
Notes: イントロダクション
<number>

## Slide 2: Switchover of AIDC line
At IPACG/39, JCAB reported as follows:
  AIDC line between FAA and JCAB was switched over from leased line to AMHS on 9 July 2013.
  AIDC transaction time via AMHS was generally within 20 seconds, which was longer than via leased line, this was acceptable for AIDC operation.
<number>
Notes: <number>

## Slide 3: Increase of AIDC transaction timeouts
JCAB received information from FAA that the number of AIDC transaction timeouts was on the increase from January 2014.
On investigation, the following fact was found:
  Consecutive AIDC transaction timeouts occurred in a short time period;
  This time period came out irregularly by the frequency of once or twice a month.
  In this time period, it takes several minutes until FIMS (system handling ATS messages in JCAB) transmits an AIDC message to AIDC server after receiving it from AMHS.
<number>

## Slide 4: Number of timeouts (February 2014)
<number>

## Slide 5: Number of timeouts (March 2014)
AIDC transaction timeouts occurred 77 times.
AIDC transaction timeouts occurred 23 times.
<number>

## Slide 6: Number of timeouts (April 2014)
AIDC transaction timeouts occurred 20 times.
<number>

## Slide 7: Number of timeouts (May 2014)
AIDC transaction timeouts occurred 39 times.
AIDC transaction timeouts occurred 19 times.
<number>

## Slide 8: Number of timeouts (June 2014)
<number>
AIDC transaction timeouts occurred 20 times.

## Slide 9: Number of timeouts (July 2014)
<number>
AIDC transaction timeouts occurred 85 times.

## Slide 10: Number of timeouts (August 2014)
<number>

## Slide 11: Cause of AIDC transaction timeouts
A transmission delay occurred in a data transmitting from FIMS to AIDC server, when a data congestion at FIMS occurred.
FIMS can process up to 100 ATS messages (include AIDC messages) which received from AMHS and AFTN lines, per minute.
When significant number of timeouts occurred, FIMS was receiving over 250 ATS messages per minute.
<number>

## Slide 12: Cause of AIDC transaction timeouts
These messages contained the ATS messages not passing through RJJJ in a usual condition.
It can be inferred that when AFTN alternate sub-network was established due to AFTN line trouble which had occurred somewhere in the world, ATS messages accumulated in AFTN network flowed into RJJJ.
<number>

## Slide 13: Cause of AIDC transaction delay
RJJJ
Other ATSU
FIMS
AMHS
server
AIDC
server
AFTN
station
AFTN
station
DELAY
A transmission delay will occur when FIMS receives over 100 ATS messages per minute from AMHS and AFTN.
AMHS link
AFTN
station
<number>

## Slide 14: Alternate routing of AFTN line
<number>
RJJJ
KSLC
A
B
E
C
D
Z
AFTN station
Ordinary routing
Alternate routing
AFTN line trouble

## Slide 15: Countermeasures for this issue
The measure to be taken for this problem is under consideration in JCAB.
<number>