## Slide 1: PARC Communications WG RCP Overview
Tom Kraft
Chief Scientific & Technical Advisor for Aeronautical Communications
Federal Aviation Administration (FAA) tom.kraft@faa.gov tel.: 425-917-6580 fax: 425-917-6590
IPACG 22

## Slide 2: PARC
Performance-based operations Aviation Rulemaking Committee (PARC)
  Comprises members from the FAA & the aviation community at large
  Provides recommendations to FAA’s Senior Management for action & implementation
  Effective in implementing RNAV/RNP
Notes: I would like to introduce a new activity under the auspices of the Performance-based operations Aviation Rulemaking Committee (PARC).
This new activity will be performed by the Communications Working Group.
Before I talk about the Communications Working Group, I want to say just a few words about the PARC itself.
The PARC [read sub-bullets]
Optional: You may have heard of the Terminal Area Operations Aviation Rulemaking Committee (TAOARC). The TAOARC was renamed to the PARC in February of 2004.

## Slide 3: “New” Communications Working Group under PARC
To produce a road map to apply required communication performance (RCP), initially to the implementation of
  30/30 NM separation minima
  Clearance delivery in U.S. domestic en route airspace
To produce a roadmap for data link in all airspace domains (oceanic & domestic)
  Include interoperability criteria
  Consider convergence
  Address technological issues
Notes: Mainly, the communications working group will produce for the PARC two roadmaps for communications supporting performance-based operations
An RCP roadmap, which will include applying RCP initially to the implementation of 30/30 separation minima and clearance delivery in U.S. domestic en route airspace.
A data link roadmap for all airspace domains, which will include interoperability criteria, considering convergence and technological issues.
The Communications Working Group will also
Develop regulatory criteria and guidance material, as appropriate, and
Participate in ICAO and industry standards work to promote global seamless airspace development.

## Slide 4: Performance-based operations
Balances capability & performance of
  Communications
  Navigation, e.g., RNAV/RNP
  Surveillance, e.g., ADS
  Air Traffic Management
Builds on what we have to improve
What is RNP [x] airspace?
What is applying separation using ADS?
Notes: Performance-based operations depends on capability and performance of many aspects of a complex system involving people, procedures, technical elements, and different functionality.
One of the objectives in transitioning to performance-based operations is to build on what exists in aircraft and in air traffic service provision to optimize operational benefits.
Another objective is to exploit modern technology by establishing standards that define the “minimum acceptable” capability and performance required for an intended operation and independent of any particular technology.

## Slide 5: Safety & standards
Goal: Performance-Based System
Required Capability & Performances
  Communication
  Navigation
  Surveillance
  Total ATM System
Technology standards
Required
Navigation
Performance
Required Total System
Performance
Required
Surveillance
Performance
Required
Communication
Performance
Notes: Each of the elements of the system are inter-related and together, depending on the capability and performance of each of the elements, support the performance-based operation.
It is important to note that, in a performance-based system, interoperability and related technologies are an underlying assumption to enable the performance-based operation.

## Slide 6: ICAO Doc 4444, PANS/ATM
5.4.2.6 Longitudinal separation minima based on distance using RNAV where RNP is specified
5.4.2.6.3 The following [longitudinal] separation minimum may be applied:
Separation minimum
RNP type
93 km
(50 NM)
10
Communication requirement
Surveillance requirement
Distance verification requirement
Direct controller-pilot communications
Procedural position reports
At least every 24 minutes
Notes: Separation minima are almost always a key ingredient to attaining any operational benefit.
And also in determining the “minimum acceptable” criteria for qualifying enabling technologies and operations.
Standards for implementing separation minima can be found in ICAO Doc 4444, Procedures for Air Navigation Services — Air Traffic Management (PANS-ATM) and other related ICAO material.

## Slide 7: ICAO Doc 4444, PANS/ATM
5.4.2.6.3.1 During the application of the 93 km (50 NM) [longitudinal] separation, when an aircraft fails to report its position, the controller shall take action within 3 minutes to establish communication. If communication has not been established within 8 minutes of the time the report should have been received, the controller shall take action to apply an alternative form of separation.
Notes: As we all know, we must be careful as there are many underlying assumptions to understand and ensure their validity when the separation minima are implemented in the intended airspace.
PANS/ATM provides criteria for the communication and surveillance performance in a way that is different from how the criteria for the navigation performance are provided.
The performance criteria for the navigation capability are provided by specifying an RNP type for the separation minima.
The RNP type is then used as a basis for prescribing navigation capability and performance within an airspace, for aircraft and operator approval, and for monitoring during continued operations.

## Slide 8: ICAO Doc 4444, PANS/ATM
Longitudinal separation minimum
RNP type
93 km
(50 NM)
10
Communication requirement
Surveillance requirement
Distance verification requirement
Direct controller-pilot communications
Procedural position reports
At least every 24 minutes
10
Direct controller-pilot communications
27 minutes max ADS report interval
Assumed?
4
Direct controller-pilot communications
Assumed?
32 minutes max ADS report interval
55.5 km
(30 NM)
4
Direct controller-pilot communications
Assumed?
14 minutes max ADS report interval
Notes: This chart is intended to show that ICAO Doc 4444, PANS/ATM provides different ways that are acceptable when desired to implement a 50NM longitudinal separation minimum.
During the conclusions of the study presented by the FAA Technical Center and Rutger University it was noted that we need to consider ways for implementing mixed separation minima in the same airspace.
We may also want to consider implementing the same separation minima, e.g., 50 NM longitudinal, except in different ways depending on the aircraft capabilities.
I note the procedural issues to be resolved. We also will need to resolve issues with managing the criteria for the different capabilities and performances required of each aircraft in the “mixed” fleet within the airspace.

## Slide 9: RCP types currently proposed
RCP type
Transaction time (sec)
Continuity (probability/ flight hour)
Availability (probability/ flight hour)
Integrity (acceptable rate/ flight hour)
RCP 240
240
0.99
0.999
10-5
RCP 180
180
0.99
0.999
10-5
RCP 120
120
0.99
0.999
10-5
RCP 45
45
0.99
0.999
10-5
Notes: The Operational Data Link Panel (OPLINKP) is developing a Manual on RCP. This manual, and related revisions to ICAO Annex material, is expected to be completed for the first panel meeting in Montreal, CANADA, scheduled in September 2005.
This table shows a list of RCP types currently proposed in the draft manual.
In this form, the RCP types are general and are intended to minimize a proliferation of many RCP types.
They are intended to be used when specifying the performance requirements for communications supporting a performance-based operation or air traffic management (ATM) function, such as 30 NM longitudinal separation.

## Slide 10: What RCP type might look like
Within a standard
Within an AIP/NOTAM
Within a flight plan
When monitoring during operations
Notes: The slides that follow will give you an idea of what RCP might look like:
Within a standard, which is used for approval of the different elements making up the communications supporting a performance-based operation.
When the RCP type is prescribed within an airspace
When filing the flight plan, and
When monitoring during operations.
Please keep in mind that these charts are provided to exemplify an application of the RCP concept.
It is not meant to be a comprehensive solution for applying the RCP concept to implementing a 30 NM longitudinal separation minimum.

## Slide 11: ICAO Doc 4444, PANS/ATM
5.4.2.6.4.3.2 The communication system provided to enable the application of the separation minima in 5.4.2.6.4.3 shall allow a controller, within 4 minutes, to intervene and resolve a potential conflict by contacting an aircraft using the normal means of communication. An alternative means shall be available to allow the controller to intervene and resolve the conflict within a total time of 10½ minutes, should the normal means of communication fail.
Notes: This slide refers to some performance requirements related to the communications supporting the implementation of separation minima.
This particular requirement applies when an RNP is specified, when using ADS, and also when using direct controller-pilot communications or DCPC.

## Slide 12
Communication
Controller
Surveillance
ATM function: separation assurance,
communications & controller intervention buffer
Surveillance
Flight crew
Navigation
ATS unit
ATM functional capabilities
ATM functional capabilities
Operational communication transaction
ATM context
ATM context
A
Z
RCP type
Human initiates transaction
Initiator is confident that transaction is satisfactorily complete
Aircraft
Notes: The criteria for implementing the separation minima, in accordance with PANS/ATM, assumes certain performance of a communications and controller intervention buffer.
The communications and controller intervention buffer expresses the time it takes from when a conflict is detected to when the aircraft is displaced, ultimately resolving the conflict.
PANS/ATM requires a direct controller-pilot communications or DCPC capability using data link, for the controller to intervene.
To apply an RCP type to DCPC, it will be necessary to determine the points at which the communication starts and when it ends, in the context of the total time allocated to the communications and controller intervention buffer. In this example, some assumptions need to be made:
The DCPC communication begins at the time the controller starts to compose the instruction for the aircraft.
The DCPC communication ends when the controller understands the response from the aircraft e.g., WILCO.
It is noted that this particular communication describes an operational transaction (two-way dialogue) from the controller’s perspective and will include the performance of the flight crew.

## Slide 13: What RCP type might look like
“180” is the time in seconds (3 minutes) at which the controller (e.g., for intervention) or pilot (e.g., for weather deviation) would initiate contingency procedures if the communication is not completed.
The RCP type “180” also signifies how dependable the system needs to be. It can be translated into engineering & operational terms based on service availability, undetected anomalous behavior of the system, & the percentage of communications that are successfully completed within 180 seconds.
RCP 180
Longitudinal separation
Nav
Comm
Surv/ATM
Function
RNP 4
Performance
RNAV
DCPC - Intervention
Conflict detection
14 minutes
max position update rate
55.5 km (30 NM)
Notes: It is further assumed that 180 seconds or 3 minutes of the total 4 minutes required for the controller to intervene and resolve the conflict is allocated to the direct controller-pilot communication (DCPC).
It is also noted that the RCP type, in addition to a time requirement, also signifies other performance, such as integrity, availability, and continuity.

## Slide 14: What RCP type might look like
Establish compliance targets to:
  Set operational timers for contingency procedures
  Provide the basis for different approval types, e.g., air traffic service provision, aircraft type design approval, ops approval
  Operationally monitor & resolve non-compliant performance
RCP 180
Initiator
Responder
Technical Comm
Time
20
20
140
Air traffic service provision - 130
Aircraft - 10
Part
Communication service allocation – 120
Notes: Compliance targets are needed
To set operational timers, such as, to provide indication to the controller or flight crew for when to execute a contingency procedure.
To provide a basis for different approval types, for example, to approve the aircraft type design.
To operationally monitor and resolve non-compliant performance.
The values provided in the chart are only to exemplify the need for allocation and are not intended to suggest that these values are the allocations for an RCP type of 180.
In fact, it may be necessary to provide different allocations for the same RCP type depending on the technologies and the architectures used to enable the communications supporting the performance-based operation.

## Slide 15: What RCP type might look like
Aeronautical Information Publication (AIP)/Notice to Airmen (NOTAM)
  ATM Function, e.g., 30/30 NM separation
    RCP Requirements, e.g., RCP 180
    Interoperability, e.g., FANS 1/A, ATN
    Approval of operator for RCP operations, includes aircraft equipage, their communication service provisions, training, procedures, maintenance, etc.
    Flight plan criteria
    Operational monitoring criteria
Notes: The RCP criteria, as discussed on the previous slides, are specified in the standard for a particular ATM function. In airspace where the ATM function is being implemented, the AIP/NOTAM, prescribes the RCP criteria in accordance with the standard. The AIP/NOTAM will
Provide criteria for operators approval, which includes proper equipage, adequate communication service provision and internetworking, flight crew training, maintenance, and so on, and
Provide criteria for monitoring within that airspace to ensure operations continue to stay within acceptable performance limits.

## Slide 16: What RCP type might look like
Flight Plan
  Field Type 10
    “J”  ATC data communications “capability”
    “R”  RNP navigation “capability”
    “D”  surveillance/ADS “capability”
  Field Type 18
    “DAT/FANS/RCP180”  communication “performance”
    "NAV/RNP4“  navigation “performance”
    “SUR/…”  surveillance “performance”
Notes: I recognize that there are issues with filing the flight plan. We do not seem to have enough designators.
This chart is to exemplify how RCP type might look in a flight plan. The chart is not too different from what is currently prescribed by some States who are implementing a 30 NM longitudinal separation.
It is noted that the chart is not complete. Other considerations will include, for example, filing for satellite voice capability.

## Slide 17: What RCP type might look like
Operational monitoring
  Those portions where the variability of performance cannot be reliably predicted
  To resolve non-compliance
COMPLIANCE TARGETS
ACTUAL PERFORMANCE
Establish compliance targets
Validate assumptions
Analyze actual performance
Complying with RCP type
RCP type [for
ATM function (x)]
Z
A
e.g., 60 sec one way tech comm + other performance + assumptions = actual operational communication performance  RCP type
Notes: There have been concerns related to difficulties in monitoring operational performance. Prescribing an RCP type does not necessarily mean that the entire communications is monitored.
It is my personal view that, as a minimum, you would need to monitor those portions where the variability of performance cannot be reliably predicted prior to initial operational use. It is also desirable to monitor parts of the system separately for timely resolution of non-compliant performance.
What is monitored is analyzed, considering the assumptions, and conclusions can be made as to the acceptability of the actual operational performance based on the RCP type.

## Slide 18
Example
Notes: This chart provides more examples of how RCP types might be used in all airspace domains.
It is noted that the RCP type only makes sense when it is used in a total system context.

## Slide 19: Interoperability Issues
European ATN mandate & commitments, include technology accommodation
  Centers by January 2008
  New aircraft by March 2009, retrofit by March 2014
NAT investigating operational requirements for ATN trials
EUR/NAT activity to
  Develop Plan to implement ATM services that use data link over 15-20 yr period
  Develop Plan to converge data link services & technologies
  Symposium, March 2005, Paris, France
Notes: As mentioned earlier in my presentation, interoperability and related technologies are an underlying assumption to enable the performance-based operation.
I want to bring to your attention the work starting in Europe and the North Atlantic.
This work is investigating issues, mainly because two different and real technologies are not compatible. FANS 1/A and the ICAO aeronautical telecommunication network (ATN) are planned to be operational throughout the world for a long time to come.
The ICAO Paris office is hosting a Symposium at the end of March to exchange information on the issues.
The PARC Communications Working Group will also be investigating the issues with mixed technologies as well, as it relates to the U.S. National Airspace System and will be coordinating with the European and the North Atlantic regional planning groups.

## Slide 20: Conclusions
RCP will address issues with:
  Communication capability & performance standards
  Prescribing the use of those standards in airspace
  Compliance, qualification & approval of parts of the total system, initially & for continued operations
Interoperability is an underlying assumption to the application of RCP to communications supporting performance-based operations
Notes: In conclusion, I would summarize that [read the slide]

## Slide 21: Discussion
For more information or to participate in this activity, contact
  Tom Kraft at tom.kraft@faa.gov
  Ann Tedford at ann.tedford@faa.gov
Thank you