## Slide 1: Aviation Rumble Strip Project Update RPD 133 March 16, 2016

## Slide 2: Utilizing a Center of Excellence
  PEGASAS
Partnership to Enhance General Aviation Safety, Accessibility and Sustainability

## Slide 3: 2015 Purdue Airport Rumble Strip Test Site
Thermoplastic
Saw Cut
Temporary

## Slide 4
Temporary

## Slide 7: Saw Cut Options
Square Cut
Bevel Cut

## Slide 8: Thermoplastic
Easy to construct
Semi-intrusive
Permanent
Proven to withstand winter ops in roadway environment

## Slide 9
PEGASAS Test Configuration
Thermoplastic Sawcut Temporary

## Slide 10: Aircraft Used in Study
CESSNA 172
CIRRUS SR20
CESSNA 152
SKY ARROW
PIPER PA 34
CRJ-100ER
CESSNA 152
PIPER PA 28

## Slide 11: Acceleration Graph
Temporary
Saw Cut
Thermoplastic
Aircraft: Cessna 172 Speed:5 knots
Notes: bg

## Slide 12
2.805
2.739
2.63
Affects on Pilots and Airframe Rail-to-Seat Plots for 10 kts
Significant airframe acceleration must occur for pilot to feel rumble strip
Airframe affected by 2 to 3X the acceleration force felt by pilot, over time airframe manufacturers feel this may cause damage to the gears.
Seat
vs.
Rail

## Slide 13: April 2015 Durability Testing

## Slide 14: Tech Center Test Results
Day | Load Aircraft | Passes | Square Cut | Beveled | Temporary
Day 1 | 10k lbs. E190 | 1000 passes | Began crumbling at 500 passes | No change | No change
Day 2 | 15k lbs. CRJ-700 | 1000 passes | Continued crumbling | No change | No change
Day 3 | 30k lbs. 757-200 | 1000 passes | Heavily worn | No change | Sign of warn, but no damage
Day 4 | 45k lbs. 738/A321 | 500 passes | Heavily worn | No change | Connection point becoming loose
 | 60k lbs. 748/A380 | 10 passes | Heavily worn | No change | ~1/8” depression

## Slide 16: European Rumble Strip Study Deployed on Active Taxiway for 3 months at Southampton Intl Airport, England
19.7”
19.7”

## Slide 17: European Rumble Strip Study
Each segment 11.8” wide
39.4’ long
0.47” high
19.7”
19.7”
    Feedback invited from pilots (35 responses) and ground vehicle operators (10 reports)
    Pilots report rumble strips were discernible (varied by aircraft) but difficult to differentiate from other taxiway features (e.g., rough pavement)
      Half assessed impact as “excessive”
      Pilots did not recognize purpose and considered rumble strips a distraction
    Did not affect capacity
    Deemed ineffective for incursion prevention

## Slide 18: Our Evaluation Results

## Slide 19: Problems with Durability of 90 degree Saw Cut at KLAF and at NJ Tech Center
Saw Cut

## Slide 20: Constructability Challenges with 45 degree Bevel Saw Cut at KLAF and at NJ Tech Center
Saw Cut

## Slide 21: Thermoplastic
Easy to construct
Semi-intrusive
Permanent
Proven to withstand winter ops in roadway environment

## Slide 22: NOT on Airports! Rumble Strips were Damaged by Snowplows after First Snow and Were Subsequently Removed to Avoid FOD on Airfield at KLAF

## Slide 23: Thermoplastic has Problems with Durability

## Slide 24: Temporary Rumble Strips
Allows temporary installation
Interlocking joints
Segments: 13” wide, 36” long, ¾” high, 35 lbs
Can be installed by one person

## Slide 25: Conclusions
All Rumble Strip types evaluated, if installed permanently, may cause damage, with continual use, to the size of aircraft used in study.
Saw Cut Strip
  Durability of 90 degree
  Constructability with 45 degree bevel
Temporary Rumble Strips may be useful as a tactile warning to aircraft when used to identify a temporary change at an airport such as a construction areas etc.

## Slide 26
Questions/Comments?

## Slide 27: Infra-Red Requirements for developing a Elevated LED High Intensity Runway Edge Light, L-862(L) (HIRLs) with IR emitter March 16, 2016

## Slide 28: Infra-Red Requirements for LED HIRLs
About 10 years ago, the FAA published a final rule permitting Enhanced Flight Vision System (EFVS) operations to be conducted below DA/DH or MDA down to 100 feet above the touchdown zone elevation.
The EFVS manufacturers addressed concerns about their equipment not being able to see an image on a Heads Up Display (HUD) LED lights in the runway environment, due to little to no heat (IR) in the needed wavelength.
Traditionally, the NAS doesn’t have a requirement for airport lighting to emit IR energy. Airport lighting standards are solely based on the visible spectrum (intensity, brightness, color, beam spread).

## Slide 29: Infra-Red Requirements for LED HIRLs
In 2008, the RTCA SC-213, Enhanced Flight Vision Systems and Synthetic Vision Systems committee took on the task to identify the IR amount needed for EFVS. After two years, they were unsuccessful in establishing the required amount of IR.
In 2010, the SAE G-20 Committee was formed and originally tasked by AFS-400 to “address the possible adverse impact to EFVS operations by transitioning airport approach and surface lighting systems from incandescent to LED’s.” They also took on the task to identify the IR amount needed for EFVS. To this date, the they have not been able to identify the IR amount needed for EFVS.

## Slide 30: Infra-Red Requirements for LED HIRLs
Because of these concerns, FAA Office of Airports issued the guidance in the AIP handbook Effective September 30, 2014 restricting the use of AIP funds for certain LED lights including LED Obstruction Lights, LED Approach Lights, and LED High Intensity Runway Edge Lights.
In an attempt to lift the AIP restriction from funding LED HIRLs, AAS requested this research to explore the requirements for developing a FAA L-862(L) (HIRL) with an IR emitter, designation to be L-862(L-IR) and to ensure its compatibility with aircraft currently equipped with EFVS.

## Slide 31: OBJECTIVES
Develop IR requirement based on legacy L-862 incandescent fixture measurement, and use visual light requirements from FAA AC 150/5345-46 (current version), and FAA EB 67D.
Perform IR measurements (IR power output in watts per steradian, and IR beam pattern) on the legacy tungsten-halogen FAA L-862 (HIRL), which current EFVS system’s utilizes, to determine current IR output.

## Slide 32: Process
Post a Broad Agency Announcement (BAA)
Prepare Request for Proposal (RFP) to develop prototype L-862 (L-IR).
Award contract to ultimately build prototypes
Conduct validation operational flight tests through the Office of Flight Standards.
Conduct cost analysis and comparison for LED fixture with IR to LED fixture without IR.

## Slide 33: Phase I: Broad Agency Announcement (BAA)
Announcement posted 2/02/16
Announcement closed 2/19/16
Evaluation period 2/22/16 to 3/10/16
Contracts notifies candidates 3/25/16
for Phase II Request For Proposal (RFP)

## Slide 34: Three-page Technical Summary
At a minimum summary shall contain:
Purpose of Research
Description of Research and the Science of How and Why it works
Current State of Development
Estimated Time to Complete
Description of testing & Evaluation procedures
Estimated Funds required
Only offers' whose Technical Summary is considered capable of meeting existing or future program requirements will be asked to submit a formal Phase II proposal.

## Slide 35: Phase II: Request For Proposal (RFP)
Proposal submission 3/28/16 to 6/25/16
Evaluation period 6/27/16 to 7/25/16
Contracts Award notification of Phase II 8/25/16
Phase II 9/01/16 to 2/28/17
Request for submission of a full proposal does NOT guarantee AWARD selection

## Slide 36: Objectives of Contract
Develop prototypes:
Option 1: Produce Six (6) L-863(L-IR) fixtures to meet IR output of L-862 and photometric performance from EB67D.
Option 2: Produce Six (6) Self-contained IR only emitter with necessary optics to meet requirements of item 1 and include design to interface with current runway edge lighting system.
Option 3: Develop a method to activate only the IR emitter when needed for EFVS operations.

## Slide 37: Phase II Proposal
Volume I: TECHNICAL proposal (not to exceed 40 pages) should include:
  A Validation Plan
  Steps to develop:
    A FAA L-862(L) with an IR emitter and to ensure their compatibility with current EFVS
    A standalone IR emitter and to ensure their compatibility with current EFVS
Volume II: COST/FUNDING proposal
Cost and Cost proposals will be evaluated as acceptable or unacceptable only.

## Slide 38: Phase II Evaluation
4 Technical areas listed in order of decreasing importance:
  Technical Merit
  Utility to the FAA Airport Safety R&D program
  Team Competency and Experience
  Effective Plan for Project Completion

## Slide 39: Schedule

## Slide 40
Questions/Comments?

## Slide 41: RPD 151
By: Robert Bassey
Date: March 16, 2016

## Slide 42: RPD 151 – Visual Guidance
FY 2016 Accomplishments
Research Goals
Funding Requirements
Reduced Pilot Disorientation
Increase Surface Operations Safety
Need
Provide better visual cues to pilots to reduce the risk of incursion
 | FY 15 | FY 16 | FY 17 | FY 18
Funding Target ($000) | 2400 | 2400 | 1500 | 1520
Address issues impacting the use of LED lighting technology across the NAS and its impact on safe operations

## Slide 43
LED Lighted “X”
Research

## Slide 44: LED Lighted “X” Testing
Notes: Arms are approximately 15’ 9” long
9 light sources

## Slide 45: LED Lighted “X” Testing Overview
Photometrics
  Color (chromaticity) and Intensity (candela)
Performance Standards
  Appearance, Set-up, and Operation
Flight Testing - Incandescent and LED Lighted “X’s”
  Acquisition and Shape Recognition Distances (in nautical miles)
  Visibility
  Brightness
  Glare
Notes: We are testing the LED lighted X to the incandescent lighted X standards
Photometric Testing
comparative tests – LED and Incandescent
Color testing is complete
Certified by Intertek – February 2016
Performance Standards – Paragraph 3.3 in AC 150/5345-55
Test LED to L893 Performance Standards
All complete except:
  Measuring the color of the yellow X. It should be “aviation yellow.”
  Photometrics
    Appearance = light sources arranged in the shape of an X, light sources equally spaced, arms painted yellow on all sides, flash 2.5 seconds on/off, etc.
Set-Up = portable, set up in >5min on the runway
  Takes longer to set-up – not a deal breaker.
  All light sources are equally spaced, except two, located in the bottom left of the “X”
    Operation = fail safe protection, run 24 hrs on portable power supply, switch between day and night intensities
**The team plans to make recommendations to update the Performance Standards discussed in the AC**
- Examples – set-up time remove or change from 5 min – 10 min?; built in inclinometer (lighted), level (lighted), and photocell
Flight Testing
Day and Night VMC
“X’s” installed on the runway numbers as directed in the Operational Safety During Construction on Airports AC
Flight testing the LED to the conclusions derived from incandescent lighted “X” testing completed in the late 80s
  Acquisition distance – 5 nm both day and night
  Recognize shape – 1.5 nm both day and night
We are measuring beam spread – 15 degrees each side of runway centerline; vertical coverage from 0 – 10 degrees, at a range of 1.5 NM

## Slide 46: Flight Testing
Orlando Melbourne International Airport (MLB); Melbourne, Florida
Purdue University Airport (LAF); Lafayette, Indiana
Ohio State University Airport (OSU); Columbus, Ohio
Notes: Runway lighting configuration:;
Edge lights off at OSU and Purdue; on at MLB
Airports have various light pollution
Tested by students with various flight certificates (e.g. student pilot – commercial pilot)
Flight instructor flies the flight profile, subject pilot evaluates the “X”
Flight profile – 1,000 feet – straight in approach
  day = 10 nm from airport
  Night – 15 nm from airport

## Slide 47: Incandescent and LED Lighted “X’s” Day Flight - MLB
Notes: Picture only
Side-by side test – LED (left) Incandescent (right)
This picture was taken when we were on final to land on Runway 27L

## Slide 48: LED Lighted “X” Night Flight - MLB
Notes: I minute video clip.
Thoughts on having FIT take side-by-side (LED/Incnadescent) go-pro footage. They flight test on Tuesday? I think it would be good to show the group a side by side of the LED and incandescent lighted “X”.
LED lighted X:
Popped, was sharp and crisp.
Was “bright enough”
No glare issue
We could clearly recognize its shape

## Slide 49: Project Milestones and Schedule
Milestone | Completion Date
Performance Standards | March 2016
Photometric Testing | April 2016
Flight Testing | March 2016
Final Report | June 2016
Notes: Performance standards – all completed except measuring color of the yellow X
Photometrics – Chromaticity testing is complete; need to complete intensity testing

## Slide 50
LED Electrical Infrastructure
Research

## Slide 51: Issues resulting from LED implementation in the Current 6.6A Series Airfield Lighting System
Added complexity and cost to the LED fixture due to the addition of electronics to mimic the non-linear dimming curve of incandescent lighting.
Notes: Just to review…we’re looking at what the most efficient and effective infrastructure for LEDs.

## Slide 52: Architectures Tested
Notes: Examples of the vault centric and fixture centric architecture

## Slide 53: Roadmap Testing Phase
Alpha testing at FAATC, May 2015
  Integration including mixing of product
  Fixtures will be instrumented and monitored by FAA equipment to determine performance
  Identify any deficiencies, or adjustments to be made
Beta testing at PEGASAS Airport March, 2016
  Similar set up as alpha testing
  Large circuit
  Legacy mode will be available in case there is an issue with the circuit
Notes: Upcoming testing

## Slide 54: Purdue Airport Taxiway “C” (Beta Test Circuit)

## Slide 57: New Technologies
The FAA R&D Visual Guidance Program has continued to explore technologies to increase surface safety and reduce the rate of runway incursions
  A literature review report was completed in November, 2015
  One technology recommended in the report that is being considered for further study at the present time is addressable airfield signage

## Slide 58: Previous Addressable Sign Study

## Slide 59: Current LED Addressable Signage

## Slide 60: Potential Applications (cont.)

## Slide 61: Research Proposed
A comprehensive study is proposed to evaluate the human factors challenges and technical requirements for addressable signage
The outcome of this study will be recommendations for standards for addressable signage use and technical specifications

## Slide 62
Robert.Bassey@faa.gov
609-485-5816
www.airporttech.tc.faa.gov
Questions/Comments?