## Slide 1: Aviation Rumble Strip Project Update March 16, 2016

## Slide 2: Utilizing a Center of Excellence
  PEGASAS
Partnership to Enhance General Aviation Safety, Accessibility and Sustainability

## Slide 3: 2015 Purdue Airport Rumble Strip Test Site
Thermoplastic
Saw Cut
Temporary

## Slide 4
Temporary

## Slide 7: Saw Cut Options
Square Cut
Bevel Cut

## Slide 8: Thermoplastic
Easy to construct
Semi-intrusive
Permanent
Proven to withstand winter ops in roadway environment

## Slide 9
PEGASAS Test Configuration
Thermoplastic Sawcut Temporary

## Slide 10: Aircraft Used in Study
CESSNA 172
CIRRUS SR20
CESSNA 152
SKY ARROW
PIPER PA 34
CRJ-100ER
CESSNA 152
PIPER PA 28

## Slide 11: Acceleration Graph
Temporary
Saw Cut
Thermoplastic
Aircraft: Cessna 172 Speed:5 knots
Notes: bg

## Slide 12
2.805
2.739
2.63
Affects on Pilots and Airframe Rail-to-Seat Plots for 10 kts
Significant airframe acceleration must occur for pilot to feel rumble strip
Airframe affected by 2 to 3X the acceleration force felt by pilot, over time airframe manufacturers feel this may cause damage to the gears.
Seat
vs.
Rail

## Slide 13: April 2015 Durability Testing

## Slide 14: Tech Center Test Results
Day | Load Aircraft | Passes | Square Cut | Beveled | Temporary
Day 1 | 10k lbs. E190 | 1000 passes | Began crumbling at 500 passes | No change | No change
Day 2 | 15k lbs. CRJ-700 | 1000 passes | Continued crumbling | No change | No change
Day 3 | 30k lbs. 757-200 | 1000 passes | Heavily worn | No change | Sign of warn, but no damage
Day 4 | 45k lbs. 738/A321 | 500 passes | Heavily worn | No change | Connection point becoming loose
 | 60k lbs. 748/A380 | 10 passes | Heavily worn | No change | ~1/8” depression

## Slide 16: European Rumble Strip Study Deployed on Active Taxiway for 3 months at Southampton Intl Airport, England
19.7”
19.7”

## Slide 17: European Rumble Strip Study
Each segment 11.8” wide
39.4’ long
0.47” high
19.7”
19.7”
    Feedback invited from pilots (35 responses) and ground vehicle operators (10 reports)
    Pilots report rumble strips were discernible (varied by aircraft) but difficult to differentiate from other taxiway features (e.g., rough pavement)
      Half assessed impact as “excessive”
      Pilots did not recognize purpose and considered rumble strips a distraction
    Did not affect capacity
    Deemed ineffective for incursion prevention

## Slide 18: Our Evaluation Results

## Slide 19: Problems with Durability of 90 degree Saw Cut at KLAF and at NJ Tech Center
Saw Cut

## Slide 20: Constructability Challenges with 45 degree Bevel Saw Cut at KLAF and at NJ Tech Center
Saw Cut

## Slide 21: Thermoplastic
Easy to construct
Semi-intrusive
Permanent
Proven to withstand winter ops in roadway environment

## Slide 22: NOT on Airports! Rumble Strips were Damaged by Snowplows after First Snow and Were Subsequently Removed to Avoid FOD on Airfield at KLAF

## Slide 23: Thermoplastic has Problems with Durability

## Slide 24: Temporary Rumble Strips
Allows temporary installation
Interlocking joints
Segments: 13” wide, 36” long, ¾” high, 35 lbs
Can be installed by one person

## Slide 25: Conclusions
All Rumble Strip types evaluated, if installed permanently, may cause damage, with continual use, to the size of aircraft used in study.
Saw Cut Strip
  Durability of 90 degree
  Constructability with 45 degree bevel
Temporary Rumble Strips may be useful as a tactile warning to aircraft when used to identify a temporary change at an airport such as a construction areas etc.

## Slide 26
Questions/Comments?