## Slide 1: Pavement Design and Evaluation
RPA P5
REDAC Subcommittee on Airports
David R. Brill, P.E., Ph.D.
March 15, 2017

## Slide 2: RPA P5 – Pavement Design and Evaluation
Need
There is a need for advanced, computer-based pavement design & evaluation solutions to protect the FAA’s investment in airport pavement. The FAARFIELD program provides confidence that pavements will meet the required service life. Savings to the AIP will result from reduced construction costs and fewer runway closures.
Research Goals
Continue to update and modernize the FAARFIELD design software.
New ACN-PCN system of reporting airport pavement strength by FY17.
Incorporate top-down cracking mode in FAARFIELD rigid design by FY18.
Fully integrate FAARFIELD thickness design with LCCA procedures by FY22.
FY 2016-7 Accomplishments
Released FAARFIELD v. 1.4.
Test new FAARFIELD-based ACN-PCN method.
Tech Report: Flexible pavement new subgrade failure model.
Prototype new FAARFIELD GUI.
Funding Requirements
Project | Contract Funds ($K) |  | 
 | FY 2017 | FY 2018 | FY 2019
P5. Pavement Design and Evaluation | 1200 | 1190 | 1235
P5.1. Design Improvements | 750 | 740 | 870
P5.2. ACN-PCN Improvements | 250 | 225 | 135
P5.3. Analysis | 200 | 225 | 230

## Slide 3: AC 150/5320-6F & FAARFIELD 1.41
Released Nov. 10, 2016

## Slide 4: FAARFIELD 1.4 – Release Version

## Slide 5: FAARFIELD 1.4 – What’s New?
Completely revised flexible and rigid failure models based on current NAPTF full-scale test data.
Reduced excess stabilized base thickness requirement.
Improved, more accurate 3D finite element model.
Completely rewritten concrete overlay design procedure.
Automatically generates PDF design report.
Automated, software-based compaction criteria.
Updated aircraft library aligned with COMFAA 3.0.
Include non-airplane vehicles in library (ARFF vehicles, etc.)
Support for user-defined gear configurations.
Advanced, energy-based asphalt fatigue models.
All data files now stored in document directories.

## Slide 6: FAARFIELD 1.41 Design Comparisons
Paper for ASCE Intl. Conference on Highway Pavements & Airfield Technology, Phila., August 2017
FLEXIBLE PAVEMENTS
RIGID PAVEMENTS

## Slide 7: Technical Reports
Replacement of FAARFIELD Tandem Factors with CDF Methodology
October 2016
Documents changes to evaluation of tandem gear damage
Development of New Subgrade Failure Model for Flexible Pavements in FAARFIELD
In publication
Documents new FAARFIELD 1.41 design models

## Slide 8: FAARFIELD PCN Evaluation
Directly uses FAARFIELD structure and traffic list.
NO alpha factor, layer equivalency factors, top-of-base k, etc.
Eventual replacement for COMFAA 3.0 & support spreadsheets.

## Slide 9: Flowchart of PCN Calculation

## Slide 10: Legacy Fortran Libraries
Existing Fortran libraries are modified from original 1995 programs.
Still distributed by FAA under a software sharing agreement with Lawrence Livermore National Laboratory, the original NIKE3D developer.
Very significant limitations for .NET programming.
  Unmanaged code.
  Not under the control of .NET memory management services.
  May lead to memory conflicts or crashes at runtime.
  Obsolete data storage and retrieval methods.
  Few young programmers have knowledge of Fortran.

## Slide 11: FAARFIELD Calling Structure
REPLACED BY:
FAAMeshClassLib
Visual Basic.NET Class Library
New Visual Basic.NET Class Library to replace NIKE3D.dll
In Progress (FY18)

## Slide 12: GUI Modernization
Modernize the FAARFIELD graphical user interface (GUI).
  Job and section entry.
  Improved start-up screen.
  Improved screen re-sizing and appearance.
  Improved flow between screens.
  Rationalize data file structure.
  Remove program logic from GUI controls.
Activities:
  Draft framework – complete
  GUI prototype demo – June 2017

## Slide 13: Top-Down Cracking Mode (Rigid)
Current efforts are focused on artificial neural networks (ANN) for multi-slab model with curling.
Fast, accurate solutions within the defined problem space.
Grant to Iowa State U.
  P.I. Dr. Halil Ceylan
  2nd year of 3-year project.
Paper at 2017 TRB:
  Neural-Network Based Multiple-Slab Response Models for Top-Down Cracking Mode in Rigid Airport Pavements Subjected to Boeing B-777 Loading
ANN Development: Input Parameters

## Slide 14: Questions?