## Slide 1: RPA S9
Cape May Research Taxiway
REDAC March
Murphy Flynn
March 15, 2017

## Slide 2: RPA S9 Airport Research Taxiway
FY 2017 Planned Milestones
Research Goals
Funding Requirements
Conduct Airport Safety and Pavement Research Efforts in an Operational Environment, close to the Tech Center
Test bed for airport: signage marking, lighting, electrical infrastructure, safety and security sensors and pavement technologies.
Construction Completed – Spring 2017
Electrical Infrastructure Research Team Testing
Need
RPA S4 – Airport Research Taxiway | FY17 | FY18 | FY19
 | $ 350,000 | $ 100,000 | $ 100,000
The FAA's Research Taxiway provides researchers with a single site to design, test, evaluate, monitor, and report on the performance of state-of-the-art airport safety and pavement technologies on a continual basis.

## Slide 3: Project Scope
TW C
RW 14-32
Rehabilitation of 3,250 ft. of TW C between TW B and RW 10-28
  Paving and Lighting
Equip the TW with State of the Art Lighting Control System
Lighting Controls can be turned over to DRBA when FAA not conducting Research.

## Slide 4: Paving Layout
Legend
PG 76-22 Marshal P-410
PG 64-22 Marshall P-401
PG 64-22 Superpave P-401
WMA (PG 76-22) P-401
Stone Matrix Asphalt
NJ State Mix
Electrical Vault
Pavement Sensor Strips

## Slide 5: WWD Taxiway C Update
Memorandum of Agreement between FAA and Delaware River and Bay Authority (DRBA).
  November 15, 2010 through September 30, 2030.
Grants the FAA the “right to construct, operate and maintain Research Infrastructure” at Cape May County Airport (WWD) in Erma, NJ

## Slide 6: WWD Taxiway C Update
Paving completed December 2016
Lighting infrastructure completed February 2017
System commissioning February 24, 2017
Scheduled turnover to Government March 2017

## Slide 7: WWD Taxiway C Update
Standard TW Edge lights – Tied to DRBA cabinet for their control when FAA not on site

## Slide 8: WWD Taxiway C Update
Electrical Infrastructure designed with many-fold spare capacity to run parallel circuits independently.
Oversized electrical vault with room to add systems and devices
  Six standard L829 Regulators to power lighting systems

## Slide 9: WWD Taxiway C Update
No research light fixtures currently installed, cans in place for:
  In Pavement CL Lights
  Elevated RW Edge Lights
  Two CL Radii configurations at old RW 14-32 intersection
  Take Off Hold Lights
  Standard RW Entrance Lights
  Short Configuration RW Entrance Lights
  In Pavement RW Guard Lights
  Elevated RW Guard Lights
  TDZ Lights
  Clearance bar

## Slide 10: WWD Taxiway C Update
All field service panels have fiber- Ethernet to communicate directly back to vault – and 120 V outlets
  Allows sensors to be put in line to monitor circuits from multiple locations

## Slide 11: WWD Taxiway C Update
  Numerous empty sign pads for experimental signs.

## Slide 12: Safety Research Plans
Support Electrical Infrastructure Research Team (EIRT)
  Vault Centric LED Lighting Circuit Architecture
  Fixture Centric Architecture Research
    Currently being conducted at Purdue University
    Bring Research here for more access

## Slide 13: Safety Research Plans
Test Bed for Visual Guidance Research
  LED and other lighting innovations
  Signs and Paint Markings
Runway Surface Safety Research
  Friction:
    Evaluation of various pavement surfaces over time
    Testing of various devices
UAS - Currently an FAA approved test site

## Slide 14
Field Characterization Tests During Construction
  Characterize the base and asphalt concrete materials.
  Establish the baseline for the environmental effect tests
  Verify the binder grade of asphalt used in each mixture
Evaluated the uniformity of the pavement structure.
Pavement Research Plans

## Slide 15: Pavement Research Plans
Laboratory Characterization
  Measure the asphalt mixture properties such as the modulus, rutting resistance and cracking resistance using laboratory tests.
  Verify the binder grade of asphalt used in each mixture

## Slide 16: Pavement Research Plans
Investigate the effect of environment and aging on asphalt concrete
  Utilize HWD, PSPA and strain gauge response under HWD
Evaluate temperature effects on the HWD, PSPA and strain gauge response tests
  Develop temperature correction approaches to convert all test results to reference temperature.
Measure the temperature profile in asphalt concrete.
  Evaluate the influence of temperature profile on the strain gauge response.

## Slide 17: Pavement Research Plans
Field Core Aging Tests
  Evaluate the environmental effect on asphalt mixture properties such as the modulus, rutting resistance and cracking resistance using laboratory tests.
  Evaluate the environmental effect on asphalt binder using recovered binder from field cores.

## Slide 18: Cape May Research TW
Murphy Flynn
  Murphy.Flynn@faa.gov