## Slide 1: National Jet Fuels Combustion Program
Status Update
Mohan Gupta, Ph.D.
Asst. Chief Scientist
Office of Environment and Energy
Federal Aviation Administration
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 2: Objective: Streamline Fuel Approval Process
Specification Properties
Engine/APU Testing
Fit-For-Purpose Properties
Component/Rig/APU Testing
ASTM Research Report
ASTM Specification
TIER 1
TIER 2
TIER 3
TIER 4
ASTM D4054 Qualification Process
OEM Review
& Approval
ASTM Balloting
Process
~$500K, 500 gal
~$5,000K, 10,000+ gal
PRIMARY COST DRIVER

## Slide 3: Challenges
Challenges to Alternative Fuel Approval Process
  Cost/duration of fuel approval process
    Fuel quantities for rig/engine tests
  OEMs uncertainty over effects of novel fuel composition and chemistry on combustor operability

## Slide 4: ASTM D4054 Alternative Qualification Process
Specification Properties
Fit-For-Purpose Properties
ASTM Research Report
ASTM Specification
TIER 1
TIER 2
TIER 3
TIER 4
Primary FOMs
Other Rig/Engine Testing
OEM Review & Approval
ASTM Balloting Process

## Slide 5: Integrated Approach
An applied research program with near-term utility to support ASTM approval process – one of the Objectives of the National Alternative Jet Fuels R&D Strategy
Area # 7
Employ a number of both conventional and alternative jet fuels for screening, survey and detail testing and modeling.

## Slide 6: Year 1 Objectives
Spray Rig Testing
Advanced Combustion Testing
Referee Rig Testing
CFR Spray Model
CFR Chemistry Model
CFR Combustion Model
Bring rig tests on-line
Characterize sensitivities of Cat A fuel, Cat C fuel, and dodecane
Develop basic modeling approaches and demonstrate sensitivities to rig test fuels
Characterize flow quality and diagnostics
Demonstrate models can be integrated into common LES platform
D4054 FFP Data
Assess FOM:
LBO
Alt Relight
Cold Start of Candidate Fuels
OEM CFD and Spray Models and guidance for fuels testing
Enablers for future cost savings

## Slide 7
Year 1 Data Flow and Modeling Development
Area 1
Area 3
Advanced Combustion Testing
CFR Chemistry Model
CFR Combustion Model
Area 2
Area 4
Generate ignition delay and species data for Cat A and C fuels
Generate combustion data for Cat A and C fuels
Develop chemical kinetics models for Cat A and C fuels
Reduce kinetics model, develop advanced combustion models, and simulate turbulent combustion experiments
Spray Rig Testing
CFR Spray Model
D4054 FFP Data
Area 5
Generate spra data for Cat A and C fuel
Develop property-dependent spray model and perform LES of spray rigs
Referee Rig Testing
Area 6
Map rig characteristics, generate LBO data for Cat A fuels and selected and Cat C fuels
Area 5
D4054 FFP Data
Assess FOM:
LBO
Alt Relight
Cold Start of Candidate Fuels
OEM CFD and Spray Models and guidance for fuels testing
Enablers for future cost savings
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 8: Benefits
Streamlines current ASTM approval process
  Fewer rig/engine tests
    Eliminates duplicative OEM testing
  Reduces costs and accelerates schedule
  Increases throughput of new fuel approvals
  Help eliminate unsuitable fuels in early stage of fuel testing
Reduces fuel quantities required for approval
  Replace/reduce combustor/engine tests with rig tests/modeling
Reduces engine OEM risk/uncertainty
  Provides greater understanding of fuel chemistry effects on combustion
  Provides greater understanding of the performance of novel fuel chemistry
  OEM participation in development of tests and models
Improved industry modeling and design tools
  Supports compositionally-based fuel approvals
  Supports identification of acceptable fuel composition boundaries for future engine designs

## Slide 9: Program Success Criteria for the First Year
Demonstrate that one or more tests have sensitivity to a test fuel over a range of conditions that offer the potential of their being used as part of a methodology for simplifying the alternative fuel certification process
Demonstrate that a validated surrogate chemistry model can be developed that has the potential of being used to predict fuel-sensitive test results over a suitable range of conditions
Demonstrate a combustion modeling approach that can be integrated into an OEM’s procedures that offers the potential of being used to predict fuel effects on combustor operability and simplify the alternative fuel certification process
Program continuity depends upon meeting the First Year Program Success Criteria.

## Slide 10: Program Organizational Structure
Program Leadership
Mohan Gupta (FAA) and Mel Roquemore (AFRL)
Steering Committee
(Feds+OEMs+Research Team Leads+Med Colket)
Modeling-Data Validation and Integration
(in coordination with Med and Josh)
Modeling Working Group II (Areas 2, 4 and 5 PIs + Other Research Leads)
Success Criteria II
Testing Working Group I
(Areas 1, 3, 5, and 6 PIs + Other Research Leads)
Success Criteria I
Working Group III
(Will be formed later)
Success Criteria III
Area 7
Med Colket and Josh Heyne
One mid-month formal telecon individually with each WG
(and as often as needed)
One Month-end formal plenary telecon with both WGs
(and as often as needed)
Overall Program Direction and Guidance
Technical Coordination, Integration and Analysis
Subject-specific Ad hoc Subcommittees

## Slide 11: NJFCP - Timeline
Apr
Oct 27-30, 2014 MACCCR Meeting
Dec 3-4, 2014
Kickoff Meeting
Report on Fuels Survey & Screening
May 21-22, 2015
Semiannual Meeting (to be held at GE, Cincinnati): Progress towards meeting success criteria and adaptations needed going forward
Oct-end, 2015 Semiannual Meeting:
Status towards meeting success criteria
Nov-end, 2015:
Submission of first-year results and deliverables
Program continuity depends upon meeting the success criteria
Initial Program Duration
Jan
Feb
Mar
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Mid-month 2-hour telecon with each WG
Month-end 2-hour Plenary telecon
Feb
Mar
Progress Report
We are here
ASCENT and CAAFI Meetings
OEM input and feedback throughout the year

## Slide 12: Category A Fuels
Represent range of currently available fuel properties and compositions
  Worst case = high viscosity, high density, low H content
Inventory
(gal)
3180
3476
18295
Fuels have been sent out to all teams
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 13: Category C Fuels Prioritized
Highly unusual fuel – Neat Gevo ATJ-SPK – low Cetane (~15), highly biomodal, very flat boiling (~21 C)
Bimodal carbon distribution fuel – Aromatic front end – trimethyl benzene & C14 iso-paraffins (C14: T10=217, T90=234 C)
Low cetane number fuel – 50/50 or 60/40 blend of Gevo ATJ-SPK/Sasol IPK – low Cetane (~20-25), otherwise jet like carbon dist & distillation curve
Flat distillation curve fuel – C10 n-paraffins/iso-paraffins (T10=163, T90=167) – trimethyl benzene can be added to make fully-synthetic fuel (TMB 165 C)
High viscosity fuel – A blend including Amyris SIP
High cyclo-paraffin content fuel – Neat or higher blend of Virent HDO SK
Will employ tiered fuels evaluation approach
Will also test n-dodecane fuel to support modeling groups.
Currently, sending fuels to all testing teams
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 14
NJFCP Area Highlights: 1 of 2
Testing Working Group:
Area 1 Chemical Kinetic Studies (Hanson/Bowman): Ignition delay and speciation data collected for Cat A fuels; small differences observed for petroleum-based fuels above 1100K. Shifting to lower temperatures and alternative fuels
Area 3 Turbulent Combustion Experiments (Lieuwen): Developed system for rapid switching between fuels. Preparing for pre-screening tests to determine optimum tests conditions for fuel screening tests.
Area 5 Spray Measurements (Lucht): Diagnostic approaches established. Awaiting confirmation on fuel nozzle (done), operating conditions, and resolution of ITAR issues.
Area 6 Referee Rig Tests (Stouffer): Combustion instabilities mapped, fully engaged with OEMs, and undergoing rig shakedown. OEM Committee established to set preferred operating conditions for screening tests. Experimental refinements in progress.
14
14
Federal Aviation
Administration
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 15
NJFCP Area Highlights: 2 of 2
Modeling Working Group:
Area 2 Chemical Kinetic Modeling (Wang): Beta-version of hybrid kinetics mechanism developed for A-2 fuel, demonstrated pressure dependence and ability to reduce species for CFD. Validating model against rich side chemistry and product species.
Area 4: Fuel-Dependent CFD Modeling (Menon/Sankaran/Ihme): Example n-dodecane kinetics model reduced to 24 species and demonstrated application in LDI burner. Grid generated for referee rig. New combustion model developed. Awaiting kinetics model for A-2 fuel and boundary/inlet conditions.
  Area 5 Spray Modeling (Ihme): Working on development and implementation of non-ideal droplet evaporation, multicomponent evaporation using functional group-based approach (UNIFAC) and group contribution methods to determine vapor pressure and model verification. Next step: description of Cat-A evaporation.
15
15
Federal Aviation
Administration
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 16: Program Sponsors, Contributors, Performers and Industry Members
STEERING COMMITTEE
(Federal, OEMs, University PIs)
Guidance
Fed Gov’t
-FAA
-ARL
-AFRL
-NASA
-NIST
-DLA
-Navy
-DOE
-Funding
-Test Facilities
-Fuels
Industry
-Honeywell
-GE
-Pratt & Whitney
-Williams
-Rolls-Royce
-Fuel Producers
-Parker Hannifin
-Chem/Kinetics Modeling
-Engine Operability
-Fuel Evaluation Methodology
-Reduced cost
NJFCP
ASCENT Universities: GaTech, UDRI, UIUC, Stanford, Purdue, OSU Non-ASCENT: Princeton, UConn
Other Contributors:
NASA, AFRL, NIST, Army Lab, NRC Canada, DLR, Sandia Lab, OEMs
ASCENT Advisory Committee Members
(CAAFI, Boeing, Shell, Gevo)
Guidance
International: NRC Canada & DLR
A total of 34 entities
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015

## Slide 17: Industry/International Interaction and Involvement
Role of OEMs
OEMs are recipient of the outcomes of this program in terms of validated streamlined generic fuels testing and modeling capability for ASTM approval
Serve in the Program Steering Committee
Perform in-house research (testing and modeling) activities
Fuels Selection
Cost-share with ASCENT universities
Role of CAAFI and Fuel Industry
Participation through ASCENT Advisory Committee
Help the program on emerging alternate jet fuel types and their chemical composition to guide the program direction
Role of International Partners
NRC-Canada:
  Will conduct high altitude and fuel nozzle spray tests ($500K NRC investment)
  Provided cost-share to ASCENT universities
DLR: Will perform tests using the same/similar fuels. Participation will help to understand the delta and trends even though test devices used will be different.
National Jet Fuels Combustion Program
REDAC E&E Subcommittee Meeting
March 17, 2015