## Slide 1: Departure and Arrival Concepts to Reduce Noise
Presented To: REDAC E&E Subcommittee
By: Office of Environment & Energy (AEE)
Joe DiPardo, AEE-100 Chris Dorbian, AEE-4
Date: August 1, 2017

## Slide 2: Current Challenge – Noise
Despite traffic growth, community noise exposure has decreased by a factor of 20
Yet, implementation of precision aircraft navigation over last few years has been accompanied by increased airport community concerns regarding noise
A/C already much quieter – what can be done operationally?
AEE is working to ensure that airspace planners have the best tools and toolbox to enable low noise procedures
Image Source: Massport

## Slide 3: Multiple Efforts Underway to Develop Noise-Mitigating Operational Procedures
FAA–Massport MOU (BOS case study; FAA collaborative effort on Noise)
“Toolbox” of procedures & procedural changes to mitigate noise
ASCENT-23 Developed analytical framework for assessing operational procedures
AEDT Development efforts underway to improve modeling capabilities
Industry/Gov’t. Collaboration
Potential industry collaboration
Potential NASA Research Transition Team (RTT)
Airport Technology Research Projects (ARP-AEE collaboration)
Flight Management System enhancements (CLEEN)
ATO Mission Support Services (AJV) “Low Altitude PBN” Research (performed by MITRE)
MIT
Notes: MOU establishes a framework for cooperation between Massport & FAA to explore operational changes to mitigate noise impacts
This is a BOS specific case study; Massport is providing funding to MIT (& HMMH) to help them with this
FAA side of this MOU is a collaborative effort across LOBs to provide expertise and to evaluate proposed changes
Massport has enlisted MIT; basis for that is AEE work w/MIT to develop analytical framework for assessing operational procs under ASCENT-23
RTTs ensure NASA research needed for NextGen is identified, conducted, and effectively transferred to the FAA
FMS – May be opportunity there to leverage FMS development work to pursue noise benefit, and may also be a necessity as we look at procs to incorporate FMS considerations, and CLEEN is a mechanism to do that

## Slide 4: Limitations of Industry-Standard Noise Analysis Method
Current noise analysis method: Noise-Power-Distance (NPD) based computations (AEDT, INM)
  Requires thrust and distance interpolation from flight test data
  Crude accounting of noise effects for different flap/gear settings & operational procedures
Two options for improving noise analysis method:
  Expand database of NPD curves to include advanced configuration/thrust settings
  Compute noise directly using a physics-based approach
Chart: Noise Power Distance (NPD) Curves GE CF6-50 (Airbus A300)
| 200 | 400 | 630 | 1000 | 2000 | 4000 | 6300 | 10000 | 16000 | 25000
40,000lb Departure | 106.8 | 102.9 | 100.1 | 97.1 | 92 | 85.8 | 81 | 75.9 | 69.9 | 63.4
25,000lb Departure | 103.7 | 99.3 | 96.1 | 92.7 | 87.1 | 80.6 | 75.8 | 70.5 | 64.3 | 57.5
10,000lb Arrival | 99.9 | 95 | 91.4 | 87.5 | 81.3 | 74.6 | 69.7 | 64.2 | 57.7 | 50.7
25,000lb Arrival | 103.7 | 99.3 | 96.1 | 92.7 | 87.1 | 80.6 | 75.8 | 70.5 | 64.3 | 57.5
Physics-Based Noise Computation Method

## Slide 5: Physics-Based Noise Modeling Framework
Notes: Physics-Based Noise Analysis Framework

## Slide 6
Concepts for Mitigating Aviation Noise Impacts
Moving Noise Away from People
Changing the Noise Signature
Dispersing Noise

## Slide 7: Moving Noise Away from People

## Slide 8
Runway 22R Departures: 2010-2015
2010

## Slide 9
Runway 22R Departures: 2010-2015
2015

## Slide 10: Runway 22R and 22L Departure Procedure Concepts
Reduced separation with Rwy 27 arrival flow
Early turn after takeoff to reduce noise at Castle Island and surrounding areas

## Slide 11
22R, 22L, and 15R Departure Tracks
*2,100ft (15R dep)
†2,900ft (15R dep)
*2,500ft (22R dep)
†4,000ft (22R dep)
* Lowest Observed A320 Departure at FOXXX
† Median A320 Departure at FOXXX
ILS Altitude: 950’

## Slide 12: 22R/22L Departure Spacing with 27 Arrivals (Early Turn) and 15R Departure Waypoint Relocation
22R Early turn:
  Initial turn at 500’ AGL
  Direct-to initial waypoint located on target departure corridor
Runway 15R Departure Fix:
  Current procedure uses same departure fix as 22R departures (FOXXX)
  Potential benefit from changing departures to use fix offset from Hull

## Slide 13: Noise Exposure: 22R/22L Early Turn
60
60
60
60
60
60
65
65
65
65
70
70
70
60
60
60
60
60
60
65
65
65
65
70
70
70
Baseline Flight Track Baseline Noise Contours Early Turn Flight Track Early Turn Noise Contours
 | 60dB | 65dB | 70dB
Baseline | 36,807 | 11,698 | 2,649
Early Turn | 26,821 | 6,517 | 510
Difference | 9,986 | 5,181 | 2,139
22R/22L Early Turn and Waypoint Relocation
Aircraft: B737-800
Metric: LAMAX
Noise Model: AEDT
Population Exposure

## Slide 14: Discussion Points with ATO
Reduced procedural separation with 27 arrivals
  Procedural separation requirements?
  Early turn option when 27 arrivals not in use
  Multiple SIDs for use in varying runway configurations
    Procedural deconfliction requirements
Implementation issues
  Minimum turn altitude?
  ARINC 424 leg types to best capture narrowbody & heavy departures
    Track to fix (TF), Course to fix (CF), Direct to Fix (DF)
Process for new waypoint definition

## Slide 15: Runway 4R Arrivals: 2010-2015
2010

## Slide 16
2015
Runway 4R Arrivals: 2010-2015

## Slide 17: Runway 4R Arrival Noise Mitigations
Standard steep approaches
2-segment steep approaches
Late turn to final
  RNAV (Lighthouse-like approach paths)
  RNP(Canarsie-like approach paths)
Overflight of areas with high ambient noise
– (i.e. Expressway approach)
Milton

## Slide 18: 3° and 3.77° Continuous Descent Approach Comparison
BADA-4 model indicates that steeper glideslopes may be feasible for some aircraft types
Feedback from operators: Airbus aircraft in planned descent autoflight mode cannot exceed 3.77° glideslope angle
B757-200 Steep Approach
Significant Concerns from Airline Technical Pilots and ATC for Operational Feasibility

## Slide 19: Two-Segment Approach Concept
B757-200 Two Segment Steep Approaches
Significant Concerns from Airline Technical Pilots and ATC for Operational Feasibility

## Slide 20: Changing the Noise Signature

## Slide 21: Runway 33L Departures: 2010-2015
2010

## Slide 22
2015
Runway 33L Departures: 2010-2015

## Slide 23: Standard Departure Definition
Standard departure procedures vary by airline
Typical profile includes thrust reduction at 1,000’ AGL followed by an acceleration to 250 kt climb speed and flap retraction

## Slide 24: Increasing Speed Causes Increased Airframe Noise
As speed increases, airframe noise becomes as loud or louder than engine noise
250 KTAS
220 KTAS
190 KTAS
160 KTAS
Airframe Louder
Engine Louder
Engine Noise Dominates (Low Speed)
Airframe Noise Dominates (High Speed)

## Slide 25: Delayed Acceleration Climbs
Thrust reduction at 1,000’ AGL followed by an acceleration to 200 kt or 220 kt climb speed and appropriate flap retraction secondary acceleration at TBD altitude

## Slide 26: 737-800: Delayed Acceleration Climb – 180 knots
Aircraft | B737-800
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 33L: Maintain Standard Climb Thrust & 180 KIAS to 10,000’
Population Exposure
Preliminary
 | 60dB | 65dB | 70dB
Standard Departure | 237,952 | 105,869 | 38,599
Delayed Acceleration | 172,598 | 59,392 | 24,025
Difference | 65,354 | 46,477 | 14,574

## Slide 27
Aircraft | B737-800
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 33L: Maintain Standard Climb Thrust & 200 KIAS to 10,000’
Population Exposure
Preliminary
 | 60dB | 65dB | 70dB
Standard Departure | 237,952 | 105,869 | 38,599
Delayed Acceleration | 169,124 | 66,585 | 26,811
Difference | 68,828 | 39,285 | 11,788
737-800: Delayed Acceleration Climb – 200 knots

## Slide 28
Aircraft | B737-800
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 33L: Maintain Standard Climb Thrust & 220 KIAS to 10,000’
Population Exposure
Preliminary
 | 60dB | 65dB | 70dB
Standard Departure | 237,952 | 105,869 | 38,599
Delayed Acceleration | 190,128 | 75,469 | 28,239
Difference | 47,824 | 30,401 | 10,359
737-800: Delayed Acceleration Climb – 220 knots

## Slide 29
Aircraft | B737-800
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 33L: Maintain Standard Climb Thrust & 240 KIAS to 10,000’
Population Exposure
Preliminary
 | 60dB | 65dB | 70dB
Standard Departure | 237,952 | 105,869 | 38,599
Delayed Acceleration | 220,781 | 91,525 | 31,007
Difference | 17,171 | 14,345 | 7,592
737-800: Delayed Acceleration Climb – 240 knots

## Slide 30: Preliminary Fuel Burn and Time Impact
Reduced speed climb profiles impact total trip fuel burn and flight time
Magnitude varies by speed and aircraft type
 | B738 |  | E170 |  | B773 | 
Climb Speed | Fuel Burn Increase (kg) | Time Increase (s) | Fuel Burn Increase (kg) | Time Increase (s) | Fuel Burn Increase (kg) | Time Increase (s)
180 kts | 141 | 121 | 55 | 92 | 674 | 178
200 kts | 54 | 65 | 12 | 43 | 321 | 107
220 kts | 21 | 30 | 4 | 22 | 160 | 52
240 kts | 4 | 8 | 1 | 6 | 32 | 12
Preliminary: Do Not Distribute

## Slide 31: Discussion Points with ATO
Implications and precedent for speed restrictions on RNAV SIDs
Speed restriction on SID vs. ATC-cleared speed restriction
Questions:
  Airspace conflicts given steeper climbs
  Altitude limit on SIDs (current 5000’)
  What should altitude limit for speed constraint be?

## Slide 32: Dispersing Noise

## Slide 33: Runway 33L Departures: 2010-2015
2015
Using Open SIDs to Re-introduce Dispersion
2010
What were design constraints on existing RNAV SID?

## Slide 34: Introducing Open SID Concept
Open SIDs are RNAV departure procedures that allow for embedded ATC radar vector segments.
– Vectoring can be used to guide an aircraft to join an RNAV track, remove an aircraft from an RNAV track, or a combination of both.
Open SIDs were authorized by an FAA memo signed in 2015.
2,000 foot turn
4,000 foot turn

## Slide 35: Discussion Points with ATO
Compatibility with current Open SID procedures
  CLT procedures
  Other PBN SID examples
    i.e. LAX ORCKA1
Options for initiating direct-to
  Altitude
    Precedent/concerns for direct-to on altitude
  Controller vectors
  Other
Method for maintaining procedural separation (e.g. Rwy27 departures) under Open SID
Other methods for introducing track dispersion using PBN?

## Slide 36: Current Status of FAA Noise Research

## Slide 37: Extensive FAA Coordination
Monthly “Noise Operations Research Meeting” to coordinate activities
  Reps from AEE, AJV, ANG, ARP, AVS
Short Term Initiative on Noise (shared across FAA LOBs/SOs)
ATO input on FAA-Massport MOU coming in from local facilities, New England Region (ANE), and FAA HQ (AJV, AFS, ARP, etc.)

## Slide 38: Industry Collaboration - UPS Visit
FAA/MIT visited UPS Louisville facility in July
UPS reviewed two of their projects:
  CDA developed and now in regular operation at Sacramento Mather Airport  3-7 dB reduction in target area 10 miles from the airport
  Trial of dual-segment steeper approaches at Cologne Bonn Airport  observed benefit on the order of 1 dB, though some question of the reliability of their noise measurements
~3.5 hours in simulator, during which MIT flew many of the Massport concepts
MIT can run sim trajectory data through noise model – use it to validate their flight profile generator
UPS offered to fly additional procedures if needed
UPS also looking into sharing noise measurement data for use in developing relationships between noise footprint and speed/flap/slat settings
  Potentially reach out to Boeing for validation
Notes: Representatives from multiple FAA offices (AEE, AJV, ANG, AFS) traveled with the MIT researches to meet with three of UPS's chief test pilots

## Slide 39: Next Steps
Continue to explore operational concepts with the potential to reduce noise
Work with ATO/ARP/AVS to identify/mitigate implementation barriers and constraints
Determine path forward for deploying concepts and integrating noise considerations into ATC / pilot decision-making, leveraging research and noise evaluation framework

## Slide 40: Backup Slides

## Slide 41: Solution set could be defined by type of noise impact and density of operations
 | Noise exposure due to flight concentration | Noise exposure due to “off-peak” operations
Potential Noise Mitigation |  | 
“Equitable” distribution (fanning, respite, etc.)
Airspace Planning
Change high density operational procedures (limited tools in toolbox)
Sound Insulation / Land Use Planning
Operating Restrictions
Change low density operational procedures (more tools in toolbox)
Is it possible to integrate noise considerations into ATC / pilot decision-making?

## Slide 42: 15R Waypoint Relocation
15R Departure Waypoint Relocation
Aircraft: B737-800
Metric: LAMAX
Noise Model: AEDT
 | 60dB | 65dB | 70dB
Baseline | 14,367 | 1,765 | 84
Early Turn | 13,140 | 1,781 | 147
Difference | 1,227 | -16 | -63
Population Exposure

## Slide 43: Limitations in the Design of Steep Approaches
According to JetBlue pilots, the Airbus A320 FMS will also not allow for the computation of VNAV paths that are steeper than 3.77°
According to TERPS, the following are the standard maximum approach angles authorized on a final approach segment:
Precision Approach:
Aircraft Approach Category Maximum Angle
C D
3.60°
3.10°
Non-Precision Approach:
Aircraft Approach Category
Maximum Angle
C D
3.77°
3.50°

## Slide 44: Safety Concerns - High-Energy Approaches
Runway Excursions
Figure source: The Boeing Company http://www.boeing.com/resources/boeingdotcom/company/about_bca/pdf/statsum.pdf

## Slide 45
Aircraft | B777-300
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 33L: Maintain Standard Climb Thrust & 220 KIAS to 10,000’
Population Exposure
Preliminary
 | 60dB | 65dB | 70dB
Standard Departure | 455,746 | 275,879 | 118,685
Delayed Acceleration | 437,415 | 262,310 | 105,182
Difference | 18,331 | 13,569 | 13,502
777-300: Delayed Acceleration Climb – 220 knots

## Slide 46
Aircraft | E-170
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 33L: Maintain Standard Climb Thrust & 220 KIAS to 10,000’
Population Exposure
Preliminary
 | 60dB | 65dB | 70dB
Standard Departure | 147,222 | 58,441 | 10,437
Delayed Acceleration | 97,728 | 33,306 | 9,298
Difference | 49,493 | 25,135 | 1,139
E-170: Delayed Acceleration Climb – 220 knots

## Slide 47: Runway 27 Departures: 2010-2015
2010

## Slide 48: Runway 27 Departures: 2010-2015
2015

## Slide 49: Delayed Acceleration Climb – 200 knots
Aircraft | B737-800
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 27: Maintain Standard Climb Thrust & 200 KIAS to 10,000’
Population Exposure
 | 60dB | 65dB | 70dB
Standard Departure | 200,576 | 102,274 | 37,078
Delayed Acceleration | 181,206 | 67,635 | 14,375
Difference | 19,370 | 34,639 | 22,703
Preliminary

## Slide 50
Aircraft | B737-800
Metric | LA,MAX
Noise Model | ANOPP
Notes | Runway 27: Maintain Standard Climb Thrust & 220 KIAS to 10,000’
Population Exposure
 | 60dB | 65dB | 70dB
Standard Departure | 200,576 | 102,274 | 37,078
Delayed Acceleration | 187,400 | 76,261 | 21,066
Difference | 13,177 | 26,014 | 16,011
Preliminary
Delayed Acceleration Climb – 220 knots

## Slide 51: AJV Low Altitude PBN Research
AEE is monitoring and coordinating with AJV project being conducted by MITRE
Site-specific concept development using near-term candidate concepts (primarily dispersion techniques)
Also exploring applicability of Equivalent Lateral Spacing Operations (ELSO) standard for noise dispersal (ATR funded)
  Examine operational scenarios for ELSO
  Develop process for identifying noise-optimal headings
  Assess noise, fuel, emissions, and throughput tradeoffs
Source: MITRE CAASD