## Slide 1: Aircraft Engine Particulate Matter: Measurement and Modeling

## Slide 2: Outline
Background
Research efforts on nvPM number size distribution and formation in gas turbine engines
Research efforts on PM modeling from commercial aircraft
Discussion on emissions from new entrants

## Slide 3: Impact of Emissions on Surface Air Quality
Fuel composition and engine design determine emissions
Atmospheric transformation, dispersion and removal determine pollutant concentration
Tank-to-Wake Actual Combustion Emissions
CO2 + H2O + NOX + SOX + soot + CO + HC + N2 + O2
Fuel: CnHm + S
N2 + O2
Air:
Volatile PM
Non-volatile PM

## Slide 4: PM2.5 vs UFP
PM2.5 (particles less than 2.5µm in diameter) referred to as “fine” particles are believed to pose the greatest health risks.
Aircraft engines produce particles of less than 2.5µm in diameter that are solid at the exit plane (non-volatile particulate matter or nvPM).
Aircraft contribution to PM2.5 on a mass basis is very small. However, particles of aviation origin are also smaller in size and belong to the class of “Ultrafine” Particles (UFP) that may be more harmful than “fine” particles.
Emitted UFP mass and number may be relevant to quantifying health consequences.
Notes: It is well known that there is no PM standard for aircraft engines. The first order approximation is used to estimate PM mass concentrations from certification smoke number measurements. It should be noted that the smoke number standard was developed originally as a visibility standard.

## Slide 5
Air Quality – Measurements versus Modeling
Schematic presentation of emissions, dispersion, concentrations and impacts with their interaction at airport level (graphic from CAEP/10-WP/54 ISG White Paper on Air Quality)
Avalable at: http://www.icao.int/environmental-protection/Pages/env2016.aspx

## Slide 6: Air Quality Impacts of Aviation - in Perspective 1
Individual airport-attributable PM2.5 contributions compared to all-source contributions as a function of airport operations
Each dot represents one of the top 66 U.S. airports
Dotted line shows the % of airport-attributable PM2.5 compared to total PM2.5 from all sources
All U.S. airports contribute less than 1% of the ambient PM2.5 from all sources
Source:
Boone, S. S. Penn, J. Levy and S. Arunachalam (2015). Calculation of sensitivity coefficients for individual airport emissions in the continental United States using CMAQ-DDM3D/PM, In Proceedings of the 34th International Technical Meeting on Air Pollution, Montpellier, France, May 2015.

## Slide 7: Air Quality Impacts of Aviation - in Perspective 2
Total annual AQ impacts from combustion emissions in U.S.
Sources:
Dedoussi and Barrett, “Air pollution and early deaths in the United States. Part II: Attribution of PM2.5 exposure to emissions species, time, location and sector,” Atmospheric Environment 99 (2014). http://dx.doi.org/10.1016/j.atmosenv.2014.10.033
Yim et al., “Global, regional and local health impacts of civil aviation emissions,” Environ. Res. Lett. 10 (2015). doi:10.1088/1748-9326/10/3/034001
* Note the aviation emissions are based on the LTO cycle and are an estimate for the US. The MIT research group calculates that North America LTO emissions result in 650 premature mortalities when accounting for both PM and ozone. Including full flight emissions results in 1,500 premature mortalities for North America and 16,000 premature mortalities globally (uncertainty range is 8,300–24,000).

## Slide 8: Source Characterization
Non-volatile Particulate Matter (nvPM): Emitted particles that exist at gas turbine engine exhaust nozzle exit plane that do not volatilise when heated to a temperature of 350°C.
Characterization of nvPM mass and number emissions
Size distribution

## Slide 9
All combustion particles are less than 0.1 microns (less than 100nm)
nvPM particles are bigger than vPM particles.
EI nvPM Mass from 1-400mg/kg (0.001-0.4g/kg)
For comparison EI NOX 5-70g/kg
But nvPM number 5*1013 – 5*1015 #/kg
Except on lean burn which is at atmospheric level of number (note equivalent to 1010 to 1011)
Smoke measurement deemed outdated

## Slide 10: Technology Effects on nvPM Mass and Number
EIMass and EINumber vs. Thrust for two modern combustors
Power
No Landing Takeoff (LTO) nvPM Standard

## Slide 11: By Contrast, NOX is Well Behaved
EINOx vs. Thrust for a Modern Rich Burn Combustor
Impact of engine NOX standards

## Slide 12: nvPM Standard: Reduction at Source
CAEP/10 agreed to the inaugural engine nvPM Certification Requirement and nvPM Emissions Standard
CAEP/10 Certification Requirement
  Standardized nvPM Measurement System
  New Appendix 7 to Annex 16 Vol. II
Engine nvPM Emissions Standard
  CAEP/10 Standard based on smoke visibility limit
  New Chapter 4 to Annex 16 Vol. II

## Slide 13: The CAEP/10 nvPM Standard Regulatory Level
Visible Exhaust Plume
Invisible Exhaust Plume

## Slide 14
CAEP/11 nvPM Remits
Provide representative engine data for assessing the nvPM emissions standard for mass and number regarding turbofan/turbojet engines ≥26.7kN by February 2017.
Provide recommendations on technology responses, stringency options and applicability to CAEP Steering Group 2017.
Develop an aircraft engine based LTO nvPM mass and number standard for turbofan/turbojet engines ≥26.7kN.
Investigation the possible replacement of the smoke number standard for engine categories ≥26.7kN and other engine categories <26.7kN.
Develop improved nvPM model inputs to both local air quality models

## Slide 15
CAEP/11 LTO Based nvPM Mass and Number Standard Tasks
Full Standard Setting Process in CAEP/11:
  Develop metric system
  Develop stringency options
  Develop technology response
  Conduct cost effectiveness analyses
  Determine LTO-based nvPM mass and number regulatory levels
Refine and finalize corrections for ambient conditions, fuel sensitivity and engine-to-engine variability
Refine steps to replace SN standard with nvPM mass and number standard based on CAEP/10 nvPM standard

## Slide 16
Data from Representative Engines
Engine Tests
  21 of the 24+2 representative engines have been tested
  Multiple Engine Tests on 7 engine types
Provided funding for 6 engine tests
Data from 21 types and 58 thrust variants have been made available to CAEP in agreed upon format
  Two more engines will be reported shortly
  Alternative approaches for three engines
  Minimal impact of missing engines on the metric systems

## Slide 17: nvPM Data Update
nvPM Values Database includes 21 Engines with 58 thrust variants
Chart Showing Large Variation in LTO nvPM Mass Data of Production Engines
Chart Showing Large Variation in LTO
nvPM Number Data of Production Engines
LTO nvPM Mass
LTO nvPM Number

## Slide 18
Ambient Conditions Corrections
Provided funding for nvPM measurements during a NASA rig test
  Not a commercial combustor but an N+3 Technology
  Both cruise and sea level static conditions simulated
Provided funding – GE annular rig test
  Commercial combustor
  A large matrix of test conditions simulated
  Initial ambient conditions correction function for both nvPM mass and number developed.
  Being evaluated by other engine manufacturers
Qualitatively similar results from the NASA Lean Direct Injection (LDI) combustor

## Slide 19
Fuel Sensitivity Corrections
Swiss Federal Office of Civil Aviation (FOCA) funded three tests on fuel sensitivity
  CFM commercial engine
  Fuel hydrogen content spanned the cert fuel spec range
NASA/ DLR Emission and Climate Impact of Alternative Fuels Experiment (ECLIF) Data
  On-wing IAE Engine
  Wider range of fuel hydrogen content
Provided funding for a consistent data analysis
Initial fuel sensitivity correction is in place and refinement is in progress

## Slide 20
Engine-to-Engine Variability – Development of Characteristic Value
FAA provided funding for a test of 25 production engines of the same type
A number of engines have finished testing
Data analysis is in progress
Plan to complete by Q4, 2017

## Slide 21
nvPM Modeling Inputs to Inventory Models
WG3/PMTG has reached initial agreement to replace FOA3 with a new method: Smoke COrrelation for Particle Estimation – CAEP11 (SCOPE11)
  Based on about 1400 Smoke Number and nvPM Mass Concentration from the representative engine tests
  ICAO Doc 9989 will be updated with this method
Supported the development of the cruise nvPM model
  nvPM mass emissions could be modeled with the proposed number
  nvPM number emissions will also use a recommended method.

## Slide 22
Technology Standards for Engine nvPM Emissions: Summary
Major Milestone: Visibility-based nvPM standard and certification requirement agreed to at CAEP10 meeting.
Progress is being made toward the development of nvPM mass and number standards
May need additional work on refining ambient conditions corrections
Impact of alternative fuels on nvPM emissions need to be quantified

## Slide 23: Ambient Monitoring and Source Attribution
Near Airport Source Attribution
Characterization of PM mass, number and Size Distribution
Source Attribution to a Sector
Combination of Measurement and Plume Modeling

## Slide 24: ASCENT 18: Monitoring and Modeling
Monitoring Plan at Boston Logan International Airport with high resolution instruments
Plume Modeling and Statistical Analysis
Source Attribution

## Slide 25
High resolution fast response mass instrument
7 nm D50 Condensation Particle Counter

## Slide 26
PM Modeling Scales
global
regional
airport
operation

## Slide 27: PM Modeling Framework for Commercial Aircraft
Air Quality Modeling
Exposure
Aviation Emissions
Non-Aviation Emissions
Weather
Population
Health Impacts
Concentration-Response Functions
Valuation Functions
Pollutant Distribution
Benefits and Costs
Local
NAS
Global
Plume
CMAQ
Geos Chem
Diff. Toxicity
A18
A19
A20

## Slide 28
ASCENT 20: AIRPORT LEVEL and NAS WIDE
Community Multiscale Air Quality (CMAQ) Model:
  Airport Level
  nvPM and vPM
  Total PM2.5 and UFP Mass for Health Impacts
  PM2.5 and UFP number and Size Distribution

## Slide 29
ASCENT 20: AIRPORT LEVEL and NAS WIDE
Airport-based emissions: U.S. airport total fuel burn and emissions for year 2005 and estimated the total contribution from the top 66, 100, 150, 200 and 300 airports relative to all U.S. airports fuel burn
Top 300 airports cover ~97% of the U.S. aviation fuel burn
Number concentrations of UFP at major airports in North America were simulated by CMAQ
Increase in nitrate PM (secondary vPM) due to NOX from LTO emissions in the downwind areas of airports – Preliminary Result

## Slide 30
ASCENT 19: NAS WIDE and GLOBAL
Impact of background Emissions and Uncertainty
Total PM Mass
  LTO
  Full Flight

## Slide 31: Background Ammonia
Background ammonia concentrations peak in India and China

## Slide 32: Aviation Surface PM2.5: LTO and Full Flight
LTO
Full Flight

## Slide 33
Ambient PM Monitoring and Modeling: Summary
Systematic source attribution study is in progress
  Combines monitoring and modeling
Airport and NAS wide aviation induced PM2.5 and UFP mass, number and size distribution being addressed using CMAQ
The uncertainties in aviation induced PM2.5 and UFP are being investigated using global models

## Slide 34: New Entrants for Commercial Aviation
Unmanned Aerial Vehicles
  Small Gasoline Engines
  Battery Operated
Commercial Space – Rocket Emissions
  May be a significant source of PM

## Slide 35
Engine Type | Fuel | Max Rated Thrust | Engine Emissions |  |  |  |  |  | Aircraft |  | 
 |  |  | Fuel Venting | SN | HC | CO | NOx | nvPM | Examples | Fuel Venting | CO2
Turboprop (TP) | Av Gas/ Jet A | > 1,000kW |  |  |  |  |  |  |  |  | MTOW over 8,618kg
Turbofan(TF)/ Turbojet (T3, T8) | Jet A | < 26.7kN |  |  |  |  |  |  |  |  | MTOW over 5,700kg
 | Jet A | > 26.7kN |  |  |  |  |  |  |  |  | 
Supersonic Transport (TSS) | Jet A | > 26.7kN |  |  |  |  |  |  |  |  | 
Current Aviation Emission Regulations
(40 CFR Part 87/14 CFR Part 34 & Annex 16 Volumes II + III)

## Slide 36: PM emissions from Rockets
Differential emission indices DEI X with respect to: (a) particle number, (b) surface area, and (c) mass.
The points represent the average of four encounters, while the curves are lognormal fits to the data.
From Schmid et al., 2003.

## Slide 37: PM emissions from Commercial Rockets
Very basic assumptions indicate that rocket emissions are approaching that of aviation with even moderate growth
Nature of prior work and assumption leave large uncertainties in impact estimates
Possible future growth: need better estimates and more quantitative analysis

## Slide 38
QUESTIONS?

## Slide 39
S. Daniel Jacob, Ph.D.
Emissions Division
Federal Aviation Administration Office of Environment and Energy
Email: daniel.jacob@faa.gov