## Slide 1: Alternative Jet Fuels Testing Efforts
Presented to: REDAC Subcommittee on Environment
By: Cecilia Shaw, Nate Brown and Levent Ileri
Office of Environment & Energy
Federal Aviation Administration
Date: August 3, 2017
Notes: We work with many different stakeholders including some you met with this morning
Govt. agencies
Businesses
Universities
U.S. Vision
Alternative Jet Fuels must be “drop-in”, have equivalent safety and better environmental performance than petroleum Jet fuel
Enable all possible fuels that meet criteria
Government role to address key barriers
Work through Public-Private Partnerships
Fund University research
Address the whole supply chain
Leverage expertise and resources of other government agencies and other countries
Aviation should be a lead user of alternative fuels

## Slide 2: FAA Alternative Jet Fuel Activities
Testing
  Support Cert/Qual testing
  Improve Cert/Qual process (NJFCP)
  Emissions measurements
Analysis
  Environmental sustainability
  Techno-economic analysis
  Future supply
Coordination
  Interagency
  Public-Private
  State & Regional
  International
Notes: Areas of support

## Slide 3: Status of Alternative Jet Fuel Approvals
  Since 2009 five fuels included in the ASTM International alternative jet fuel specification (D7566)
Notes:   5 fuels are included in the ASTM International alternative jet fuel specification (D7566):
    2009 - Fischer-Tropsch Synthetic Paraffinic Kerosene(FT-SPK)
    2011 - Hydroprocessed Esters and Fatty Acids (HEFA)
    2014 - Synthesized Iso-Paraffinic fuels (SIP)
    2015 - Fischer-Tropsch Synthetic Kerosene with Aromatics (FT-SKA)
    2016 - Alcohol-to-Jet (ATJ-SPK)
  6 fuels are currently undergoing evaluation and additional fuels will be evaluated in the future

## Slide 4: Alternative Jet Fuel Testing
ASTM International manages jet fuel specification
FAA supports the evaluation of alternative jet fuels
Support ASTM D4054 certification & qualification testing activities to develop data for new approvals
OEM review process
Data gathering & analysis
Understanding correlation
between fuel properties
and combustor operability
Notes: 1) Near term effort to Support ASTM D4054 testing activities to enable development of data for approvals
  BAA/SEMRS/CLEEN
    Honeywell APU testing of 7 fuels underway
  ASCENT Project 31
    IHI BB oil (similar to HEFA) will start testing in 2018
2) Support for Research Report Review & Coordination
  Via CLEEN
  Support organized approach to fuels in ASTM pipeline
  Boeing, GE, Honeywell, P&W, RR and SWRi
3) Data Gathering
  Alternative Jet Fuel Test Data Library (ASCENT A33) -- focus on creating a library to catalogue the test data that has and will be collected from previous, current and future alternative fuels testing. Plan to establish a framework for the database, as well as host a web-portal that will make the data collected accessible to the general public.
  Worldwide Jet Fuel Data (SEMRS) – Metron & A4A project gathering fuel specification data of conventional jet fuel at airports throughout the US and the world. Track the spec properties at the various airports over time to give insight to the variation of properties in conventional jet fuel, and substantiate a tolerance level for spec properties in alternative fuels. Conventional jet fuel property data at multiple areas can be useful in aircraft emissions modeling and future alternative fuel blending efforts.
4) Mid term effort to streamline ASTM International jet fuels approval process
  Develop generic fuel composition/chemistry evaluation methodology
    Standardized rig/lab tests
    Chemical kinetic/combustion modeling
  Collaborative OEM/university/federal effort

## Slide 5: Currently funded Alt Jet Fuel Testing Activities
CLEEN II
  GE Testing
  Rolls Royce Testing
ASCENT COE
  P31: Testing Support & D4054 Clearinghouse Concept
  P25-P30, P34: National Jet Fuels Combustion Program
  P33: Alternative Jet Fuel Database Library
  New: GC x GC Project

## Slide 6: CLEEN II Alt Fuels Testing - GE
92% HEFA-SPK + 8% SAK (aromatics)
  Fully synthetic
  Virent providing 900 gallons of SAK - expected to arrive Q1 2018
  US Air Force providing 10,000 gallons of HEFA-SPK
  Full Annular Combustor Rig (FAR) testing expected to start possibly not before Q2 2018
  Supports the approval of SAK as well as fully synthetic fuels
ATJ-SPK testing in support of NJFCP
  Testing will be on 100% Gevo sourced Alcohol-to-Jet (ATJ-SPK)
  Testing is to correlate NJFCP tests with full combustor tests
  3000 gallons of Gevo ATJ-SPK fuel arrived at GE end of June
  Tier 3 testing was ready to start at the end of June; delayed to Oct/Nov due to test cell maintenance and test priorities
Provide combustor type in the FAR
What is tier 3 testing? Will GE be doing it?
Notes: TAPS III combustor will be used in the full annular rig test
-ATJ-SPK testing will be focused on operability (ignition and LBO) which is Tier 3 type – research oriented, not approval/qualification.

## Slide 7: CLEEN II Alt Fuels Testing – Rolls Royce
LanzaTech blend with Swift Fuels mesitylene
  Fully formulated synthetic blend jet fuel
  90% LanzaTech - ATJ-SPK (Ethanol-based ATJ)
  10% Swift non-renewable mesitylene – aromatic fuel blending component
  Fit for purpose testing anticipated to start Q4 2017
Will this support C/Q of Lanzatech fuel and/or fully synthetic blends? If so, then capture it in a bullet point
who is doing the work?

## Slide 8: Project 31 - D4054 Clearinghouse Concept
Candidate AJF In
FAA Seed Money Under ASCENT Center of Excellence
Structured as a Cost Share Arrangement
Accepts In-Kind Contributions (testing partners)
Also Accepts Direct Contributions
University of Dayton Research Institute (UDRI)
UDRI Contact
Dr. Steven Zabarnick
Steven.Zabarnick@udri.udayton.edu
(937) 255-3549
8
Stakeholder Engagement / Support Needed!
Final Research Report Out
Notes: ASCENT Project 31A

## Slide 9: D7566 Generic Annex
Fuel Producer
Fail
AJF Production
D4054
Testing
OEM Review
ASTM Ballot
Pass
Pass
Fail
ASTM D7566 Pathway Specific Annex
Permit Production of ANY Pathway at Nominal Blend %
Specific Criteria to Ensure Compositional Control and Product Quality
Meets Existing Annex?
Meets Generic Annex?
No
Yes
Notes: -D7566 Generic Annex is currently under consideration by ASTM

## Slide 10: Overview of NJFCP Program
Program uniqueness:
Integrated systemwide approach involving all stages of testing and modeling areas for identical conditions
Real-time communication and share of info among all 6 areas (experimentalists and modelers) and OEMs
Brings state of the art knowledge, computer capabilities, and engineering experience together
Fit-for-purpose testing
Area 7: Program interface and integration
ASTM Tier 3/4
ASTM Tier 1/2
NJFCP Objective: relate fuel properties to combustion figures of merit
Notes: FAA has new Center of Excellence for Aviation and Environment (get real name), also termed the Aviation Sustainability Center (ASCENT). Industry advised that “Rules and Tools” was valuable and needed to be resurrected. FAA prime mover. Go through flow of getting data…plus improved models to industry

## Slide 11
Fuel Candidates and Screening
Reference Fuels Required to
Characterize Rig and Engine Fuel Response
Category A:
Three Conventional (Petroleum) Fuels
“Best” case (A-1)
“Average” (A-2)
“Worst” case (A-3)
Category C:
Six “Test Fluids” with Unusual Properties
C-1: low cetane, narrow boiling (downselected)
C-2: bimodal boiling, aromatic front end
C-3: high viscosity
C-4: low cetane, wide boiling
C-5: narrow boiling, full fuel (downselected)
C-6: high cycloparaffins (OEMs also prefer)
Note: chart provides a measure of the boiling point of the fuel being examined
Check statement
Notes: •A-1 (JP-8), ‘best’ case Jet A
•A-2 (Jet A), ‘average’ case Jet A
•A-3 (JP-5), ‘worst’ case Jet A
•C-1 (100% Gevo Alcohol-to-Jet), low cetanenumber
•C-2 (C-14 iso-paraffin blended with 1,3,5-trimethylbenzene), bi-modal with aromatic front end
•C-5 (C-10 iso-paraffin blended with 1,3,5-trimethylbenzene), ‘flat’ distillation range

## Slide 12: Figures of Merit Mapping
T₃ - P₃ Regimes of Interest
NJFCP goal is to map fuel and geometry variation to stability loops that are related to Lean Blow Out and ignition probability (Cold Start and Altitude Relight)
Note: T3 and P3 are the combustor inlet temperature and pressure for a gas turbine engine
This chart was missing much of what was conveyed in Chart 10 of V01. I tried to fix this – please check that I got it right
Three operating regimes identified as sensitive to fuel properties and thus AJF
These fuel sensitive phenomena can be translated to relevant temperatures and pressures for testing.
Notes: These fuel sensitive phenomena, Figures of Merit, can be translated to relevant temperatures to relevant temperatures and pressures for testing
- Three operating regimes have been identified as sensitive to fuel properties and thus Alternative Jet Fuels (AJF)
-Three operating regimes are: Lean Blow Out, Cold Start, Altitude Relight
Requires extensive fuel and geometry testing
  Perhaps more fuels that have been identified in the program would need to be tested.
  Multiple swirlers, nozzles, and semi-/full annular configurations would need to be tested.

## Slide 13: Derived Cetane Number (DCN) Prediction of Lean Blow Out (LBO)
  Worse LBO behavior
  Better LBO behavior
*Means do not include OSU data as the onset of extinction, not LBO, is measured.
DCN predicts LBO as auto-ignition extends lean stability limit for swirl stabilized single cup rigs at NJFCP reference conditions
How does this chart show that DCN predicts LBO? I don’t see DCN anywhere on the chart

## Slide 14: Shocktube Testing
431 nm
Ring Dye Laser
4.3 mm Laser
216 nm
Ti:Sapphire Laser
3.39mm HeNe Laser
UV/Vis/IR
Emission
Detectors
Incident Beam Detector
P5
T5
P2
T2
VRS
CH3 
C2H5
CH 
C2H4 
 T(t)
Fuel
C2H2 CH4
Aromatics
i-C4H8 C3H6
3.0-3.4 mm Lasers
11mm QC Laser
10.5 mm CO2 Gas Lasers
Transmitted Beam Detector
Pressure gauges
Pressure & UV Emission used for IDT
IR Lasers used for Speciation
What does this chart tell me? That we have a shock tube with some lasers? Have we used it for something? If so, what? Please revise chart such that it conveys some information that will be useful to the REDAC
Notes:   Understanding the chemical breakdown of fuel at the high temperature conditions in a combustor. Pyrolysis occurs at a faster timescale than oxidation. Measuring pyrolysis products and correlating with ignition and blowout.
Two types of shock tube experiments are performed:
1- Ignition delay time measurements – provide global characterization of fuel behavior
2 – Species time history measurements – Provides detailed description of fuel decomposition products

## Slide 15: Combustion Rig
  Purpose: Understanding the process of blow out and ignition and sensitivities to Fuel/Air ratio, temperature, altitude. Can we decouple fuel effects from rig effects?
1. High Shear Stabilization & Blowoff
Important figure of merit for OEMs
Screen fuels for different blowoff conditions
Measure detailed flow field data for model validation and boundary conditions
2. Forced Ignition
Important figure of merit
Screen fuels for different ignition probability
Develop ignition models and support experimentally
3. Turbulent Flame Speed
Strong influence on figures of merit
Screen fuels for different turbulent flame speeds
Are these the same Figures of Merit as was provided on Slide 12?
Is this an additional figure of merit beyond those in Slide 12
Is this an additional figure of merit beyond those in Slide 12
I grabbed text from chart 12 for this as it seemed to be useful
Notes:   Understanding the process of blow out and ignition, sensitivities to F/A ratio, temperature, altitude. Can we decouple fuel effects from rig effects?
Combustion performance measurements with conventional fuels and fuels with unconventional chemistries determines sensitivities to properties
High shear task demonstrates correlation between fuel properties and blowoff
• Forced ignition task model demonstrates fuel chemistry influence on forced ignition
• Turbulent flame speed task produces large fuel sensitivity parameter studies
1st picture: High shear Rig

## Slide 16: Referee Rig
  OEM designed single cup combustor testing fuels in realistic environment.
  Designed under previous Air Force “Rules and Tools’ program.
Have we used this rig for anything? If so, what have we learned?
Notes: Realistic combustor to be used as a referee for the effect of alt fuels on combustion characteristics.
The referee rig is used to conduct and analyze combustion experiment for conventional and alt fuels. It’s used for fuel sensitivity demonstration for lean blowout, ignition and stability characteristics
.
Bottom right: Referee combustor operating near LBO
Bottom Left: Single cup Swirl Stabilized Referee combustor

## Slide 17: Spray Rig
Differential PT connected to the Airbox and Vessel
Vessel Temp. Thermocouple
Vessel Pressure Transducer
Main and Fuel Line Thermocouples
Variable Ambient Pressure Spray (VAPS) Rig
Operating Conditions: LBO and Chilled Fuel
Results: Lean Blowout (LBO)
  Effects of measurement plane
  Effects of ΔPpilot and ΔP/P
  Down-Selected Fuel Results
  X-Fuel Results
  Overall Fuel Comparison
Results: Chilled Fuel
  Effects of ΔPpilot and ΔP/P
  Overall Fuel Comparison
  Comparison of Chilled and LBO A-2 Results
What have we learned from using this rig?
Notes:   - Captures the effect of fuel physical properties (viscosity, freeze point, etc.) on spray quality

## Slide 18: University of Sheffield (1 of 3)
PI: Dr. Bhupendra Khandelwal, Low Carbon Combustion Center, University of Sheffield
Test Campaign 1: Develop a numerical tool to predict LBO limit based on correlations developed in test campaign
  test large number of conventional fuels, novel fuels and blends with a wide range of properties for their LBO limit
  testing would be done on a single can combustor
  correlations between key fuel properties and LBO performance will be investigated
Can we get a different title?
The next 3 slides should be condensed to 2 slides

## Slide 19: University of Sheffield (2 of 3)
Test Campaign 2: Analyze the performance of different blends of aromatics species with a base component to systematically evaluate the effect on seal performance, particulate mass concentration and smoke emissions.
Selection of specific aromatics and blends can lead to reduced particulate and smoke emissions while giving right amount of elastomer and fuel systems compatibility.
Number of aromatics species is 20
Total # of test points is about 80
Combustor of an aero engine and a Honeywell GTCP85 APU. Systematically selected aromatics and blends would be tested on seal compatibility test rig.
What bullet level is this points supposed to be at?

## Slide 20: University of Sheffield (3 of 3)
Systematic testing of fuel specification in both test campaigns will be done. Testing includes GC x GC, Lubricity, Viscosity, Density, C/H Ratio, Trace Metals, Aromatic Speciation, Cetane number and specific energy
Final Report: September 30, 2017

## Slide 21: What did we learn so far from NJFCP?
Purpose of the NJFCP: Improve understanding of fuel effects on combustion and streamline the current ASTM fuel approval process through testing and modeling
FAA has funded this project for 3 years thus far
Two yearly meetings with OEMs and University PIs
Tasked NJFCP and OEMs last November to inform the FAA with early benefits of this program:
  Confidence Levels, Modeling and Funding, and Summary

## Slide 22: NJFCP Report Out: Confidence Level
NJFCP and OEMs agreed that
More than doubled their confidence levels (15% to 30%) on identifying chemical/kinetic properties of fuels
Improved understanding of the various Figures of Merit (FOMs) - primarily Lean Blow Out (LBO)
OEMs agree that we may not get to 100% confidence in 5 years; however, the progress is moving asymptotically and it is very likely that we may get to 80% confidence level with sufficient funding
The increased confidence affects the OEM fuel approval process by lowering risk of how fuel property variation can affect operability and therefore can reduce Tier 3 and 4 testing requirements

## Slide 23: NJFCP Report Out: Modeling and Funding
The activities help OEMs model fuel effects with CFD analysis
Modeling capability is important to assess large range of product designs but OEMs acknowledge that modeling capability will take long time to develop
There was a concern that NASA funding for modelling may not be enough, and by design, the focus of the NASA program is based on newer and lower TRL models. So FAA may need to step back in to fund modelling activities. ($ is unknown)
It was noted that the AFRL, “referee rig” is central test facility of the program and much more testing (cold ignition) in that rig will be important. For this reason, AFRL would welcome some FAA funding for the Referee Rig work to meet all the tasks for that rig.
5 years is probably good number if NJFCP efforts are shown to be successful, probably around $250k-$500k/yr on top of NASA support
Is that 5 years in total or 5 additional years? What does it mean if NJFCP efforts are shown to be successful?

## Slide 24: NJFCP Report Out: Summary of Three Years
Capabilities and understanding developed under NJFCP is reducing risk and increasing confidence on fuel effects which may enable OEMs to streamline when and if a new fuel should be further evaluated before it is sent to ASTM for approval. Confidence levels have doubled.
OEMs agreed that capabilities and understanding developed under NJFCP could save significant time spent executing tier 3 and 4 activity because OEMs will have better understanding of the kinetic properties and risks for fuel effects in engines.
The tools (referee rigs and CFD) and knowledge gained from NJFCP have shown potential to enable the OEMs to reduce their risk when determining acceptability of candidate alternative jet fuels. This will allow them to approve these fuels more quickly and with greater confidence.

## Slide 25: New ASCENT Project Two-Dimensional Gas Chromatography Method Documentation and Analysis
Two dimensional gas chromatography is a novel analysis technique to accurately characterize fuel composition. However, GC x GC is lacking standardized procedure and is not utilized by ASTM.
FAA is establishing a project to conduct foundational investigative tasks to document and standardize the test method currently used for two dimensional gas chromatography analysis of alternative jet fuel candidates

## Slide 26: ASCENT Project 33: Alternative Jet Fuel Test Database Library
Fuel specification and rig testing data, technical papers, fuel approval reports
  400+ documents
  ~300 POSFs covering alternative and conventional jet fuels
Looking to support ASTM Generic Annex through tools and test data access
  Potential to extend fuel blending property prediction
Notes: POSF is a organizational symbol same thing as we are AEE
- POSF is NOT an acroynm

## Slide 27: ASCENT Project 33: Websites
Data Library:
  http://altjetfuels.illinois.edu/
For more information:
  https://ascent.aero/project/alternative-fuels-test-database-library/

## Slide 28: Where We Stand Today
Commercial flights on SAJF are taking place
1.1 million gallons in 2016 from one commercial producer, one demonstration
U.S. Alternative Jet Fuel Procurements1
Notes:
Based on voluntarily reported data from Airlines for America (A4A), Department of Defense (Defense Logistics Agency, DLA-Energy) and Gulfstream Inc.
United Airlines & Altair Fuels
Gulfstream & Altair Fuels
Alaska Airlines & Gevo Inc.
28

## Slide 29: Future Outlook and Priorities
Continue efforts to support certification / qualification process by leveraging shared funding and staffing approaches, improved methods, and enhanced specification requirements
Continue to develop tools to evaluate the readiness of feedstocks and fuels and their potential economic, social and environmental benefits
Continue coordinating and aligning efforts to develop US alternative jet fuel supply and enable commercial deployment.
Share best practices across the supply chain and with partners worldwide

## Slide 30: Summary
Alternative jet fuels are a key component of FAA strategy in meeting environmental goals
R&D efforts making progress on overcoming key challenges via testing, analysis and coordination
Public private partnerships have played key role in standing up an industry
Strong domestic and international coordination is essential
Industry is building momentum with many AJF advancement and highlights in 2016
Continue R&D efforts via testing, analysis and coordination in the future

## Slide 31
Cecilia Shaw CLEEN Program, FAA AEE Email: cecilia.shaw@faa.gov
Nathan Brown CLEEN Program, FAA AEE Email: nathan.brown@faa.gov
Levent Ileri CLEEN Program Manager, FAA AEE Email: levent.ileri@faa.gov

## Slide 32: Fuels under consideration at Univ of Sheffield