## Slide 1: Emissions Roadmap Update
Office of Environment & Energy

## Slide 2: Outline
Setting the Scene
FY17 Priorities
Future Priorities
Project Updates

## Slide 3: NAS-wide Energy Efficiency Trend
Chart: Kg of Fuel/RTk
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
BTS T2 | 0.4231 | 0.424 | 0.40832 | 0.38326 | 0.37516 | 0.35918 | 0.35148 | 0.34789 | 0.34097 | 0.34238 | 0.32881 | 0.32698 | 0.33145 | 0.32834
0.328
0.329
0.359
0.331
0.423
2000-2013
22% increase in energy efficiency

## Slide 4
1990-2015
54% increase in domestic enplanements
4.8% increase in domestic fuel burn

## Slide 5: FY17 Emissions Research Overview
ASCENT Project | Description | Emissions Roadmap
2 | nvPM Emissions Engine Measurements | 
10 | Forecast Technology and Influence of Commercial SST | 
18 | Health Effects of Aviation Emissions | 
19 | CMAQ-based Airport AQ Model Development | 
20 | Fast-time APMT-I AQ Model Development (Adjoint) | 
21 | Updates to APMT-I Climate Model | 
22 | Independent Evaluation of APMT-I Climate Model | 
24 | Emissions effects of fuel components Closing out… | 
39 | CBA of removing Naphthalene from Jet-A | 
48 | Engine nvPM Emissions Standard Setting Support | 
Emissions Source Characterization
Certification and Regulations
Emissions Tools Development
Climate Impacts Research
Aviation Emissions Modeling
Health Impacts Research
Emissions Guidance Research

## Slide 6: FY18, FY19 and Beyond
 | FY18 | FY19 | Beyond
Emissions Source Characterization |  |  | 
nvPM emissions ambient and fuel corrections | X |  | 
Emissions effects of alternative fuels | X | X | X
Removing Naphthalene from Jet-A | X |  | 
Certification and Regulations |  |  | 
Domestic Implementation of aircraft CO2 emissions std | X | X | X
Domestic Implementation of engine nvPM emissions std | X | X | X
ICAO engine nvPM emissions stringency | X | X | X
Health Impacts Research |  |  | 
Ultra-fine particle measurements at airports | X | X | 
Emissions Tools Development |  |  | 
Airport AQ Model Development | X | X | X
Fast-time APMT-I AQ Model Development (Adjoint) | X |  | 
Updates to APMT-I Climate Model | X | X | 
Aviation Emissions Modeling |  |  | 
ICAO engine nvPM emissions stringency | X | X | X

## Slide 7: A2: nvPM Emissions Engine Measurements
Successfully funded 7 nvPM emissions engine tests
  Only one test remaining
  Upcoming in 1 month
Ambient Conditions Corrections campaign
  Combustor rig test
  Upcoming in 2 months
Engine-to-Engine variability tests
  25 engines of same type measured off production line
  Upcoming in 3 months
Next Steps
  NASA engine tests at altitude
  Potentially additional ambient conditions and fuel sensitivity correction measurement tests

## Slide 8: A2: nvPM Emissions Engine Measurements
Impact of Technology on nvPM Mass Emissions for Engines in Different Thrust Class
“old” vs. “new” technology

## Slide 9
Impact of Technology on nvPM Number Emissions for Engines in Different Thrust Class
“old” vs. “new” technology
A2: nvPM Emissions Engine Measurements

## Slide 10: A10: Forecast Technology and Influence of Commercial SST
Define potential demand and develop a forecast supersonic air travel (out to 2050)
3 types of SST
  Type1: operate at supersonic speeds in unrestricted areas and subsonic speeds over other areas
  Type2: same as Type 1 except has technology to fly at Mach cut-off speeds over prohibited areas.
    Uses atmospheric characteristics to prevent sonic booms from propagating to the ground (Mach 1.1 to 1.15)
  Type3: aircraft designed to produce very low sonic boom levels during all phases of supersonic flight
Fuel burn, CO2, H2O, and if possible NOx, by altitude
Comparison of fuel burn to subsonic traffic
Estimate community & en-route noise impacts

## Slide 11: A18: Health Effects of Aviation Emissions
Conduct field campaign to measure ultra-fine particulate matter at airports
  Under flight paths using PDARS radar tracks
Perform statistical analysis
Carry out monitor vs. modeling comparisons

## Slide 12: A19: CMAQ-based Airport AQ Model Development
NAS-wide AQ modeling + CMAQ DDM 2nd order sensitivity analysis work
Work with BU re UFP monitoring & modeling comparisons
Conduct Northern Hemisphere CMAQ analysis
Gridding Tool Development
Real Weather: WRF and MERRA work
Work with Nation Aviation University in Kiev Ukraine
Attainment-to-nonattainment from aviation emissions

## Slide 13: A20: Fast-time APMT-I AQ Model Development (Adjoint)
Adding fine grids:
  Canadian + SE Asia + European grid,
Emissions uncertainties work
Conduct multi-scale adjoint modeling
Evaluation of ammonia propagation into tool
Transition from research to operations for tool

## Slide 14: A21: Updates to APMT-I Climate Model
Continue tool development
Inclusion of global impacts of regional emissions
Investigate regional damages of regional temperature changes (from CICERO)
Update of contrail impacts beyond fuel burn scaling

## Slide 15: A22: Independent Evaluation of APMT-I Climate Model
UIUC to review and evaluate…
Exercise latest version of APMT-I Climate tool
Evaluate inclusion of regional impacts capabilities after review of CICERO memorandum
Review of future contrail updates

## Slide 16: A39: CBA of removing Naphthalene from Jet-A
Objective:
  Gather and perform analyses regarding reduction and/or removal of naphthalene from jet fuel in a refinery, and then to quantify the public health, global climate change, and economic impacts of reduction and/or removal of naphthalene in jet fuel.
2-year project. Kicked-off in September 2016
Consider changes in both nvPM and sulfur oxide emissions that could accompany the changes in fuel composition.

## Slide 17: A48: ICAO/CAEP Engine nvPM Emissions Standard
CAEP/10 agreed to the inaugural engine nvPM Certification Requirement and nvPM Emissions Standard
CAEP/10 Certification Requirement
  Standardized nvPM Measurement System
  New Appendix 7 to Annex 16 Vol. II
Engine nvPM Emissions Standard
  CAEP/10 Standard based on smoke visibility limit
  New Chapter 4 to Annex 16 Vol. II
Notes: It is well known that there is no PM standard for aircraft engines. The first order approximation is used to estimate PM mass concentrations from certification smoke number measurements. It should be noted that the smoke number standard was developed originally as a visibility standard.

## Slide 18: The CAEP/10 nvPM Standard
The CAEP/10 nvPM standard enables:
  Reporting of certified LTO nvPM mass and number Emission Indices (EIs) for all in-production engines of >26.7 kN rated thrust
  Establishment of a regulatory level for the nvPM mass concentration equivalent to smoke number regulatory level. Sets the stage for:
    Health and climate relevant nvPM standards
    Expected removal of the Smoke Number standard for engines of rated thrust >26.7 kN
  Use of standardized nvPM measurement system
    Designed for use with existing probe/rake systems and simultaneous operation with gaseous measurement system.
  Comparison of engine technology and engine types for nvPM emissions

## Slide 19: Standardized nvPM Measurement System – Appendix 7
Notes: While research grade PM sampling systems have been used to acquire nvPM mass and number concentrations, a conceptual non-volatile PM sampling system was developed by January 2011 by SAE E31. The probe is on the left with FS1 indicating the first splitter. Until the first splitter, the particle or gas transfer system remains identical to that of the Annex 16 gaseous sampling system. At the first splitter, there is a 1:3 split with one line continuing on to the Annex 16 system. A PM line connects to an eductor where the PM sample is diluted with Nitrogen to prevent volatile PM from forming. The sample is then taken downstream through a standard length of line through a cyclone in to the mass and number concentration measuring instruments.

## Slide 20
FOCA Empa ETH
= Reference Systems
nvPM Measurement Systems: Reference and OEM systems
U.S. Air Force, Arnold Engineering Development Complex

## Slide 21
CAEP/11 nvPM Remits
Provide representative engine data for assessing the nvPM emissions standard for mass and number regarding turbofan/turbojet engines ≥26.7kN by February 2017.
Provide recommendations on stringency options and applicability to CAEP Steering Group Sept/2017.
Develop an aircraft engine based LTO nvPM mass and number standard for turbofan/turbojet engines ≥26.7kN.
Investigation the possible replacement of the smoke number standard for engine categories ≥26.7kN and other engine categories <26.7kN.
Develop improved nvPM model inputs to both local air quality models

## Slide 22
CAEP/11 LTO Based nvPM Mass and Number Standard Tasks
Full Standard Setting Process in CAEP/11:
  Develop metric system
  Develop stringency options
  Develop technology response
  Conduct cost effectiveness analyses
  Determine LTO-based nvPM mass and number regulatory levels
Refine and finalize corrections for ambient conditions, fuel sensitivity and engine-to-engine variability
Refine steps to replace SN standard with nvPM mass and number standard based on CAEP/10 nvPM standard