## Slide 1
Volpe The National Transportation Systems Center
Divya C. Chandra and Rebecca Markunas USDOT Volpe Center, Cambridge, MA
2 September 2015
U.S. Department of Transportation
Office of the Assistant Secretary for Research and Technology
John A. Volpe National Transportation Systems Center
Volpe The National Transportation Systems Center
Advancing transportation innovation for the public good
Subjective Instrument Procedure Complexity Line Pilot Interviews and Discussions
* This research is funded by the Federal Aviation Administration Human Factors Research and Engineering Division (ANG-C1) in support of Aviation Safety (AVS). Program Managers: Regina Bolinger and Sherry Chappell. Technical Sponsors: Kathy Abbott, Mark Steinbicker, and John Swigart.
Notes: Began research program in late 2007
  Supports NextGen
  Small, highly specialized team
  Several products generated

## Slide 2: Goals: The Big Picture
Give pilots clear instructions on route to fly for arrivals (STARs), departures (SIDs), and approaches (IAPs)
Clearly convey any restrictions on speed and altitude
Allow flexibility for efficiency
Accommodate as many aircraft types as possible
Consider human performance, workload, and potential for confusion
http://commons.wikimedia.org/wiki/File:Map-USA-Southwest01.png
?

## Slide 3: Viewpoints
Procedure design
  Content and instructions
Cartographic design / chart depictions
  Communicating the content
Interrelated with operations, avionics, aircraft performance, pilot training
http://en.wikipedia.org/wiki/Switchboard_operator
Pilot
Designer
Airplane
Chart
Operator
Regulator
Human Factors?
ATC

## Slide 4: Current Research Questions and Goals
Primary
  What makes a procedure subjectively “difficult” for line pilots?
    Develop a comprehensive list of factors related to subjective procedure complexity
  Can we use this understanding to design procedures that are implemented more smoothly?
    Develop actionable recommendations…
Secondary
  Understand how pilots use charts today, especially SIDs and STARs.

## Slide 5: Activities Timeline
Initial data collection
(May-Sept)
Analysis
(Oct)
Preliminary working paper
(Nov)
Partial draft report
(July)
Full draft report
(Dec)
Final data
collection
(Dec)
Analysis
(Jan/Feb)
FAA AFS
(March)
Jeppesen
(Aug)
ICAO
(Oct)
CNS TF
(April)
Analysis
(May/June)
Presentation
Document
NextGen Admin
(May)
2015
2014
CNS TF
(Dec)

## Slide 6: Study Overview
Participants, Procedure, and Task
  3 hours of observation and discussion with groups of 2-3 line pilots from the same operator
  Office setting
  Review 6 procedures (2 SIDs, 2 STARs, and 2 IAPs)
  Two researchers take notes
  Informed consent & modest payment ($200)
Equipment
  Static chart images, current for each session
  Jeppesen paper (or electronic) charts

## Slide 7: Participants
45 pilots across 19 sessions
  From 3 major airlines, 1 regional airline, 1 air taxi, 3 corporate
  All currently use Jeppesen charts
Broad range of aircraft types
  All equipped with FMS
  Advisory VNAV or Coupled VNAV
  Some with autothrottle, some without

## Slide 8: Data and Analysis
Independent notes from two researchers
  Real-time transcripts
    No audio/video recordings
    No response times or timing data
    No quantitative performance measures or analyses
  Summarized all sessions into a common format using a template and rubric
For each “question of interest,” extracted data from all sessions into a single file to compare responses
  Look for qualitative patterns in the responses

## Slide 9: Sample Findings
Pilot reviews and briefings
Procedure design
Chart design
Operational complexity
  Interactions between aircraft systems, procedure design, and operational factors
Subjective complexity factors and framework
Still under review

## Slide 10: Defining Subjective Complexity
Subjective complexity is present when a task requires extra mental or physical steps by the pilot.
  Examples
    Increased memory/awareness/attention
    More button pushes than necessary
  Phrases such as “be careful when” or “pay attention to” or “don’t forget to” or “better ask” or “it only works when” indicate subjective complexity.

## Slide 11: Sources of Subjective Complexity
Procedure design issues (alone)
  Waypoint names
  Sudden changes (e.g., descent rate, airspeed)
  Constraint verification and monitoring
Procedure issues that create charting issues
  Procedure variability
  Transitions
  Consistency between SIDs/STARs and IAPs
Chart issues (alone)
  Non-contiguous paths
  Chart composition
Operational complexity
  e.g., ATC intervention, weather, traffic

## Slide 12: Operational Complexity Factors
ATC interventions
Aircraft equipment or performance
Crew factors
Operator factors
Environment factors
These issues cannot be fully resolved through better procedure design, but procedure designers need to consider them.

## Slide 13: Procedure and Chart Complexity
Procedure Issues
Procedure-induced Chart Issues
Chart- specific Issues
e.g., non-contiguous paths
Chart composition, e.g., arrangement of elements, arrangement of sections, inconsistencies
Lateral, vertical, speed, constraints, flyability, clarity, etc.

## Slide 14: Subjective Complexity Factors: A Pilot-Centered Framework
Overall Procedure and Chart Complexity
Arrangement of sections
Placement of elements within sections
Inconsistencies
Procedure Complexity
Ambiguity
Constraints
Waypoint Names
Sudden Changes
Holds
Vectors
Airspace restrictions
Operational Complexity
Noncontiguous graphical path depiction
Notes
Variation
Transitions
Procedure-Induced Chart Complexity
Chart-Specific Complexity
A subjective complexity factor is one that requires an extra mental or physical step by the pilot.
Not every aspect of the procedure design creates complexity.
Everything that is complicated about the procedure design is reflected in the chart.

## Slide 15: Questions?
For further information
Divya.Chandra@dot.gov
617-494-3882
http://www.volpe.dot.gov/our-work/safety-management-and-human-factors/human-factors-research-instrument-procedures-faa-nextgen

## Slide 16: Acknowledgements
FAA Technical Sponsors and Program Managers
USDOT Volpe Center
  Andrew Kendra, Vince Orlando, Maura Lohrenz
Subject Matter Experts
  Jeppesen
  Pilot participants
  Pilot recruitment POCs
  FAA AeroNav Products
  Reviewers of study plan and script

## Slide 17: Participants’ Aircraft Systems and Types
Advisory VNAV only, no autothrottle
  Embraer 145
  Bombardier CRJ 200
Coupled VNAV, no autothrottle
  Boeing 737 Classic
  Citation X (CE750)
  Gulfstream 200
  Bombardier Challenger 300
Coupled VNAV and autothrottle
  Embraer 190, with company restriction to use managed speed only above 10000 ft alt
  Boeing 737 NextGen (NG)
  Boeing 757/67
  Airbus 320
  Gulfstream 450
  Bombardier Challenger 604 and 605