## Slide 1
ATD-1: Overview
August 9, 2016

## Slide 2: Outline
ATD-1 Overview
TSAS Activities
FIM Activities
Conclusion

## Slide 3: ATD-1 at a Glance
The first of a series of NASA ATM Technology Demonstration (ATD) projects to provide benefits to the commercial aviation community through the development of new technologies
Integrated Arrival Solution
Terminal Sequencing and Spacing (TSAS) + Interval Management (IM)
Key Steps
  Finish research on TSAS and IM that began in years prior
  Build prototype systems
  Demonstrate prototype systems
  Transfer technologies to Industry and FAA
IM prototype and flight test team: NASA, The Boeing Company, Honeywell, United Airlines, and FAA
Accelerate NextGen and reduce time to market by addressing tech transfer challenges between research, development and implementation for key capabilities

## Slide 4: Operational Context
Increasing level of automation, accuracy, maturity…
Increasing level of efficiency
Independent Scheduling
Integrated Scheduling and Spacing
NOTE: Nominal +/- spacing precision
Is indicated in parentheses.
Terminal vectoring
Excess separation
Step-down Descents
Trajectory-based Operations
Reduced excess separation
Efficient Descents
En Route
Metering
(~60 sec)
TMA
Terminal
Metering
TMA-TM
Ground-based
Spacing Aids
(~15 sec)
TSAS
Flight Deck-based
Spacing Aids
(~5 sec)
FIM

## Slide 5: ATD-1 Formulation
In 2010
  Elements of NASA terminal ATM research progressed to high-fidelity human-in-the-loop (HITL) simulations. Stakeholder input and feedback was positive; the research aligned with FAA priorities
In 2011
  Office of Management and Budget and Congress requested NASA to:
    Accelerate ATM technology transition, including ADS-B In
    Conduct more relevant flight research emphasizing enhancing aviation safety and airspace efficiency
    ATD-1 initiated as part of the Systems Analysis, Integration, and Evaluation Project within NASA’s Airspace Systems Program
In 2012
  The ADS-B In Aviation Rulemaking Committee and FAA Reauthorization Act of 2012 both identified the need to demonstrate promising ADS-B In applications to help the community understand the benefits of ADS-B In

## Slide 6: ATD-1 Objectives
Demonstrate increased, more consistent use of Performance-Based Navigation (PBN)
  RNAV/RNP arrival procedures from cruise to touchdown
  Optimized Profile Descents (OPD) using speed control
  Simultaneous high throughput and fuel-efficient terminal ops
Demonstrate ADS-B In Spacing Application
  NASA ADS-B In merging and spacing algorithm (ASTAR)
Accelerate transfer of NASA scheduling and spacing technologies for inclusion in NAS/NextGen
  Terminal metering based upon Traffic Management Advisor research
  Airborne spacing application based upon Interval Management research
  Controller spacing tools based upon Controller Managed Spacing research

## Slide 7: ATD-1: Integrated Arrival Solution
CMS
Controller-Managed Spacing
in Terminal Airspace
TMA-TM
Traffic Management Advisor
with Terminal Metering
FIM
Flight Deck Interval Management
for Arrival Operations
NASA Technologies plus
ADS-B Infrastructure Area Navigation (RNAV)
Arrivals Required Navigation Performance (RNP)
Optimized Profile Descents (OPD)

## Slide 8: Operational Scenario
Time-based scheduling provides runway arrival times and fix crossing times for arriving aircraft.
En route speed and path assignments correctly space aircraft for descents on RNAV/RNP OPDs to assigned runways.
Most flight crews use FMS to fly OPDs along RNAV/RNP routes – largely without controller intervention.
Aircraft are delivered to meter fixes according to schedule, but with small spacing errors that need to be reduced to maximize throughput and avoid spacing violations.
Terminal controllers correct residual spacing errors and cope with disturbances and off-nominal events using tools and display enhancements based on 4-D trajectories.
Meter Fix
Meter Fix
Some flight crews use onboard speed guidance to achieve and maintain precise traffic spacing.
250+ NM
50 NM
Merge Point

## Slide 9: ATD-1 HITL Simulations (FY)
  FIAT 3
  Integration of RTMA 3.12 w/TSS and STARS ELITE w/TSS in PHX airspace
  IMAC
  Validate IM procedure, algorithm, phraseology for new clearance types; Evaluate IM display elements
  ASTAR13 + TBFM 4.2.x in DEN airspace
  REACT w/FAA+ MITRE
  Enable RNP-AR procedures using ATD-1 tools in DAL airspace
  NASA TMA-TM + CMS
  CMS Flight Deck #1 & #2
  Examine crew workload & strategies when flying schedule-based OPDs using CMS in LAX airspace
  Evaluate crew response to “nominal” CMS speed clearances using RTMA-TM 3.12 + CMS in PHX airspace
  IM-NOVA
  Assess acceptability of ATD-1 ConOps crew procedures
  ASTAR11 + NASA TMA-TM + CMS in DFW airspace
  RAPTOR
  Assess if ASTAR12 satisfies the ATD-1 requirements for FIM
  ASTAR12 + RTMA 3.12 w/TSS in PHX airspace
  FIAT-1
  Initial ATD-1 integration of TM algorithms into RTMA –TM 3.12 + CMS + ASTAR11 in LAX airspace
  FIAT-2
  Validate RTMA 3.12 w/TSS + ASTAR11 in PHX airspace
  FIAT-4
  Validate ASTAR12 performance in PHX airspace
  RTMA 3.12 w/TSS and STARS ELITE w/TSS + ASTAR12
  FIAT-5 & ORM
  Validate TBFM 4.2.x w/TSS & STARS SCOUT R2 w/TSS in PHX airspace
  Pre-Ops Int prep
  CA-1, CA-2, CA-3
  Initial ATD-1 system integration of NASA TMA-TM + CMS + ASTAR11 in DFW airspace
  Controller evaluation of tools, workload, proposed phraseology
2014
2012
2013
2015
  Ops Int @ Tech Center
  Identify changes for GIM-S/TSS integrated operations; Recommend AT procedures & training for TSS operational use
  TBFM 4.2.3 w/TSS & GIM-S and STARS SCOUT R2 w/TSS in PHX airspace
  TSS-2 w/FAA+MITRE
  Evaluate PBN arrival procedures under robust wind and heavy traffic conditions in PHX airspace
  RTMA 3.12 w/TSS
  TSS-1 w/FAA+MITRE
  Evaluate ATD-1 tools using advanced PBN procedures with mixed-equipage in LAX airspace
  NASA TMA-TM + CMS
  CA-5.1, CA-5.2
  Compare baseline & TSS performance measures using PHX West & East Flow operations using RTMA 3.12 w/TSS
  CA-5.3
  Compare ATD-1 performance measures using PHX West & East Flow operations using RTMA 3.12 w/TSS + ASTAR12
  TSS/ATPA/ RECAT
  Evaluate TAMR CHI integration
  GIM-S
  Evaluate MFX delivery ops
  ISIM
  Assess FIM HMI Options
  ASTAR11 + NASA TMA-TM + CMS in PHX airspace
  CA-4, CA-4.1
  ATD-1 system integration of RTMA-TM 3.12 + CMS + ASTAR11 in PHX airspace
  Corrected RUC truth winds & forecast winds
Notes: Updated 2/23/15: ATD-1 HITLs
-- Updated TBFM version in OIA, ATPA boxes
-- Per MM: Animation order and color by sim grouping (FIAT, CA, FIM, FAA, FY15); Arranged by FY; FY15 pop up together
-- NASA ATC TSS: REACT (Mar 2012), CMS Flt Deck 1 (Mar/Apr 2012), TSS-1 (Sep 2012), FIAT-1 (Oct 2012), FIAT-2 (Mar 2013), TSS-2 (Apr 2013), FIAT-3 (Aug 2013), CMS Flt Deck 2 (Nov/Dec 2013), FIAT-4 (Feb 2014), FIAT-5 (Dec 2014), OIA Risk Mitigation (ORM) Ops Int Prep (Mar 2015)
-- NASA AOL TSS: CA-1 (Jan 2012), CA-2 (Apr 2012), CA-3 (Jun 2012), CA-4 (Dec 2012), CA-4.1 (Mar 2013), CA-5.1 (Jul 2013), CA-5.2 (Sep 2013), CA-5.3 (Apr 2014), GIM-S Performance Eval for OIA (Apr 2015), TSS/ATPA/RECAT (May 2015), Research Platform for ZAB/ZDV/ZNY (3Q-4QFY15)
-- NASA FIM: IM-NOVA (Aug/Sep 2012), ISIM (Apr 2013), ASTAR Batch 1 (Jul 2013), RAPTOR (Jan/Feb 2014), ASTAR Batch 2 (Sep/Oct 2014), ASTAR Batch 3 (Apr 2015), IMAC (Jul 2015)
-- Ops Int @ TC (May 2015)
-- 1st ASTOR build with ASTAR12 is 9/5/2013 (per TSmith)

## Slide 10: Outline
ATD-1 Overview
TSAS Activities
FIM Activities
Conclusion

## Slide 11: NASA/FAA OIA Team

## Slide 12: TSAS Activities
Operational Integration Assessment (OIA)
  May 2015: OIA conducted at FAA Tech Center
  July: Provided briefings of some preliminary results to the FAA
  Sept: Final Report drafted
  Nov: Additional results briefed during Tech Transfer 4 TIM at FAA HQ
  Final Report being updated to reflect additional results and stakeholder comments
  Jan 2016: Final Report with all updates will be delivered to the FAA
  Mar 2016: OIA Data Package will be prepared and delivered to the FAA
    Provides the FAA with additional materials to support implementation of TSAS

## Slide 13: Outline
ATD-1 Overview
TSAS Activities
FIM Activities
Conclusion

## Slide 14: Flight-deck Interval Management (FIM)
Flight deck automation that provides air speeds to pilots allowing them to more accurately space their aircraft behind another aircraft based on an operationally desired spacing goal prescribed by Air Traffic Control (ATC)
Includes ground automation enhancements
14
FIM Aircraft
Target/Lead Aircraft

## Slide 15: FIM Activities - Prototyping
Objectives:
  Demonstrate ADS-B In Application
    Address ADS-B In ARC Final Report: ADS-B In demonstrations needed
    Address FAA Reauthorization Act of 2012: ADS-B In demonstrations needed
  Accelerate transfer of NASA scheduling and spacing technologies/accelerate key NextGen capability
Avionics Phase 1
  Feasibility and Trade Studies on Hardware/Software for FIM using ASTAR
ASTAR Flight Test
  Proof of Concept flight test for operational risk reduction
Avionics Phase 2
  Build, test, fly and report on FIM system based on ASTAR
Transfer prototypes to FAA

## Slide 16: Avionics Phase 1
Prototyping Initiated in 2012
Phase 1:
  Feasibility and trade studies performed by the Boeing Company
  NASA Airborne Spacing for Terminal Arrival Routes (ASTAR) FIM algorithm was demonstrated in flight test cabs at Boeing facilities using ACSS system in Feb 2013
  Several members of FAA attended
All deliverables included in ATD-1 Tech Transfer package

## Slide 17: ASTAR Flight Test
Proof-of-concept ADS-B In application flight test in December 2014
Purpose:
  Assess risks associated with ADS-B In application flight trials
  Get an initial look at NASA FIM application performance in flight
FIM application on board Boeing EcoDemonstrator 787
Arrivals into Moses Lake, WA
Boeing also provided second aircraft as ADS-B Out source
NASA and Boeing staff monitored operations from ZSE and MWH
Conducted successfully and results were positive
Presented to US Congress during NASA Technology Day on the Hill
Media
  http://www.nasa.gov/press/2014/december/nasa-tests-software-that-may-help-increase-flight-efficiency-decrease-aircraft/
  http://www.ainonline.com/aviation-news/air-transport/2014-12-18/boeing-concludes-latest-round-ecodemonstrator-trials

## Slide 18: NASA Testing on the Boeing EcoDemonstrator 787

## Slide 19: Avionics Development/ Flight Test Scope
Build, test, and fly a prototype FIM Avionics System in air transport category aircraft
  System and Hardware Development
  FIM application Software Development
  Hardware/Software Integration and Testing
  Avionics System and FIM Application Documentation
  Ground and Flight Tests
Six Working Groups managed by Boeing with participation by NASA, Boeing, Honeywell, United Airlines, and FAA
  Requirements WG: baseline final requirements to align with RTCA FIM MOPS
  Human/Machine Interface WG: baseline final pilot interface for FIM avionics system
  Control Law WG: baseline final ASTAR FIM algorithm implementation in FIM avionics system
  Flight Test WG: develop flight test plans
  Data Gathering/Analysis WG: develop data collection plans
  Hardware/Aircraft WG: baseline hardware and aircraft configurations for all aircraft
Conduct analyses of results and report out

## Slide 20: Flight Test Operational Environment
Operational environment
  Seattle Center and Grant County International Airport (MWH) in Washington State
    Arrival operations performed at MWH with some in cruise
    Custom arrival procedures designed for state-of-the-art NAS development
  3 Aircraft available
    Honeywell Dassault Falcon as DO-260B ADS-B Out lead
    Honeywell B757-200 as DO-260B ADS-B In/Out FIM aircraft
    United Airlines B737-900ER as DO-260B ADS-B In/Out FIM aircraft
  Voice comm for clearances
38 Test Conditions – 82 Flight Hours+Transit
Observers embedded in local FAA facilities
Flight Crew procedures defined by HMI design and SMEs
ATC procedures defined by the FAA Facilities

## Slide 21: Schedule at a Glance
Award June 2015
Kickoff July 2015
PDR September 2015
CDR May 2016
SAR December 2016
Pilot Orientation December 2016
FRR January 2017
Flight Test January/February 2017
Analysis Complete May 2017
Closeout June 2017

## Slide 22: Outline
ATD-1 Overview
TSAS Activities
FIM Activities
Conclusion

## Slide 23: Concluding Remarks
NASA is working with key stakeholders to improve high density terminal arrival operations by developing new concepts and prototypes, and providing expertise to accelerate a key ADS-B In Application and sequencing and spacing tools for NextGen
TSAS technologies have already been transferred to the FAA for a 2018 IOC
IM concepts and technologies are being developed for a flight test and subsequent transfer to the FAA and OEMs for further development and testing as needed