## Slide 1: Runway Safety Metric (RSM)
Firdu Bati, AJI-3
March, 2017
RSM Stakeholders

## Slide 2: Background
The primary goal of safety metrics is to gauge the safety performance of the National Airspace System (NAS), at the system and facility levels.
Existing runway safety metrics focus solely on runway incursion type counts, not accidents and excursions.
RSM Goal: Develop a runway safety metric that includes accident, Runway Excursion (RE), Runway Incursion (RI), and Surface Incident (SI) data.

## Slide 3: Approach
Collect applicable accident and incident data.
  National Transportation Safety Board (NTSB), RI-SI, and RE data sources
Use modeling to assign risk weights to all kinds of outcomes.
  Weighted outcomes include injuries, damage, incursion types, surface incidents, and excursions
  Weights are based on outcomes’ “proximities” to fatality and are ordered based on SME input [Injury → Damage → Incident]
  For accidents, weighting gives some credit for saving lives and minimally-damaged aircraft
Aggregate all event weights for each fiscal year to get a FY score.

## Slide 4: Weighting Schematic

## Slide 5: Combined Risk & Event Count
  *Risk decreased, incident increased, accident relatively constant over time

## Slide 6: Commercial Risk & Event Count
  *Risk decreased, incident increased, accident relatively constant over time

## Slide 7: Non-Commercial Risk & Event Count
  *Risk decreased, incident increased, accident relatively constant over time

## Slide 8: Commercial Risk & Ops (Per Million)
  *Risk decreased, Ops slightly decreased over time

## Slide 9: Non-Commercial Risk & Ops (Per Million)
  *Risk increased and started decreasing, Ops decreased over time

## Slide 10: Conclusion
Systematic approach followed to develop Runway Safety metric
Inclusive of all relevant datasets
Quantitative technique to assign severity weights
Baseline/target is in development
Expected deployment date: FY 19

## Slide 11: Backup Slides

## Slide 12: Technical Approach
Prepare National Transportation Safety Board (NTSB), RI-SI Database, and RE Database data.
Assume the worst possible accident involves fatal injury.
Assign weights to accidents and incidents based on relative “distance” to fatality.

## Slide 13: Data Pre-Processing
NTSB data selection
  Reports without phase codes relevant to the runway environment were removed
  Remaining data classified as runway collision, taxiway collision, runway excursion by training a text mining model and validating results
Data merging
  RE and RI-SI data have already been reviewed by domain expects and categorized
  Some overlap between RE and NTSB datasets; duplicates were removed (NTSB records retained)

## Slide 14: FY16 Dataset
 | Runway Collision | Taxiway Collision | Runway Excursions
# of Events | 237 | 302 | 9,653
 | A | B | C | D | E | SI
# of Events | 235 | 319 | 5,472 | 7,967 | 12 | 8,936
 | Runway Excursions
# of Events | 1,276
NTSB (FY81 – FY16)
RI-SI (FY98 – FY16)
RE (FY12 – FY16)

## Slide 15: Event Count

## Slide 16: Three Step Weighting Process
Weights are assigned to types of accidents based on proximity to a fatal accident.
Appropriate domain expert assumptions are used to reorder the weights:
  Injury
  Damage
  Incident without injury/damage
Incidents are assigned weights based on their corresponding accident types.

## Slide 17: Information Gain as a Measure of Uncertainty

## Slide 18: Information Gain as a Measure of Uncertainty
Bayesian Network employed
  Accounts for correlation between different outcomes
  Computes information gain

## Slide 19: SME-Based Reordering Logic
Model output ranks some damage higher than injury.
Domain experts provided qualitative direction resulting in reordering.
  Injury
  Damage
  Incident

## Slide 20: SME-Based Reordering Logic
  Compute information gain (model output)
  Compute relative significance of highest gain
  Normalize it so the relative gain sums to 1
  Order gain using cumulative significance
  Compute relative significance to new highest gain
  Shift significance by maximum gain to compute relative significance to fatality

## Slide 21: Entropy-Based Relative Weight
Commercial
Non-Commercial

## Slide 22: Weights – Penalty & Credit
Injuries
  Penalty and credit terms for injured and non-injured, respectively
Damage
  Penalty and credit terms for damaged and non-damaged, respectively
Incidents
  Ratio of the weight of the corresponding accident type to frequency of incident
| , |

## Slide 23: Credit – Penalty Correction Term
Example Two accidents
  A: 5/5 injured
  B: 5/200 injured
Without credit term,
  Both A & B: 5 * .75 = 3.75
With credit,
  A: (5*.75) = 3.75
  B; (5*.75) – (.975*.75) = 3.02

## Slide 24: Relative Weights – Commercial
Note: Y-Axis uses Logarithmic scale

## Slide 25: Relative Weights – Non-Commercial
Note: Y-Axis uses Logarithmic scale

## Slide 26: Application of Weights
Two potential applications:
  Aggregation: sum of all undesired outcome weights
  Worst-outcome: weight of the worst outcome
  *The choice makes little difference in the relative risk profile primarily due to the limiting effect of the worst-outcome [adding small numbers to a large number]

## Slide 27: Combined Risk & Event Count
  *Risk decreased, incident increased, accident relatively constant over time

## Slide 28: Commercial Risk & Event Count
  *Risk decreased, incident increased, accident relatively constant over time

## Slide 29: Non-Commercial Risk & Event Count
  *Risk decreased, incident increased, accident relatively constant over time

## Slide 30: Commercial Risk & Ops (Per Million)
  *Risk decreased, Ops slightly decreased over time

## Slide 31: Non-Commercial Risk & Ops (Per Million)
  *Risk increased and started decreasing, Ops decreased over time

## Slide 32: Assumptions
Assumed the following hierarchy of accident/incident severity based on domain expert input: fatality, injury, aircraft damage, incidents.
Incident to accident mapping assumption
  RIs  Runway Collision
  SIs  Taxiway Collision
  RE Incidents  RE Accident
Assumed the following criteria should be used to split the dataset by Commercial and Non-Commercial
  Part 121, 129, 135: Commercial
  Others: General Aviation / Non-Commercial
Incident data are only available starting in 1997; however, the model used accident data since 1982.
  This is more conservative

## Slide 33: Conclusion
Systematic approach followed to develop Runway Safety metric
Inclusive of all relevant datasets
Quantitative technique to assign severity weights
Baseline/target is in development