## Slide 1: Safety Risk Management Proposals for Airborne Electronic Hardware, Software, Systems and Information Security
Notes: 33

## Slide 2: Executive Summary
We are proposing substantially increased use of Safety Risk Management to allocate FAA resources to Systems, Software, and Hardware Development Assurance
Our proposals can result in
  An order of magnitude fewer regulatory audits for major manufacturers
  The development of comprehensive, high-level objectives for Development Assurance Processes, providing much more flexibility for manufacturers to use new technology and processes
  Leveraging industry electronic component management standards and maintaining review of 95% of Airborne Electronic Hardware (AEH) at the Systems level
Our proposals allow the continued application of appropriate safety margins while allowing incremental improvement in safety through technology

## Slide 3: Executive Summary (2)
Our proposals involve six thrusts:
  Process-based vs. Product-Based—Applying Appropriate Oversight
  High-Level Objectives for Development Assurance Processes
    Provide alternative processes to, for example, RTCA DO-178 B/C
  Group Domain Audits on Historical Data
  Utilization of Risk-Based Decision Management Tools
  COTS AEH Reviewed during Systems Development Assurance, maintaining current approach of AC20-152
    RTCA DO-254A applicable only to custom micro-coded components
  Minimization of the number of Issue Papers

## Slide 4: Executive Summary (3)
Our proposals involve extensive coordination with Industry and other Regulatory Authorities, particularly EASA
  Executive involvement will be particularly critical to help overcome barriers to harmonization
Our proposals involve extensive socialization and significant training within the FAA

## Slide 5
Software Overview

## Slide 6
Risk Based Assurance Migration
Inflexible, duplicative design evaluation and assurance
Prescriptive, domain specific, detailed objectives
vs
Domain and technique Independent goal level objectives
Separate domain phase based audits based on incomplete phase data
vs
Grouped Domain audits on complete historical data
Migration to proposed risk based assurance does not invalidate current approach. Current processes can continue to be used for as long as the applicant chooses. The current processes form a subset of a broader set of acceptable solutions.
LEGEND:
Risk based proposal
Current approach
Poor matching of assurance effort to potential risk
Arbitrary mapping of design assurance criteria to risk
vs
Use of RBDM techniques to map criteria
Project based approval
vs
Process based approval
Unwarranted over auditing of applicants/developers for design assurance
Notes: One of the issues is associated with how we approve systems. Currently we evaluate the design (e.g. software) of each product even if the same organization and process produced the product. However our current approaches really aren’t evaluating the properties of the project but evaluating the process by which they are being developed and then examine small samples of the product data to see if they are following their process. This results in needless expenditure of time and effort by both the AA and the applicant/developer.
If we look at this from a risk based approach, we can see that we really only need to evaluate an applicant’s/developer’s process for compliance and after an initial evaluation of a product, and then go into a monitoring approach to detect any deviations. This moves the accoutability for producing a compliant project out of the FAA and back onto the applicant while still ensuring that they meet the regulatory guidance and regulations.

## Slide 7
4 AA audits
4 OEM audits
HLR(SW) req
LLR & architecture (design) req
Source code
Executable code
SW development Plans
Company X FMS developer
Periodic & event triggered audits
4 AA audits
4 AA audits
4 OEM audits
Project Based
Process Based
4 AA audits
4 OEM audits
HLR(SW) req
LLR & architecture (design) req
Source code
Executable code
SW development Plans
Company X FMS developer
4 AA audits
4 OEM audits
4 AA audits
4 OEM audits
4 AA audits
4 OEM audits
4 AA audits
4 OEM audits
4 AA audits
4 OEM audits
Notes: Our current system doesn’t really line up with the accountability framework the FAA is promoting. The FAA is taking on the responsibility for showing that each product meets the guidelines even if produced by the same manufacturer, using the same plans, and the same organization. Once the FAA has established that the organization is capable of producing compliant projects, it should be the applicant/developer who is responsible for maintaining that capability; not the FAA.

## Slide 8
Company X FMS Systems team
HLR(SW) req
LLR & architecture (design) req
Source code
Executable code
SW development Plans
Audit 1
Audit 1
Audit 1
Audit 1
Audit 1
Audit 2
Audit 1
Audit 1
Audit 3
Audit 1
Audit 1
Audit 4
Summary
Company X FMS HWteam
Company X FMS SW team
Single end of project audit
Complete project data
Initial steps can be done right now - today!
Notes: In order to evaluate the suitability of the design assurance data the current FAA guidance for SW and HW (and to a lesser extent systems) in the form of orders requires that in process audits be done on incomplete data at the different stages of development. First on the plans, then on the design, then on the actual code/FPGA, and finally a review of the summary information. If there are multiple airworthiness authorities and multiple OEMs, they each generally perform their own audits. Sometimes these can be coordinated sometimes night. Because the systems, HW, and software developments are asynchronous then so are the audits. However when the product is completed, all of the data from all the disciplines is available.
The risk is that the applicant has made a mistake and will have to rework the project at the very end. The applicant can elect to use the current system or, based on confidence in their ability, choose to do a final audit.

## Slide 9: “Right-Sizing” Number and Scope of Audits
Bilateral agreements with EASA and other regulatory authorities should be at the boundary of the approvals and associated criteria - not the details of the process of arriving at the approvals.
Regulatory agencies now working with each other and aircraft OEMs to “right-size” the number of regulator-required OEM audits of vendors

## Slide 10: Aircraft Systems Development Processes

## Slide 11: What is Airborne Electronic Hardware (AEH) Today?

## Slide 12: Two Categories of AEH
AEH Custom Coded Micro Components (CCMC) to DO-254 processes or equivalent & Intellectual Property (IP) cores
COTS (includes everything except CCMC)
  Commercial –Off-The-Shelf (COTS) Parts
  Complex COTS
  Simple COTS
  COTS sub-assemblies
  Line Replaceable Units (LRU)
  Circuit Board Assemblies
  Microprocessors
  Multi-Core Processors
  Integrated Circuits
  Data Busses (e.g., AFDX Ethernet)
  Discrete components
  Connectors
  Chassis
  etc.

## Slide 13: AEH Discrete Components

## Slide 14: AEH Integrated Circuit Components

## Slide 15: Circuit Board without Components

## Slide 16: Circuit Board with Components (sheet 1 of 3)

## Slide 17: Circuit Board with Components (sheet 2 of 3)

## Slide 18: Circuit Board with Components (sheet 3 of 3)

## Slide 19: Partial AEH Assembly

## Slide 20: IMA Cabinet

## Slide 21: AFDX Ethernet Data Bus

## Slide 22: AEH Schematic

## Slide 23: Aircraft Architecture

## Slide 24: Boeing 777 Flight Deck

## Slide 25: EASA / FAA Harmonization Issues
AC 20-152
2 pages
AC 20-152
2 pages
8110.105
36 pages
2005
2008
AC 20-152
2 pages
8110.105
36 pages
AEH CM
67 pages
2012
DO-254 for custom microcoded devices
Additions
CM,
Simple & Complex verification,
COTS IP,
Traceability
Additions
COTS,
Circuit Boards,
SEE,
Suppliers,
Change impact analysis,
PRs
FAA
FAA
EASA
Notes: The AEH guidance has evolved over the last 15years. Prior to 2005 there was a complex electronic hardware issue paper that was applied on some projects. AC 20-152 was only 2 pages. Order 8110.105 clarified the AEH guidance and addressed new topics such as COTS Intellectual Property. EASA’s Certification Memo (CM) added a bunch more topics. I personally provided comments to the EASA CM which highlighted that FAA and EASA would not be harmonized on topics such as COTS and circuit boards.

## Slide 26: EASA / FAA Next Meeting
Airborne Electronic Hardware (AEH) Harmonization Meeting was held during January 26-28, 2016 in Washington, DC
  FAA plans to harmonize EASA 67 page certification memo items with a new A(M)C
  EASA 67 page certification memo is highlighted in blue on previous slide
  Key to success is to reduce and streamline EASA certification memo content
  Reach consensus with EASA / FAA and Industry

## Slide 27: General Research Activities
NASA, Volpe, Atlantic City Technical Center
Aircraft certification’s Software and Digital Systems (SDS) research and Development Plan
  Software Development Techniques and Tools
  Airborne Electronic Hardware Design Techniques and Tools
  Onboard Network Security and Integrity
  Systems Considerations for Complex Software Intensive systems
    System Architecture Virtual Integration (SAVI)
    System Complexity Effects on Aircraft Safety
    Single Event Effects (SEE) Mitigation Techniques
    System Level Validation and Verification of Technical Standard Order (TSO) Requirements

## Slide 28: Safety Risk Management & AEH Regulatory Oversight

## Slide 29: Safety Risk Management Reviews
Evaluating AEH safety risk control strategies and effectiveness by reviewing:
  System problem report trends (increasing or decreasing) directly related to AEH parts
  In service difficulty reports
  Number and types of failures of AEH parts that have caused unsafe conditions in aircraft systems
  Airworthiness Directives (FAA has issued thousands over the last 10 years are any directly related to AEH parts?)
  Product Service History
  Review rapid changes in complex AEH parts technology that may create new failure modes
  When it is determined that safety risk control strategies are in place and are effective, than regulatory oversight activities may be reduced

## Slide 30: RBDM Implementation
The Risk Based Decision Making (RBDM) is part of the FAA Administrator’s Strategic plan
  In support of the RBDM initiative, the AIR-134 branch is evaluating the types of design error escapes from the DO-178B/C and DO-254 assurance processes as well as operational service problems with AEH parts
  We are collecting data from various sources (e.g., industry, international civil aviation authorities and other FAA data sources)
  Before we publish any new guidance, we want to make sure that there is a safety case to justify additional guidance in revisions to AC 20-152, AC 20-115C, AC 20-174, and DO-254

## Slide 31: FAA Strategic Plan Focus
  ASISP
    We’re focusing in, for the most part, on electronic connectivity to internal and external aircraft systems and networks
    We believe that the greatest threat is the exploitation of aircraft electronic access points

## Slide 32: ASISP Historical Overview
Since 2005 the FAA Aviation Safety (AVS) service has been using research and applying special conditions / companion issue papers to address electronic cyber-security threats to aircraft systems and networks (First special condition issued on B787 airplane program)
The FAA Transport Airplane Directorate has issued over twenty special conditions for certain make and model airplanes to address:
(1) Aircraft Electronic Systems Security Protection from unauthorized external access
      Addresses threats from external connectivity to aircraft systems from public networks such as the internet (refer to item 1 in figure 1)
(2) Isolation of Aircraft Electronic System Security Protection from Unauthorized Internal Access
      Addresses threats across aircraft systems domains such as potential hacking of entertainment systems (refer to item 2 in figure 1)

## Slide 33: ARAC Working Group Overview
As a result of the December 18, 2014 ARAC meeting, the FAA assigned and the Aviation Rulemaking Advisory Committee (ARAC) accepted a task establishing the ASISP working group
Two teams have been formed as follows;
(1) Transport Category Airplanes greater than 19 passenger seats
(2) General Aviation, Rotorcraft, and Transport Category airplanes less than 19 passenger seats
Team 1 plans to implement RTCA SC-216 industry standards which have parallel system and security development processes
Team 2 is proposing to address security requirements by using the traditional system, hardware and software development assurance processes
The final report is due August, 2016 and will include recommendations on both initial certification and continued airworthiness considerations for ASISP

## Slide 34: Change Impact Analysis (CIA)
  For every aircraft modification, a change impact analysis is required (According to RTCA DO-326A)
  The results of the change impact analysis may be used to determine if aircraft level or system level Security Risk Assessment is required
  Security Risk Assessment can be relatively simple or complex depending on the aircraft architecture and intended function of the information technology applications
  In most cases, federated avionics systems with uni-directional data busses (e.g., ARINC-429) that connect to the threat of public services should have system level, not aircraft level, Security Risk Assessment
  If it not possible to determine if mitigations are adequate at the system level, then Aircraft Security Risk Assessment will be required

## Slide 35: Aircraft Systems Information Security Protection (ASISP)
Notional Aircraft Domains
CNS/ATM & NextGen Services
Communication Navigation & Surveillance
Air Traffic Control Centers
GPS & Ground Navigation Aids
Airline Networks
(ACARS)
Internet / Public Networks
Controls
1
3
1
2
3
2
Network Security Access Points
Air Traffic Services (ATS) Provider
Non-Air Traffic Services Provider
FAA Air Traffic Services Connectivity
Internal Aircraft Network Security Controls
E-Enabled Aircraft Connectivity including FLS

## Slide 36: Aircraft Rules, Processes & Standards
Federal Aviation Regulation's (FARs)
FAR 25.1301 “General Requirements for Intended Function”
FAR 25.1309 “Equipment Systems and Installation”
Special Conditions establish the rule basis for Aircraft Systems Information Security Protection (ASISP) for certain make and model aircraft with new and novel architectures
  Companion Issue Papers to Special Conditions provide a means of compliance
Development Assurance Industry Process Standards
RTCA DO-178C “Software Development Guidance”
RTCA DO-254 “Airborne Electronic Hardware Development Guidance”
ARP 4754a “Guidelines for Development of Civil Aircraft and Systems”
ARP 4761 “Guidelines and Methods for Conducting the Safety Assessment Process on Civil Airborne Systems”
ASISP Industry Standards for Transport Category Airplanes
RTCA, DO-326a, DO-355, DO-356 “Industry standards for ASISP include initial certification and continued airworthiness to address the ever-evolving security threat environment”
Technical Standard Orders (TSO) for External Aircraft Connectivity
FAA TSO’s invoke certain industry standards for aircraft safety, performance and interoperability connectivity requirements to United States Air Traffic Service Providers (ATS)
TSO’s include aircraft standards for connectivity to Air Traffic Management (ATM), NextGen Communication, Navigation, and Surveillance (CNS) services and public networks
Notes: The final slide, when Issue Papers and Special Conditions are required the Issue Papers and Special Conditions should require a Security Plan that address these topics.
CISSP listed in first item is Certified Information Systems Security Professional awarded by ISC2. There are other organizations such as SANS that award security certifications.
Security Controls listed in fifth item can be technical, operational, or management. See National Institute of Standards Special Publication 800-53A.

## Slide 37: Security Research Projects
37
Candidates for Security Research
  Data Networks
  Data Links (e.g., ACARS)
  Security Controls
  Security Risk Assessment Process Effectiveness
  Connecting EFB portable systems using the AEEC Aircraft Interface Device (AID) standard
  Commercial-Off-The Shelf (COTS) components
  Security Penetration Testing
  Unmanned Aircraft Systems (UAS)
  Aircraft security health monitoring
Notes: 37

## Slide 38: What is EFB Aircraft Systems Information Security Protection Today?

## Slide 39: Portable EFB Connectivity to Aircraft Networks
Portable EFB Connectivity requirements
  All of the security controls for aircraft network connectivity to portable EFB systems must be designed approved by aircraft certification
  The aircraft network security access points must be designed to ensure that no failure of a portable EFB system may adversely effect the network
  No credit is given for security controls resident in the portable EFB system for network connectivity to aircraft
AEEC EFB Aircraft Interface Device (AID)
  Protocol converter between ARINC-429 (LAN) and IPAD network
  4 ARINC-429 receivers
  2 ARINC-429 transmitters (Aircraft printer and ACARS)

## Slide 41: Typical Application & Services
Cockpit Terminal - EFB
Attendant EFB
Wireless
Cabin
Distribution
Airborne
Communication
Links (ACARS, XM,
Sirius,JetConnect)
Flight Ops
Weather
Electronic Manuals/Charts
Cabin Surveillance
Surface Moving Maps
Flight Papers/Data
Typical Applications and Services
Onboard/Passenger
Rebooking/IRROPS
Customer Profiles
Buy On Board
Live Audio
Email/WAP Browsing
Maintenance
*FIX
Flight Data Downloads
Electronic Logbook
Maintenance Data Collection
Electronic MEL
Server
Air to Air
Data Link
(Sirius/XM or
JetConnect)

## Slide 42: Questions & Wrap-Up