## Slide 1: Helicopter Flight Data Monitoring Research for ASIAS Presented to: REDAC – SAS Subcommittee Meeting Alexandria, VA
Presented By:
Cliff Johnson, ANG-E272, Research Engineer, NextGen, FAA William J. Hughes Technical Center, Atlantic City, NJ
Sep. 14, 2016

## Slide 2: Research Project Motivation
A system for secure, confidential, and protected safety analysis of flight data records
Participating operators are the key stakeholders, users and beneficiaries of the system
Early development and maintenance by HAI, transferred to MITRE for full-scale operation, both independent 3rd parties with strong ties to operators and industry
Research components of development and safety analysis supported by PEGASAS team for rotorcraft operations and FDM
Supported by the FAA in its mission to promote and advance flight safety
What is ASIAS?
Why ASIAS for Rotorcraft?
U.S. Helicopter Fatal Accident & Fatality Rates

## Slide 3
U.S. Helicopter Fatal Accident & Fatality Rate
Flight hours source:
-Years 12-14 from FAA's GA & Part 135 Activity Survey.
-Years 15-16 from FAA's Aerospace Forecast FY2016-2036.
Notes: 3

## Slide 4: “Priority” Occurrence Category by CAST/ICAO Common Taxonomy Team (CICTT) CY 2009 – 2013 (104 fatal accidents)
Top 3 Occurrence Categories = 50% of 104 fatal accidents.
LOC-I = Loss of Control – Inflight
UIMC = Unintended Flight In IMC
LALT = Low Altitude Operations

## Slide 5: Fatal Accidents by Industry CY 2009 – 2013 (104 fatal accidents)

## Slide 6: USHST V2.0 Goal
20% reduction in the U.S. helicopter fatal accident rate by CY2020
  Four year goal
    Start Date: January, 2016
    End Date: December, 2019
  Baseline for measurement
    5 year average for the U.S. fatal accident rate
    Average of CYs 09-10, 12-14 = 0.76
    CY11 excluded due to problems with FAA’s GA Survey that year
  To achieve goal of a 20% reduction by CY2020:
    Fatal accident rate reduced from 0.76 to 0.61 or less by the end of CY 2019

## Slide 7
U.S. Helicopter Fatal Accident Rate
Flight hours source:
-5 Yr Baseline from FAA's GA & Part 135 Activity Survey.
-2016 from FAA's Aerospace Forecast FY2016-2036.
Goal by end of CY 2019:
20% reduction from 5 year baseline
0.39, Jan-Mar
Notes: 7

## Slide 8
Rotorcraft Research for ASIAS
ASIAS Rotorcraft Analysis Capabilities
Supports the USHST Goal of 20% Reduction in the Fatal Accident Rate for Helicopters by 2020
Safety Metrics
HFDM Analysis Techniques
HFDM Modeling Techniques
HFDM Cockpit Audio/Video Analysis
Data Mining for Safety Events
Identification of High-Risk Safety Events
Industry Involvement
Potential Mitigation Partner
FDM Equipment Working Group
Program Management
Outreach
Flight Tests
HFDM Device Integration & Calibration
Data Analysis
Modeling & Simulation
Outreach
Data Transcription
HFDM Research Repository
HFDM Architecture Design
HFDM Working Group
Notes: There are some dialog regarding incorporating UAS in ASIAS

## Slide 9: FAA Helicopter Flight Data Monitoring Research Team Members
Prof. Dimitri Mavris – PI
Hernando Jimenez – Co-PI
Kyle Collins
Simon Briceno
Alek Gavrilovski
Alexia Payan
Prof. Karen Marais – PI
Arjun Rao – Co-PI
Inseok Hwang
Arjun Rao
Sanghuyn Shin
Prof. Stephen Cusick – PI
Keith Cianfrani
Cliff Johnson – Rotorcraft ASIAS Research Lead
FAA (ANG) WJHTC Atlantic City, NJ
Walt Hogan – Research Sponsor
FAA (AVP) Washington, DC
Alex Ahlstein – ASIAS Group Leader
Mike Yablonski – Principal Aviation Systems Engineer
MITRE-CASSD
*Note: MITRE role involves collaboration with research activities for integration with overall ASIAS.
Ed DiCampli, Chief Operating Officer– PI
Harold Summers, Director of Flight Operations
Jay Clark, Manager, Information Systems
Kipp Lau, RASIAS FDM Consultant
Robert Liguori, RASIAS IT Consultant
Keith Cianfrani, FDM Specialist/Outreach
Tyler Travis
Lana Manovych
Jean-Christophe Geffard
Steve Cullen
Scott Sunder

## Slide 10
Concept of Rotorcraft HFDM Research Repository for ASIAS
Participating Operators
PEGASAS Research Team for Rotorcraft ASIAS
Analysis ToolSuite Creator
Flight Data Records
Analysis Results
Aggregate Results
Own-Access User
Aggregate Results
De-identified Data Access User
FAA, Sponsor
Database
Analysis Toolkit
Interface & Display
Rotorcraft ASIAS
Analysis Tools
All Missions
Flight Training
Charter
EMS
Oil/Gas
Logging
Police
News
Cargo Lift
…
Visualizations, Algorithms, Event Definitions
Secure
System
System Developer & Administrator

## Slide 11: Helicopter Flight Data Analysis Conceptual View
FDAU
Microphones
Cockpit camera
QAR
Data acquisition
Data processing
Onboard computer
Data analysis

## Slide 12: Rotorcraft ASIAS HFDM Research Architecture
HFDM Data Collection | HFDM Database Persistence | HFDM Business-logic Routines | HFDM Analytics Connectivity
Upload | Interchange Standard | Metric Routines | Web Services
Transforms | MongoDB | Analytic Routines | Messaging
Mediation Routing | Hadoop | Aggregate Routines | Access / Security
Database Loading | De-identify | Notification Routines | 
3rd-Party Product Integration (INPUTS)
Recording Devices
Simulators
Data Sources
Web Services
External Analytics Capabilities (OUTPUTS)
HFDM Research Website
Enterprise Data Access
Aggregate Reports
Simulators Support

## Slide 13: HFDM Data Processing Architecture

## Slide 14: HFDM Prototype Repository

## Slide 15: HFDM FDR/Simulator Integration

## Slide 16: Safety Metrics for Rotorcraft Operations
Research Objective: Define Safety Metrics for Rotorcraft from HFDM data
Tailored to address highest causal factors from USHST Fatal Accident Rate
High Priority
In flight
LOC
CFIT
On the ground
Roll-over
Medium priority
In flight
Close to ground
Low priority
In flight
Helipad overrun
Autorotation
Unstabilized approach
System failure/malfunction
LTE
IMC
Fuel low
Proximity to Obstacles/Weather/Other aircraft
Abnormal runway contact
LOC
Vortex Ring State
Unstabilized approach
Hard landing
Bird strike
External load
On the ground
Runway incursion/excursion
Abrupt maneuver

## Slide 17: Proximity to Obstacles – Single Flight Metric
Speed vector
Closure speed
Closure distance
N
E
ϕ
(lat,long)
(lat,long)
0 1000 2000 3000 4000 5000 6000 7000
6
5
4
3
2
1
0
Closure Distance to Obstacle (feet)
104
Time steps
Time steps
140
120
100
80
60
40
20
0
0 1000 2000 3000 4000 5000 6000 7000
Closure Speed (knots)
Helicopter Speed
Closure
Speed
Notes: This slide contains animations.
The illustration shows what variables are being calculated: closure distance and closure speed.
These variables are calculated for each obstacle within the safety box.
The closure distance is obtained assuming that the helicopter is travelling directly towards the obstacle and the closure speed is the component of the helicopter speed vector directed towards the obstacle.
For instance, for the obstacle circled in red (click), the closure distance and closure speed look like the graphs.
As the helicopter approaches the obstacle, the closure distance decreases and the closure speed increases.
The closure distance is minimum at closest approach, while the closure speed goes to zero (the helicopter is passing by the obstacle but travels at 90 degrees compared to the helicopter-obstacle line).
For each obstacle within the safety box, one can calculate the closure time as the ratio of the closure distance to the closure speed.
The closure time is then used to determine potentially hazardous obstacles located within a critical closure time from the helicopter.

## Slide 18: Proximity to Weather Metric
% of Recording Time
Weather Severity Level
% of Recording Time
Weather Severity Level
More than ~10 flights
CIWS Weather Severity Levels +
Flight Data Records
Vertical Integrated Liquid water (VIL)
Longitude
Latitude
Black – Wx Sev. 1
Blue – Wx Sev. 2
Green – Wx Sev. 3
Yellow – Wx Sev. 4
Magenta – Wx Sev. 5
Red – Wx Sev. 6
Weather Severity Level
% of Recording Time
Longitude
Latitude
Less than ~10 flights
Notes: For the proximity to weather safety metric, we start with several simulated flights in the Atlanta area and the associated CIWS (Corridor Integrated Weather System) weather severity levels obtained from Tom Tessitore and team webserver.
There are two types of analyses that may be performed depending on the number of flights/recordings considered.
* If we have less than ~10 flights/recordings, then we may look at the color-coded flight paths depicting the severity level of the weather encountered during those flights. We may also determine the distributions of percentages of total flight times spent at each weather severity level for each of the flights considered.
This type of graph provides some information as to the global level of safety (across multiple flights) for a given operator with respect to potentially severe weather.
In this case, the total number of flights considered is rather low (8 flights) so the histogram chart is appropriate. From this, we can identify some more critical flights/recordings that may warrant further investigation, such as flight #8 here for which the percentages of time spent at weather severity levels 3, 4, and 5 are the highest amongst the flights considered.
* When the number of flights become large, the flight paths and histogram depictions become too crowded and it is impossible to derive useful information. In such a case, it is more interesting to represent percentages of flight time spent at each weather severity level as a cloud of points (one point for each flight) and then to derive some general statistics. For example, on the graph in the top-right corner, each dot at each weather severity level represents the percentage of flight time spent at this weather severity level for a given flight (there are 8 flights and therefore 8 dots for each weather severity level).
The graph in the bottom-right corner which is a box plot, shows 3 statistics of the percentage of flight time spent at each weather severity level for all the flights considered, based on the data in the top graph:
The median (red line)
The 25th and 75th percentiles (bottom and top lines of the blue box)
Also shown are :
Any outliers (red cross)
The min and max values
This allows the operator to identify some overall operational safety trends.
These capabilities have been handed over to Robert for implementation into the system.

## Slide 19: Stabilized/Unstabilized Approach Metric
Combined database
Airport/Helipad/Runway Data + Flight Data Records
Notes: This last slide presents an overview of the data required and the approach envisioned for prototyping the (un)stabilized approach safety metric.
We start with the airport facilities and airport runways databases from the FAA that we combine into a single database listing the type of airport, its ICAO ID, location, elevation, and longest runway dimensions (length, width) or helipad dimensions.
We also have 15 flight data records from the FAA flight tests depicted on the graph to the left.
From these flight data records, we can isolate the “final” portion of flight from the landing site that we could consider being an approach. For example, on the google Earth representation, we considered the last 1.5 nm before landing.
On the graph to right, we depict the evolution of the vertical speed for the last 1.5 nm of each flight, or in other words, for what could be considered the “approach” for all flights.
Problems with flight records: Robert is investigating…
Still investigating the best way to prototype this safety metric.

## Slide 20: Loss of Control Safety Metrics
https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/helicopter_flying_handbook/media/hfh_ch11.pdf
https://www.faasafety.gov/gslac/ALC/course_content.aspx?cID=104&sID=452&preview=true
30% of all accidents involve Loss of Control (LOC)
Going after major LOC categories
Autorotation
VRS
Dynamic Rollover

## Slide 21: Loss of Control Modeling
Autorotation
VRS
Dynamic Rollover
Actuator disk
Power available
Power required curve
Autorotation possible at these forward velocities, at the specified descent rate
- Power required +
ΔP
Power required
Increase descent rate
Notes: The goal is to develop a physics-based metric for each of these conditions that will allow dangerous flight states to be detected. Part of the motivation for basing the detection on physical quantities is that it makes the detection more objective, which in turns allows the same condition to be established for a different vehicle and different weight/configuration. These metrics are to be used alongside existing safety events in R-ASIAS; the new physics based metrics can provide a degree of traceability and consistency across operators, helicopter types.
So far we have been using different models for each metric and condition associated with loss of control. This has let us look at these conditions “quickly”, but we are getting to where the integration of the various models makes sense. So from here on we are looking at dynamic models, using the rigid body from the dynamic rollover modeling, and the some aerodynamics developed for the autorotation and VRS modeling. More sophisticated models exist and may be used, but it’s all about implementing a useful model in a timely fashion and proceeding with further development as necessary.

## Slide 22: Loss of Control Prototyping
Dynamic Rollover
VRS
Autorotation
Dynamic model for rollover detection
Vortex Ring State
Autorotation
Notes: In autorotation the all the power required is supplied not by the engine but by the tradeoff of kinetic and potential energy. There is an minimum descent speed for each forward velocity that allows autorotation to be sustained, which is represented by the dashed blue line, which corresponds to zero power required. This alone is already an improvement over the typical safety events which are a simplification of the actual shape of this boundary. Since we have can use the incoming flight data to calculate the instantaneous power requirement we can detect when this power requirement becomes positive, meaning the rotor begins slowing down.
Next is vortex ring state, sometimes known as settling with power, but here we will make a distinction between the two for the sake of clarity. We are not looking to calculate the complex airflow through and around the rotor in VRS, which is a much bigger problem, but to extract the flight states where VRS can be encountered. This is done by calculating the inflow velocity at a particular flight condition and determining whether the tip vortices accumulate at the rotor or are convected away. If the free-stream flow is at a sufficiently high angle to the rotor disk (as in descent or quick-stop maneuvers) then the vortices accumulate at the disk and VRS can occur. The models employed are a further development of those used for autorotation and accurately (they are validated) capture the average flow in this flight state. With minor modifications the theory used is suitable for dynamic simulation.
At the bottom is a result from the dynamic model, and a benefit here is that we have the time component which lets us express the safety consistently for a much larger variety of conditions than VRS and autorotation, and other such conditions with “well defined” boundaries (power criterion or vortex transport criterion). With the time information as a criterion, we can express the boundaries in some logical set of parameters

## Slide 23: HFDM Cockpit Video Data Processing/Analysis
Attitude Estimation using Data Mining | Flight Information Extraction from Panel
Notes: Hernando,
I have added a movie which shows the results with our algorithm in the slide. If you click the slide, the movie will show up, and it will be played with another click. Three bullets explain the framework for the video and audio analysis (which was used in the presentation at Heliexpo 2015.)
The left side of the table is about the helicopter’s attitude estimation using data mining techniques.
In there, the first figure (upper-left) represents the original image that we obtained from the public domain (Youtube).
The second figure shows the gray-based image generated using an image averaging technique (i.e., mean of multiple gray-based frames).
The third figure is the image to show the boundary detection for the points which have high differences between the intensities of pixels after removing noise (e.g., a helicopter frame, pilots and a flight instrument panel).
The fourth figure is the image to show the estimated bank angle after applying data mining techniques on the points in the previous figure.
Similarly, the right side of the table is about the flight state information extraction from flight instrument panels using data mining techniques.
The first figure represents the original image that we generated using X-plane for developing and testing our algorithm.
The second figure shows the gray-based image generated using an image averaging technique (i.e., mean of multiple gray-based frames) after removing noise (in this subtask, noise is the outside view and pilots).
The third figure is the image to show that our algorithm using data mining techniques detects the boundaries of the indicators and gauges.
The fourth figure is the image to show that our algorithm identifies the position of the gauge by applying the linear fit on the boundary of the gauge in the previous figure.
Lastly, the movie shows how well our algorithm follows the gauge in the indicator.

## Slide 24: Audio Analysis – Cockpit Alarm Detection and Identification
Research team has developed a cockpit alarm detection and identification algorithm composed of:
  Alarm detection: Short Time Fourier Transform (STFT) to obtain time-based frequency information and Cumulative Sum Chart (CUSUM) for statistical change detection
  Alarm identification: Correlation analysis with alarm database
Input:
audio data
Output:
Alarm types and occurrence times
autopilot_disco
dash_MIDDLE
Notes: STFT analysis is able to convert the sections of the audio signal to the frequency domain. However this alone is not enough to detect individual alarms
Since multiple alarm sounds occur concurrently, we can’t clearly remove the noises. So STFT is not enough to detect their occurrence times.
Due to this reason, CUSUM is used to identify changes in the STFT analysis to located when individual alarms occur. Rather than simply looking for the presence of alarm frequencies, we look at the change over time to determine start and end times.
Alarm Detection is achieved by performing sequential frequency analysis to identify instances when alarms are triggered and when they end. This information can be integrated with that extracted from image analysis to gain a more comprehensive understanding of a rotorcraft’s flight. As before, this algorithm can be used to extract information for FDM programs or in accident investigation.

## Slide 25: Audio Analysis – Engine/Rotor Noise
Cockpit audio is analyzed in the frequency domain, correlated with flight parameters and represented as a statistical model
The noise profile can be used to estimate engine data (such as torque and/or rpm)
If flight data is available, it can be compared with estimates to identify anomalous behavior
Flight parameters can be estimated by frequency analysis and the statistical model
Engine has a higher than expected frequency for some data points
Notes: Using the model created in the previous step, audio from the cockpit can be analyzed to estimate the engine parameters during flight.
If the true value of the flight parameters is available from onboard sensors, it can be compared with the estimates to identify anomalous sounds. The resulting anomalous can be of two types; intermittent or constant anomaly.
Intermittent anomalies indicate short instances in flight when the noise behavior lies outside the expected frequencies. This can provide insight into when or in what regimes the helicopter engine is behaving abnormally. While there may be a multitude of reasons behinds this aberration, this manner of analysis provides the operator the tools to identify and evaluate such instances.
Constant anomalies refer to flights when the cockpit background noise is significantly different from what is expected based on the flight parameters through the majority of the flight. This may be a result of a larger issue with the engine, poorly configured/positioned microphones or a number of other reasons. But once again, this analysis provides the operator to investigate a potential problem before it can lead to any incident.

## Slide 26: Identifying High-Risk Safety Events
Analysis of helicopter accident and incident data to assess severity and frequency of occurrence chains.
Statistical analysis of FDR data to estimate probabilities of safety events.
Mapping of FDM safety events to occurrence chains with SME input.
Occurrence Chain |  | Percent | Ranking
First Occurrence | Second Occurrence |  | 
Loss of control-inflight (250) | - | 13.1% | 1
Inflight collision with object (220) | - | 5.6% | 2
Loss of engine power (350) | Forced landing (180) | 5.5% | 3
Loss of engine power-non-mechanical (353) | Forced landing (180) | 5.3% | 4
Inflight collision with terrain/water (230S) | - | 5.2% | 5

## Slide 27: Data Mining for HFDM
Classification
Association
Clustering
Regression
Supervised
Unsupervised
Type of technique
.
.
.
.
.
.
.
.
.
.
.
.
Promising initial results
Unsupervised techniques have been applied with success
Clustering and sequence mining most common in aviation applications
Spatio-temporal techniques seem like a natural fit
A wide variety of “feature extraction” approaches have been reported
Unsupervised technique applied to simulated data
Analysis was performed using both event-based detection and the data mining approach
New and previously undefined conditions were detected

## Slide 28: Data Mining Application Determining Helicopter Phase of Flight
Rotorcraft phase of flight definition based on authoritative sources
Data processing / smoothing
ICAO common taxonomy team – ICAO
FAA helicopter flying handbook – FAA
Principles of helicopter flight from W. J. Wagtendonk - POH
Low pass filter (FFT with Gaussian filter)
Moving average (backward, center)
Local regression (weights, 1st or 2nd order)
Robust local regression (neglect outliers)
Savitzky-golay (1st or 2nd order, successive fitting)
Piece-wise linear regression
Digitization

## Slide 29: FAA HFDM Test Flights

## Slide 30: FAA R&D Test Flights
Test Platform
  FAA’s Sikorsky S-76A Helicopter, Equipped with ADS-B Out (1090ES)
HFDM / HFDR Devices
  Current devices: Appareo Vision 1000, L3 Light Data Recorder, Honeywell Skyconnect Tracker 3, Ballard, Stratus, MEMSIC AHRS, iLevil AHRS, GoPro Cameras (6), General Aviation Airborne Recording Device (GAARD)
  Additional devices: Skytrac, North FDS/Outerlink IRIS, Latitude iONode, others
Research Goals
  Identify, examine, and install several different HFDM/HFDR units
  Collect/process data from each HFDM/HFDR system for different scenarios/conditions
Research Outputs
  Helicopter FDM Data to be used to define and validate future analysis of events, parameters, exceedances, recording rates, etc. from anomalous data
  Installation guidelines and optimal locations for each system
Notes: Research Goals:
  Identify, examine, and install several different FDM/FDR units
  Collect/process data from each FDM/FDR system for different scenarios/conditions
Research Outputs:
  AVP: Baseline Helicopter FDM Data to be used to define and validate future analysis of events, parameters, exceedances, recording rates, etc. from anomalous data
  AFS: Installation guidelines and optimal locations for each FDR system
Supports both AVP & AFS TCRG Requirements

## Slide 31: FAA R&D Test Flights
GAARD & Foreflight Mobile Applications during data collection
Notes: Research Goals:
  Identify, examine, and install several different FDM/FDR units
  Collect/process data from each FDM/FDR system for different scenarios/conditions
Research Outputs:
  AVP: Baseline Helicopter FDM Data to be used to define and validate future analysis of events, parameters, exceedances, recording rates, etc. from anomalous data
  AFS: Installation guidelines and optimal locations for each FDR system
Supports both AVP & AFS TCRG Requirements

## Slide 32: Rotorcraft ASIAS Timeline
Secure Operator Participation
Develop governance, establish agreements, insure data protection and confidentiality, test and monitor data transfer, elicit operator feedback, ensure and monitor value added to operators, enhance system to meet emerging operator needs
Develop Rotorcraft ASIAS System
Requirements analysis, system architecting and design, implementation, standards for data formatting/processing prototyping, testing, incremental delivery of tools and capabilities, integration with existing ASIAS communities
Support Rotorcraft ASIAS Research
Establish generic event set, identify event set gaps, video/audio processing, safety metrics, software capabilities, data fusion, accident mapping, performance models, FDM flight testing, data mining and knowledge discovery with FDM data
Conduct Outreach and Community Engagement
Establish outreach efforts within the Helicopter Community, present research topics & results at Heli-Expo, industry forums/events, HFDM Working Groups, mitigation partner
2013
2015
2017
2019
Research Prototype || Full Integration with ASIAS

## Slide 33: Questions?