## Slide 1: FAA UAS Concept Maturation, Validation & Requirements Development
Presented to: SAS REDAC Committee
Presented by: Sherri Magyarits
NextGen Organization
Advanced Concepts Branch
Maureen Keegan
Air Traffic Organization
Technical Analysis & Operational Requirements Group
Date: September 15, 2016

## Slide 2: Our Focus
Concept development, validation, and requirements
Systems engineering process to provide structure and traceability
Operational perspective
Notes: Concept and requirements development
  How it’s the way we determine changes we need to make, etc to bring something new into nas
System engineering…
No matter what the problem…defined process in place, structured approach
Operational perspective
  Work reported here represents a piece of the faa uas development story, class of airspace
  Not regulatory – but work coordinated across faa lines of business to ensure concurrence

## Slide 3: Framing the Challenge of Integrating UAS into the NAS
UAS operations are on the rise
  Model Aircraft/Hobbyist Operations
  Low Altitude Visual Line Of Sight (VLOS) Operations
  Low Altitude Beyond Visual Line Of Sight (BVLOS) Operations
  Public UAS Operations (All Sizes and Airspace)
  Integrated UAS Operations
Notes:   How we’ve united around the problem and the work that needs to be done
  Will show how work ties together to address these areas by end of briefing
  Consistent view throughout FAA

## Slide 4: Briefing Contents
Operational Concept Development
Strategic Plans Moving Forward
Deep Dive Example - Traceability from ConOps to 2016 Projects
Wrap Up
Current Activities

## Slide 5: Operational Concept Development

## Slide 6: Historical Summary of UAS Concept Development
Developed and delivered FAA UAS Concept of Operations (ConOps) v2.0 for mature state, integrated UAS operations
Derived initial UAS operational requirements from the FAA ConOps
Initiated concept maturation effort to address mid-term concerns / needs (e.g., predicted surge in sUAS operations)
Developed, refined, and vetted mid-term (predominantly segregated) and mature state (integrated) UAS operational scenarios and requirements
Developed and vetted service/scenario responsibility allocation tables to determine FAA/ANSP and UAS operator/pilot in command roles
Completed UAS Concept Maturation Plan and UAS Operations Evolution Strategy (OES)
Completed Low Altitude UAS Operating Concepts paper
Developed requirements to support ATC notification/authorization
  2012
  2016

## Slide 7: FAA UAS ConOps Overview Development Strategy Concept Assumptions

## Slide 8: High-Level UAS ConOps Development
Developed FAA UAS Concept of Operations (ConOps) for mature state integrated UAS operations, due to growing interest and demand for UAS access to airspace
  ConOps addresses beyond visual line of sight (BVLOS) UAS operations.
  ConOps intentionally did not address sUAS operations operating within visual line of sight (VLOS) of the operator, due to the concurrent drafting of Part 107, which was expected to cover those operations.

## Slide 9: ConOps Development Approach
  What is ‘Integrated’?
  ‘File and fly’ operations. Integrated operations require
  no mitigations to operate in the NAS.
  Objectives
  Begin the systems engineering process of identifying operational and system-level requirements necessary to achieve integrated operations
  Establish framework for alignment of UAS efforts across FAA (roadmaps, research plans and activities) to validate and inform path to integration
Identify touch points and interactions with NextGen systems, capabilities, and operational improvements
Document FAA expectations of UAS operators, in terms of operations, performance, and airworthiness
Public
Integrated

## Slide 10: ConOps Development Approach (cont’d)
Multi-FAA Line of Business (LOB) Development & Review Team
Established multi-organizational development team comprised of FAA and UAS subject matter experts (SMEs) to encompass air traffic, safety, and system perspectives and foster early internal stakeholder acceptance of the vision
Narrative
Written primarily from an air traffic perspective
  Timeframe is milestone-driven
Obtained signatures of concurrence from FAA Executives in the Safety, Air Traffic, NextGen, Airports, and Policy & Environment organizations

## Slide 11: Summary of Key Integration Assumptions
UAS are aircraft and behave in a manner similar to manned aircraft. This includes meeting the performance and equipage requirements established for the airspace class and/or route in which they are operating.
Certification of airworthiness and a capability analogous to that required under “see and avoid” requirements of 14 CFR Part 91 are pre-requisites to NAS integration.
UAS adhere to current and future ATC procedures, requirements, and instructions using standard phraseology. The FAA creates no new airspace classes specifically to support UAS.
Autonomous operations are not authorized – meaning, the Pilot in Command (PIC) can always assume direct control of the aircraft during normal operations. There is a 1-to-1 relationship between the PIC and the UA.
ATC remains responsible for separation services as required by airspace class and flight plan type using applicable separation minima.
FAA policy, guidelines, and automation support priority for individual flights, and equitable access to airspace and air traffic services.
11

## Slide 12: No Visual Compliance
For BVLOS operations:
UAS cannot comply with Visual Flight Rules (VFR) or with any clearance that includes a visual component, as these rules are based the use of human natural vision (not the use of technology to perform such functions)
Current regulations that address the use of human visual references are not based on measurable or quantitative criteria; and therefore cannot be used as a basis for establishing instrument equivalency
Today’s IFR provides a basis for flying without natural vision, however many visual operations exist under today’s IFR
New regulations/rulemaking and procedures are required

## Slide 13: UAS Operational Shortfalls & Requirements ConOps Decomposition FAA Requirements UAS Operator Requirements

## Slide 14: ConOps Decomposition
  * “Requirements” is an umbrella term for concept level operational requirements, agency actions, & policy needs, as well as “expectations” of compliance and performance on the part of the UAS operator.
  Requirements/expectations are not static – they will continue to be matured, validated or invalidated, & updated.
Consolidation Vetting
Validation Review
Potential
Requirements *
for Integrated UAS Operations
Refined Set of Requirements for Integrated UAS Operations
UAS ConOps v2.0 Narrative
Certification
Flight Planning
Operational Approval
Policy
Safety
Operations
Training
Categorization
FAA
UAS Operator

## Slide 15: FAA Requirements

## Slide 16: UAS Operator Requirements
Shared with UAS test sites in 2014 in form of ‘Potential Research Areas’

## Slide 17: UAS Concept Maturation

## Slide 18: Concept Maturation Overview
  Ensure coverage of the evolution of UAS operations
    Generate scenarios that cover the gap between current day and the mature state vision (contained in the ConOps). Focus on the ‘mid-term’ timeframe (~2018-2020)
    Further identify policy, procedural, regulatory, and other issues associated with predicted types of UAS operations covering the evolution of UAS operations
    Review existing mature state scenarios (contained in the ConOps) to incorporate updated perspectives – scenarios that reflect rolling evolution
    Prioritize work based on lead times to incorporate changes into the NAS (procedures, air traffic control (ATC) automation support, policy) and evolve demand forecast data

## Slide 19: Mid-Term Timeframe Definition
Forecast Considerations
If a NAS system enhancement was not slated for probable delivery by 2018, it was considered not available
For example
  Data communications
  NAS Voice Switch
Commercial COA
UAS undergoing certification
COA for Ops: no DAA cap
sUAS (VLOS) flying without COA
Larger UAS ADV-B equipped
On-board DAA not required for Class A: Positive Control Airspace
C2 MOPS non-satellite
C2 via non-satellite
Authorized to transition through Classes D, E, G without a COA (limited duration)
Authorized to fly in Class A w/out COA
C2 MOPS satellite
C2 via satellite
G-G Comm
Transit certified DAA
Type Certs based on MOPS
Fully certified DAA equipment
Authorized to transition through Classes D, E, G without a COA
Type certifications based on MOPS
2013
Mature State
Mid-Term
2018-2020
NAS Programs
Operational Milestones

## Slide 20: Concept Maturation Products
Mid-term (VLOS, EVLOS, & BVLOS) and updated mature state (integrated) operational scenarios (22)
Scenario service/responsibility allocation tables of FAA/Air Navigation Service Provider (ANSP), UAS Operator/Pilot-in-Command (PIC), and Manned Aircraft PIC responsibilities
Low altitude operating concepts paper – documenting FAA perspectives (based on concept maturation work) for operations not covered in the FAA UAS ConOps.
Updated and expanded shortfalls and operational requirements to inform FAA investments

## Slide 21: Operational Scenarios Mid-Term Operational Scenarios Mature State Operational Scenarios

## Slide 22: Summary of Mid-Term Operational Scenarios
Scenario Name | Flight Plan | Airspace | Purpose of Flight | Aircraft | Mid-Term Highlights
Flight Planning | IFR, Notify | All | N/A | All | Negotiation of flight plan prior to departure and updates during flight.
Surface Operations | N/A | Class C or Class D | N/A | All | For ground movement on towered airports. Interact with other traffic & ATC on the surface.
Border Patrol/ Monitoring | IFR | Class D arr/dep, aerial work in Class A | Border patrol | Predator B | Planned maneuver and unplanned deviation. Go-around.
Atmospheric Monitoring (HALE) | IFR | Class A, Class E high altitude | Environmental Sensing | HALE | Slow transition through Class A. Long-endurance above FL600.
Search and Rescue | IFR | Class G, Class E - TFR | Search and Rescue at night | ScanEagle | Search operations Class E airspace.
Agricultural Monitoring | Notify | Class G, D | Agriculture mapping | Trimble UX5 | Survey of farmer’s land to provide detailed information to the farmer about his crops.
Pipeline Surveillance | Notify | Class G, transition Class D | Pipeline monitoring | ScanEagle | Designated route specifically for UAS (under 500 ft. AGL).
Accident Scene (HazMat) Investigation | Notify | Class B | Monitoring specific situations on the ground | ShadowHawk, Aeryon Scout | Control in and around urban areas. Flyaway in terminal area.
Maritime Surveillance | IFR | Class A oceanic | Surveillance | Global Hawk | Oceanic high and low altitude.
Offshore Surveillance with Due Regard | IFR | Oceanic off-shore, Class A, Class D airport | Surveillance Due Regard, off-shore | ScanEagle | Oceanic Due Regard off-shore operations picking up IFR flight plan back into airport in Class D.
Lost Link | IFR | Class D, A | Demonstrate LL procedures for Terminal and En-route | All | Lost link/contingency route activation, ground-ground CPDLC, procedural changes.

## Slide 23: Mid-Term Scenario Distinctions
Use of Segregation
  Segregated operations require some form of mitigation—instituted by FAA and/or ATC (e.g., authorizing the use of a UR or allocating an airspace volume [either of which may or may not be exclusionary to other airspace users]) or by the UAS operator (e.g., operating away from people and property)—to compensate for lack of certified airborne DAA and/or other shortfalls (e.g., C2 latency).
Notification in lieu of an IFR flight plan
Public
Commercial BVLOS
Commercial VLOS

## Slide 24: Summary of Mature State Operational Scenarios
Scenario Name | Flight Plan | Airspace | Purpose of Flight | Aircraft | Mature State Highlights
Flight Planning | IFR, Notify | All | N/A | All | Negotiation of flight plan prior to departure and updates during flight.
Surface Operations | N/A | Class C or Class D | N/A | All | For ground movement on towered airports. Interact with other traffic and ATC on the surface.
Border Patrol/ Monitoring | IFR | Class C arr/dep, aerial work in Class A and Class E | Border patrol | Predator B | Planned maneuver and unplanned deviation. Negotiated delay in return to airport. Go-around.
Atmospheric Monitoring (HALE) | IFR | Class A, Class E high altitude | Environmental Sensing | HALE | Slow transition through Class A. Long-endurance above FL600.
Search and Rescue | Notify | Class G | Survey at night | ScanEagle | Survey operations in Class G airspace.
Highway Traffic Reporting | IFR | Class D departure, Class B aerial work | Media and traffic reporting | Fire Scout helicopter | Follow defined route. Hovering operations.
Environmental Sampling | IFR | Class E with Class B transition | Monitor coal plant air emissions | Aerosonde | Class B transition, grid pattern in Class E. 4D trajectory operations. Early termination for weather.
Cargo/Mail Delivery | IFR | Class D departure, Class E en route and arrival | Cargo delivery | Cessna Caravan | ATM weather reroute and pilot weather deviation.
Oceanic Cargo/Mail Delivery | IFR | Class A oceanic, Class B arrival | International cargo | B747 | Oceanic high altitude point-to-point operations. In-trail climb procedure. High-density airspace operations to include OPD.
Delegated Separation Environmental Sampling | IFR | Class E | Exploration in Class E | Shadow | IFR flight with delegated separation for exploration in Class E airspace.
Lost Link | IFR | Class A | Demonstrate what ‘known and predictable’ means | Any UA certified to operate in Class A | LL profile, standardized LL contingency plans, LL recovery plans and procedures.

## Slide 25: Roles & Responsibilities
UAS Steering Group (USG)
Service/Responsibility Allocation Tables

## Slide 26: UAS Steering Group (USG)
USG organized as cross-organizational forum
  Included representation from FAA across lines of business (LOBs)
  Provided executive direction and guidance for maturation and validation of UAS operational concepts
  Reviewed and provided input to concept maturation products as they evolved
  Recognized interdependency of issues
  Used to gain agreement/consensus regarding scenarios’ narratives, objectives, outcomes, and requirements

## Slide 27: Service/Responsibility Allocations
Identified the need to resolve specific uncertainties and unknowns associated with the UAS operational scenarios
Allocated responsibilities among the ANSP and pilot-in-command (PIC) of UAS / manned aircraft for functions such as:
  Flight Planning
  Flight Data Processing
  NOTAMs
  Separation
  Hazard Avoidance (terrain/obstacles, weather)
  Advisories (traffic, weather, wake turbulence)
Identified gaps and shortfalls to inform rulemaking, airspace needs, and procedures development
Reached consensus on the allocations via vetting with UAS Steering Group (USG)

## Slide 28: Sample Service/Responsibility Allocation Table

## Slide 29: Sample Service/Responsibility Allocation Table
Notes: UAS use acceptable means of DAA with collision avoidance capability (in red).

## Slide 30: Low Altitude Operating Concepts

## Slide 31: Low Altitude Concept Development
Focused on low altitude UAS operations and explored under what circumstances the UAS ‘file and fly’ IFR requirement (ConOps v2.0) is not practical or doable and/or where a new operating concept (i.e., notification) needs to be described
Developed concept paper on low altitude, predominantly segregated scenarios, and included narrative on UAS Traffic Management (UTM) operations, that fall outside the scope of the UAS ConOps
Identified shortfalls associated with today’s UAS capabilities and FAA infrastructure in conducting low altitude operations and developed potential mitigations for allowing access (e.g., through use of airspace constructs) in response to increasing demand
Derived associated operational requirements for both the FAA and the UAS operator

## Slide 32: Low Altitude Operating Concepts Paper
Covers VLOS, EVLOS, BVLOS, & Integrated operations
Low altitude arbitrarily defined as <1200 ft. AGL
6 scenarios presented (not all UTM scenarios represented)
Key aspects
  Notification/Authorization or Flight Plan
  Use of Airspace Constructs or Authorized Areas of Operations
  Clear Delineation of Responsibilities among UAS operator/PIC, ANSP, manned aircraft operators/PICs
Based on multi-year UAS executive and subject matter expert reviews of concept and scenario products

## Slide 33: Airspace Constructs and Scenarios
Structured/Designated Route over Low Populated Areas (BVLOS)
Ex: Pipeline Surveillance
Dynamic Allocated Airspace over Low Populated Areas (BVLOS)
Ex: Search and Rescue
Below 400ft AGL in Authorized Areas of Operation
UTM Operations
Extended Visual over Low Populated Areas
Ex: Agricultural Monitoring
Integrated Operations (BVLOS)
Ex: Highway Traffic Reporting
Dynamic Allocated Airspace over Populated Areas (VLOS)
Ex: Accident Scene Investigation

## Slide 34: Strategic Plans Moving Forward

## Slide 35: From Concepts to Operational Focus Areas
Notes: Developed AJV-7 UAS Concept Maturation Plan to address air traffic–related challenges to support the evolution of UAS operations in the NAS
  Plan identifies concept maturation activities AJV-7 proposes to lead (i.e., sponsor) or support (i.e., consult or participate in), subject to availability of funding/resources
  Activities are identified in the form of concept maturation questions that need to be answered through supporting concept exploration, development, and validation efforts
Foundational inputs include the FAA UAS ConOps and the Mid-Term UAS Scenarios:
  UAS ConOps – describes integrated UAS operations in the future NAS and contains mature state (integration) scenarios designed to demonstrate a variety of operations
  Mid-Term UAS Scenarios – describes how UAS are envisioned to operate in the NAS when certain policies and procedures have not yet been established and certain capabilities, such as airborne DAA, have not been certified for operational use
These two products informed subsequent artifacts:
  UAS concept-level requirements were derived for services, automation systems, capabilities, procedures, training, and policies, and were allocated to either the FAA or the UAS operator community
    UAS requirements allocated to the FAA were then aligned and grouped by their relevant shortfalls
  Service/Responsibility Allocation Tables were developed for each Mid-Term and Mature State UAS scenario and vetted with the UAS Steering Group (USG)
  ATO UAS Operations Evolution Strategy (OES) was developed based on the vision established in ConOps and scenarios
AJV-7 UAS Concept Maturation Plan supports the OES milestones and addresses FAA shortfalls required to enable a number of UAS mid-term and mature state (i.e., far-term) operations.
Note: Completed, ongoing, and planned UAS concept development/research efforts will serve as an input for further scoping and detailing the work that AJV-7 will lead or support. This will be addressed during the development of supporting concept maturation proposals

## Slide 36: Concept Maturation (CM) Plan Activities Template
Associated Requirement(s)
Associated Shortfall

## Slide 37: Operations Evolution Strategy (OES)
Internal reference document to facilitate UAS integration planning
Discusses the evolution of UAS operations and key air traffic related milestones that must be achieved to transition from current day accommodation of UAS on a case-by-case basis to integration
Provides insight into how the milestones contribute to enabling a number of representative UAS operational scenarios in the mid-term and mature state timeframes
Milestones are grouped by the following swimlanes:
  Airspace Management, Policy, and Procedures
  Safety
  ATC/ATM Training
  ATC/ATM Automation
  Certification and Flight Rules

## Slide 38: Operations Evolution Strategy (OES) (cont.)
UAS Mission-Specific Operations and Scenarios
UAS Non–Mission-Specific Operations and Scenarios

## Slide 39: CM Activities to Lead
Activity ID | Concept Maturation Activity | Associated Shortfall | Associated FAA Req(s) | Priority | FY Funding
R1.16 | ATC Receipt and Display of Contingency Information | S1.16 | 1-120 | High | FY16 & FY17
R2.2 | Radar Detection, Differentiation, and Tracking of Non-Cooperative UAS with Small Radar Cross Sections | S2.2 | TBD | High | FY16
R4.8 | Impact of Proposed Control Link and Communications Latency Thresholds on ATC | S4.8 | 1-51, 1-70 | High | FY17
R1.19 | Impact of Communications Latency Exceeding Acceptable Thresholds on ATC | S1.19 | 1-108 | High | FY17
R1.15.1 | Thresholds for Lost Link Duration | S1.15.1 | 1-65 | High | FY17
R1.10 | Impact of UAS Performance Limitations in the Terminal Domain | S1.10 | 1-133 | High | FY17 or FY18
R4.6 | Incorporating UAS Type Designations and Performance Characteristics into ATC Automation | S4.6 | 1-129 | High | FY18
R4.2 | Trajectory Modeling of Unique (Planned and Unplanned) UAS Flight Profiles | S4.2 | 1-7, 1-91 | High | FY17 or FY18
R4.3 | Conflict Detection and Resolution for Unique UAS Flight Profiles | S4.3 | 1-92 | High | FY17 or FY18
R4.12 | UAS Flight Data for Flight Object | S4.12 | 1-68 | High | FY18
R4.1.1 | Increasing Flight Plan Route Elements and Characters | S4.1.1 | 1-89, 1-102 | High | FY18
R5.12 | ATC Interaction with Airborne DAA | S5.12 | 1-111 | High | FY18
R1.5 | Impact of Long Duration UAS Operations on ATC | S1.5 | 1-96 | Medium | FY18
R4.1.3 | Flight Planning Capabilities for Long Duration Flights | S4.1.3 | 1-6, 1-93 | Medium | FY18
R4.1.4 | Flight Plan Feedback for UAS | S4.1.4 | 1-8, 1-78 | Medium | FY18
R4.1.5 | Processing Flight Plans with Fixes in Latitude/Longitude Format | S4.1.5 | 1-132 | Low | FY18
R4.1.6 | Incorporating UAS 4D Trajectory Data into Flight Plans | S4.1.6 | 1-97 | Low | FY18
R4.4 | Incorporating Operational Priority Assignments into ATC/TFM Automation | S4.4 | 1-44, 1-123 | Low | FY18
R4.9 | Data Communications for UAS | S4.9 | 1-42 | Low | FY18
R4.5 | Automation Support for Demand and Capacity Balancing | S4.5 | 1-134 | Low | FY18
R4.11 | Lost Link Beacon Code | S4.11 | 1-114 | N/A (Being Addressed) | N/A
R4.1.2 | Identifying UAS Type Designations and Performance Characteristics | S4.1.2 | 1-80, 1-105 | N/A (Being Addressed) | N/A

## Slide 40: CM Activities to Support
Activity ID | Concept Maturation Activity | Associated Shortfall | Associated FAA Req(s) | Priority | FY Funding
R1.1.1 | Notification of UAS Operations when a Flight Plan is Not Required | S1.1.1 | 1-130 | High | FY16
R1.1.2 | Flight Planning and Flight Rules when an IFR Flight Plan is Not Required | S1.1.2 | 1-113, 1-117 | High | FY16 & FYXX
R1.14 | Conditions Under Which Lost Link Constitutes an Emergency | S1.14 | 1-127 | High | FY17
R1.13 | ATC Procedures and Phraseology for Lost Link and Flight Termination Events | S1.13 | 1-124, 1-125, 1-126 | High | FY17
R1.20 | Segregation Alternatives for BVLOS UAS Operations in Controlled and Uncontrolled Airspace | S1.20 | 1-131 | High | FY18
R1.6 | ATC Procedures and Phraseology for Unique UAS Flight Profiles | S1.6 | 1-106 | High | FY17 or FY18
R1.4 | Collection and Distribution of UAS Mission-Related Information | S1.4 | 1-107 | High | FY18
R1.18 | ATC Procedures for Lost Communications Events | S1.18 | 1-119 | High | FY18
R5.8 | Alternatives to Visual-Based Separation and Navigation | S5.8 | 1-61 | High | FY18
R1.17 | ATC Procedures for Loss of DAA | S1.17 | 1-37 | Medium | FY18
R1.12 | FAA Guidelines for UAS Operator Contingency Responses (Plans) | S1.12 | 1-53 | Medium | FY18
R1.3 | Operational Priority for UAS Flights or Flight Segments | S1.3 | 1-9, 1-62 | Low | FY18
R1.9.1 | Concept for Delegated Separation | S1.9.1 | 1-10, 1-116 | Low | FY18
R1.9.2 | ATC Procedures and Phraseology for Delegated Separation | S1.9.2 | 1-112 | Low | FY18
R5.4 | Proposed Control Link Latency Thresholds | S5.4 | 1-51 | N/A (Being Addressed) | N/A
R5.5 | Proposed Communications Latency Thresholds | S5.5 | 1-70 | N/A (Being Addressed) | N/A
R1.15.2 | Acceptable DAA Maneuvers During Lost Link Events | S1.15.2 | 1-115 | N/A (Being Addressed) | N/A
R5.6 | Quantitative Values for DAA Self-Separation and Collision Avoidance Functions | S5.6 | 1-60, 1-109 | N/A (Being Addressed) | N/A

## Slide 41: DEEP DIVE: Traceability from ConOps to 2016 Projects
Contingency Information

## Slide 42: FAA UAS ConOps Excerpts
UAS operators develop contingency responses based upon established FAA guidelines and pre-defined procedures as part of the approval process, consistent with operational requirements.
UAS operators provide the contingency information and procedures during flight planning, which are then accessible to ATC through automation and associated decision support tools.
Contingency responses may apply uniformly for the entire flight trajectory, or may change for each discrete flight segment.
Regardless of the reason for the contingency operation, the UAS response is known, predictable, and benign to the greatest extent possible in its impact to ATC and other air traffic.

## Slide 43: Associated Shortfall & Requirement
Shortfall S1.16 – The ability for ATC to obtain timely contingency information (and display it when required) is inadequate.
Requirement 1-120 – ATC will obtain the applicable pre-determined (and approved) contingency information from automation and/or the PIC (and display it when required).

## Slide 44: Allocation Tables (Mid-Term)

## Slide 45: Allocation Tables (Mature State)

## Slide 46: ATO UAS OES Milestones
OES discusses the following contingency-related milestones:
  AMP-5 – Develop Contingency Procedures
  TR-2 – Train ATC on Contingency Procedures
These milestones must be realized to support all of the following categories of UAS operations:

## Slide 47: Concept Maturation Activity
Activity ID | Concept Maturation Activity | Associated Shortfall | Associated FAA Req(s) | AJV-7 Role | Priority
R1.16 | ATC Receipt and Display of Contingency Information [OES MS Supported: AMP-5] | S1.16 | 1-120 | Lead | High
Concept Maturation Questions:
What types of contingency information needs to be provided to ATC (e.g., lost link routes, flight termination routes; procedures for loss of DAA, loss of communications, other equipment problems) and what are the information requirements (i.e., scope of information that needs to be provided)?
What is the best mechanism for ATC to obtain, store, and verify contingency information from the UAS operator pre-departure?
  If a UAS operator files a flight plan
  If a UAS operator provides notification to FAA through other means
Is it feasible to provide relevant contingency information to ATC during the time of the contingency?
If a UA deviates off a planned flight plan route in the en route or terminal domain, how will ATC obtain, store, and verify updated contingency information?
What are the best mechanisms for ATC / ATM to display contingency information?
Notes:
DoD suggests consideration of the following: adopt the capability to select each fix or waypoint on a controller’s display to identify and activate any associated contingency routes or actions.
Closely related concept maturation activity: R1.4 (Collection and Distribution of UAS Mission-Related Information)

## Slide 48: FY16 Tasking
ATC Receipt and Display of Contingency Information [When an IFR Flight Plan is Filed] – Identify contingency information and display requirements for terminal and en route automation systems when filing an IFR flight plan is required. Conduct interface alternatives analyses to establish the best mechanisms for delivering and displaying contingency information to ATC/ATM.
Task | Start | End | Deliverables
Task 1: Literature review | T | T+3 | En Route and Terminal UAS Contingency Requirements Literature Review Results [Report or Briefing]
Task 2a: En Route Cognitive Walkthrough | T+3 | T+7 | Information and Display Requirements for UAS Contingencies for En Route Systems When an IFR Flight Plan is Filed [Report]
Task 2b: Terminal Cognitive Walkthrough | T+7 | T+10 | Information and Display Requirements for UAS Contingencies for Terminal Systems When an IFR Flight Plan is Filed [Report]
Task 3: Review Contingency Information and Display Requirements | T+10 | T+11 | N/A
Task 4: Identify Affected Terminal and En Route Systems, System Architectures, and Capability Gaps | T+11 | T+14 | N/A
Task 5a: Perform En Route Interface Alternatives Analyses | T+14 | T+17 | UAS Contingencies Interface Alternatives Analyses Results for En Route Systems when an IFR Flight Plan is Filed [Report]
Task 5b: Perform Terminal Interface Alternatives Analyses | T+17 | T+20 | UAS Contingencies Interface Alternatives Analyses Results for Terminal Systems when an IFR Flight Plan is Filed [Report]

## Slide 49: FY16 Tasking (cont.)
ATC Receipt and Display of Contingency Information [When a Notification is Submitted] – Develop the concept, operational scenarios, and operational and information requirements for UAS contingency management when a notification is submitted (in lieu of an IFR flight plan). Determine applicability and suitability of the interface alternatives analyses results for the notification concept.
Task | Start | End | Deliverables
Task 1: Concept Development | T | T+6 | Draft Concept for Contingency Management (for Notification) [Document]
Task 2: Scenario Development | T | T+6 | Draft Operational Scenarios for Contingency Management (for Notification) [Document or Slides]
Task 3: Requirements Development | T | T+9 | Draft Requirements for Contingency Management (for Notification) [Document]
Task 4: Concept, Scenarios, and Requirements Vetting with CPCs | T+9 | T+13 | Final versions of above 3 deliverables
Task 5: Interface Alternatives Assessment | T+17 | T+23 | Assessment for Applicability of Interface Alternatives Analysis Results [Document]

## Slide 50: Notification/Authorization Hobbyist & sUAS Operations Near Airports/Towers Uncontrolled Airspace Operations

## Slide 51: Hobbyist & sUAS Operations Near Airports/Towers
Focused on developing requirements for an automated system intended to support model aircraft operations requiring ATC notification, and sUAS operations requiring ATC authorization prior to operating near airports
Workgroup consisted of representatives from across the Air Traffic Organization, NextGen, Legal and NATCA
Scope in support of Part 101-E and Part 107:
  Develop information requirements (i.e., identify information that needs to be provided to ATC)
  Develop requirements for an automated means to support the ATC notification / authorization processes
Requirements are levied on the system, the operator, and ATC
System requirements were provided to the FAA’s Program Management Office (PMO) for implementation

## Slide 52: Uncontrolled Operations
Proposed effort focused on developing and implementing a Flight Information Management System to effectively support the submission of UAS flight intent where filing an IFR flight plan is not practical, doable, or necessary
The system will predominantly support sUAS operations in low-altitude uncontrolled airspace, including UAS Traffic Management (UTM) operations—but could extend to larger UAS, higher altitudes, controlled airspace, and possibly urban areas (if deemed appropriate)
Intent is to provide a means for
  Other airspace users to access UAS flight information to support de-confliction with other aircraft
  ATC to maintain awareness of UAS activity, provide feedback to the UAS operator, and provide separation and advisory services, as required [if notification extends to controlled airspace]

## Slide 53: UTM Concept Elements

## Slide 54: UTM RTT
Subgroups established to address
  Concepts and Use Cases (Overarching)
  Data and Information Exchange (Notification & Airspace)
  Information Architecture
  Performance (Communications & Navigation)
  Sense and Avoid (Surveillance & Control)
54

## Slide 55: Current Activities

## Slide 56: FY16 Activities
ATC Receipt and Display of Contingency Information [When an IFR Flight Plan is Filed] – Identify contingency information and display requirements for terminal and en route automation systems when filing an IFR flight plan is required. Conduct interface alternatives analyses to establish the best mechanisms for delivering and displaying contingency information to ATC/ATM.
ATC Receipt and Display of Contingency Information [When a Notification is Submitted] – Develop the concept, operational scenarios, and operational and information requirements for UAS contingency management when a notification is submitted (in lieu of an IFR flight plan). Determine applicability and suitability of the interface alternatives analyses results for the notification concept.

## Slide 57: FY16 Activities (cont’d)
Scenario Impact Analysis (Modeling & Fast-Time Simulations) – Explore and quantify the operational impacts of low-altitude mid-term UAS operational scenarios (and the concepts on which they are based) on the NAS and its operators in a fast-time modeling activity.
Risk Assessment – No Radar Detection, Differentiation, and Tracking Capability of Non-Cooperative UAS with Small Radar Cross Sections – Assess the risk associated with primary radar not detecting and identifying reduced radar cross section (RCS) aircraft, such as UAS, operating in terminal airspace.

## Slide 58: Wrap Up

## Slide 59: Mapping to UAS Operations Evolution
Products | Hobbyist | Commercial VLOS | Commercial BVLOS | Public | Integrated
FAA UAS ConOps, Version 2.0 |  |  |  |  | 
UAS Operational Requirements |  |  |  |  | 
Mid-Term UAS Scenarios |  |  |  |  | 
Mid-Term UAS Scenario Allocation Tables |  |  |  |  | 
Mature State UAS Scenarios |  |  |  |  | 
Mature State UAS Scenario Allocation Tables |  |  |  |  | 
UAS Concept Maturation Plan |  |  |  |  | 
UAS Operations Evolution Strategy (OES) |  |  |  |  | 
Low Altitude UAS Operating Concepts |  |  |  |  | 
ATC Notification/Authorization Requirements for Interim Capability (In progress) |  |  |  |  | 
UAS Flight Information Management System (Proposed) |  |  |  |  | 

## Slide 60: Next Steps
Continue to explore the evolution of UAS operations while addressing future integration of UAS into the NAS.
Continue identifying and maturing UAS needs as they relate to air traffic systems and services, and refining operational requirements associated with ATM automation, airspace management, policies, and procedures.
Continue to conduct the necessary concept engineering, requirements development, and investment analysis activities required to introduce NAS changes to support UAS operations.

## Slide 61: Questions?