## Slide 1: Office of Commercial Space Transportation
GAO Indemnification Study
COMSTAC, Business/Legal WG
Randy Repcheck
October 9, 2012

## Slide 2: Outline
Statutory Provisions for Financial Responsibility
GAO Study
Third Party Maximum Probable Loss Methodologies
Way Forward

## Slide 3: Statutory Provisions for Financial Responsibility
Notes: 3

## Slide 4: Insurance
Licensees and Permittees must obtain liability insurance or demonstrate financial responsibility to compensate for the maximum probable loss (MPL) from claims by:
  A third party for death, bodily injury, or property damage or loss; and
  The U.S. Government for damage or loss to government property.
Statutory ceilings:
  Third party - $500M maximum
  Government property - $100M maximum

## Slide 5: Indemnification
The U.S. Government will indemnify, subject to Congressional appropriation, a licensee for any claims above the insured amount.
  Up to $1.5B adjusted for inflation
  Approx. $2.7B
Space flight participants are not eligible for indemnification.
This provision sunsets on December 31, 2012.
  Previous sunsets: 1993, 1999, 2000, 2004, 2009

## Slide 6: Cross-Waivers
A licensee must sign reciprocal waivers of claims with its contractors, its customers, and the U.S. government.
Each party waives and releases claims against the other parties to the waivers and agrees to assume financial responsibility for:
  Property damage it sustains, and
  For bodily injury or property damage sustained by its own employees.
Purpose is to reduce litigation expenses by requiring launch participants to assume responsibility for their own losses.
Crew and space flight participants must execute reciprocal waivers of claims with the federal government.

## Slide 7: GAO Study
Notes: 7

## Slide 8: Scope of GAO Study
GAO was asked to address:
  The U.S. government’s indemnification policy compared to policies of other countries,
  The ability and willingness of the insurance market to provide additional coverage,
  The effects of ending indemnification on the competitiveness of U.S. launch companies, and
  The federal government’s potential costs for indemnification.

## Slide 9: Indemnification In Other Countries
GAO Finding:
The United States provides less commercial space launch indemnification for third party losses than China, France, and Russia.

## Slide 10: Insurance Market
GAO Finding:
The insurance market is generally willing and able to provide up to $500 million per launch as coverage for third party liability.
Because the amount of insurance FAA requires launch providers to obtain averages about $99 million per launch, insurers could provide some of the coverage currently available through CSLAA.
However, the amount and price of insurance that could be provided could change quickly if a large loss were to occur.

## Slide 11: Competitiveness
GAO Finding:
The effects on global competition from the United States eliminating CSLAA indemnification are unknown.
Launch companies and customers believe that ending federal indemnification could lead to higher launch prices for U.S.-based launch companies, making them less price competitive.
  How much is not clear.
Whether higher launch prices alone would be sufficient reason for a launch customer to choose a foreign company over a U.S. company is unclear.

## Slide 12: USG’s Potential Costs
GAO Finding:
The potential cost to the federal government of indemnifying third party losses is currently unclear because it depends in part on the method used by the FAA to calculate the amount of insurance that launch companies must purchase, a calculation that may not be sound.
FAA has used the same method since 1988 and has not updated crucial components, such as the cost of a casualty.
Estimating probable losses from a rare catastrophic event is difficult, and insurance industry officials and risk modeling experts said that FAA’s method is outdated.

## Slide 13: USG’s Potential Costs (cont.)
GAO Finding (cont.):
FAA has not had outside experts or risk modelers review the appropriateness of its method.
An inaccurate calculation that understates the amount of insurance a launch provider must obtain would increase the likelihood of costs to the federal government; a calculation that overstates the amount of insurance needed would raise the cost of insurance for the launch provider.
FAA said use of more sophisticated methodologies would have to be balanced with the additional costs to both FAA and the launch companies.

## Slide 14: Third Party Maximum Probable Loss Methodologies
Notes: 14

## Slide 15: Important Factors for Any Method
Third Party Threshold Value
  The chance of loss exceeding the required insurance is lower than 1 in 10,000,000 (or 10-7).
  A measure of potential US Government liability.
Cost of a Casualty
  FAA uses $3,000,000, although not defined in regulation.
  Covers both fatalities and serious injuries.
  May not be conservative, but any change must be made in concert with methodology change.

## Slide 16: Overlay Method Approach
Use the inert debris produced by a flight termination system activation as an upper bound for the debris produced by an aerodynamic or explosive breakup.
Overlay the debris over a credible population center and calculate casualties:
  Casualties = PD x CA
    PD – Population Density
    CA – Casualty Area
Calculate casualties due to secondary effects (fires, collapsing buildings, etc.).
  Estimated to be 1.5 times number of casualties due to debris.

## Slide 17: Overlay Method Approach (cont.)
Estimate total casualties:
  Total Casualties = (Casualties Due To Debris) + (Casualties Due To Secondary Effects)
Multiply total casualties by $3M (cost of a casualty).
Add 50% to this cost to account for property damage.

## Slide 18: Overlay Method (cont.) Example
Assume:
  PD = 6,000 persons/nmi2
  CA = 30,000 ft2
Casualties due to debris ≈ 5
Casualties due to secondary effects ≈ 8
Total Casualties = 13
Total cost of casualties = $39 million
After accounting for third party property damage ($19.5M) -
  MPL = $58.5 million

## Slide 19: Risk Profile Method Approach
The outcome is a plot that shows the probability of a given number of casualties or more versus the number of casualties.
Computed using thousands of simulated accidents with a debris footprint computed for each, with resulting casualties and property damage.
This method requires:
  Behaviors of a failing vehicle.
  Probabilities of each scenario.
  A description of the debris created.
  Numbers and locations of people at risk.
  Vulnerability models for exposed people and structures.

## Slide 20: Risk Profile Method Example Output

## Slide 21: Way Forward
Notes: 21

## Slide 22: GAO Recommendation
To better ensure the accuracy of FAA’s determination of the amount of insurance coverage required for an FAA commercial space launch license, we recommend that the Secretary of Transportation direct the Associate Administrator for Commercial Space Transportation to review and periodically reassess FAA’s maximum probable loss methodology—including assessing the reasonableness of the assumptions used.
For these reviews, the Associate Administrator should consider using external experts such as risk modelers, document the outcomes, and adjust the methodology, as appropriate, considering the costs.

## Slide 23: AST Efforts
The FAA is currently reviewing its current methodology for calculating MPL.
  Risk profile or other methodology may offer improvements.
  Will not add precision if no improvement in accuracy.
  Estimating the cost of extreme events remains difficult.
If its budget allows, the FAA will solicit outside expertise for this review.
The FAA will also plan to periodically review and update, if necessary, its MPL methodology.